## Slide 1: 15-744: Computer Networking
L-2 Design Considerations

## Slide 2: Announcements
Project
  Project ideas list – will update by Wed
  Project idea discussion meetings (15min)
    Thursday/Friday (1/26,1/27)
    Will bring signup to Wed lecture
    Think of two project ideas that interest you
  Project proposal
    ~1pg – intro/related work/plan of work
    due by email noon 2/1
Zhuo’s Office Hours - Wed 1:30-2:30pm
<number>

## Slide 3: Lecture: Design Considerations
<number>
How to determine split of functionality
  Across protocol layers
  Across network nodes
Assigned Reading
  [SRC84] End-to-end Arguments in System Design
  [Cla88] Design Philosophy of the DARPA Internet Protocols
Optional Reading
  [CT90] Architectural Considerations for a New Generation of Protocols
  [Clark02] Tussle in Cyberspace: Defining Tomorrow’s Internet

## Slide 4: Outline
<number>
Design principles in internetworks
IP design

## Slide 5: Goals [Clark88]
<number>
Connect existing networks
  initially ARPANET and ARPA packet radio network
Survivability
  ensure communication service even in the presence of network and router failures
Support multiple types of services
Must accommodate a variety of networks
Allow distributed management
Allow host attachment with a low level of effort
Be cost effective
Allow resource accountability

## Slide 6: Goal 0: Connecting Networks
<number>
How to internetwork various network technologies
  ARPANET, X.25 networks, LANs, satellite networks, packet networks, serial links…
Many differences between networks
  Address formats
  Performance – bandwidth/latency
  Packet size
  Loss rate/pattern/handling
  Routing
Notes: <number>
What are some choices?

## Slide 7: Challenge 1: Address Formats
<number>
Map one address format to another?
  Bad idea  many translations needed
Provide one common format
  Map lower level addresses to common format

## Slide 8: Challenge 2: Different Packet Sizes
<number>
Define a maximum packet size over all networks?
  Either inefficient or high threshold to support
Implement fragmentation/re-assembly
  Who is doing fragmentation?
  Who is doing re-assembly?

## Slide 9: Gateway Alternatives
<number>
Translation
  Difficulty in dealing with different features supported by networks
  Scales poorly with number of network types (N^2 conversions)
Standardization
  “IP over everything” (Design Principle 1)
  Minimal assumptions about network
  Hourglass design

## Slide 10: IP Standardization
Minimum set of assumptions for underlying net
  Minimum packet size
  Reasonable delivery odds, but not 100%
  Some form of addressing unless point to point
Important non-assumptions:
  Perfect reliability
  Broadcast, multicast
  Priority handling of traffic
  Internal knowledge of delays, speeds, failures, etc
Also achieves Goal 3: Supporting Varieties of Networks
<number>
Notes: <number>

## Slide 11: IP Hourglass
Need to interconnect many existing networks
Hide underlying technology from applications
Decisions:
  Network provides minimal functionality
  “Narrow waist”
Tradeoff: No assumptions, no guarantees.
Technology
Applications
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...
<number>
Notes: <number>

## Slide 12: IP Layering (Principle 2)
<number>
Relatively simple
Sometimes taken too far
Router
Router
Host
Host
Application
Transport
Network
Link

## Slide 13: Survivability
If network disrupted and reconfigured
  Communicating entities should not care!
  No higher-level state reconfiguration
How to achieve such reliability?
  Where can communication state be stored?
<number>
 | Network | Host
Failure handing | Replication | “Fate sharing”
Net Engineering | Tough | Simple
Switches | Maintain state | Stateless
Host trust | Less | More
Notes: <number>

## Slide 14: Principle 3: Fate Sharing
Lose state information for an entity if and only if the entity itself is lost.
Examples:
  OK to lose TCP state if one endpoint crashes
    NOT okay to lose if an intermediate router reboots
  Is this still true in today’s network?
    NATs and firewalls
Survivability compromise: Heterogeneous network  less information available to end hosts and Internet level recovery mechanisms
Connection State
State
No State
<number>
Notes: <number>

## Slide 15: Principle 4: Soft-state
<number>
Soft-state
  Announce state
  Refresh state
  Timeout state
Penalty for timeout – poor performance
Robust way to identify communication flows
  Possible mechanism to provide non-best effort service
Helps survivability

## Slide 16: Principle 5: End-to-End Argument
<number>
Deals with where to place functionality
  Inside the network (in switching elements)
  At the edges
Argument
  There are functions that can only be correctly implemented by the endpoints – do not try to completely implement these elsewhere
  Guideline not a law

## Slide 17: Example: Reliable File Transfer
<number>
Solution 1: make each step reliable, and then concatenate them
Solution 2: end-to-end check and retry
OS
Appl.
OS
Appl.
Host A
Host B
OK

## Slide 18: E2E Example: File Transfer
Even if network guaranteed reliable delivery
  Need to provide end-to-end checks
  E.g., network card may malfunction
  The receiver has to do the check anyway!
Full functionality can only be entirely implemented at application layer; no need for reliability from lower layers
Does FTP look like E2E file transfer?
  TCP provides reliability between kernels not disks
Is there any need to implement reliability at lower layers?
<number>

## Slide 19: Discussion
<number>
Yes, but only to improve performance
If network is highly unreliable
  Adding some level of reliability helps performance, not correctness
  Don’t try to achieve perfect reliability!
  Implementing a functionality at a lower level should have minimum performance impact on the applications that do not use the functionality

## Slide 20: Examples
<number>
What should be done at the end points, and what by the network?
  Reliable/sequenced delivery?
  Addressing/routing?
  Security?
  What about Ethernet collision detection?
  Multicast?
  Real-time guarantees?

## Slide 21: Goal 2: Types of Service
Principle 6: network layer provides one simple service: best effort datagram (packet) delivery
  All packets are treated the same
Relatively simple core network elements
Building block from which other services (such as reliable data stream) can be built
Contributes to scalability of network
No QoS support assumed from below
  In fact, some underlying nets only supported reliable delivery
    Made Internet datagram service less useful!
  Hard to implement without network support
  QoS is an ongoing debate…
<number>
Notes: <number>

## Slide 22: Types of Service
TCP vs. UDP
  Elastic apps that need reliability: remote login or email
  Inelastic, loss-tolerant apps: real-time voice or video
  Others in between, or with stronger requirements
  Biggest cause of delay variation: reliable delivery
    Today’s net: <100ms RTT
    Reliable delivery can add seconds.
Original Internet model: “TCP/IP” one layer
  First app was remote login…
  But then came debugging, voice, etc.
  These differences caused the layer split, added UDP
<number>
Notes: <number>

## Slide 23: Goal 4: Decentralization
<number>
Principle 7: Each network owned and managed separately
  Will see this in BGP routing especially
Principle 7’: Be conservative in what you send and liberal in what you accept
  Unwritten rule
Especially useful since many protocol specifications are ambiguous
E.g. TCP will accept and ignore bogus acknowledgements

## Slide 24: The “Other” goals
<number>
5. Attaching a host
  Host must implement hard part   transport services
    Not too bad
6. Cost effectiveness
  Packet overhead less important by the year
  Packet loss rates low
  Economies of scale won out
  Internet cheaper than most dedicated networks
But…

## Slide 25: 7. Accountability
<number>
Huge problem
Accounting
  Billing? (mostly flat-rate. But phones have become that way also - people like it!)
  Inter-ISP payments
    Hornet’s nest. Complicated. Political. Hard.
Accountability and security
  Huge problem.
  Worms, viruses, etc.
    Partly a host problem. But hosts very trusted.
  Authentication
    Purely optional. Many philosophical issues of privacy vs. security.
  Greedy sources aren’t handled well

## Slide 26: Other IP Design Weaknesses
<number>
Weak administration and management tools
Incremental deployment difficult at times
  Result of no centralized control
  No more “flag” days
  Are active networks the solution?

## Slide 27: Summary: Internet Architecture
<number>
Packet-switched datagram network
IP is the “compatibility layer”
  Hourglass architecture
  All hosts and routers run IP
Stateless architecture
  no per flow state inside network
IP
TCP
UDP
ATM
Satellite
Ethernet

## Slide 28: Summary: Minimalist Approach
<number>
Dumb network
  IP provide minimal functionalities to support connectivity
    Addressing, forwarding, routing
Smart end system
  Transport layer or application performs more sophisticated functionalities
    Flow control, error control, congestion control
Advantages
  Accommodate heterogeneous technologies (Ethernet, modem, satellite, wireless)
  Support diverse applications (telnet, ftp, Web, X windows)
  Decentralized network administration

## Slide 29: Summary
Successes: IP on everything!
Drawbacks… but perhaps they’re totally worth it in the context of the original Internet. Might not have worked without them!
“This set of goals might seem to be nothing more than a checklist of all the desirable network features. It is important to understand that these goals are in order of importance, and an entirely different network architecture would result if the order were changed.”
<number>

## Slide 30: Changes Over Time
Developed in simpler times
  Common goals, consistent vision
With success came multiple goals – examples:
  ISPs must talk to provide connectivity but are fierce competitors
  Privacy of users vs. government’s need to monitor
  User’s desire to exchange files vs. copyright owners
Must deal with the tussle between concerns in design
<number>

## Slide 31: New Principles?
Design for variation in outcome
  Allow design to be flexible to different uses/results
Isolate tussles
  QoS designs uses separate ToS bits instead of overloading other parts of packet like port number
  Separate QoS decisions from application/protocol design
Provide choice  allow all parties to make choices on interactions
  Creates competition
  Fear between providers helps shape the tussle
<number>

## Slide 32: Integrated Layer Processing (ILP)
Layering is convenient for architecture but not for implementations
Combining data manipulation operations across layers provides gains
  E.g. copy and checksum combined provides 90Mbps vs. 60Mbps separated
Protocol design must be done carefully to enable ILP
Performance bottlenecks
  In paper: presentation overhead, application-specific processing >> other processing
  Today: memory bandwidth
<number>

## Slide 33: Application Lever Framing (ALF)
<number>
Objective: enable application to process data ASAP
Application response to loss
  Retransmit (TCP applications)
  Ignore (UDP applications)
  Recompute/send new data (clever application)
Expose unit of application processing (ADU) to protocol stack

## Slide 34: Application Data Units Requirements
<number>
ADUs can be processed in any order
Naming of ADUs should help identify position in stream
Size
  Enough to process independently
  Impact on loss recovery
  What if size is too large?

## Slide 35: NSF Programs
Stagnation
  100x100  Clean Slate Design
  PlanetLab
  Overcoming the Internet Impasse through Virtualization  GENI
Internet architecture projects
    Named Data Networking
    MobilityFirst
    eXpressive Internet Architecture
<number>
Notes: <number>

## Slide 36: Named Data Networking
In the beginning...
  First applications strictly focused on host-to-host interprocess communication:
    Remote login, file transfer, ...
  Internet was built around this host-to-host model.
  Architecture is well-suited for communication between pairs of stationary hosts.
... while today
  Vast majority of Internet usage is data retrieval and service access.
  Users care about the content and are oblivious to location. They are often oblivious as to delivery time:
    Fetching headlines from CNN, videos from YouTube, TV from Tivo
    Accessing a bank account at www.bank.com.
<number>

## Slide 37: What does the network look like…
ISP
ISP
<number>

## Slide 38: What should the network look like…
ISP
ISP
<number>

## Slide 39: MobilityFirst Architecture
<number>

## Slide 40: A History of Internet Evolution
Hard to change IP
  …especially after 1990
<number>
IP
Applications
Technology
Innovation both above and below IP
Notes: <number>

## Slide 41: XIA: An Evolvable Internet Architecture
How do we design a network in which we can gracefully introduce new functionality?
Network design
How should the end-points change when the networks provide new functionality?
End-point design
<number>
Notes: <number>

## Slide 42: XIA: Evolvable Set of Principals
Identifying the intended communicating entities reduces complexity and overhead
  No need to force all communication at a lower level (hosts), as in today’s Internet
Allows the network to evolve
<number>
Host
Content
Services
Future
Entities
a581fe9 ...
d9389fa …
024e881 …
39c0348 …

## Slide 43: Outline
<number>
Design principles in internetworks
IP design

## Slide 44: IP Address Problem (1991)
<number>
Address space depletion
  In danger of running out of classes A and B
Why?
  Class C too small for most domains
  Very few class A – IANA (Internet Assigned Numbers Authority) very careful about giving
  Class B – greatest problem
    Sparsely populated – but people refuse to give it back

## Slide 45: IP Address Utilization (‘98)
<number>
http://www.caida.org/outreach/resources/learn/ipv4space/

## Slide 46: IPv4 Routing Problems
<number>
Core router forwarding tables were growing large
  Class A: 128 networks, 16M hosts
  Class B: 16K networks, 64K hosts
  Class C: 2M networks, 256 hosts
32 bits does not give enough space encode network location information inside address – i.e., create a structured hierarchy

## Slide 47: Solution 1 – CIDR
<number>
Assign multiple class C addresses
Assign consecutive blocks
RFC1338 – Classless Inter-Domain Routing (CIDR)

## Slide 48: Classless Inter-Domain Routing
<number>
Do not use classes to determine network ID
Assign any range of addresses to network
  Use common part of address as network number
  e.g., addresses 192.4.16 - 196.4.31 have the first 20 bits in common. Thus, we use this as the network number
  netmask is /20, /xx is valid for almost any xx
Enables more efficient usage of address space (and router tables)

## Slide 49: Solution 2 - NAT
<number>
Network Address Translation (NAT)
Alternate solution to address space
  Kludge (but useful)
Sits between your network and the Internet
Translates local network layer addresses to global IP addresses
Has a pool of global IP addresses (less than number of hosts on your network)

## Slide 50: NAT Illustration
<number>
Global Internet
Private
Network
Pool of global IP addresses
Operation: Source (S) wants to talk to Destination (D):
  Create Sg-Sp mapping
  Replace Sp with Sg for outgoing packets
  Replace Sg with Sp for incoming packets
D & S can be just IP addresses or IP addresses + port #’s
P
G
Dg
Sp
Data
NAT
Destination
Source
Dg
Sg
Data

## Slide 51: Solution 3 - IPv6
<number>
Scale – addresses are 128bit
  Header size?
Simplification
  Removes infrequently used parts of header
  40byte fixed size vs. 20+ byte variable
IPv6 removes checksum
  Relies on upper layer protocols to provide integrity
IPv6 eliminates fragmentation
  Requires path MTU discovery
  Requires 1280 byte MTU

## Slide 52: IPv6 Changes
<number>
TOS replaced with traffic class octet
Flow
  Help soft state systems
  Maps well onto TCP connection or stream of UDP packets on host-port pair
Easy configuration
  Provides auto-configuration using hardware MAC address to provide unique base
Additional requirements
  Support for security
  Support for mobility

## Slide 53: IPv6 Changes
<number>
Protocol field replaced by next header field
  Support for protocol demultiplexing as well as option processing
Option processing
  Options are added using next header field
  Options header does not need to be processed by every router
    Large performance improvement
    Makes options practical/useful

## Slide 54: Summary: IP Design
<number>
Relatively simple design
  Some parts not so useful (TOS, options)
Beginning to show age
  Unclear what the solution will be

## Slide 55: Next Lectures: Routing
<number>
Optional lecture on Monday
  Link-layer
  RIP, OSPF

## Slide 56: EXTRA SLIDES
<number>

## Slide 57: Fragmentation
<number>
IP packets can be 64KB
Different link-layers have different MTUs
Split IP packet into multiple fragments
  IP header on each fragment
  Various fields in header to help process
  Intermediate router may fragment as needed
Where to do reassembly?
  End nodes – avoids unnecessary work
  Dangerous to do at intermediate nodes
    Buffer space
    Multiple paths through network

## Slide 58: Fragmentation is Harmful
<number>
Uses resources poorly
  Forwarding costs per packet
  Best if we can send large chunks of data
  Worst case: packet just bigger than MTU
Poor end-to-end performance
  Loss of a fragment
Reassembly is hard
  Buffering constraints

## Slide 59: Path MTU Discovery
<number>
Hosts dynamically discover minimum MTU of path
Algorithm:
  Initialize MTU to MTU for first hop
  Send datagrams with Don’t Fragment bit set
  If ICMP “pkt too big” msg, decrease MTU
What happens if path changes?
  Periodically (>5mins, or >1min after previous increase), increase MTU
Some routers will return proper MTU
MTU values cached in routing table

## Slide 60: How is IP Design Standardized?
<number>
IETF
  Voluntary organization
  Meeting every 4 months
  Working groups and email discussions
“We reject kings, presidents, and voting; we believe in rough consensus and running code” (Dave Clark 1992)
  Need 2 independent, interoperable implementations for standard
IRTF
  End2End
  Reliable Multicast, etc..

## Slide 61: IPv4 Header – RFC791 (1981)
<number>
Source Address
Destination Address
0
4
16
24
32
Version
IHL
Type of Service
Total Length
Identification
Flags
Fragment Offset
Time to Live
Protocol
Header Checksum
Options
Padding
8
19

## Slide 62: IP Type of Service
<number>
Typically ignored
Values
  3 bits of precedence
  1 bit of delay requirements
  1 bit of throughput requirements
  1 bit of reliability requirements
Replaced by DiffServ

## Slide 63: Fragmentation Related Fields
<number>
Length
  Length of IP fragment
Identification
  To match up with other fragments
Flags
  Don’t fragment flag
  More fragments flag
Fragment offset
  Where this fragment lies in entire IP datagram
  Measured in 8 octet units (11 bit field)

## Slide 64: Other Fields
<number>
Header length (in 32 bit words)
Time to live
  Ensure packets exit the network
Protocol
  Demultiplexing to higher layer protocols
Header checksum
  Ensures some degree of header integrity
  Relatively weak – 16 bit
Options
  E.g. Source routing, record route, etc.
  Performance issues
    Poorly supported

## Slide 65: Addressing in IP
<number>
IP addresses are names of interfaces
Domain Name System (DNS) names are names of hosts
DNS binds host names to interfaces
Routing binds interface names to paths

## Slide 66: Addressing Considerations
<number>
Fixed length or variable length?
Issues:
  Flexibility
  Processing costs
  Header size
Engineering choice: IP uses fixed length addresses

## Slide 67: Addressing Considerations
<number>
Structured vs flat
Issues
  What information would routers need to route to Ethernet addresses?
    Need structure for designing scalable binding from interface name to route!
  How many levels? Fixed? Variable?

## Slide 68: IP Addresses
<number>
Fixed length: 32 bits
Initial classful structure (1981)
Total IP address size: 4 billion
  Class A: 128 networks, 16M hosts
  Class B: 16K networks, 64K hosts
  Class C: 2M networks, 256 hosts
High Order Bits
0
10
110
Format
7 bits of net, 24 bits of host
14 bits of net, 16 bits of host
21 bits of net, 8 bits of host
Class
A
B
C

## Slide 69: IP Address Classes (Some are Obsolete)
<number>
Network ID
Host ID
Network ID
Host ID
8
16
Class A
32
0
Class B
10
Class C
110
Multicast Addresses
Class D
1110
Reserved for experiments
Class E
1111
24

## Slide 70: Some Special IP Addresses
<number>
127.0.0.1: local host (a.k.a. the loopback address
Host bits all set to 0: network address
Host bits all set to 1: broadcast address

## Slide 71: Subnet Addressing – RFC917 (1984)
<number>
For class A & B networks
Very few LANs have close to 64K hosts
  For electrical/LAN limitations, performance or administrative reasons
Need simple way to get multiple “networks”
  Use bridging, multiple IP networks or split up single network address ranges (subnet)
  Must reduce the total number of network addresses that are assigned
CMU case study in RFC
  Chose not to adopt – concern that it would not be widely supported 

## Slide 72: Subnetting
<number>
Variable length subnet masks
  Could subnet a class B into several chunks
Network
Host
Network
Host
Subnet
1111..
00000000
..1111
Mask

## Slide 73: Subnetting Example
<number>
Assume an organization was assigned address 150.100
Assume < 100 hosts per subnet
How many host bits do we need?
  Seven
What is the network mask?
  11111111 11111111 11111111 10000000
  255.255.255.128

## Slide 74: Subnet Addressing Example
<number>
H1
H2
H3
H4
R1
150.100.12.128
150.100.12.154
150.100.12.176
150.100.12.129
150.100.12.0
150.100.12.4
To Internet
150.100.12.55
150.100.12.24
150.100.0.1
Assume a packet arrives with address 150.100.12.176
Step 1: AND address with subnet mask

## Slide 75: IPv4 Problems
<number>
Addressing
Routing

## Slide 76: IPv6 Header
<number>
Source Address
Destination Address
0
4
16
24
32
Version
Class
Flow Label
Payload Length
Next Header
Hop Limit
12
19

## Slide 77: Principle 4
<number>
Fate sharing
Critical state only at endpoints
Only endpoint failure disrupts communication
Helps survivability

## Slide 78: Internet & End-to-End Argument
<number>
Only one higher level service implemented at transport layer: reliable data delivery (TCP)
  Performance enhancement; used by a large variety of applications (Telnet, FTP, HTTP)
  Does not impact other applications (can use UDP)
  Original TCP & IP were integrated – Reed successfully argued for separation
Everything else implemented at application level