## Slide 1: 15-744 Computer Networks
Background Material 1:
Getting stuff from here to there
Notes: Overview, not depth

## Slide 2: Internet Layered Architecture
Switch
Router
Host
Host
Application
Transport
Network
Data Link
Presentation
Session
Physical
Today’s
focus

## Slide 3: IP Service Model
Best effort service
Datagram
  Each packet self-contained
    All information needed to get to destination
    No advance setup or connection maintenance
  Analogous to letter or telegram
0
4
8
12
16
19
24
28
31
version
HLen
TOS
Length
Identifier
Flag
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data
Header
IPv4 Packet
Format

## Slide 4: IP Header Fields
Header length (in 32 bit words)
Time to live (TTL)
  Ensure packets exit the network
Protocol
  Demultiplexing to higher layer protocols
Header checksum
  Ensures some degree of header integrity
  Relatively weak – 16 bit
Options
  E.g. Source routing, record route, etc.
  Performance issues
    Poorly supported

## Slide 5: Fragmentation Related Fields
Length
  Length of IP fragment
Identification
  To match up with other fragments
Flags
  Don’t fragment flag
  More fragments flag
Fragment offset
  Where this fragment lies in entire IP datagram
  Measured in 8 octet units (11 bit field)

## Slide 6: Keep in Mind…
Scale
  Billions of routers/hosts with IPv4 addresses (2^32)
Distributed management
  Little control about topology, etc.
IPv4 was designed in 1980s

## Slide 7: Outline
IP routing
  Addressing
  Forwarding
  Routing
  Name Lookup
Other
  NAT, VPN

## Slide 8: Addressing
Who should receive the message?
Addressing determines which packets are kept and which packets are thrown away
yak yak…

## Slide 9: IP Addresses
Fixed length: 32 bits
Initial classful structure (1981) (not relevant now!!!)
Total IP address size: 4 billion
  Class A: 128 networks, 16M hosts
  Class B: 16K networks, 64K hosts
  Class C: 2M networks, 256 hosts
High Order Bits
0
10
110
Format
7 bits of net, 24 bits of host
14 bits of net, 16 bits of host
21 bits of net, 8 bits of host
Class
A
B
C

## Slide 10: IP Address Classes (Some are Obsolete)
Network ID
Host ID
Network ID
Host ID
8
16
Class A
32
0
Class B
10
Class C
110
Multicast Addresses
Class D
1110
Reserved for experiments
Class E
1111
24

## Slide 11: IP Addresses: How to Get One?
Network (network portion):
Allocated from ISP’s address space:
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 12: IP Addresses: How to Get One?
How does an ISP get block of addresses?
  From Regional Internet Registries (RIRs)
    ARIN (North America, Southern Africa), APNIC (Asia-Pacific), RIPE (Europe, Northern Africa), LACNIC (South America)
How about a single host?
  Hard-coded by system admin in a file
  DHCP: Dynamic Host Configuration Protocol: dynamically get address: “plug-and-play”
    Host broadcasts “DHCP discover” msg
    DHCP server responds with “DHCP offer” msg
    Host requests IP address: “DHCP request” msg
    DHCP server sends address: “DHCP ack” msg
Notes: IANA (Internet Assigned Numbers Authority) really has control over addresses and allocates them to the RIRs
Currently, ICANN (Internet Corporation for Assigned Names and Numbers) has contract to run IANA

## Slide 13: IP Address Problem (1991)
Address space depletion
  In danger of running out of classes A and B
Why?
  Very few class A – IANA (Internet Assigned Numbers Authority) very careful about giving
  Class C too small for most domains
  Class B – greatest problem
    Sparsely populated – but people refuse to give it back
    Class B networks too big for LANs (64K hosts)
    For electrical/LAN limitations, performance or administrative reasons

## Slide 14: IP Address Utilization (‘98)
http://www.caida.org/outreach/resources/learn/ipv4space/

## Slide 15: Multiple Solutions
Classless Inter-Domain Routing (CIDR)
  Assign multiple consecutive class C addresses
  RFC1338 –Classless Inter-Domain Routing (CIDR)
IPv6
Network address translation (NAT)
  Later

## Slide 16: Solution 1: Classless Inter-Domain Routing (CIDR) – RFC1338
Allows arbitrary split between network & host part of address
  Do not use classes to determine network ID
  Use common part of address as network number
  E.g., addresses 192.4.16.0 - 192.4.31.255 have the first 20 bits in common. Thus, we use these 20 bits as the network number  192.4.16.0/20

## Slide 17: Solution 2 – IPv6

## Slide 18: IPv6 Changes
Scale – addresses are 128bit
  Header size?
Simplification
  Removes infrequently used parts of header
  40byte fixed size vs. 20+ byte variable
IPv6 removes checksum
  Relies on upper layer protocols to provide integrity
IPv6 eliminates fragmentation
  Requires path MTU discovery
  Requires 1280 byte MTU

## Slide 19: IPv6 Changes
TOS replaced with traffic class octet
Flow
  Help soft state systems
  Maps well onto TCP connection or stream of UDP packets on host-port pair
Easy configuration
  Provides auto-configuration using hardware MAC address to provide unique base
Additional requirements
  Support for security
  Support for mobility

## Slide 20: IPv6 Changes
Protocol field replaced by next header field
  Support for protocol demultiplexing as well as option processing
Option processing
  Options are added using next header field
  Options header does not need to be processed by every router
    Large performance improvement
    Makes options practical/useful

## Slide 21: Outline
IP routing
  Addressing
  Forwarding
  Routing
  Name Lookup
Other
  NAT, VPN

## Slide 22: Internet[work]
Internet[work]
A collection of interconnected networks
Host: network endpoints (computer, PDA, light switch, …)
Router: node that connects networks
  How do we forward messages?
Notes: What if want to communicate between hosts on different Ethernets? Internet as interoperability layer

## Slide 23: 1. Global Address Example
Receiver
Packet
R
Sender
2
3
4
1
2
3
4
1
2
3
4
1
R2
R3
R1
R
R
R  3
R  4
R  3
R
Notes: nice thing: makes minimal assumptions about the network!

## Slide 24: Original IP Route Lookup
Address would specify prefix for forwarding table
  Simple lookup
www.cmu.edu address 128.2.11.43
  Class B address – class + network is 128.2
  Lookup 128.2 in forwarding table
  Prefix – part of address that really matters for routing
Forwarding table contains
  List of class+network entries
  A few fixed prefix lengths (8/16/24)
Large tables
  2 Million class C networks

## Slide 25: Classless Inter-Domain Routing (CIDR) – RFC1338
Allows arbitrary split between network & host part of address
  Do not use classes to determine network ID
  Use common part of address as network number
  E.g., addresses 192.4.16 - 192.4.31 have the first 20 bits in common. Thus, we use these 20 bits as the network number  192.4.16/20
Enables more efficient usage of address space (and router tables)  How?
  Use single entry for range in forwarding tables
  Combined forwarding entries when possible

## Slide 26: Longest Prefix Match
Longest Prefix Match: Search for the routing table entry that has the longest match with the prefix of the destination IP address
Search for a match on all 32 bits
Search for a match for 31 bits
…..
32. Search for a match on 0 bits
Host route, loopback entry  32-bit prefix match
Default route is represented as 0.0.0.0/0  0-bit prefix match
128.143.71.21
The longest prefix match for 128.143.71.21 is for 24 bits with entry 128.143.71.0/24
packet will be sent to R4

## Slide 27: Route Aggregation
Longest prefix match algorithm permits the aggregation of prefixes with identical next hop address to a single entry
Destination | Next Hop
20.0.0.0/14 | R2
Destination | Next Hop
20.2.0.0/16 | R2
20.1.1.0/28 | R2

## Slide 28: Other ways to forward: 2. Source Routing Example
Receiver
Packet
R1, R2, R3, R
Sender
2
3
4
1
2
3
4
1
2
3
4
1
R2
R3
R1
R2, R3, R
R3, R
R
Notes: plus: router functionality is extremely simple
minus:
source has the burden of finding a route,
header size

## Slide 29: Routing to the Network
Provider
Packet to 10.1.1.3 arrives
Path is R2 – R1 – H1 – H2
H2
H3
H4
R1
10.1.1/24
10.1/16
10.1.8/24
10.1.0/24
10.1.1.3
10.1.2/23
R2
10.1.0.2
10.1.8.4
10.1.1.1
10.1.2.1
H1
10.1.1.2
10.1.8.1
10.1.2.1
10.1.0.1
10.1.2.2
10.1.1.4

## Slide 30: Routing Within the Subnet
Routing table at R2
H2
H3
H4
R1
10.1.1/24
10.1/16
10.1.8/24
10.1.0/24
10.1.1.3
10.1.2/23
R2
10.1.0.2
10.1.8.4
10.1.1.1
10.1.2.1
H1
Destination
Next Hop
Interface
127.0.0.1
127.0.0.1
lo0
Default or 0/0
provider
10.1.16.1
10.1.8.0/24
10.1.8.1
10.1.8.1
10.1.2.0/23
10.1.2.1
10.1.2.1
10.1.0.0/23
10.1.2.2
10.1.2.1
Packet to 10.1.1.3
Matches 10.1.0.0/23
10.1.1.2
10.1.8.1
10.1.2.1
10.1.0.1
10.1.2.2
10.1.1.4

## Slide 31: Routing Within the Subnet
Routing table at R1
Destination
Next Hop
Interface
127.0.0.1
127.0.0.1
lo0
Default or 0/0
10.1.2.1
10.1.2.2
10.1.0.0/24
10.1.0.1
10.1.0.1
10.1.1.0/24
10.1.1.1
10.1.1.4
10.1.2.0/23
10.1.2.2
10.1.2.2
Packet to 10.1.1.3
Matches 10.1.1.2/31
  Longest prefix match
10.1.1.2/31
10.1.1.4
10.1.1.1
H2
H3
H4
R1
10.1.1/24
10.1/16
10.1.8/24
10.1.0/24
10.1.1.3
10.1.2/23
R2
10.1.0.2
10.1.8.4
10.1.1.1
10.1.2.1
H1
10.1.1.2
10.1.8.1
10.1.2.1
10.1.0.1
10.1.2.2
10.1.1.4

## Slide 32: Routing Within the Subnet
H2
H3
H4
R1
10.1.1/24
10.1/16
10.1.8/24
10.1.0/24
10.1.1.3
10.1.2/23
R2
10.1.0.2
10.1.8.4
10.1.0.1
10.1.1.1
10.1.2.2
10.1.8.1
10.1.2.1
10.1.16.1
H1
Routing table at H1
Destination
Next Hop
Interface
127.0.0.1
127.0.0.1
lo0
Default or 0/0
10.1.1.1
10.1.1.2
10.1.1.0/24
10.1.1.2
10.1.1.1
10.1.1.3/31
10.1.1.2
10.1.1.2
Packet to 10.1.1.3
Direct route
  Longest prefix match
10.1.1.2
10.1.1.4

## Slide 33: Host Routing Table Example
From “netstat –rn”
Host 128.2.209.100 when plugged into CS ethernet
Dest 128.2.209.100  routing to same machine
Dest 128.2.0.0  other hosts on same ethernet
Dest 127.0.0.0  special loopback address
Dest 0.0.0.0  default route to rest of Internet
  Main CS router: gigrouter.net.cs.cmu.edu (128.2.254.36)
Destination Gateway Genmask Iface
128.2.209.100 0.0.0.0 255.255.255.255 eth0
128.2.0.0 0.0.0.0 255.255.0.0 eth0
127.0.0.0 0.0.0.0 255.0.0.0 lo
0.0.0.0 128.2.254.36 0.0.0.0 eth0

## Slide 34: Outline
IP routing
  Addressing
  Forwarding
  Routing
  Name Lookup
Other
  NAT, VPN

## Slide 35: Routing with Global Address
Receiver
Packet
R
Sender
2
3
4
1
2
3
4
1
2
3
4
1
R2
R3
R1
R
R
R  3
R  4
R  3
R
Notes: nice thing: makes minimal assumptions about the network!

## Slide 36: Distance-Vector Routing
Idea
  At any time, have cost/next hop of best known path to destination
  Use cost  when no path known
Initially
  Only have entries for directly connected nodes
A
E
F
C
D
B
2
3
6
4
1
1
1
3
Initial Table for A |  | 
Dest | Cost | Next Hop
A | 0 | A
B | 4 | B
C |  | –
D |  | –
E | 2 | E
F | 6 | F
Notes: Was first used in ARPANET until 1979, when it was replaced by link-state routing

## Slide 37: Distance-Vector Update
Update(x,y,z)
d  c(x,z) + c(z,y) # Cost of path from x to y with first hop z
if d < d(x,y)
# Found better path
return d,z # Updated cost / next hop
else
return d(x,y), nexthop(x,y) # Existing cost / next hop
x
z
y
c(x,z)
d(z,y)
d(x,y)

## Slide 38: Distance Vector: Link Cost Changes
Link cost changes:
Good news travels fast
Bad news travels slow - “count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 39: Distance Vector: Split Horizon
If Z routes through Y to get to X :
Z does not advertise its route to X back to Y
algorithm
terminates
X
Z
1
4
50
Y
60
?
?
?

## Slide 40: Distance Vector: Poison Reverse
If Z routes through Y to get to X :
Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
Eliminates some possible timeouts with split horizon
Will this completely solve count to infinity problem?
X
Z
1
4
50
Y
60
algorithm
terminates

## Slide 41: Poison Reverse Failures
update
“Count to infinity”
Solution
  Make “infinity” smaller
  What is upper bound on maximum path length?
Table for A |  | 
Dst | Cst | Hop
C | 7 | F
Table for B |  | 
Dst | Cst | Hop
C | 8 | A
Table for F |  | 
Dst | Cst | Hop
C | 1 | C
Table for F |  | 
Dst | Cst | Hop
C |  | –
Table for A |  | 
Dst | Cst | Hop
C |  | –
Forced
Update
Table for B |  | 
Dst | Cst | Hop
C | 14 | A
Forced
Update
F
C
6
1
1
1
B
D
A
4

Table for D |  | 
Dst | Cst | Hop
C | 9 | B
Forced
Update
Table for A |  | 
Dst | Cst | Hop
C | 13 | D
Better
Route
Table for D |  | 
Dst | Cst | Hop
C | 15 | B
Table for A |  | 
Dst | Cst | Hop
C | 19 | D
Forced
Update
•
•
•
Forced
Update

## Slide 42: Link State Protocol Concept
Every node gets complete copy of graph
  Every node “floods” network with data about its outgoing links
Every node computes routes to every other node
  Using single-source, shortest-path algorithm
Process performed whenever needed
  When connections die / reappear

## Slide 43: Sending Link States by Flooding
X Wants to Send Information
  Sends on all outgoing links
When Node B Receives Information from A
  Send on all links other than A
X
A
C
B
D
(a)
X
A
C
B
D
(b)
X
A
C
B
D
(c)
X
A
C
B
D
(d)

## Slide 44: Comparison of LS and DV Algorithms
Message complexity
LS: with n nodes, E links, O(nE) messages
DV: exchange between neighbors only O(E)
Speed of Convergence
LS: Complex computation
  But…can forward before computation
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
  (faster with triggered updates)
Space requirements:
  LS maintains entire topology
  DV maintains only neighbor state

## Slide 45: Scale problem (again)
Flat routing doesn’t scale
  Storage  Each node cannot be expected to store routes to every destination network
  Convergence times increase
  Communication  Total message count increases
Key observation
  Need less information with increasing distance to destination
  Need lower diameters networks
Solution: area hierarchy

## Slide 46: Routing Hierarchy
Partition Network into “Areas”
  Within area
    Each node has routes to every other node
  Outside area
    Each node has routes for other top-level areas only
    Inter-area packets are routed to nearest appropriate border router
Constraint: no path between two sub-areas of an area can exit that area
Backbone Areas
Lower-level Areas
Area-Border
Router

## Slide 47: Area Hierarchy Addressing
1
2
3
1.1
1.2
2.1
2.2
3.1
3.2
2.2.1
2.2.2
1.2.1
1.2.2
3.2.1
start
end

## Slide 48: Path Sub-optimality
1
2
3
1.1
1.2
2.1
2.2
3.1
3.2
2.2.1
3 hop red path
vs.
2 hop green path
start
end
3.2.1
1.2.1
Can result in sub-optimal paths

## Slide 49: Outline
IP routing
  Addressing
  Forwarding
  Routing
  Name Lookup
Other
  NAT, VPN

## Slide 50: DNS Design: Zone Definitions
root
edu
net
org
uk
com
ca
gwu
ucb
cmu
bu
mit
cs
ece
cmcl
Single node
Subtree
Complete Tree
Zone = contiguous section of name space
  E.g., Complete tree, single node or subtree
A zone has an associated set of name servers
  Must store list of names and tree links

## Slide 51: Typical Resolution
Client
Local
DNS server
root & edu
DNS server
ns1.cmu.edu
DNS server
www.cs.cmu.edu
NS ns1.cmu.edu
www.cs.cmu.edu
NS ns1.cs.cmu.edu
A www=IPaddr
ns1.cs.cmu.edu
DNS
server

## Slide 52: Workload and Caching
Are all servers/names likely to be equally popular?
  Why might this be a problem? How can we solve this problem?
DNS responses are cached
  Quick response for repeated translations
  Other queries may reuse some parts of lookup
    NS records for domains
DNS negative queries are cached
  Don’t have to repeat past mistakes
  E.g. misspellings, search strings in resolv.conf
Cached data periodically times out
  Lifetime (TTL) of data controlled by owner of data
  TTL passed with every record

## Slide 53: Subsequent Lookup Example
Client
Local
DNS server
root & edu
DNS server
cmu.edu
DNS server
cs.cmu.edu
DNS
server
ftp.cs.cmu.edu
ftp=IPaddr
ftp.cs.cmu.edu

## Slide 54: Link Layer Address Lookup
How does one find the Ethernet address of an IP host?
ARP (Address Resolution Protocol)
  Broadcast search for IP address
    E.g., “who-has 128.2.184.45 tell 128.2.206.138” sent to Ethernet broadcast (all FF address)
  Destination responds (only to requester using unicast) with appropriate 48-bit Ethernet address
    E.g, “reply 128.2.184.45 is-at 0:d0:bc:f2:18:58” sent to 0:c0:4f:d:ed:c6

## Slide 55: Outline
IP routing
  Addressing
  Forwarding
  Routing
  Name Lookup
Other
  NAT, VPN

## Slide 56: NAT: Opening Client Connection
Internet
Client 10.2.2.2 wants to connect to server 198.2.4.5:80
  OS assigns ephemeral port (1000)
Connection request intercepted by firewall
  Maps client to port of firewall (5000)
  Creates NAT table entry
Corporation X
W
NAT
W: Workstation
S: Server Machine
10.2.2.2:1000
S
198.2.4.5:80
243.4.4.4
Int Addr | Int Port | NAT Port
10.2.2.2 | 1000 | 5000
Firewall has valid IP address

## Slide 57: NAT: Client Request
Internet
Firewall acts as proxy for client
  Intercepts message from client and marks itself as sender
Corporation X
W
NAT
W: Workstation
S: Server Machine
10.2.2.2:1000
S
198.2.4.5:80
243.4.4.4
10.5.5.5
source: 10.2.2.2
dest: 198.2.4.5
src port: 1000
dest port: 80
source: 243.4.4.4
dest: 198.2.4.5
src port: 5000
dest port: 80
Int Addr | Int Port | NAT Port
10.2.2.2 | 1000 | 5000

## Slide 58: NAT: Server Response
Internet
Firewall acts as proxy for client
  Acts as destination for server messages
  Relabels destination to local addresses
Corporation X
W
NAT
W: Workstation
S: Server Machine
10.2.2.2:1000
S
198.2.4.5:80
243.4.4.4
10.5.5.5
source: 198.2.4.5
dest: 243.4.4.4
src port: 80
dest port: 5000
source: 198.2.4.5
dest: 10.2.2.2
src port: 80
dest port: 1000
Int Addr | Int Port | NAT Port
10.2.2.2 | 1000 | 5000

## Slide 59: Extending Private Network
Internet
Supporting Road Warrior
  Employee working remotely with assigned IP address 198.3.3.3
  Wants to appear to rest of corporation as if working internally
    From address 10.6.6.6
    Gives access to internal services (e.g., ability to send mail)
Virtual Private Network (VPN)
  Overlays private network on top of regular Internet
Corporation X
W
W
W
S
W: Workstation
S: Server Machine
198.3.3.3
10.6.6.6
10.X.X.X
W
NAT

## Slide 60: Supporting VPN by Tunneling
Concept
  Appears as if two hosts connected directly
Usage in VPN
  Create tunnel between road warrior & firewall
  Remote host appears to have direct connection to internal network
H
F
R
R
198.3.3.3
243.4.4.4
10.5.5.5
10.6.6.6
F: Firewall
R: Router
H: Host

## Slide 61: Implementing Tunneling
Host creates packet for internal node 10.6.1.1.1
Entering Tunnel
  Add extra IP header directed to firewall (243.4.4.4)
  Original header becomes part of payload
  Possible to encrypt it
Exiting Tunnel
  Firewall receives packet
  Strips off header
  Sends through internal network to destination
H
F
R
R
198.3.3.3
243.4.4.4
10.5.5.5
10.6.6.6
Payload
source: 198.3.3.3
dest: 243.4.4.4
dest: 10.1.1.1
source: 10.6.6.6

## Slide 62: Sending from A to B in Ethernet
59
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame

## Slide 63: Ethernet Frame Structure
Addresses: 6 bytes
  Each adapter is given a globally unique address at manufacturing time
    Address space is allocated to manufacturers
      24 bits identify manufacturer
      E.g., 0:0:15:*  3com adapter
    Frame is received by all adapters on a LAN and dropped if address does not match
  Special addresses
    Broadcast – FF:FF:FF:FF:FF:FF is “everybody”
    Range of addresses allocated to multicast
      Adapter maintains list of multicast groups node is interested in
63

## Slide 64: Ethernet Frame Structure (cont.)
63
Preamble: 8 bytes
  101010…1011
  Used to synchronize receiver, sender clock rates
CRC: 4 bytes
  Checked at receiver, if error is detected, the frame is simply dropped
Type: 2 bytes
  Indicates the higher layer protocol, mostly IP

## Slide 65: Collision and MAC
A
B
C
Time

## Slide 66: Ethernet MAC (CSMA/CD)
Packet?
Sense Carrier
Discard Packet
Send
Detect Collision
Jam channel b=CalcBackoff(); wait(b);
attempts++;
No
Yes
attempts < 16
attempts == 16
Carrier Sense Multiple Access/Collision Detection

## Slide 67: Ethernet Backoff Calculation
Exponentially increasing random delay
  Infer senders from # of collisions
  More senders  increase wait time
First collision: choose K from {0,1}; delay is K x 512 bit transmission times
After second collision: choose K from {0,1,2,3}…
After ten or more collisions, choose K from {0,1,2,3,4,…,1023}

## Slide 68: Scale
What breaks when we keep adding people to the same wire?
yak yak…

## Slide 69: Scale
What breaks when we keep adding people to the same wire?
Only solution: split up the people onto multiple wires
  But how can they talk to each other?
yak yak…

## Slide 70: Reconnecting LANs
When should these boxes forward packets between wires?
How do you specify a destination?
How does your packet find its way?
yak yak…

## Slide 71: Link-layer Routing Example
Receiver
Packet
R
Sender
2
3
4
1
2
3
4
1
2
3
4
1
S2
S3
S1
R
R
R  3
R  4
R  3
R
Notes: nice thing: makes minimal assumptions about the network!

## Slide 72: Transparent Switches
Design goals:
  Self-configuring without hardware or software changes
  Switches do not impact the operation of the individual LANs
Three parts to making switches transparent:
  Learning addresses/host locations
  Forwarding frames
  Spanning tree algorithm

## Slide 73: Learning and Frame Forwarding
Default: broadcast to all ports (except the one the packet arrives)
The switch “learns” what MAC addresses are reachable from each of its ports, and creates table entries.
A table entry: MAC address, port, age
For every packet, the switch “looks up” the entry for the packets destination MAC address and forwards the packet on that port.
Timer is used to flush old entries
8711C98900AA
2
MAC
Address
Port
A21032C9A591
1
99A323C90842
2
301B2369011C
2
695519001190
3
15
Age
36
01
16
11
Switch
1
3
2
Notes: A switch starts with an empty forwarding table. when it receives a packet for which it does not have a table entry, it broadcasts it...
it also keeps learning which MAC addresses are reachable through each port and populates its table
entries expire

## Slide 74: Spanning Tree Bridges
More complex topologies can provide redundancy.
  But can also create loops.
What is the problem with loops?
Solution: spanning tree
host
host
host
host
host
host
host
host
host
host
host
host
Switch
Switch

## Slide 75: IP Fragmentation Example
IP
Header
IP
Data
Length = 2000, M=1, Offset = 0
1980 bytes
IP
Data
IP
Header
Length = 1840, M=0, Offset = 1980
1820 bytes
host
router
MTU = 1500
IP
Header
IP
Data
Length = 1500, M=1, Offset = 0
1480 bytes
IP
Header
IP
Data
Length = 520, M=1, Offset = 1480
500 bytes
IP
Header
IP
Data
Length = 1500, M=1, Offset = 1980
1480 bytes
IP
Header
IP
Data
Length = 360, M=0, Offset = 3460
340 bytes

## Slide 76: Important Concepts
IP service
  Best effort, simplicity of routers
  Allows highly decentralized implementation
  Each step involves determining next hop
IP forwarding
  global addressing, alternatives, lookup tables
IP addressing
  hierarchical, CIDR
IP packets
  header fields, fragmentation