## Slide 1: 15-744: Computer Networking
L-4 BGP

## Slide 2: Next Lecture: Interdomain Routing
BGP
Assigned Reading
  MIT BGP Class Notes
  [Gao00] On Inferring Autonomous System Relationships in the Internet

## Slide 3: Outline
Need for hierarchical routing
BGP
  ASes, Policies
  BGP Attributes
  BGP Path Selection
  iBGP
  Inferring AS relationships
Multi-Homing
Stability Issues

## Slide 4: Routing Hierarchies
Flat routing doesn’t scale
  Each node cannot be expected to have routes to every destination (or destination network)
Key observation
  Need less information with increasing distance to destination
Two radically different approaches for routing
  The area hierarchy
  The landmark hierarchy

## Slide 5: Areas
Divide network into areas
  Areas can have nested sub-areas
  Constraint: no path between two sub-areas of an area can exit that area
Hierarchically address nodes in a network
  Sequentially number top-level areas
  Sub-areas of area are labeled relative to that area
  Nodes are numbered relative to the smallest containing area

## Slide 6: Routing
Within area
  Each node has routes to every other node
Outside area
  Each node has routes for other top-level areas only
  Inter-area packets are routed to nearest appropriate border router
Can result in sub-optimal paths

## Slide 7: Path Sub-optimality
1
2
3
1.1
1.2
2.1
2.2
3.1
3.2
2.2.1
3 hop red path
vs.
2 hop green path
start
end
3.2.1
1.2.1

## Slide 8: A Logical View of the Internet
National (Tier 1 ISP)
  “Default-free” with global reachability info
  Eg: AT & T, UUNET, Sprint
Regional (Tier 2 ISP)
  Regional or country-wide
  Eg: Pacific Bell
Local (Tier 3 ISP)
  Eg: Telerama DSL
Tier 1
Tier 1
Tier 2
Tier 2
Tier 2
Tier 3
Customer
Provider

## Slide 9: Landmark Routing: Basic Idea
Areas are not the only way to scale  Landmark hierarchy
Source wants to reach LM0[a], whose address is c.b.a:
  Source can see LM2[c], so sends packet towards c
  Entering LM1[b] area, first router diverts packet to b
  Entering LM0[a] area, packet delivered to a
Not shortest path
Packet may not reach landmarks
LM2[c]
LM1[b]
r0[a]
LM0[a]
r2[c]
r1[b]
Network Node
Path
Landmark Radius

## Slide 10: Landmark Routing: Example
d.d.a
d.d.b
d.d.c
d.d.e
d.d.d
d.d.f
d.i.k
d.i.g
d.d.j
d.i.i
d.i.w
d.i.u
d.d.k
d.d.l
d.n.h
d.n.x
d.n.n
d.n.o
d.n.p
d.n.q
d.n.t
d.n.s
d.n.r
d.i.v

## Slide 11: Routing Table for Router g
Landmark
Level
Next hop
LM2[d]
LM0[e]
LM1[i]
LM0[k]
LM0[f]
2
1
0
0
0
f
k
f
k
f
Router g
Router t
r0 = 2, r1 = 4, r2 = 8 hops
How to go from d.i.g to d.n.t? g-f-e-d-u-t
How does path length compare to shortest path? g-k-I-u-t
d.d.a
d.d.b
d.d.c
d.d.e
d.d.d
d.d.f
d.i.k
d.i.g
d.d.j
d.i.i
d.i.w
d.i.u
d.d.k
d.d.l
d.n.h
d.n.x
d.n.n
d.n.o
d.n.p
d.n.q
d.n.t
d.n.s
d.n.r

## Slide 12: Outline
Need for hierarchical routing
BGP
  ASes, Policies
  BGP Attributes
  BGP Path Selection
  iBGP
  Inferring AS relationships
Multi-Homing
Stability Issues

## Slide 13: Autonomous Systems (ASes)
Autonomous Routing Domain
  Glued together by a common administration, policies etc
Autonomous system
  Term for BGP’s ARDs
  Has an unique 16 bit ASN assigned to it and typically participates in inter-domain routing
Examples:
  MIT: 3, CMU: 9
  AT&T: 7018, 6341, 5074, …
  UUNET: 701, 702, 284, 12199, …
  Sprint: 1239, 1240, 6211, 6242, …
How do ASes interconnect to provide global connectivity
How does routing information get exchanged

## Slide 14: Nontransit vs. Transit ASes
ISP 1
ISP 2
Nontransit AS
might be a corporate
or campus network.
Could be a “content
provider”
NET A
Traffic NEVER
flows from ISP 1
through NET A to ISP 2
(At least not intentionally!)
IP traffic

## Slide 15: Customers and Providers
Customer pays provider for access to the Internet
provider
customer
IP traffic
provider
customer

## Slide 16: The Peering Relationship
peer
peer
customer
provider
Peers provide transit between
their respective customers
Peers do not provide transit
between peers
Peers (often) do not exchange $$$
traffic
allowed
traffic NOT
allowed
A
B
C

## Slide 17: Peering Wars
Reduces upstream transit costs
Can increase end-to-end performance
May be the only way to connect your customers to some part of the Internet (“Tier 1”)
You would rather have customers
Peers are usually your competition
Peering relationships may require periodic renegotiation
Peering struggles are by far the most
contentious issues in the ISP world!
Peering agreements are often confidential.
Peer
Don’t Peer

## Slide 18: Routing in the Internet
Link state or distance vector?
  No universal metric – policy decisions
Problems with distance-vector:
  Bellman-Ford algorithm may not converge
Problems with link state:
  Metric used by routers not the same – loops
  LS database too large – entire Internet
  May expose policies to other AS’s

## Slide 19: Solution: Distance Vector with Path
Each routing update carries the entire path
Loops are detected as follows:
  When AS gets route check if AS already in path
    If yes, reject route
    If no, add self and (possibly) advertise route further
Advantage:
  Metrics are local - AS chooses path, protocol ensures no loops

## Slide 20: BGP-4
BGP = Border Gateway Protocol
Is a Policy-Based routing protocol
Is the EGP of today’s global Internet
Relatively simple protocol, but configuration is complex and the entire world can see, and be impacted by, your mistakes.
1989 : BGP-1 [RFC 1105]
  Replacement for EGP (1984, RFC 904)
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771]
  Support for Classless Interdomain Routing (CIDR)
Notes: EGP –exterior gateway protocol , not to be confused with specific protocol used in earlier ARPANET etc.. Different revisions..current version is pretty new ! Add ons – functionality, addressing

## Slide 21: BGP Operations (Simplified)
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 22: Interconnecting BGP Peers
BGP uses TCP to connect peers
Advantages:
  Simplifies BGP
  No need for periodic refresh - routes are valid until withdrawn, or the connection is lost
  Incremental updates
Disadvantages
  Congestion control on a routing protocol?
  Inherits TCP vulnerabilities!
  Poor interaction during high load

## Slide 23: Four Types of BGP Messages
Open : Establish a peering session.
Keep Alive : Handshake at regular intervals.
Notification : Shuts down a peering session.
Update : Announcing new routes or withdrawing previously announced routes.
announcement =
prefix + attributes values

## Slide 24: Policy with BGP
BGP provides capability for enforcing various policies
Policies are not part of BGP: they are provided to BGP as configuration information
BGP enforces policies by choosing paths from multiple alternatives and controlling advertisement to other AS’s
Import policy
  What to do with routes learned from neighbors?
  Selecting best path
Export policy
  What routes to announce to neighbors?
  Depends on relationship with neighbor

## Slide 25: Examples of BGP Policies
A multi-homed AS refuses to act as transit
  Limit path advertisement
A multi-homed AS can become transit for some AS’s
  Only advertise paths to some AS’s
  Eg: A Tier-2 provider multi-homed to Tier-1 providers
An AS can favor or disfavor certain AS’s for traffic transit from itself

## Slide 26: Export Policy
An AS exports only best paths to its neighbors
  Guarantees that once the route is announced the AS is willing to transit traffic on that route
To Customers
  Announce all routes learned from peers, providers and customers, and self-origin routes
To Providers
  Announce routes learned from customers and self-origin routes
To Peers
  Announce routes learned from customers and self-origin routes

## Slide 27: Import Routes
From
peer
From
peer
From
provider
From
provider
From
customer
From
customer
provider route
customer route
peer route
ISP route

## Slide 28: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
filters
block

## Slide 29: BGP UPDATE Message
List of withdrawn routes
Network layer reachability information
  List of reachable prefixes
Path attributes
  Origin
  Path
  Metrics
All prefixes advertised in message have same path attributes

## Slide 30: Path Selection Criteria
Information based on path attributes
Attributes + external (policy) information
Examples:
  Hop count
  Policy considerations
    Preference for AS
    Presence or absence of certain AS
  Path origin
  Link dynamics

## Slide 31: Important BGP Attributes
Local Preference
AS-Path
MED
Next hop

## Slide 32: LOCAL PREF
Local (within an AS – i.e. iBGP) mechanism to provide relative priority among BGP routers (choose highest Local Pref)
R1
R2
R3
R4
I-BGP
AS 256
AS 300
Local Pref = 500
Local Pref =800
AS 100
R5
AS 200

## Slide 33: LOCAL PREF – Common Uses
Handle routes advertised to multi-homed transit customers
  Should use direct connection (multihoming typically has a primary/backup arrangement)
Peering vs. transit
  Prefer to use peering connection, why?
In general, customer > peer > provider
  Use LOCAL PREF to ensure this

## Slide 34: AS_PATH
List of traversed AS’s
Useful for loop checking and for path-based route selection (length, regexp)
AS 500
AS 300
AS 200
AS 100
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200
170.10.0.0/16
180.10.0.0/16

## Slide 35: Multi-Exit Discriminator (MED)
Hint to external neighbors about the preferred path into an AS
  Non-transitive attribute
  Different AS choose different scales
Used when two AS’s connect to each other in more than one place

## Slide 36: MED
Typically used when two ASes peer at multiple locations
Hint to R1 to use R3 over R4 link (lowest MED)
Cannot compare AS40’s values to AS30’s
R1
R2
R3
R4
AS 30
AS 40
180.10.0.0
MED = 120
180.10.0.0
MED = 200
AS 10
180.10.0.0
MED = 50

## Slide 37: MED
MED is typically used in provider/subscriber scenarios
It can lead to unfairness if used between ISP because it may force one ISP to carry more traffic:
SF
NY
ISP1 ignores MED from ISP2
ISP2 obeys MED from ISP1
ISP2 ends up carrying traffic most of the way
ISP1
ISP2

## Slide 38: Route Selection Process
Highest Local Preference
Shortest ASPATH
Lowest MED
i-BGP < e-BGP
Lowest IGP cost
to BGP egress
Lowest router ID
Traffic engineering
Enforce relationships
Throw up hands and
break ties

## Slide 39: Internal BGP (I-BGP)
Same messages as E-BGP
Different rules about re-advertising prefixes:
  Prefix learned from E-BGP can be advertised to I-BGP neighbor and vice-versa, but
  Prefix learned from one I-BGP neighbor cannot be advertised to another I-BGP neighbor
  Reason: no AS PATH within the same AS and thus danger of looping.

## Slide 40: Internal vs. External BGP
BGP can be used by R3 and R4 to learn routes
How do R1 and R2 learn routes?
Option 1: Inject routes in IGP
  Only works for small routing tables
Option 2: Use I-BGP
R3
R4
R1
R2
E-BGP
AS1
AS2

## Slide 41: Internal BGP (I-BGP)
R3 can tell R1 and R2 prefixes from R4
R3 can tell R4 prefixes from R1 and R2
R3 cannot tell R2 prefixes from R1
R2 can only find these prefixes through a direct connection to R1
Result: I-BGP routers must be fully connected (via TCP)!
  contrast with E-BGP sessions that map to physical links
R3
R4
R1
R2
E-BGP
I-BGP
AS1
AS2

## Slide 42: Route Reflector
eBGP update
iBGP updates
Mesh does not scale
RR
RR
RR
Each RR passes only best routes, no longer N2 scaling problem

## Slide 43: Policy Impact
Different relationships – Transit, Peering
Export policies  selective export
“Valley-free” routing
  Number links as (+1, 0, -1) for customer-to-provider, peer and provider-to-customer
  In any path should only see sequence of +1, followed by at most one 0, followed by sequence of -1

## Slide 44: How to infer AS relationships?
Can we infer relationship from the AS graph
  From routing information
  From size of ASes /AS topology graph
  From multiple views and route announcements
[Gao00]
  Three-pass heuristic
  Data from University of Oregon RouteViews
[SARK01]
  Data from multiple vantage points

## Slide 45: [Gao00] Basic Algorithm
Phase 1: Identify the degrees of the ASes from the tables
Phase 2: Annotate edges with “transit” relation
  AS u transits traffic for AS v if it provides its provider/peer routes to v.
Phase 3: Identify P2C, C2P, Sibling edges
  P2C  If and only if u transits for v, and v does not, Sibling otherwise

## Slide 46: How does Phase 2 work?
Notion of Valley free routing
  Each AS path can be
    Uphill
    Downhill
    Uphill – Downhill
    Uphill – P2P
    P2P -- Downhill
    Uphill – P2P – Downhill
How to identify Uphill/Downhill
  Heuristic: Identify the highest degree AS to be the end of the uphill path (path starts from source)

## Slide 47: Outline
Need for hierarchical routing
BGP
  ASes, Policies
  BGP Attributes
  BGP Path Selection
  iBGP
  Inferring AS relationships
Multi-Homing
Stability Issues

## Slide 48: Multi-homing
With multi-homing, a single network has more than one connection to the Internet.
Improves reliability and performance:
  Can accommodate link failure
  Bandwidth is sum of links to Internet
Challenges
  Getting policy right (MED, etc..)
  Addressing

## Slide 49: Multi-homing to Multiple Providers
Major issues:
  Addressing
  Aggregation
Customer address space:
  Delegated by ISP1
  Delegated by ISP2
  Delegated by ISP1 and ISP2
  Obtained independently
ISP1
ISP2
ISP3
Customer

## Slide 50: Address Space from one ISP
Customer uses address space from ISP1
ISP1 advertises /16 aggregate
Customer advertises /24 route to ISP2
ISP2 relays route to ISP1 and ISP3
ISP2-3 use /24 route
ISP1 routes directly
Problems with traffic load?
138.39/16
138.39.1/24
ISP1
ISP2
ISP3
Customer

## Slide 51: Pitfalls
ISP1 aggregates to a /19 at border router to reduce internal tables.
ISP1 still announces /16.
ISP1 hears /24 from ISP2.
ISP1 routes packets for customer to ISP2!
Workaround: ISP1 must inject /24 into I-BGP.
138.39.0/19
138.39/16
ISP1
ISP2
ISP3
Customer
138.39.1/24

## Slide 52: Address Space from Both ISPs
ISP1 and ISP2 continue to announce aggregates
Load sharing depends on traffic to two prefixes
Lack of reliability: if ISP1 link goes down, part of customer becomes inaccessible.
Customer may announce prefixes to both ISPs, but still problems with longest match as in case 1.
138.39.1/24
204.70.1/24
ISP1
ISP2
ISP3
Customer

## Slide 53: Address Space Obtained Independently
Offers the most control, but at the cost of aggregation.
Still need to control paths
ISP1
ISP2
ISP3
Customer

## Slide 54: Outline
Need for hierarchical routing
BGP
  ASes, Policies
  BGP Attributes
  BGP Path Selection
  iBGP
  Inferring AS relationships
Multi-Homing
Stability Issues

## Slide 55: Safety: No Persistent Oscillation
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Varadhan, Govindan, & Estrin, “Persistent Route Oscillations in Interdomain Routing”, 1996
Notes: Jargon!! Remind us about filtering, ranking, and the high-level intuitive description of the property
Start off describing what AS 1 does
Put on varadhan et al.

## Slide 56: Main Idea of Optional Paper
Permit only two business arrangements
  Customer-provider
  Peering
Constrain both filtering and ranking based on these arrangements to guarantee safety
Surprising result: these arrangements correspond to today’s (common) behavior
Gao & Rexford, “Stable Internet Routing without Global Coordination”, IEEE/ACM ToN, 2001

## Slide 57: Signs of Routing Instability
Record of BGP messages at major exchanges
Discovered orders of magnitude larger than expected updates
  Bulk were duplicate withdrawals
    Stateless implementation of BGP – did not keep track of information passed to peers
    Impact of few implementations
  Strong frequency (30/60 sec) components
    Interaction with other local routing/links etc.

## Slide 58: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(*R,1R,2R)
(0R,*R,2R)
(0R,1R,*R)

## Slide 59: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,*1R,2R)
(*0R,-,2R)
(*0R,1R,-)
W
W
W



(*R,1R,2R)
(0R,*R,2R)
(0R,1R,*R)

## Slide 60: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,*1R,2R)
(-,-,*2R)
(01R,*1R,-)
01R
01R



(-,*1R,2R)
(*0R,-,2R)
(*0R,1R,-)

## Slide 61: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,-,*2R)
(-,-,*2R)
(*01R,10R,-)
10R
10R



(-,*1R,2R)
(-,-,*2R)
(01R,*1R,-)

## Slide 62: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,-,-)
(-,-,*20R)
(*01R,10R,-)
20R
20R



(-,-,*2R)
(-,-,*2R)
(*01R,10R,-)

## Slide 63: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,*12R,-)
(-,-,*20R)
(*01R,-,-)
12R
12R



(-,-,-)
(-,-,*20R)
(*01R,10R,-)

## Slide 64: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,*12R,21R)
(-,-,-)
(*01R,-,-)
21R
21R
(-,*12R,-)
(-,-,*20R)
(*01R,-,-)




## Slide 65: BGP Oscillations
Can possible explore every possible path through network  (n-1)! Combinations
Limit between update messages (MinRouteAdver) reduces exploration
  Forces router to process all outstanding messages
Typical Internet failover times
  New/shorter link  60 seconds
    Results in simple replacement at nodes
  Down link  180 seconds
    Results in search of possible options
  Longer link  120 seconds
    Results in replacement or search based on length

## Slide 66: Route Flap Storm
Overloaded routers fail to send Keep_Alive message and marked as down
I-BGP peers find alternate paths
Overloaded router re-establishes peering session
Must send large updates
Increased load causes more routers to fail!

## Slide 67: Route Flap Dampening
Routers now give higher priority to BGP/Keep_Alive to avoid problem
Associate a penalty with each route
  Increase when route flaps
  Exponentially decay penalty with time
When penalty reaches threshold, suppress route

## Slide 68: Next Lecture: Software Forwarding
Friday: project group meeting
Programming abstractions for routers
  Click
  OpenFlow
Assigned Reading
  OpenFlow: Enabling Innovation in Campus Networks
  The Click Modular Router