## Slide 1: 15-744: Computer Networking
L-5 Software Forwarding

## Slide 2: Outline
Need for hierarchical routing
BGP
  ASes, Policies
  BGP Attributes
  BGP Path Selection
  iBGP
  Inferring AS relationships
Multi-Homing
Stability Issues
Notes: <number>

## Slide 3: Multi-homing
With multi-homing, a single network has more than one connection to the Internet.
Improves reliability and performance:
  Can accommodate link failure
  Bandwidth is sum of links to Internet
Challenges
  Getting policy right (MED, etc..)
  Addressing

## Slide 4: Multi-homing to Multiple Providers
Major issues:
  Addressing
  Aggregation
Customer address space:
  Delegated by ISP1
  Delegated by ISP2
  Delegated by ISP1 and ISP2
  Obtained independently
ISP1
ISP2
ISP3
Customer

## Slide 5: Address Space from one ISP
Customer uses address space from ISP1
ISP1 advertises /16 aggregate
Customer advertises /24 route to ISP2
ISP2 relays route to ISP1 and ISP3
ISP2-3 use /24 route
ISP1 routes directly
Problems with traffic load?
138.39/16
138.39.1/24
ISP1
ISP2
ISP3
Customer

## Slide 6: Pitfalls
ISP1 aggregates to a /19 at border router to reduce internal tables.
ISP1 still announces /16.
ISP1 hears /24 from ISP2.
ISP1 routes packets for customer to ISP2!
Workaround: ISP1 must inject /24 into I-BGP.
138.39.0/19
138.39/16
ISP1
ISP2
ISP3
Customer
138.39.1/24

## Slide 7: Address Space from Both ISPs
ISP1 and ISP2 continue to announce aggregates
Load sharing depends on traffic to two prefixes
Lack of reliability: if ISP1 link goes down, part of customer becomes inaccessible.
Customer may announce prefixes to both ISPs, but still problems with longest match as in case 1.
138.39.1/24
204.70.1/24
ISP1
ISP2
ISP3
Customer

## Slide 8: Address Space Obtained Independently
Offers the most control, but at the cost of aggregation.
Still need to control paths
ISP1
ISP2
ISP3
Customer

## Slide 9: Outline
Need for hierarchical routing
BGP
  ASes, Policies
  BGP Attributes
  BGP Path Selection
  iBGP
  Inferring AS relationships
Multi-Homing
Stability Issues
Notes: <number>

## Slide 10: Safety: No Persistent Oscillation
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Varadhan, Govindan, & Estrin, “Persistent Route Oscillations in Interdomain Routing”, 1996
Notes: <number>
Jargon!! Remind us about filtering, ranking, and the high-level intuitive description of the property
Start off describing what AS 1 does
Put on varadhan et al.

## Slide 11: Main Idea of Optional Paper
Permit only two business arrangements
  Customer-provider
  Peering
Constrain both filtering and ranking based on these arrangements to guarantee safety
Surprising result: these arrangements correspond to today’s (common) behavior
Gao & Rexford, “Stable Internet Routing without Global Coordination”, IEEE/ACM ToN, 2001

## Slide 12: Signs of Routing Instability
Record of BGP messages at major exchanges
Discovered orders of magnitude larger than expected updates
  Bulk were duplicate withdrawals
    Stateless implementation of BGP – did not keep track of information passed to peers
    Impact of few implementations
  Strong frequency (30/60 sec) components
    Interaction with other local routing/links etc.

## Slide 13: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(*R,1R,2R)
(0R,*R,2R)
(0R,1R,*R)

## Slide 14: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,*1R,2R)
(*0R,-,2R)
(*0R,1R,-)
W
W
W



(*R,1R,2R)
(0R,*R,2R)
(0R,1R,*R)

## Slide 15: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,*1R,2R)
(-,-,*2R)
(01R,*1R,-)
01R
01R



(-,*1R,2R)
(*0R,-,2R)
(*0R,1R,-)

## Slide 16: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,-,*2R)
(-,-,*2R)
(*01R,10R,-)
10R
10R



(-,*1R,2R)
(-,-,*2R)
(01R,*1R,-)

## Slide 17: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,-,-)
(-,-,*20R)
(*01R,10R,-)
20R
20R



(-,-,*2R)
(-,-,*2R)
(*01R,10R,-)

## Slide 18: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,*12R,-)
(-,-,*20R)
(*01R,-,-)
12R
12R



(-,-,-)
(-,-,*20R)
(*01R,10R,-)

## Slide 19: BGP Limitations: Oscillations
AS 0
AS 2
AS 1
R
(-,*12R,21R)
(-,-,-)
(*01R,-,-)
21R
21R
(-,*12R,-)
(-,-,*20R)
(*01R,-,-)




## Slide 20: BGP Oscillations
Can possible explore every possible path through network  (n-1)! Combinations
Limit between update messages (MinRouteAdver) reduces exploration
  Forces router to process all outstanding messages
Typical Internet failover times
  New/shorter link  60 seconds
    Results in simple replacement at nodes
  Down link  180 seconds
    Results in search of possible options
  Longer link  120 seconds
    Results in replacement or search based on length
Notes: <number>

## Slide 21: Route Flap Storm
Overloaded routers fail to send Keep_Alive message and marked as down
I-BGP peers find alternate paths
Overloaded router re-establishes peering session
Must send large updates
Increased load causes more routers to fail!

## Slide 22: Route Flap Dampening
Routers now give higher priority to BGP/Keep_Alive to avoid problem
Associate a penalty with each route
  Increase when route flaps
  Exponentially decay penalty with time
When penalty reaches threshold, suppress route

## Slide 23: Next Lecture: Software Forwarding
Friday: project group meeting
Programming abstractions for routers
  Click
  OpenFlow
Assigned Reading
  OpenFlow: Enabling Innovation in Campus Networks
  The Click Modular Router

## Slide 24: Outline
IP router design
IP route lookup
Click
OpenFlow

## Slide 25: IP Router Design
Different architectures for different types of routers
High speed routers incorporate large number of processors
Common case is optimized carefully

## Slide 26: What Does a Router Look Like?
Currently:
  Network controller
  Line cards
  Switched backplane
In the past?
  Workstation
  Multiprocessor workstation
  Line cards + shared bus

## Slide 27: Line Cards
Network interface cards
Provides parallel processing of packets
Fast path per-packet processing
  Forwarding lookup (hardware/ASIC vs. software)

## Slide 28: Network Processor
Runs routing protocol and downloads forwarding table to line cards
  Some line cards maintain two forwarding tables to allow easy switchover
Performs “slow” path processing
  Handles ICMP error messages
  Handles IP option processing

## Slide 29: Switch Design Issues
Have N inputs and M outputs
  Multiple packets for same output – output contention
  Switch contention – switch cannot support arbitrary set of transfers
    Crossbar
    Bus
      High clock/transfer rate needed for bus
    Banyan net
      Complex scheduling needed to avoid switch contention
Solution – buffer packets where needed

## Slide 30: Outline
IP router design
IP route lookup
Click
OpenFlow

## Slide 31: Original IP Route Lookup
Address classes
  A: 0 | 7 bit network | 24 bit host (16M each)
  B: 10 | 14 bit network | 16 bit host (64K)
  C: 110 | 21 bit network | 8 bit host (255)
Address would specify prefix for forwarding table
  Simple lookup

## Slide 32: Original IP Route Lookup – Example
www.cmu.edu address 128.2.11.43
  Class B address – class + network is 128.2
  Lookup 128.2 in forwarding table
  Prefix – part of address that really matters for routing
Forwarding table contains
  List of class+network entries
  A few fixed prefix lengths (8/16/24)
Large tables
  2 Million class C networks
32 bits does not give enough space encode network location information inside address – i.e., create a structured hierarchy

## Slide 33: CIDR Revisited
Supernets
  Assign adjacent net addresses to same org
  Classless routing (CIDR)
How does this help routing table?
  Combine routing table entries whenever all nodes with same prefix share same hop
  Routing protocols carry prefix with destination network address
  Longest prefix match for forwarding

## Slide 34: CIDR Illustration
Provider is given 201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider

## Slide 35: CIDR Shortcomings
Multi-homing
Customer selecting a new provider
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23 or Provider 2 address
Provider 1
Provider 2

## Slide 36: Outline
IP router design
IP route lookup
Click
OpenFlow

## Slide 37: The End of Networking Research?
The Internet is a “success disaster”
  Many successful applications
  Critical for economy as a whole
  Too huge a vested infrastructure
  Vendors loathe to change anything
Fear in community: “ossification”
  New ideas cannot get deployed

## Slide 38: Three stages
Active networking era
  Case for “programmable” network devices
“Separation” of control vs data era
  Specifically about routing etc
OpenFlow/Network OS era

## Slide 39: Software-Based Routers
Enabling innovation in networking research
Software data planes
Readings:
  OpenFlow: Enabling Innovation in Campus Networks
  The Click Modular Router
Optional reading
  RouteBricks: Exploiting Parallelism To Scale Software Routers

## Slide 40: Click overview
Modular architecture
  Router = composition of modules
  Router = data flow graph
An element is the basic unit of processing
Three key components of each element:
  Ports
  Configuration
  Method interfaces
Notes: The high level idea of click as the title suggests is to build a modular router. That is u want to break up a router processing task into multiple smaller modules and then compose the processing as a fta flow graph between these modules. The basic unit is a clicke element. And each element has trheee key compknetns ==-portsn , configuraiton stringfs, and method interfgaces that other elements can querye
<number>

## Slide 41: Simple Tee Element
Notes: Here is an exmaple of a very simple Tee element that takes in incoming packets and duplicates into 2 output ports. The ;ement class is Tee. It takes a config tring 2 giving number of ports. And the finction is just copy packets from input to outpu
<number>

## Slide 42: Two types of “connections”
Push
  Source element has finished processing
  Sends it downstream
  E.g., FromDevice
Pull
  Destination is ready to process
  Initiates packet transfer
  E.g., ToDevice
Notes: Now these ports that connect elements are of two types – push or pull. Push is when a src element has finished processign and wants to hand off. This is a natural thing for e..g, when u have incpoking pkts. The dual of this is the pull. The destination gives “upcall” saying its ready to receive the next pacekt. E.g., this might be relevant for tranmissint devices to inform that they are ready to send. The smentics is push is connected to push and pull is connected to pull. U need some special things like queues to mix and match.
<number>

## Slide 43: “Flow” of processing
Notes: Lets look at a very simple exmaple u have fromdevice wih a push output. Two null elemnts that are agnistic (meaning depending on in/put being push/pull they get duynamcially assigned). In between u have a queue element with a push inpu and a pull output. Walk throush
<number>

## Slide 44: Click Config File
Notes: Click has a really simple scripting config language that lets u express the processing as a graph. Here is a very simple example
<number>

## Slide 45: Click Elements
Notes: The click element is essentialla c++ class .. U will essentially have to add the gundtions for configuring and push/pull logic. This is showing a very very simple nukk element tht does nothing. Obvipously u will be expected to do something more intelligent
<number>

## Slide 46: Other elements
Packet Classification
Scheduling
Queueing
Routing
What you write…
Notes: Ther eare many modules in click .. Classifiers, schduling, queuning, routing, and many other use contributed modules. Plus whatever u write!
<number>

## Slide 47: Idea: Polling
Under heavy load, disable the network card’s interrupts
Use polling instead
  Ask if there is more work once you’ve done the first batch
Click paper we read – does pure polling
Notes: The solution to this problems is essnetiall to diable interrupts under high load and use polling/batching.
<number>

## Slide 48: Takeaways
Click is a flexible modular router
Shows that s/w x86 can get pretty good performance
Extensible/modular
Widely used in academia/research
  Play with it!

## Slide 49: Outline
IP router design
IP route lookup
Click
OpenFlow

## Slide 50: Innovations in campus wiring closets
Experiments we’d like to do
  Mobility management
  Network-wide energy management
  New naming/addressing schemes
  Network access control
Problem with our network
  Paths are fixed (by the network)
  IP-only
  Addresses dictated by DNS, DHCP, etc
  No means to add our own processing

## Slide 51: OpenFlow Switching
A way to run experiments in the networks we use everyday.
Bring GENI to college campuses.
A “pragmatic” compromise
  Allow researchers to run experiments in their network…
  …without requiring vendors to expose internal workings.
Basics
  An Ethernet switch (e.g. 128-ports of 1GE)
  An open protocol to remotely add/remove flow entries

## Slide 52: Experimenter’s Dream (Vendor’s Nightmare)
Standard
Network
Processing
hw
sw
Experimenter writes experimental code on switch/router
User-
defined
Processing

## Slide 53: No obvious way
Commercial vendor won’t open software and hardware development environment
  Complexity of support
  Market protection and barrier to entry
Hard to build my own
  Prototypes are flakey
  Software only: Too slow
  Hardware/software: Fanout too small (need >100 ports for wiring closet)

## Slide 54: Furthermore, we want…
Isolation: Regular production traffic untouched
Virtualized and programmable: Different flows processed in different ways
Equipment we can trust in our wiring closet
Open development environment for all researchers (e.g. Linux, Verilog, etc).
Flexible definitions of a flow
  Individual application traffic
  Aggregated flows
  Alternatives to IP running side-by-side
  …
Notes: <number>

## Slide 55: OpenFlow Switching
Controller
OpenFlow Switch
Flow
Table
Secure
Channel
PC
OpenFlow
Protocol
SSL
hw
sw
OpenFlow Switch specification

## Slide 56: Flow Table Entry “Type 0” OpenFlow Switch
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
+ mask
Packet + byte counters

## Slide 57: What is nice
Fits well with the TCAM abstraction
Most vendors already have this
They can just expose this without exposing internals

## Slide 58: OpenFlow Usage Models
Experiments at the flow level
  User-defined routing protocols
  Admission control
  Network access control
  Network management
  Energy management
  VOIP mobility and handoff
  …
Experiments at the packet level
  Slow: Controller handles packet processing
  Fast: Redirect flows through programmable hardware
  Modified routers, firewalls, NAT, congestion control…
Alternatives to IP
Experiment-specific controllers
Static or dynamic flow-entries

## Slide 59: Example Apps
Ethane
Amy’s own OSPF
VLAN
VoIP for Mobile
Support for non-IP

## Slide 60: Example Experiment at the flow level Mobility
Lots of interesting questions
Management of flows
Control of switches
Access control of users and devices
Tracking user location and motion

## Slide 61: Experiments at the packet level
Controller
PC
NetFPGA
Laboratory
OpenFlow-enabled
Commercial Switch
Flow
Table
Secure
Channel
Normal
Software
Normal
Datapath
Notes: <number>

## Slide 62: OpenFlow Usage Models
Experiments at the flow level
Experiments at the packet level
Alternatives to IP
  Flow-table is Layer-2 based
  e.g. new naming and addressing schemes
  …

## Slide 63: Network Management
Traffic Engineering Performance
Security
Compliance
Resilience
Notes: Networks start off providing a basic functionality – send packets from point A to point B. But that’s not the end of the story .. Administrators want to achieve other things with the network – performance
<number>

## Slide 64: Problem: Toolbox is bad!
Traffic Engineering Performance
Security
Compliance
Resilience
Notes: Toolbox today
<number>

## Slide 65: Why: Toolbox is implicit in routers!
Traffic Engineering Performance
Security
Compliance
Resilience
Motivation: Management is complex, expensive, fragile
Need: Direct control, expressive policy, network-wide views
Notes: Makes the network really brittle, makes it hard to reason whether your policy goals are being met. Toolbox relies on some complex distributed routing algorithms to converge, not clear what happens under failures etc
<number>

## Slide 66: Solution
Separate out the “data” and the “control”
Open interface between control/data planes
Logically centralized views
  Simplifies optimization/policy management
  Network-wide visibility
Notes: <number>

## Slide 67: Today: OpenFlow
Controller
Config
Config
OpenFlow
Notes: Networks start off providing a basic functionality – send packets from point A to point B. But that’s not the end of the story .. Administrators want to achieve other things with the network – performance
<number>

## Slide 68: Next Lecture: ONIX
Controller
Config
Config
E.g., ONIX, NOX, …
Notes: Networks start off providing a basic functionality – send packets from point A to point B. But that’s not the end of the story .. Administrators want to achieve other things with the network – performance
<number>

## Slide 69: Summary
Building software routers by starting with:
  closed, commercial routers vs.
  commodity PCs
Pros and cons?
Notes: <number>

## Slide 70: Next Lecture
Software-Defined Networking
Readings:
  4D: Read in full
  Onix: Read intro
  Ethane: Optional reading

## Slide 71: Software-Based Routers
Enabling innovation in networking research
Software data planes
Readings:
  OpenFlow: Enabling Innovation in Campus Networks
  The Click Modular Router
Optional reading
  RouteBricks: Exploiting Parallelism To Scale Software Routers

## Slide 72: Today: fast or programmable
Fast “hardware” routers
  throughput : Tbps
  little programmability
Programmable “software” routers
  processing by general-purpose CPUs
  throughput < 10Gbps
Notes: Best of both worlds
<number>

## Slide 73: RouteBricks
A router out of off-the-shelf PCs
  familiar programming environment
  large-volume manufacturing
Can we build a Tbps router out of PCs?
Notes: Get back to the Tbps result
<number>

## Slide 74: A hardware router
N
R
R
Processing at rate ~R per linecard
linecards
linecards
Notes: <number>

## Slide 75: A hardware router
Processing at rate ~R per linecard
Switching at rate N x R by switch fabric
switch fabric
N
R
R
linecards
linecards
Notes: <number>

## Slide 76: RouteBricks
commodity interconnect
N
R
R
Processing at rate ~R per server
Switching at rate ~R per server
servers
servers
Notes: <number>

## Slide 77: Outline
Interconnect
Server optimizations
Performance
Notes: <number>

## Slide 78: Requirements
commodity interconnect
N
R
R
Internal link rates < R
Per-server processing rate: c x R
Per-server fanout: constant
Notes: <number>

## Slide 79: A naive solution
N
R
R
R
Notes: Packet addressed *to*
<number>

## Slide 80: A naive solution
N
R
R
R
N external links of capacity R
N2 internal links of capacity R
Notes: Explain why this is expensive
<number>

## Slide 81: Valiant load balancing (VLB)
N
R
R
R/N
R/N
Notes: <number>

## Slide 82: Valiant load balancing (VLB)
N
R
R
N external links of capacity R
N2 internal links of capacity R
R/N
R/N
2R/N
Notes: <number>

## Slide 83: Valiant load balancing (VLB)
N
R
R
R/N
R/N
Per-server processing rate: 3R
W/ uniform traffic: 2R
Notes: <number>

## Slide 84: Per-server fanout?
N
R
Notes: <number>

## Slide 85: Per-server fanout?
N
R
Increase server capacity
Notes: <number>

## Slide 86: Per-server fanout?
N
R
Increase server capacity
Notes: <number>

## Slide 87: Per-server fanout?
N
R
Increase server capacity
Add intermediate nodes
    k-degree n-stage butterfly
Notes: <number>

## Slide 88: Our solution: combination
Assign max external ports per server
Full mesh, if possible
Extra servers, otherwise
Notes: <number>

## Slide 89: Recap
Valiant
load balancing +
full mesh
k-ary n-fly
N
R
R
Per-server processing rate: 2R – 3R
Notes: <number>

## Slide 90: Outline
Interconnect
Server optimizations
Performance
Notes: <number>

## Slide 91: Setup: NUMA architecture
I/O hub
Mem
Cores
Mem
  Nehalem architecture, QuickPath interconnect
  CPUs: 2 x [2.8GHz, 4 cores, 8MB L3 cache]
  NICs: 2 x Intel XFSR 2x10Gbps
  kernel-mode Click
Ports
Notes: Intel figured out
<number>

## Slide 92: Single-server performance
I/O hub
Mem
Cores
Mem
Ports
  First try: 1.3 Gbps
Notes: <number>

## Slide 93: Problem #1: book-keeping
Managing packet descriptors
  moving between NIC and memory
  updating descriptor rings
Solution: batch packet operations
  NIC batches multiple packet descriptors
  CPU polls for multiple packets
Notes: <number>

## Slide 94: Single-server performance
I/O hub
Mem
Cores
Mem
Ports
  First try: 1.3 Gbps
  With batching: 3 Gbps
Notes: <number>

## Slide 95: Problem #2: queue access
Cores
Ports
Notes: <number>

## Slide 96: Problem #2: queue access
  Rule #1: 1 core per port
Notes: <number>

## Slide 97: Problem #2: queue access
Rule #1: 1 core per port
Rule #2: 1 core per packet
Notes: <number>

## Slide 98: Problem #2: queue access
Rule #1: 1 core per port
Rule #2: 1 core per packet
Notes: <number>

## Slide 99: Problem #2: queue access
Rule #1: 1 core per port
Rule #2: 1 core per packet
Notes: <number>

## Slide 100: Problem #2: queue access
Rule #1: 1 core per port
Rule #2: 1 core per packet
queue
Notes: <number>

## Slide 101: Single-server performance
I/O hub
Mem
Cores
Mem
Ports
First try: 1.3 Gbps
With batching: 3 Gbps
With multiple queues: 9.7 Gbps
Notes: <number>

## Slide 102: Recap
State-of-the art hardware
  NUMA architecture, multi-queue NICs
Modified NIC driver
  batching
Careful queue-to-core allocation
  one core per queue, per packet
Notes: <number>

## Slide 103: Outline
Interconnect
Server optimizations
Performance
Notes: <number>

## Slide 104: Effect of application
Throughput heavily depends on workload.
Notes: <number>