## Slide 1: 15-744: Computer Networking
L-12 Queuing

## Slide 2: Queuing
<number>
Fair Queuing
Core-stateless Fair queuing
Assigned reading
  [DKS90] Analysis and Simulation of a Fair Queueing Algorithm, Internetworking: Research and Experience
  [XCP] Congestion Control for High Bandwidth-Delay Product Networks
Optional
  [SSZ98] Core-Stateless Fair Queueing: Achieving Approximately Fair Allocations in High Speed Networks

## Slide 3: Overview
TCP and queues
Queuing disciplines
RED
Fair-queuing
Core-stateless FQ
XCP
<number>

## Slide 4: Example
<number>
10Gb/s linecard
  Requires 300Mbytes of buffering.
  Read and write 40 byte packet every 32ns.
Memory technologies
  DRAM: require 4 devices, but too slow.
  SRAM: require 80 devices, 1kW, $2000.
Problem gets harder at 40Gb/s
  Hence RLDRAM, FCRAM, etc.
Notes: <number>

## Slide 5: Rule-of-thumb
<number>
Rule-of-thumb makes sense for one flow
Typical backbone link has > 20,000 flows
Does the rule-of-thumb still hold?
Notes: <number>

## Slide 6: If flows are synchronized
<number>
Aggregate window has same dynamics
Therefore buffer occupancy has same dynamics
Rule-of-thumb still holds.
t
Notes: <number>

## Slide 7: If flows are not synchronized
<number>
Probability
Distribution
B
0
Buffer Size
Notes: <number>

## Slide 8: Central Limit Theorem
<number>
CLT tells us that the more variables (Congestion Windows of Flows) we have, the narrower the Gaussian (Fluctuation of sum of windows)
  Width of Gaussian decreases with
  Buffer size should also decreases with
Notes: <number>

## Slide 9: Required buffer size
<number>
Simulation
Notes: <number>

## Slide 10: Overview
TCP and queues
Queuing disciplines
RED
Fair-queuing
Core-stateless FQ
XCP
<number>

## Slide 11: Queuing Disciplines
<number>
Each router must implement some queuing discipline
Queuing allocates both bandwidth and buffer space:
  Bandwidth: which packet to serve (transmit) next
  Buffer space: which packet to drop next (when required)
Queuing also affects latency

## Slide 12: Packet Drop Dimensions
<number>
Aggregation
Per-connection state
Single class
Drop position
Head
Tail
Random location
Class-based queuing
Early drop
Overflow drop

## Slide 13: Typical Internet Queuing
<number>
FIFO + drop-tail
  Simplest choice
  Used widely in the Internet
FIFO (first-in-first-out)
  Implies single class of traffic
Drop-tail
  Arriving packets get dropped when queue is full regardless of flow or importance
Important distinction:
  FIFO: scheduling discipline
  Drop-tail: drop policy

## Slide 14: FIFO + Drop-tail Problems
<number>
Leaves responsibility of congestion control to edges (e.g., TCP)
Does not separate between different flows
No policing: send more packets  get more service
Synchronization: end hosts react to same events

## Slide 15: Active Queue Management
<number>
Design active router queue management to aid congestion control
Why?
  Routers can distinguish between propagation and persistent queuing delays
  Routers can decide on transient congestion, based on workload

## Slide 16: Active Queue Designs
<number>
Modify both router and hosts
  DECbit – congestion bit in packet header
Modify router, hosts use TCP
  Fair queuing
    Per-connection buffer allocation
  RED (Random Early Detection)
    Drop packet or set bit in packet header as soon as congestion is starting

## Slide 17: Overview
TCP and queues
Queuing disciplines
RED
Fair-queuing
Core-stateless FQ
XCP
<number>

## Slide 18: Internet Problems
<number>
Full queues
  Routers are forced to have have large queues to maintain high utilizations
  TCP detects congestion from loss
    Forces network to have long standing queues in steady-state
Lock-out problem
  Drop-tail routers treat bursty traffic poorly
  Traffic gets synchronized easily  allows a few flows to monopolize the queue space

## Slide 19: Design Objectives
<number>
Keep throughput high and delay low
Accommodate bursts
Queue size should reflect ability to accept bursts rather than steady-state queuing
Improve TCP performance with minimal hardware changes

## Slide 20: Lock-out Problem
<number>
Random drop
  Packet arriving when queue is full causes some random packet to be dropped
Drop front
  On full queue, drop packet at head of queue
Random drop and drop front solve the lock-out problem but not the full-queues problem

## Slide 21: Full Queues Problem
<number>
Drop packets before queue becomes full (early drop)
Intuition: notify senders of incipient congestion
  Example: early random drop (ERD):
    If qlen > drop level, drop each new packet with fixed probability p
    Does not control misbehaving users
Notes: <number>
somewhat drastic reaction to overload
Uses instantaneous queue length

## Slide 22: Random Early Detection (RED)
<number>
Detect incipient congestion, allow bursts
Keep power (throughput/delay) high
  Keep average queue size low
  Assume hosts respond to lost packets
Avoid window synchronization
  Randomly mark packets
Avoid bias against bursty traffic
Some protection against ill-behaved users

## Slide 23: RED Algorithm
<number>
Maintain running average of queue length
If avgq < minth do nothing
  Low queuing, send packets through
If avgq > maxth, drop packet
  Protection from misbehaving sources
Else mark packet in a manner proportional to queue length
  Notify sources of incipient congestion

## Slide 24: RED Operation
<number>
Min thresh
Max thresh
Average Queue Length
minth
maxth
maxP
1.0
Avg queue length
P(drop)

## Slide 25: RED Algorithm
<number>
Maintain running average of queue length
  Byte mode vs. packet mode – why?
For each packet arrival
  Calculate average queue size (avg)
  If minth ≤ avgq < maxth
    Calculate probability Pa
    With probability Pa
      Mark the arriving packet
    Else if maxth ≤ avg
      Mark the arriving packet

## Slide 26: Queue Estimation
<number>
Standard EWMA: avgq = (1-wq) avgq + wqqlen
  Special fix for idle periods – why?
Upper bound on wq depends on minth
  Want to ignore transient congestion
  Can calculate the queue average if a burst arrives
    Set wq such that certain burst size does not exceed minth
Lower bound on wq to detect congestion relatively quickly
Typical wq = 0.002
Notes: <number>
Idle fix since otherwise avgq stays high during idle periods

## Slide 27: Thresholds
<number>
minth determined by the utilization requirement
  Tradeoff between queuing delay and utilization
Relationship between maxth and minth
  Want to ensure that feedback has enough time to make difference in load
  Depends on average queue increase in one RTT
  Paper suggest ratio of 2
    Current rule of thumb is factor of 3

## Slide 28: Packet Marking
<number>
maxp is reflective of typical loss rates
Paper uses 0.02
  0.1 is more realistic value
If network needs marking of 20-30% then need to buy a better link!
Gentle variant of RED (recommended)
  Vary drop rate from maxp to 1 as the avgq varies from maxth to 2* maxth
  More robust to setting of maxth and maxp

## Slide 29: Extending RED for Flow Isolation
<number>
Problem: what to do with non-cooperative flows?
Fair queuing achieves isolation using per-flow state – expensive at backbone routers
  How can we isolate unresponsive flows without per-flow state?
RED penalty box
  Monitor history for packet drops, identify flows that use disproportionate bandwidth
  Isolate and punish those flows

## Slide 30: Stochastic Fair Blue
<number>
Same objective as RED Penalty Box
  Identify and penalize misbehaving flows
Create L hashes with N bins each
  Each bin keeps track of separate marking rate (pm)
  Rate is updated using standard technique and a bin size
  Flow uses minimum pm of all L bins it belongs to
  Non-misbehaving flows hopefully belong to at least one bin without a bad flow
    Large numbers of bad flows may cause false positives

## Slide 31: Stochastic Fair Blue
<number>
False positives can continuously penalize same flow
Solution: moving hash function over time
  Bad flow no longer shares bin with same flows
  Is history reset does bad flow get to make trouble until detected again?
    No, can perform hash warmup in background

## Slide 32: Overview
TCP and queues
Queuing disciplines
RED
Fair-queuing
Core-stateless FQ
XCP
<number>

## Slide 33: Fairness Goals
<number>
Allocate resources fairly
Isolate ill-behaved users
  Router does not send explicit feedback to source
  Still needs e2e congestion control
Still achieve statistical muxing
  One flow can fill entire pipe if no contenders
  Work conserving  scheduler never idles link if it has a packet

## Slide 34: What is Fairness?
<number>
At what granularity?
  Flows, connections, domains?
What if users have different RTTs/links/etc.
  Should it share a link fairly or be TCP fair?
Maximize fairness index?
  Fairness = (xi)2/n(xi2) 0<fairness<1
Basically a tough question to answer – typically design mechanisms instead of policy
  User = arbitrary granularity

## Slide 35: Max-min Fairness
<number>
Allocate user with “small” demand what it wants, evenly divide unused resources to “big” users
Formally:
    Resources allocated in terms of increasing demand
    No source gets resource share larger than its demand
    Sources with unsatisfied demands get equal share of resource

## Slide 36: Max-min Fairness Example
<number>
Assume sources 1..n, with resource demands X1..Xn in ascending order
Assume channel capacity C.
  Give C/n to X1; if this is more than node 1 wants, divide excess (C/n - X1) to other sources: each gets C/n + (C/n - X1)/(n-1)
  If this is larger than what X2 wants, repeat process

## Slide 37: Implementing max-min Fairness
<number>
Generalized processor sharing
  Fluid fairness
  Bitwise round robin among all queues
Why not simple round robin?
  Variable packet length  can get more service by sending bigger packets
  Unfair instantaneous service rate
    What if arrive just before/after packet departs?

## Slide 38: Bit-by-bit RR
<number>
Single flow: clock ticks when a bit is transmitted. For packet i:
  Pi = length, Ai = arrival time, Si = begin transmit time, Fi = finish transmit time
  Fi = Si+Pi = max (Fi-1, Ai) + Pi
Multiple flows: clock ticks when a bit from all active flows is transmitted  round number
  Can calculate Fi for each packet if number of flows is know at all times
    This can be complicated

## Slide 39: Bit-by-bit RR Illustration
<number>
Not feasible to interleave bits on real networks
  FQ simulates bit-by-bit RR

## Slide 40: Fair Queuing
<number>
Mapping bit-by-bit schedule onto packet transmission schedule
Transmit packet with the lowest Fi at any given time
  How do you compute Fi?

## Slide 41: FQ Illustration
<number>
Flow 1
Flow 2
Flow n
I/P
O/P
Variation: Weighted Fair Queuing (WFQ)

## Slide 42: Bit-by-bit RR Example
<number>
F=10
Flow 1
(arriving)
Flow 2
transmitting
Output
F=2
F=5
F=8
Flow 1
Flow 2
Output
F=10
Cannot preempt packet
currently being transmitted

## Slide 43: Fair Queuing Tradeoffs
<number>
FQ can control congestion by monitoring flows
  Non-adaptive flows can still be a problem – why?
Complex state
  Must keep queue per flow
    Hard in routers with many flows (e.g., backbone routers)
    Flow aggregation is a possibility (e.g. do fairness per domain)
Complex computation
  Classification into flows may be hard
  Must keep queues sorted by finish times
  Finish times change whenever the flow count changes

## Slide 44: Overview
TCP and queues
Queuing disciplines
RED
Fair-queuing
Core-stateless FQ
XCP
<number>

## Slide 45: Core-Stateless Fair Queuing
<number>
Key problem with FQ is core routers
  Must maintain state for 1000’s of flows
  Must update state at Gbps line speeds
CSFQ (Core-Stateless FQ) objectives
  Edge routers should do complex tasks since they have fewer flows
  Core routers can do simple tasks
    No per-flow state/processing  this means that core routers can only decide on dropping packets not on order of processing
    Can only provide max-min bandwidth fairness not delay allocation

## Slide 46: Core-Stateless Fair Queuing
<number>
Edge routers keep state about flows and do computation when packet arrives
DPS (Dynamic Packet State)
  Edge routers label packets with the result of state lookup and computation
Core routers use DPS and local measurements to control processing of packets

## Slide 47: Edge Router Behavior
<number>
Monitor each flow i to measure its arrival rate (ri)
  EWMA of rate
  Non-constant EWMA constant
    e-T/K where T = current interarrival, K = constant
    Helps adapt to different packet sizes and arrival patterns
Rate is attached to each packet

## Slide 48: Core Router Behavior
<number>
Keep track of fair share rate α
  Increasing α does not increase load (F) by N * α
  F(α) = Σi min(ri, α)  what does this look like?
  Periodically update α
  Keep track of current arrival rate
    Only update α if entire period was congested or uncongested
Drop probability for packet = max(1- α/r, 0)

## Slide 49: F vs. Alpha
<number>
New alpha
C [linked capacity]
r1
r2
r3
old alpha
alpha
F

## Slide 50: Estimating Fair Share
<number>
Need F(α) = capacity = C
  Can’t keep map of F(α) values  would require per flow state
  Since F(α) is concave, piecewise-linear
    F(0) = 0 and F(α) = current accepted rate = Fc
    F(α) = Fc/ α
    F(αnew) = C  αnew = αold * C/Fc
What if a mistake was made?
  Forced into dropping packets due to buffer capacity
  When queue overflows α is decreased slightly

## Slide 51: Other Issues
<number>
Punishing fire-hoses – why?
  Easy to keep track of in a FQ scheme
What are the real edges in such a scheme?
  Must trust edges to mark traffic accurately
  Could do some statistical sampling to see if edge was marking accurately

## Slide 52: Overview
TCP and queues
Queuing disciplines
RED
Fair-queuing
Core-stateless FQ
XCP
<number>

## Slide 53: How does XCP Work?
<number>
Feedback
Round Trip Time
Congestion Window
Congestion Header
Feedback
Round Trip Time
Congestion Window
Feedback = + 0.1 packet
Notes: <number>

## Slide 54: How does XCP Work?
<number>
Feedback = + 0.1 packet
Round Trip Time
Congestion Window
Feedback = - 0.3 packet
Notes: <number>

## Slide 55: How does XCP Work?
<number>
Congestion Window = Congestion Window + Feedback
Routers compute feedback without any per-flow state
XCP extends ECN and CSFQ
Notes: <number>

## Slide 56: How Does an XCP Router Compute the Feedback?
<number>
Congestion Controller
Fairness Controller
Goal: Divides  between flows to converge to fairness
Looks at a flow’s state in Congestion Header
Algorithm:
If  > 0  Divide  equally between flows
If  < 0  Divide  between flows proportionally to their current rates
MIMD
AIMD
Goal: Matches input traffic to link capacity & drains the queue
Looks at aggregate traffic & queue
Algorithm:
Aggregate traffic changes by 
 ~ Spare Bandwidth
~ - Queue Size
So,  =  davg Spare -  Queue

Congestion Controller
Fairness Controller
Notes: <number>

## Slide 57: Getting the devil out of the details …
<number>
 =  davg Spare -  Queue
Theorem: System converges to optimal utilization (i.e., stable) for any link bandwidth, delay, number of sources if:
(Proof based on Nyquist Criterion)
Congestion Controller
Fairness Controller
No Parameter Tuning
Algorithm:
If  > 0  Divide  equally between flows
If  < 0  Divide  between flows proportionally to their current rates
Need to estimate number of flows N
RTTpkt : Round Trip Time in header
Cwndpkt : Congestion Window in header
T: Counting Interval
No Per-Flow State
Notes: <number>
Why is this N  1/(T*Cwnd/RTT) == # of pkts we expect to see from flow in time T… sum on this flow == 1 across all its pkts…
Next for additive  delta/N in Bwidth  delta * RTT/N in cwnd over cwnd/rtt pkts…  delta RTT^2 / (CWND * N)
For decrease  a little easier… for every packet basically want the same rate decrease – i.e. constant * RTT .. Just split across # pkts in interval

## Slide 58: Discussion
RED
  Parameter settings
RED vs. FQ
  How much do we need per flow tracking? At what cost?
FQ vs. XCP/CSFQ
  Is coarse-grained fairness sufficient?
  Misbehaving routers/trusting the edge
  Deployment (and incentives)
  How painful is FQ
XCP vs CSFQ
  What are the key differences
Granularity of fairness
  Mechanism vs. policy  will see this in QoS
<number>

## Slide 59: Important Lessons
<number>
How does TCP implement AIMD?
  Sliding window, slow start & ack clocking
  How to maintain ack clocking during loss recovery  fast recovery
How does TCP fully utilize a link?
  Role of router buffers
TCP alternatives
  TCP being used in new/unexpected ways
  Key changes needed

## Slide 60: Lessons
<number>
Fairness and isolation in routers
  Why is this hard?
  What does it achieve – e.g. do we still need congestion control?
Routers
  FIFO, drop-tail interacts poorly with TCP
  Various schemes to desynchronize flows and control loss rate (e.g. RED)
Fair-queuing
  Clean resource allocation to flows
  Complex packet classification and scheduling
Core-stateless FQ & XCP
  Coarse-grain fairness
  Carrying packet state can reduce complexity

## Slide 61: Next: Data center topology/routing
<number>
What do we make Ethernet scale to data center sizes?
Assigned reading
  Portland (read fully)
  Google (skim)
Notes: <number>

## Slide 62: EXTRA SLIDES
The rest of the slides are FYI

## Slide 63: Overview
<number>
Fairness
Fair-queuing
Core-stateless FQ
Other FQ variants

## Slide 64: Delay Allocation in FQ
<number>
Reduce delay for flows using less than fair share
  Advance finish times for sources whose queues drain temporarily
Schedule based on Bi instead of Fi
  Fi = Pi + max (Fi-1, Ai)  Bi = Pi + max (Fi-1, Ai - )
  If Ai < Fi-1, conversation is active and  has no effect
  If Ai > Fi-1, conversation is inactive and  determines how much history to take into account
    Infrequent senders do better when history is used

## Slide 65: Stochastic Fair Queuing
Compute a hash on each packet
Instead of per-flow queue have a queue per hash bin
An aggressive flow steals traffic from other flows in the same hash
Queues serviced in round-robin fashion
  Has problems with packet size unfairness
Memory allocation across all queues
  When no free buffers, drop packet from longest queue
<number>

## Slide 66: Deficit Round Robin
<number>
Each queue is allowed to send Q bytes per round
If Q bytes are not sent (because packet is too large) deficit counter of queue keeps track of unused portion
If queue is empty, deficit counter is reset to 0
Uses hash bins like Stochastic FQ
Similar behavior as FQ but computationally simpler

## Slide 67: Self-clocked Fair Queuing
<number>
Virtual time to make computation of finish time easier
Problem with basic FQ
  Need be able to know which flows are really backlogged
    They may not have packet queued because they were serviced earlier in mapping of bit-by-bit to packet
    This is necessary to know how bits sent map onto rounds
    Mapping of real time to round is piecewise linear  however slope can change often

## Slide 68: Self-clocked FQ
<number>
Use the finish time of the packet being serviced as the virtual time
  The difference in this virtual time and the real round number can be unbounded
Amount of service to backlogged flows is bounded by factor of 2

## Slide 69: Start-time Fair Queuing
<number>
Packets are scheduled in order of their start not finish times
Self-clocked  virtual time = start time of packet in service
Main advantage  can handle variable rate service better than other schemes

## Slide 70: TCP Modeling
<number>
Given the congestion behavior of TCP can we predict what type of performance we should get?
What are the important factors
  Loss rate
    Affects how often window is reduced
  RTT
    Affects increase rate and relates BW to window
  RTO
    Affects performance during loss recovery
  MSS
    Affects increase rate

## Slide 71: Overall TCP Behavior
<number>
Time
Window
Let’s concentrate on steady state behavior with no timeouts and perfect loss recovery

## Slide 72: Simple TCP Model
<number>
Some additional assumptions
  Fixed RTT
  No delayed ACKs
In steady state, TCP losses packet each time window reaches W packets
  Window drops to W/2 packets
  Each RTT window increases by 1 packetW/2 * RTT before next loss
  BW = MSS * avg window/RTT =
    MSS * (W + W/2)/(2 * RTT)
    .75 * MSS * W / RTT

## Slide 73: Simple Loss Model
<number>
What was the loss rate?
  Packets transferred between losses =
    Avg BW * time =
    (.75 W/RTT) * (W/2 * RTT) = 3W2/8
  1 packet lost  loss rate = p = 8/3W2
  W = sqrt( 8 / (3 * loss rate))
BW = .75 * MSS * W / RTT
  BW = MSS / (RTT * sqrt (2/3p))

## Slide 74: TCP Friendliness
<number>
What does it mean to be TCP friendly?
  TCP is not going away
  Any new congestion control must compete with TCP flows
    Should not clobber TCP flows and grab bulk of link
    Should also be able to hold its own, i.e. grab its fair share, or it will never become popular
How is this quantified/shown?
  Has evolved into evaluating loss/throughput behavior
  If it shows 1/sqrt(p) behavior it is ok
  But is this really true?