## Slide 1: 15-744: Computer Networking
L-17 P2P/DHT

## Slide 2: Overview
<number>
P2P Lookup Overview
Centralized/Flooded Lookups
Routed Lookups – Chord
Comparison of DHTs

## Slide 3: Peer-to-Peer Networks
<number>
Typically each member stores/provides access to content
Basically a replication system for files
  Always a tradeoff between possible location of files and searching difficulty
  Peer-to-peer allow files to be anywhere  searching is the challenge
  Dynamic member list makes it more difficult
What other systems have similar goals?
  Routing, DNS

## Slide 4: The Lookup Problem
<number>
Internet
N1
N2
N3
N6
N5
N4
Publisher
Key=“title”
Value=MP3 data…
Client
Lookup(“title”)
?
Notes: <number>
1000s of nodes.
Set of nodes may change…

## Slide 5: Centralized Lookup (Napster)
<number>
Publisher@
Client
Lookup(“title”)
N6
N9
N7
DB
N8
N3
N2
N1
SetLoc(“title”, N4)
Simple, but O(N) state and a single point of failure
Key=“title”
Value=MP3 data…
N4
Notes: <number>
O(N) state means its hard to keep the state up to date.

## Slide 6: Flooded Queries (Gnutella)
<number>
N4
Publisher@
Client
N6
N9
N7
N8
N3
N2
N1
Robust, but worst case O(N) messages per lookup
Key=“title”
Value=MP3 data…
Lookup(“title”)

## Slide 7: Routed Queries (Chord, etc.)
<number>
N4
Publisher
Client
N6
N9
N7
N8
N3
N2
N1
Lookup(“title”)
Key=“title”
Value=MP3 data…
Notes: <number>
Challenge: can we make it robust? Small state? Actually find stuff in a changing system?
Consistent rendezvous point, between publisher and client.

## Slide 8: Overview
<number>
P2P Lookup Overview
Centralized/Flooded Lookups
Routed Lookups – Chord
Comparison of DHTs

## Slide 9: Centralized: Napster
<number>
Simple centralized scheme  motivated by ability to sell/control
How to find a file:
  On startup, client contacts central server and reports list of files
  Query the index system  return a machine that stores the required file
    Ideally this is the closest/least-loaded machine
  Fetch the file directly from peer

## Slide 10: Centralized: Napster
<number>
Advantages:
  Simple
  Easy to implement sophisticated search engines on top of the index system
Disadvantages:
  Robustness, scalability
  Easy to sue!

## Slide 11: Flooding: Old Gnutella
<number>
On startup, client contacts any servent (server + client) in network
  Servent interconnection used to forward control (queries, hits, etc)
Idea: broadcast the request
How to find a file:
  Send request to all neighbors
  Neighbors recursively forward the request
  Eventually a machine that has the file receives the request, and it sends back the answer
  Transfers are done with HTTP between peers

## Slide 12: Flooding: Old Gnutella
<number>
Advantages:
  Totally decentralized, highly robust
Disadvantages:
  Not scalable; the entire network can be swamped with request (to alleviate this problem, each request has a TTL)
  Especially hard on slow clients
    At some point broadcast traffic on Gnutella exceeded 56kbps – what happened?
    Modem users were effectively cut off!

## Slide 13: Flooding: Old Gnutella Details
<number>
Basic message header
  Unique ID, TTL, Hops
Message types
  Ping – probes network for other servents
  Pong – response to ping, contains IP addr, # of files, # of Kbytes shared
  Query – search criteria + speed requirement of servent
  QueryHit – successful response to Query, contains addr + port to transfer from, speed of servent, number of hits, hit results, servent ID
  Push – request to servent ID to initiate connection, used to traverse firewalls
Ping, Queries are flooded
QueryHit, Pong, Push reverse path of previous message

## Slide 14: Flooding: Old Gnutella Example
<number>
Assume: m1’s neighbors are m2 and m3; m3’s neighbors are m4 and m5;…
A
B
C
D
E
F
m1
m2
m3
m4
m5
m6
E?
E?
E?
E?
E
E
E

## Slide 15: Flooding: Gnutella, Kazaa
<number>
Modifies the Gnutella protocol into two-level hierarchy
  Hybrid of Gnutella and Napster
Supernodes
  Nodes that have better connection to Internet
  Act as temporary indexing servers for other nodes
  Help improve the stability of the network
Standard nodes
  Connect to supernodes and report list of files
  Allows slower nodes to participate
Search
  Broadcast (Gnutella-style) search across supernodes
Disadvantages
  Kept a centralized registration  allowed for law suits 

## Slide 16: Overview
<number>
P2P Lookup Overview
Centralized/Flooded Lookups
Routed Lookups – Chord
Comparison of DHTs

## Slide 17: Routing: Structured Approaches
<number>
Goal: make sure that an item (file) identified is always found in a reasonable # of steps
Abstraction: a distributed hash-table (DHT) data structure
  insert(id, item);
  item = query(id);
  Note: item can be anything: a data object, document, file, pointer to a file…
Proposals
  CAN (ICIR/Berkeley)
  Chord (MIT/Berkeley)
  Pastry (Rice)
  Tapestry (Berkeley)
  …

## Slide 18: Routing: Chord
<number>
Associate to each node and item a unique id in an uni-dimensional space
Properties
  Routing table size O(log(N)) , where N is the total number of nodes
  Guarantees that a file is found in O(log(N)) steps

## Slide 19: Aside: Hashing
<number>
Advantages
  Let nodes be numbered 1..m
  Client uses a good hash function to map a URL to 1..m
  Say hash (url) = x, so, client fetches content from node x
  No duplication – not being fault tolerant.
  One hop access
  Any problems?
    What happens if a node goes down?
    What happens if a node comes back up?
    What if different nodes have different views?

## Slide 20: Robust hashing
<number>
Let 90 documents, node 1..9, node 10 which was dead is alive again
% of documents in the wrong node?
  10, 19-20, 28-30, 37-40, 46-50, 55-60, 64-70, 73-80, 82-90
  Disruption coefficient = ½
  Unacceptable, use consistent hashing – idea behind Akamai!

## Slide 21: Consistent Hash
<number>
“view” = subset of all hash buckets that are visible
Desired features
  Balanced – in any one view, load is equal across buckets
  Smoothness – little impact on hash bucket contents when buckets are added/removed
  Spread – small set of hash buckets that may hold an object regardless of views
  Load – across all views # of objects assigned to hash bucket is small

## Slide 22: Consistent Hash – Example
<number>
Smoothness  addition of bucket does not cause much movement between existing buckets
Spread & Load  small set of buckets that lie near object
Balance  no bucket is responsible for large number of objects
Construction
  Assign each of C hash buckets to random points on mod 2n circle, where, hash key size = n.
  Map object to random position on circle
  Hash of object = closest clockwise bucket
0
8
4
12
Bucket
14

## Slide 23: Routing: Chord Basic Lookup
<number>
N32
N90
N105
N60
N10
N120
K80
“Where is key 80?”
“N90 has K80”

## Slide 24: Routing: Finger table - Faster Lookups
<number>
N80
½
¼
1/8
1/16
1/32
1/64
1/128

## Slide 25: Routing: Chord Summary
<number>
Assume identifier space is 0…2m
Each node maintains
  Finger table
    Entry i in the finger table of n is the first node that succeeds or equals n + 2i
  Predecessor node
An item identified by id is stored on the successor node of id

## Slide 26: Routing: Chord Example
<number>
Assume an identifier space 0..8
Node n1:(1) joinsall entries in its finger table are initialized to itself
0
1
2
3
4
5
6
7
i id+2i succ
0 2 1
1 3 1
2 5 1
Succ. Table

## Slide 27: Routing: Chord Example
<number>
Node n2:(3) joins
0
1
2
3
4
5
6
7
i id+2i succ
0 2 2
1 3 1
2 5 1
Succ. Table
i id+2i succ
0 3 1
1 4 1
2 6 1
Succ. Table

## Slide 28: Routing: Chord Example
<number>
Nodes n3:(0), n4:(6) join
0
1
2
3
4
5
6
7
i id+2i succ
0 2 2
1 3 6
2 5 6
Succ. Table
i id+2i succ
0 3 6
1 4 6
2 6 6
Succ. Table
i id+2i succ
0 1 1
1 2 2
2 4 6
Succ. Table
i id+2i succ
0 7 0
1 0 0
2 2 2
Succ. Table

## Slide 29: Routing: Chord Examples
<number>
Nodes: n1:(1), n2(3), n3(0), n4(6)
Items: f1:(7), f2:(2)
0
1
2
3
4
5
6
7
i id+2i succ
0 2 2
1 3 6
2 5 6
Succ. Table
i id+2i succ
0 3 6
1 4 6
2 6 6
Succ. Table
i id+2i succ
0 1 1
1 2 2
2 4 0
Succ. Table
7
Items
1
Items
i id+2i succ
0 7 0
1 0 0
2 2 2
Succ. Table

## Slide 30: Routing: Query
<number>
Upon receiving a query for item id, a node
Check whether stores the item locally
If not, forwards the query to the largest node in its successor table that does not exceed id
0
1
2
3
4
5
6
7
i id+2i succ
0 2 2
1 3 6
2 5 6
Succ. Table
i id+2i succ
0 3 6
1 4 6
2 6 6
Succ. Table
i id+2i succ
0 1 1
1 2 2
2 4 0
Succ. Table
7
Items
1
Items
i id+2i succ
0 7 0
1 0 0
2 2 2
Succ. Table
query(7)

## Slide 31: What can DHTs do for us?
<number>
Distributed object lookup
  Based on object ID
De-centralized file systems
  CFS, PAST, Ivy
Application Layer Multicast
  Scribe, Bayeux, Splitstream
Databases
  PIER

## Slide 32: Overview
<number>
P2P Lookup Overview
Centralized/Flooded Lookups
Routed Lookups – Chord
Comparison of DHTs

## Slide 33: Comparison
<number>
Many proposals for DHTs
  Tapestry (UCB) -- Symphony (Stanford) -- 1hop (MIT)
  Pastry (MSR, Rice) -- Tangle (UCB) -- conChord (MIT)
  Chord (MIT, UCB) -- SkipNet (MSR,UW) -- Apocrypha (Stanford)
  CAN (UCB, ICSI) -- Bamboo (UCB) -- LAND (Hebrew Univ.)
  Viceroy (Technion) -- Hieras (U.Cinn) -- ODRI (TexasA&M)
  Kademlia (NYU) -- Sprout (Stanford)
  Kelips (Cornell) -- Calot (Rochester)
  Koorde (MIT) -- JXTA’s (Sun)
What are the right design choices? Effect on performance?

## Slide 34: Deconstructing DHTs
<number>
Two observations:
1. Common approach
  N nodes; each labeled with a virtual identifier (128 bits)
  define “distance” function on the identifiers
  routing works to reduce the distance to the destination
2. DHTs differ primarily in their definition of “distance”
  typically derived from (loose) notion of a routing geometry

## Slide 35: DHT Routing Geometries
<number>
Geometries:
  Tree (Plaxton, Tapestry)
  Ring (Chord)
  Hypercube (CAN)
  XOR (Kademlia)
  Hybrid (Pastry)
What is the impact of geometry on routing?

## Slide 36: Tree (Plaxton, Tapestry)
<number>
Geometry
  nodes are leaves in a binary tree
  distance = height of the smallest common subtree
  logN neighbors in subtrees at distance 1,2,…,logN
001
000
011
010
101
100
111
110

## Slide 37: Hypercube (CAN)
<number>
000
100
001
010
110
111
011
101
Geometry
  nodes are the corners of a hypercube
  distance = #matching bits in the IDs of two nodes
  logN neighbors per node; each at distance=1 away

## Slide 38: Ring (Chord)
<number>
Geometry
  nodes are points on a ring
  distance = numeric distance between two node IDs
  logN neighbors exponentially spaced over 0…N
000
101
011
010
001
110
111
100

## Slide 39: Hybrid (Pastry)
<number>
Geometry:
  combination of a tree and ring
  two distance metrics
  default routing uses tree; fallback to ring under failures
    neighbors picked as on the tree

## Slide 40: XOR (Kademlia)
<number>
00
01
11
10
01
11
10
00
Geometry:
  distance(A,B) = A XOR B
  logN neighbors per node spaced exponentially
  not a ring because there is no single consistent ordering of all the nodes

## Slide 41: Geometry’s Impact on Routing
<number>
Routing
  Neighbor selection: how a node picks its routing entries
  Route selection: how a node picks the next hop
Proposed metric: flexibility
  amount of freedom to choose neighbors and next-hop paths
    FNS: flexibility in neighbor selection
    FRS: flexibility in route selection
  intuition: captures ability to “tune” DHT performance
  single predictor metric dependent only on routing issues

## Slide 42: FRS for Ring Geometry
<number>
Chord algorithm picks neighbor closest to destination
A different algorithm picks the best of alternate paths
000
101
100
011
010
001
110
111
110

## Slide 43: FNS for Ring Geometry
<number>
Chord algorithm picks ith neighbor at 2i distance
A different algorithm picks ith neighbor from [2i , 2i+1)
000
101
100
011
010
001
110
111

## Slide 44: Flexibility: at a Glance
<number>
Flexibility | Ordering of Geometries
Neighbors (FNS) | Hypercube << Tree, XOR, Ring, Hybrid (1) (2i-1)
Routes (FRS) | Tree << XOR, Hybrid < Hypercube < Ring (1) (logN/2) (logN/2) (logN)

## Slide 45: Flexibility: at a Glance
<number>
Flexibility | Tree | Ring | Hypercube | XOR | Hybrid
FNS: #distinct routing tables | NlogN/2 | N logN/2 | 1 | NlogN/2 | NlogN/2
FRS: #distinct paths (log N hops) | 1 | 2c(log N)! | 2c(logN)! | 1 | 1
FRS: #distinct paths (> log N hops) | 0 | >> (log N)! | 0 | c(log N)! | c(log N)!
Notes: <number>

## Slide 46: Geometry  Flexibility  Performance?
<number>
Validate over three performance metrics:
  resilience
  path latency
  path convergence
Metrics address two typical concerns:
  ability to handle node failure
  ability to incorporate proximity into overlay routing

## Slide 47: Analysis of Static Resilience
<number>
Two aspects of robust routing
Dynamic Recovery : how quickly routing state is recovered after failures
Static Resilience : how well the network routes before recovery finishes
  captures how quickly recovery algorithms need to work
  depends on FRS
Evaluation:
Fail a fraction of nodes, without recovering any state
Metric: % Paths Failed

## Slide 48: Does flexibility affect static resilience?
<number>
Tree << XOR ≈ Hybrid < Hypercube < Ring
Flexibility in Route Selection matters for Static Resilience

## Slide 49: Which is more effective, FNS or FRS?
<number>
Plain << FRS << FNS ≈ FNS+FRS
Neighbor Selection is much better than Route Selection

## Slide 50: Does Geometry affect performance of FNS or FRS?
<number>
No, performance of FNS/FRS is independent of Geometry
A Geometry’s support for neighbor selection is crucial

## Slide 51: Understanding DHT Routing: Conclusion
<number>
What makes for a “good” DHT?
  one answer: a flexible routing geometry
Result: Ring is most flexible
  Why not the Ring?

## Slide 52: Next Lecture
Data-oriented networking
Required readings
  Content-centric networking (read)
  Redundancy elimination (skim)
Optional readings
    DOT, DONA, DTN
<number>

## Slide 53: Aside: Consistent Hashing [Karger 97]
<number>
N32
N90
N105
K80
K20
K5
Circular 7-bit
ID space
Key 5
Node 105
A key is stored at its successor: node with next higher ID

## Slide 54: Overview
<number>
Bittorrent
Notes: <number>

## Slide 55: Peer-to-Peer Networks: BitTorrent
BitTorrent history and motivation
  2002: B. Cohen debuted BitTorrent
  Key motivation: popular content
    Popularity exhibits temporal locality (Flash Crowds)
    E.g., Slashdot/Digg effect, CNN Web site on 9/11, release of a new movie or game
  Focused on efficient fetching, not searching
    Distribute same file to many peers
    Single publisher, many downloaders
  Preventing free-loading
<number>
Notes: <number>

## Slide 56: BitTorrent: Simultaneous Downloading
Divide large file into many pieces
  Replicate different pieces on different peers
  A peer with a complete piece can trade with other peers
  Peer can (hopefully) assemble the entire file
Allows simultaneous downloading
  Retrieving different parts of the file from different peers at the same time
  And uploading parts of the file to peers
  Important for very large files
<number>
Notes: <number>

## Slide 57: BitTorrent: Tracker
Infrastructure node
  Keeps track of peers participating in the torrent
Peers register with the tracker
  Peer registers when it arrives
  Peer periodically informs tracker it is still there
Tracker selects peers for downloading
  Returns a random set of peers
  Including their IP addresses
  So the new peer knows who to contact for data
Can have “trackerless” system using DHT
<number>
Notes: <number>

## Slide 58: BitTorrent: Chunks
Large file divided into smaller pieces
  Fixed-sized chunks
  Typical chunk size of 256 Kbytes
Allows simultaneous transfers
  Downloading chunks from different neighbors
  Uploading chunks to other neighbors
Learning what chunks your neighbors have
  Periodically asking them for a list
File done when all chunks are downloaded
<number>
Notes: <number>

## Slide 59: Self-certifying Names
A piece of data comes with a public key and a signature.
Client can verify the data did come from the principal by
  Checking the public key hashes into P, and
  Validating that the signature corresponds to the public key.
Challenge is to resolve the flat names into a location.

## Slide 60: BitTorrent: Overall Architecture
<number>
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Web Server
.torrent
Notes: <number>

## Slide 61: BitTorrent: Overall Architecture
<number>
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Get-announce
Web Server
Notes: <number>

## Slide 62: BitTorrent: Overall Architecture
<number>
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Response-peer list
Web Server
Notes: <number>

## Slide 63: BitTorrent: Overall Architecture
<number>
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Shake-hand
Web Server
Shake-hand
Notes: <number>

## Slide 64: BitTorrent: Overall Architecture
<number>
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
pieces
pieces
Web Server
Notes: <number>

## Slide 65: BitTorrent: Overall Architecture
<number>
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
pieces
pieces
pieces
Web Server
Notes: <number>

## Slide 66: BitTorrent: Overall Architecture
<number>
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Get-announce
Response-peer list
pieces
pieces
pieces
Web Server
Notes: <number>