## Slide 1: 15-744: Computer Networking
L-21 Wireless

## Slide 2: Wireless Intro
TCP on wireless links
Wireless MAC
Assigned reading
  [BPSK97] A Comparison of Mechanism for Improving TCP Performance over Wireless Links
  [BM09] In Defense of Wireless Carrier Sense
Optional
  [BDS+94] MACAW: A Media Access Protocol for Wireless LAN’s
<number>

## Slide 3: Wireless Challenges
Force us to rethink many assumptions
Need to share airwaves rather than wire
  Don’t know what hosts are involved
  Host may not be using same link technology
Mobility
Other characteristics of wireless
  Noisy  lots of losses
  Slow
  Interaction of multiple transmitters at receiver
    Collisions, capture, interference
  Multipath interference
<number>

## Slide 4: Overview
Wireless Background
Wireless MAC
  MACAW
  802.11
Wireless TCP
<number>

## Slide 5: Transmission Channel Considerations
Every medium supports transmission in a certain frequency range.
  Outside this range, effects such as attenuation, .. degrade the signal too much
Transmission and receive hardware will try to maximize the useful bandwidth in this frequency band.
  Tradeoffs between cost, distance, bit rate
As technology improves, these parameters change, even for the same wire.
  Thanks to our EE friends
Frequency
Good
Bad
Signal
<number>

## Slide 6: The Nyquist Limit
A noiseless channel of width H can at most transmit a binary signal at a rate 2 x H.
  E.g. a 3000 Hz channel can transmit data at a rate of at most 6000 bits/second
  Assumes binary amplitude encoding
<number>

## Slide 7: Past the Nyquist Limit
More aggressive encoding can increase the channel bandwidth.
  Example: modems
    Same frequency - number of symbols per second
    Symbols have more possible values
psk
Psk+ AM
<number>

## Slide 8: Capacity of a Noisy Channel
Can’t add infinite symbols - you have to be able to tell them apart. This is where noise comes in.
Shannon’s theorem:
  C = B x log2(1 + S/N)
  C: maximum capacity (bps)
  B: channel bandwidth (Hz)
  S/N: signal to noise ratio of the channel
    Often expressed in decibels (db). 10 log10(S/N).
Example:
  Local loop bandwidth: 3200 Hz
  Typical S/N: 1000 (30db)
  What is the upper limit on capacity?
    Modems: Teleco internally converts to 56kbit/s digital signal, which sets a limit on B and the S/N.
<number>

## Slide 9: Free Space Loss
Loss = Pt / Pr = (4 d)2 / (Gr Gt 2)
Loss increases quickly with distance (d2).
Need to consider the gain of the antennas at transmitter and receiver.
Loss depends on frequency: higher loss with higher frequency.
  But careful: antenna gain depends on frequency too
    For fixed antenna area, loss decreases with frequency
  Can cause distortion of signal for wide-band signals
<number>

## Slide 10: Cellular Reuse
Transmissions decay over distance
  Spectrum can be reused in different areas
  Different “LANs”
  Decay is 1/R2 in free space, 1/R4 in some situations
<number>

## Slide 11: Multipath Effects
Receiver receives multiple copies of the signal, each following a different path
Copies can either strengthen or weaken each other.
  Depends on whether they are in our out of phase
Small changes in location can result in big changes in signal strength.
  Short wavelengths, e.g. 2.4 GHz  12 cm
Difference in path length can cause inter-symbol interference (ISI).
<number>

## Slide 12: Fading - Example
Frequency of 910 MHz or wavelength of about 33 cm
<number>

## Slide 13: Overview
Wireless Background
Wireless MAC
  MACAW
  802.11
Wireless TCP
<number>

## Slide 14: Medium Access Control
Think back to Ethernet MAC:
  Wireless is a shared medium
  Transmitters interfere
  Need a way to ensure that (usually) only one person talks at a time.
    Goals: Efficiency, possibly fairness
<number>

## Slide 15: Example MAC Protocols
Pure ALOHA
  Transmit whenever a message is ready
  Retransmit when ACK is not received
Slotted ALOHA
  Time is divided into equal time slots
  Transmit only at the beginning of a time slot
  Avoid partial collisions
  Increase delay, and require synchronization
Carrier Sense Multiple Access (CSMA)
  Listen before transmit
  Transmit only when no carrier is detected
<number>

## Slide 16: CSMA/CD Does Not Work
Carrier sense problems
  Relevant contention at the receiver, not sender
  Hidden terminal
  Exposed terminal
Collision detection problems
  Hard to build a radio that can transmit and receive at same time
A
B
C
A
B
C
D
Hidden
Exposed
<number>

## Slide 17: MACA (RTS/CTS)
C
F
A
B
E
D
RTS
RTS = Request-to-Send
assuming a circular range
<number>

## Slide 18: MACA (RTS/CTS)
C
F
A
B
E
D
RTS
RTS = Request-to-Send
NAV = 10
NAV = remaining duration to keep quiet
<number>

## Slide 19: MACA (RTS/CTS)
C
F
A
B
E
D
CTS
CTS = Clear-to-Send
<number>

## Slide 20: MACA (RTS/CTS)
C
F
A
B
E
D
CTS
CTS = Clear-to-Send
NAV = 8
<number>

## Slide 21: MACA (RTS/CTS)
C
F
A
B
E
D
DATA
DATA packet follows CTS. Successful data reception acknowledged using ACK.
<number>

## Slide 22: MACA (RTS/CTS)
C
F
A
B
E
D
Reserved area
<number>

## Slide 23: MACAW: Additional Design
ACK (needed for faster TCP transfers)
DS (needed since carrier sense disabled)
RTS
CTS
Doesn’t hear CTS
Hears RTS
DS
Hears DS
DATA
<number>
Notes: <number>

## Slide 24: RRTS
RTS
DS
DATA
RTS
Problem:
CTS
RTS
Cannot send CTS
Backoff Increases
ACK
RRTS
RRTS prevents P2 from responding
RTS
CTS
DS
DATA
RTS
RTS lost
X
<number>
Notes: <number>

## Slide 25: MACAW: Conclusions
8% extra overhead for DS and ACK
37% improvement in congestion
<number>
Notes: <number>

## Slide 26: Overview
Wireless Background
Wireless MAC
  MACAW
  802.11
Wireless TCP
<number>

## Slide 27: IEEE 802.11 Overview
Adopted in 1997
Defines:
MAC sublayer
MAC management protocols and services
Physical (PHY) layers
  IR
  FHSS
  DSSS
<number>

## Slide 28: 802.11 particulars
802.11b (WiFi)
  Frequency: 2.4 - 2.4835 Ghz DSSS
  Modulation: DBPSK (1Mbps) / DQPSK (faster)
  Orthogonal channels: 3
    There are others, but they interfere. (!)
  Rates: 1, 2, 5.5, 11 Mbps
802.11a: 5Ghz OFDM. Up to 54Mbps, 19+ channels
802.11g: 2.4Ghz, up to 54Mbps
802.11n: 2.4 or 5Ghz, multiple antennas (MIMO), up to 450Mbps (for 3x3 antenna configuration)
2014 - 802.11ac: wider RF bandwidth (up to 160 MHz), more MIMO spatial streams (up to eight), downlink multi-user MIMO (up to four clients), and high-density modulation (up to 256-QAM), up to 1.3Gbps
<number>
Notes: <number>

## Slide 29: 802.11 details
Preamble
  72 bits @ 1Mbps, 48 bits @ 2Mbps
  Note the relatively high per-packet overhead
Control frames
  RTS/CTS/ACK/etc.
Management frames
  Association request, beacons, authentication, etc.
<number>

## Slide 30: Overview, 802.11 Architecture
STA
STA
STA
STA
STA
STA
STA
STA
AP
AP
ESS
BSS
BSS
BSS
BSS
Existing Wired LAN
Infrastructure Network
Ad Hoc Network
Ad Hoc Network
BSS: Basic Service Set
ESS: Extended Service Set
<number>

## Slide 31: 802.11 modes
Infrastructure mode
  All packets go through a base station
  Cards associate with a BSS (basic service set)
  Multiple BSSs can be linked into an Extended Service Set (ESS)
    Handoff to new BSS in ESS is pretty quick
      Wandering around CMU
    Moving to new ESS is slower, may require re-addressing
      Wandering from CMU to Pitt
Ad Hoc mode
  Cards communicate directly.
  Perform some, but not all, of the AP functions
<number>

## Slide 32: 802.11 Management Operations
Scanning
Association/Reassociation
Time synchronization
Power management
<number>

## Slide 33: Scanning & Joining
Goal: find networks in the area
Passive scanning
  No require transmission  saves power
  Move to each channel, and listen for Beacon frames
Active scanning
  Requires transmission  saves time
  Move to each channel, and send Probe Request frames to solicit Probe Responses from a network
<number>

## Slide 34: Association in 802.11
AP
1: Association request
2: Association response
3: Data traffic
Client
<number>

## Slide 35: Time Synchronization in 802.11
Timing synchronization function (TSF)
  AP controls timing in infrastructure networks
  All stations maintain a local timer
  TSF keeps timer from all stations in sync
Periodic Beacons convey timing
  Beacons are sent at well known intervals
  Timestamp from Beacons used to calibrate local clocks
  Local TSF timer mitigates loss of Beacons
<number>

## Slide 36: Power Management in 802.11
A station is in one of the three states
  Transmitter on
  Receiver on
  Both transmitter and receiver off (dozing)
AP buffers packets for dozing stations
AP announces which stations have frames buffered in its Beacon frames
Dozing stations wake up to listen to the beacons
If there is data buffered for it, it sends a poll frame to get the buffered data
<number>

## Slide 37: IEEE 802.11 Wireless MAC
Support broadcast, multicast, and unicast
  Uses ACK and retransmission to achieve reliability for unicast frames
  No ACK/retransmission for broadcast or multicast frames
Distributed and centralized MAC access
  Distributed Coordination Function (DCF)
  Point Coordination Function (PCF)
<number>

## Slide 38: 802.11 DCF (CSMA)
Distributed Coordination Function (CSMA/CA)
Sense medium. Wait for a DIFS (50 µs)
If busy, wait ‘till not busy. Random backoff.
If not busy, Tx.
Backoff is binary exponential
Acknowledgements use SIFS (short interframe spacing). 10 µs.
  Short spacing makes exchange atomic
<number>

## Slide 39: 802.11 DCF ([RTS/CTS/]Data/ACK)
<number>

## Slide 40: Discussion
RTS/CTS/Data/ACK vs. Data/ACK
  Why/when is it useful?
  What is the right choice
  Why is RTS/CTS not used?
<number>

## Slide 41: 802.11 Rate Adaptation
802.11 spec specifies rates not algorithm for choices
  802.11b 4 rates, 802.11a 8 rates, 802.11g 12 rates
  Each rate has different modulation and coding
Transmission Rate
then Loss Ratio
throughput decreases either way – need to get it just right
Transmission Rate
then Capacity Utilization
<number>
Notes: <number>
Current 802.11 specifications allow for multiple transmission rates at the physical layer
802(b) – 1, 2, 5.5, 11 (Megabytes per second)
802(a) – 6, 9, ,12, 18, 24, 26, 48, 54
802(g) – includes the set of a and b
Rate adaptation is critical to SYSTEM performance but is unspecified in the IEEE 802.11 standard

## Slide 42: Auto Bit Rate (ABR) Algorithms
Probe Packets
  ARF
  AARF
  SampleRate
Consecutive successes/losses
  ARF
  AARF
  Hybrid Algorithm
Physical Layer metrics
  Hybrid Algorithm
  RBAR
  OAR
Long-term statistics
  ONOE
Commercially Deployed: ARF, SampleRate and ONOE
<number>
Notes: <number>
ARF was introduced in WAVELAN II – autorate fallback --- and was the original rate adaptation algorithm
AARF – introduced in Rate Adaptation: A Practical Approach--- which is the adaptive autorate fallback
SampleRate – introduced in Bit-rate selection in Wireless networks–
Hybrid Algorithm -- introduced in Hybrid Rate Control for IEEE802.11 – uses Signal Strength (SNR) information to achieve fast responses
RBAR --- introduced in a Rate-Adaptive MAC protocol for Multihop Wireless networks – receiver based auto rate – the rate adaptation mechanism as in the receiver instead of the sender
OAR -- introduced in opportunistic Media Access for Multi-rate Ad Hoc Networks – opportunistic auto rate –goal: to send multiple back to back packets when there is an opportunity aka when there is good channel quality
ONOE introduce in Onoe Rate Control – which is an frame error based algorithm – goal : to select the highest bit rate with less then 50% frame loss

## Slide 43: Carrier Sense
<number>

## Slide 44: Maybe Carrier Sense is Fine?
<number>

## Slide 45: Single Receiver, Sender and Interferer
<number>

## Slide 46: Interferer Position
<number>

## Slide 47: ABR Helps in Disagreements
<number>

## Slide 48: Carrier Sense + ABR Works Well
<number>

## Slide 49: Key Assumptions
ABR == Shannon
  ABR is rarely this good
Interference and ABR are both stable
  Interference may be bursty/intermittent
<number>

## Slide 50: Overview
Wireless Background
Wireless MAC
  MACAW
  802.11
Wireless TCP
<number>

## Slide 51: Wireless Challenges
Force us to rethink many assumptions
Need to share airwaves rather than wire
  Don’t know what hosts are involved
  Host may not be using same link technology
Mobility
Other characteristics of wireless
  Noisy  lots of losses
  Slow
  Interaction of multiple transmitters at receiver
    Collisions, capture, interference
  Multipath interference
<number>

## Slide 52: TCP Problems Over Noisy Links
Wireless links are inherently error-prone
  Fades, interference, attenuation
  Errors often happen in bursts
TCP cannot distinguish between corruption and congestion
  TCP unnecessarily reduces window, resulting in low throughput and high latency
Burst losses often result in timeouts
Sender retransmission is the only option
  Inefficient use of bandwidth
<number>

## Slide 53: Constraints & Requirements
Incremental deployment
  Solution should not require modifications to fixed hosts
  If possible, avoid modifying mobile hosts
Probably more data to mobile than from mobile
  Attempt to solve this first
<number>

## Slide 54: Challenge #1: Wireless Bit-Errors
Router
Computer 2
Computer 1
2
3
2
2
Loss  Congestion
2
1
0
Burst losses lead to coarse-grained timeouts
Result: Low throughput
Loss  Congestion
Wireless
<number>

## Slide 55: Performance Degradation
Time (s)
Sequence number (bytes)
TCP Reno
(280 Kbps)
Best possible
TCP with no errors
(1.30 Mbps)
2 MB wide-area TCP transfer over 2 Mbps Lucent WaveLAN
<number>
Notes: <number>

## Slide 56: Proposed Solutions
End-to-end protocols
  Selective ACKs, Explicit loss notification
Split-connection protocols
  Separate connections for wired path and wireless hop
Reliable link-layer protocols
  Error-correcting codes
  Local retransmission
<number>

## Slide 57: Approach Styles (End-to-End)
Improve TCP implementations
  Not incrementally deployable
  Improve loss recovery (SACK, NewReno)
  Help it identify congestion (ELN, ECN)
    ACKs include flag indicating wireless loss
  Trick TCP into doing right thing  E.g. send extra dupacks
  What is SMART?
    DUPACK includes sequence of data packet that triggered it
Wired link
Wireless link
<number>

## Slide 58: Approach Styles (Split Connection)
Split connections
  Wireless connection need not be TCP
  Hard state at base station
    Complicates mobility
    Vulnerable to failures
    Violates end-to-end semantics
Wired link
Wireless link
<number>

## Slide 59: Split-Connection Congestion Window
Wired connection does not shrink congestion window
But wireless connection times out often, causing sender to stall
0
10000
20000
30000
40000
50000
60000
0
20
40
60
80
100
120
Time (sec)
Congestion Window (bytes)
Wired connection
Wireless connection
<number>
Notes: <number>

## Slide 60: Approach Styles (Link Layer)
More aggressive local rexmit than TCP
  Bandwidth not wasted on wired links
Adverse interactions with transport layer
  Timer interactions
  Interactions with fast retransmissions
  Large end-to-end round-trip time variation
FEC does not work well with burst losses
Wired link
Wireless link
ARQ/FEC
<number>

## Slide 61: Hybrid Approach: Snoop Protocol
Shield TCP sender from wireless losses
  Eliminate adverse interactions between protocol layers
  Congestion control only when congestion occurs
The End-to-End Argument [SRC84]
  Preserve TCP/IP service model: end-to-end semantics
  Is connection splitting fundamentally important?
Eliminate non-TCP protocol messages
  Is link-layer messaging fundamentally important?
Fixed to mobile: transport-aware link protocol
Mobile to fixed: link-aware transport protocol
<number>

## Slide 62: Snoop Overview
Modify base station
  to cache un-acked TCP packets
  … and perform local retransmissions
Key ideas
  No transport level code in base station
  When node moves to different base station, state eventually recreated there
<number>

## Slide 63: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
5
1
1
2
3
4
6
Snoop agent: active interposition agent
  Snoops on TCP segments and ACKs
  Detects losses by duplicate ACKs and timers
  Suppresses duplicate ACKs from MH
Snoop Agent
<number>
Notes: <number>

## Slide 64: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
Transfer of file from CH to MH
Current window = 6 packets
Snoop Agent
6
5
4
3
2
1
<number>
Notes: <number>

## Slide 65: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
Transfer begins
Snoop Agent
6
5
4
3
2
1
<number>
Notes: <number>

## Slide 66: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
5
1
1
2
3
4
6
Snoop agent caches segments that pass by
Snoop Agent
<number>
Notes: <number>

## Slide 67: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
5
1
2
3
4
6
Packet 1 is Lost
Snoop Agent
2
3
1
Lost Packets
1
<number>
Notes: <number>

## Slide 68: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
5
1
2
3
4
6
Packet 1 is Lost
  Duplicate ACKs generated
Snoop Agent
2
3
Lost Packets
1
4
ack 0
<number>
Notes: <number>

## Slide 69: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
5
1
2
3
4
6
Packet 1 is Lost
  Duplicate ACKs generated
Packet 1 retransmitted from cache at higher priority
Snoop Agent
2
3
Lost Packets
1
4
ack 0
5
6
1
ack 0
<number>
Notes: <number>

## Slide 70: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
5
1
2
3
4
6
Duplicate ACKs suppressed
Snoop Agent
2
3
4
ack 4
5
6
1
ack 0
X
<number>
Notes: <number>

## Slide 71: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
5
6
Clean cache on new ACK
Snoop Agent
2
3
4
ack 5
6
1
5
ack 4
<number>
Notes: <number>

## Slide 72: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
6
Clean cache on new ACK
Snoop Agent
2
3
4
ack 6
1
5
6
ack 5
ack 4
<number>
Notes: <number>

## Slide 73: Snoop Protocol: CH to MH
Correspondent Host
Mobile Host
Base Station
Active soft state agent at base station
Transport-aware reliable link protocol
Preserves end-to-end semantics
Snoop Agent
2
3
4
ack 6
1
5
6
9
7
8
ack 5
<number>
Notes: <number>

## Slide 74: Performance: FH to MH
1/Bit-error Rate (1 error every x Kbits)
Throughput (Mbps)
Typical error rates
2 MB local-area TCP transfer over 2 Mbps Lucent WaveLAN
Snoop+SACK and Snoop perform best
Connection splitting not essential
TCP SACK performance disappointing
TCP Reno
SPLIT
TCP SACK
SPLIT-SACK
Snoop
Snoop+SACK
<number>

## Slide 75: Discussion
Real link-layers aren’t windowed
  Out of order delivery not that significant a concern
TCP timers are very conservative
<number>

## Slide 76: MACAW
4 design details
  Contention is at the receiver
  Congestion is location dependent
  Fairness through learning of congestion levels
  Propagate synchronization information about contention periods
<number>
Notes: <number>

## Slide 77: Fairness in MACAW
Channel capture in MACA
  Backoff doubled every collision
  Reduce backoff on success
Solution: Copy backoffs
  This does not always work as wanted
<number>
Notes: <number>

## Slide 78: MACAW: Additional Design
Multiple Stream Model
ACK (TCP transfer!)
<number>
Notes: <number>

## Slide 79: 802.11 Glossary
Station
BSS - Basic Service Set
  IBSS : Infrastructure BSS
ESS - Extended Service Set
  A set of infrastructure BSSs.
  Connection of APs
  Tracking of mobility
DS – Distribution System
  AP communicates with another
<number>

## Slide 80: 802.11 Frame Priorities
Short interframe space (SIFS)
  For highest priority frames (e.g., RTS/CTS, ACK)
DCF interframe space (DIFS)
  Minimum medium idle time for contention-based services
Time
Busy
SIFS
DIFS
content window
Frame transmission
<number>

## Slide 81: SIFS/DIFS
SIFS makes RTS/CTS/Data/ACK atomic
RTS
CTS
Data
ACK
SIFS
SIFS
SIFS
DIFS
Time
Time
Sender1
Receiver1
RTS
Time
Sender2
DIFS
<number>

## Slide 82: 802.11 RTS/CTS
RTS sets “duration” field in header to
  CTS time + SIFS + CTS time + SIFS + data pkt time
Receiver responds with a CTS
  Field also known as the “NAV” - network allocation vector
  Duration set to RTS dur - CTS/SIFS time
  This reserves the medium for people who hear the CTS
<number>

## Slide 83: IEEE 802.11
C
F
A
B
E
D
RTS
RTS = Request-to-Send
assuming a circular range
<number>

## Slide 84: IEEE 802.11
C
F
A
B
E
D
RTS
RTS = Request-to-Send
NAV = 10
NAV = remaining duration to keep quiet
<number>

## Slide 85: IEEE 802.11
C
F
A
B
E
D
CTS
CTS = Clear-to-Send
<number>

## Slide 86: IEEE 802.11
C
F
A
B
E
D
CTS
CTS = Clear-to-Send
NAV = 8
<number>

## Slide 87: IEEE 802.11
C
F
A
B
E
D
DATA
DATA packet follows CTS. Successful data reception acknowledged using ACK.
<number>

## Slide 88: IEEE 802.11
C
F
A
B
E
D
ACK
<number>

## Slide 89: IEEE 802.11
C
F
A
B
E
D
ACK
Reserved area
<number>

## Slide 90: IEEE 802.11
C
F
A
B
E
D
DATA
Transmit “range”
Interference
“range”
Carrier sense
range
F
A
<number>

## Slide 91: Snoop Performance Improvement
Best
possible
TCP
(1.30
Mbps)
Time (s)
Time (s)
Sequence number (bytes)
Snoop (1.11 Mbps)
TCP Reno
(280 Kbps)
2 MB wide-area TCP transfer over 2 Mbps Lucent WaveLAN
<number>
Notes: <number>

## Slide 92: Benefits of TCP-Awareness
30-35% improvement for Snoop: LL congestion window is small (but no coarse timeouts occur)
Connection bandwidth-delay product = 25 KB
Suppressing duplicate acknowledgments and TCP-awareness leads to better utilization of link bandwidth and performance
0
0
10
20
30
40
50
60
70
80
20000
30000
40000
50000
60000
10000
Time (sec)
Congestion Window (bytes)
LL (no duplicate ack suppression)
Snoop
<number>
Notes: <number>

## Slide 93: Other Issues
What about mobility?
What about mobile-to-fixed communication?
<number>

## Slide 94: Handling Mobility
Correspondent Host
Base Station
Mobile Host
Base Station
Router
5
4
3
2
1
2
1
1
Send packets to multiple base stations
<number>

## Slide 95: Handling Mobility
Correspondent Host
Base Station
Mobile Host
Base Station
Router
6
5
4
3
1
3
2
1
1
2
Resend missed packets from Snoop cache on handoff
<number>

## Slide 96: Outline
Bluetooth
<number>

## Slide 97: Bluetooth basics
Short-range, high-data-rate wireless link for personal devices
  Originally intended to replace cables in a range of applications
  e.g., Phone headsets, PC/PDA synchronization, remote controls
Operates in 2.4 GHz ISM band
  Same as 802.11
  Frequency Hopping Spread Spectrum across ~ 80 channels
<number>

## Slide 98: Bluetooth Basics cont.
Maximum data rate of up to 720 Kbps
  But, requires large packets (> 300 bytes)
Class 1: Up to 100mW (20 dBm) transmit power, ~100m range
  Class 1 requires that devices adjust transmit power dynamically to avoid interference with other devices
Class 2: Up to 2.4 mW (4 dBm) transmit power
Class 3: Up to 1 mW (0 dBm) transmit power
<number>

## Slide 99: Usage Models
Wireless audio
  e.g., Wireless headset associated with a cell phone
  Requires guaranteed bandwidth between headset and base
  No need for packet retransmission in case of loss
Cable replacement
  Replace physical serial cables with Bluetooth links
  Requires mapping of RS232 control signals to Bluetooth messages
LAN access
  Allow wireless device to access a LAN through a Bluetooth connection
  Requires use of higher-level protocols on top of serial port (e.g., PPP)
File transfer
  Transfer calendar information to/from PDA or cell phone
  Requires understanding of object format, naming scheme, etc.
Lots of competing demands for one radio spec!
<number>

## Slide 100: Protocol Architecture
<number>

## Slide 101: Piconet Architecture
One master and up to 7 slave devices in each Piconet:
Master controls transmission schedule of all devices in the Piconet
  Time Division Multiple Access (TDMA): Only one device transmits at a time
Frequency hopping used to avoid collisions with other Piconets
  79 physical channels of 1 MHz each, hop between channels 1600 times a sec
<number>

## Slide 102: Scatternets
Combine multiple Piconets into a larger Scatternet
  Device may act as master in one Piconet and slave in another
  Each Piconet using different FH schedule to avoid interference
Can extend the range of Bluetooth, can route across Piconets
<number>

## Slide 103: Baseband Specification
79 1-MHz channels defined in the 2.4 GHz ISM band
  Gaussian FSK used as modulation, 115 kHz frequency deviation
Frequency Hopping Spread Spectrum
  Each Piconet has its own FH schedule, defined by the master
  1600 hops/sec, slot time 0.625 ms
Time Division Duplexing
  Master transmits to slave in one time slot, slave to master in the next
TDMA used to share channel across multiple slave devices
  Master determines which time slots each slave can occupy
  Allows slave devices to sleep during inactive slots
<number>

## Slide 104: Time slots
Each time slot on a different frequency
  According to FH schedule
Packets may contain ACK bit to indicate successful reception in the previous time slot
  Depending on type of connection...
  e.g., Voice connections do not use ACK and retransmit
Packets may span multiple slots – stay on same frequency
<number>

## Slide 105: Physical and Logical Links
Bluetooth supports two types of physical links.
Synchronous Connection Oriented (SCO):
  Slave assigned to two consecutive slots at regular intervals
    Just like TDMA...
  No use of retransmission ... why??
Asynchronous Connectionless (ACL)
  Allows non-SCO slots to be used for “on demand” transmissions
  Slave can only reply if it was addressed in previous slot by master
<number>

## Slide 106: Packet Formats
Bluetooth supports 14 different payload formats!
  Different formats for control, voice, and data packets
  Frames can span 1, 3, or 5 slots
  Different levels of error coding: No coding, 1/3, or 2/3 FEC
What is the maximum bandwidth that Bluetooth can achieve?
  Counting only application payload bytes, no CRC or FEC
  5-slot packet, no protection: 341 payload bytes
  Total time = 5 * (0.625) ms = 3.125 ms
    But ... need to count an extra slot from the master for ACK!
  Total bandwidth is therefore 341 bytes / (6 * 0.625 ms) = 721 kbps
<number>

## Slide 107: Discussion
Nice points
  A number of interesting low power modes
  Device discovery
    Must synchronize FH schemes
    Burden on the searcher
Some odd decisions
  Addressing
  Somewhat bulky application interfaces
    Not just simple byte-stream data transmission
    Rather, complete protocol stack to support voice, data, video, file transfer, etc.
      Bluetooth operates at a higher level than 802.11 and 802.15.4
<number>