## Slide 1: 15-744: Computer Networking
L-22 Making the Most of Wireless

## Slide 2: Outline
MIMO
Opportunistic forwarding (ExOR)
Network coding (COPE)

## Slide 3: How Do We Increase Throughput in Wireless?
Wired world: pull more wires!
Wireless world: use more antennas?

## Slide 4: MIMO Multiple In Multiple Out
N x M subchannels
Fading on channels is largely independent
  Assuming antennas are separate ½ wavelength or more
Combines ideas from spatial and time diversity, e.g. 1 x N and N x 1
Very effective if there is no direct line of sight
  Subchannels become more independent
N transmit
antennas
M receive
antennas

## Slide 5: Why So Exciting?
Method
SISO
Diversity (1xN or Nx1)
Diversity (NxN)
Multiplexing
Capacity
B log2(1 + r)
B log2(1 + rN)
B log2(1 + rN2)
NB log2(1 + r)

## Slide 6: Simple Channel Model
No diversity:
i x pT x h x pR = o
Adding multi-path:
i x pT x h(t) x pR = o
T
R
T
R

## Slide 7: Transmit and Receive Diversity Revisited
Receive diversity:
i x H x PR = o
Transmit diversity:
i x PT x H = o
T
R
T
R

## Slide 8: MIMO How Does it Work?
Coordinate the processing at the transmitter and receiver to overcome channel impairments
  Maximize throughput or minimize interference
Generalization of earlier techniques
  Combines maximum ratio combining at transmitter and receiver with sending of multiple data streams
T
R
Channel
Matrix
Precoding
from Nx1
Combining
from 1xN
I x PT x H x PR = O

## Slide 9: An Example of Space Coding

## Slide 10: A Math View

## Slide 11: Direct-Mapped NxM MIMO
How do we pick PR ?  Need “Inverse” of H: H-1
  Equivalent of nulling the interfering possible (zero forcing)
  Only possible if the paths are completely independent
Noise amplification is a concern if H is non-invertible – its determinant will be small
  Minimum Mean Square Error detector balances two effects
Effect of transmission R = H * C + N
M MxN N M
Decoding O = PR * R C = I
D DxM M N N
Results O = PR * H * I + PR * N
Notes: MRC maximum ratio combining

## Slide 12: Precoded NxM MIMO
How do we pick PR and PT ?
Effect of transmission R = H * C + N
M MxN N M
Coding/decoding O = PR * R C = PT * I
D DxM M N NxD D
Results O = PR * H * PT * I + PR * N

## Slide 13: Precoded NxM MIMO
How do we pick PR and PT ?
Singular value decomposition of H = U * S * V
  U and V are unitary matrices – UH*U = VH*V = I
  S is diagonal matrix
Set PR and PT to UH and VH
  Similar to approach for transmit and receive MRC
Equations suggest that we can view MIMO as a set of independent paths with strength given by the singular values of S
  Suggests giving more power to the stronger paths
  Water filling algorithm allocates power while maximizing throughput
Results O = PR * H * PT * I + PR * N
Notes: MRC maximum ratio combining; superscript H means Hermition or complex conjugate transpose

## Slide 14: MIMO Discussion
Need channel matrix H: use training with known signal
MIMO is used in 802.11n in the 2.4 GHz band
  Can use two of the non-overlapping “WiFi channels”
  Raises lots of compatibility issues
  Potential throughputs of 100 of Mbps
Focus is on maximizing throughput between two nodes
  Is this always the right goal?

## Slide 15: Outline
MIMO
Opportunistic forwarding (ExOR)
Network coding (COPE)

## Slide 16: Initial Approach: Traditional Routing
packet
packet
packet
Identify a route, forward over links
Abstract radio to look like a wired link
src
A
B
dst
C
Notes: just say picks a route, fwd over that route

## Slide 17: Radios Aren’t Wires
Every packet is broadcast
Reception is probabilistic
1
2
3
4
5
6
1
2
3
6
3
5
1
4
2
3
4
5
6
1
2
4
5
6
src
A
B
dst
C
Notes: what’s really going on is we’re abstracting  as youall know, radios don’t work like links

## Slide 18: Exploiting Probabilistic Broadcast
packet
packet
packet
packet
packet
packet
src
A
B
dst
C
packet
packet
packet
Decide who forwards after reception
Goal: only closest receiver should forward
Challenge: agree efficiently and avoid duplicate transmissions
Notes: say there’s an opportunity here, take advantage of bcast. spell it out: closest node should reduce the number of tx to get to dest. challenge:: key failure is that two people should not forward. make sure only one guy forwards

## Slide 19: Why ExOR Might Increase Throughput
Best traditional route over 50% hops: 3(1/0.5) = 6 tx
Throughput ≅ /# transmissions
ExOR exploits lucky long receptions: 4 transmissions
Assumes probability falls off gradually with distance
src
dst
N1
N2
N3
N4
75%
50%
N5
25%
Notes: new slide earlier, assume figured out design. explore why exor might improve throughput/develop a feel title -> why exor might beat trad routing.
inverse prop to #trans, up to 4 hops

## Slide 20: Why ExOR Might Increase Throughput
Traditional routing: 1/0.25 + 1 = 5 tx
ExOR: 1/(1 – (1 – 0.25)4) + 1 = 2.5 transmissions
Assumes independent losses
N1
src
dst
N2
N3
N4
25%
25%
25%
25%
100%
100%
100%
100%
Notes: say this is a contrived example

## Slide 21: ExOR Batching
Challenge: finding the closest node to have rx’d
Send batches of packets for efficiency
Node closest to the dst sends first
  Other nodes listen, send remaining packets in turn
Repeat schedule until dst has whole batch
src
N3
dst
N4
tx: 23
tx: 57 -23
≅ 24
tx: ≅ 8
tx: 100
rx: 23
rx: 57
rx: 88
rx: 0
rx: 0
tx: 0
tx: ≅ 9
N1
N2
rx: 53
rx: 85
rx: 99
rx: 40
rx: 22
Notes: add circle for source, then some more circles showing next iteration (no rx/tx numbers). say at the end, packets go through multiple iteration. add source, add n4.

## Slide 22: Reliable Summaries
Repeat summaries in every data packet
Cumulative: what all previous nodes rx’d
This is a gossip mechanism for summaries
src
N1
N2
N3
dst
N4
tx: {1, 6, 7 ... 91, 96, 99}
tx: {2, 4, 10 ... 97, 98}
batch map: {1,2,6, ... 97, 98, 99}
batch map: {1, 6, 7 ... 91, 96, 99}
Notes: just say we incude a summary in every packet
repeated
cumulative
simplify: every node is listening, include list to make it more robust

## Slide 23: Priority Ordering
Goal: nodes “closest” to the destination send first
Sort by ETX metric to dst
  Nodes periodically flood ETX “link state” measurements
  Path ETX is weighted shortest path (Dijkstra’s algorithm)
Source sorts, includes list in ExOR header
src
N1
N2
N3
dst
N4
Notes: source calculates path etx for each node to dest, talk about dijkstra, sort by lowest etx

## Slide 24: Using ExOR with TCP
Node
Proxy
ExOR
Gateway
Web
Proxy
Client PC
Web Server
TCP
TCP
ExOR Batches (not TCP)
Batching requires more packets than typical TCP window
Notes: don’t say we will, say we do. Batching interacts badly with tcp. Internet cloud. NOT using TCP in the middle – spell it out

## Slide 25: Discussion
Exploits radio properties, instead of hiding them
Scalability?
Parameters – 10%?
Overheads?

## Slide 26: Outline
MIMO
Opportunistic forwarding (ExOR)
Network coding (COPE)

## Slide 27: Background
Famous butterfly example:
All links can send one message per unit of time
  Coding increases overall throughput

## Slide 28: Background
Bob and Alice
Relay
Require 4 transmissions

## Slide 29: Background
Bob and Alice
Relay
Require 3 transmissions
XOR
XOR
XOR
Notes: Bridge the gap between theory of network coding and practical network design

## Slide 30: Coding Gain
Coding gain = 4/3
1
1+3
3

## Slide 31: Throughput Improvement
UDP throughput improvement ~ a factor 2 > 4/3 coding gain
1
1+3
3

## Slide 32: Summary
Wireless behavior is not all bad
Next lecture: Security: DDoS and Traceback
Readings:
  Practical Network Support for IP Traceback
  Amplification Hell: Revisiting Network Protocols for DDoS Abuse

## Slide 33: Coding Gain: more examples
Without opportunistic listening, coding [+MAC] gain=2N/(1+N)  2. With opportunistic listening, coding gain + MAC gain  ∞
3
5
1+2+3+4+5
2
4
1

## Slide 34: Opportunistic Coding
B’s queue | Next hop
P1 | A
P2 | C
P3 | C
P4 | D
Coding | Is it good?
P1+P2 | Bad (only C can decode)
P1+P3 | Better coding (Both A and C can decode)
P1+P3+P4 | Best coding (A, C, D can decode)
B
A
C
D
P4 P3
P3 P1
P4 P3 P2 P1
P4 P1

## Slide 35: COPE (Coding Opportunistically)
Overhear neighbors’ transmissions
Store these packets in a Packet Pool for a short time
Report the packet pool info. to neighbors
Determine what packets to code based on the info.
Send encoded packets

## Slide 36: Packet Coding Algorithm
When to send?
  Option 1: delay packets till enough packets to code with
  Option 2: never delaying packets -- when there’s a transmission opportunity, send packet right away
Which packets to use for XOR?
  Prefer XOR-ing packets of similar lengths
  Never code together packets headed to the same next hop
  Limit packet re-ordering
  XORing a packet as long as all its nexthops can decode it with a high enough probability

## Slide 37: Packet Decoding
Where to decode?
  Decode at each intermediate hop
How to decode?
  Upon receiving a packet encoded with n native packets
    find n-1 native packets from its queue
    XOR these n-1 native packets with the received packet to extract the new packet

## Slide 38: Prevent Packet Reordering
Packet reordering due to async acks degrade TCP performance
Ordering agent
  Deliver in-sequence packets immediately
  Order the packets until the gap in seq. no is filled or timer expires

## Slide 39: Summary of Results
Improve UDP throughput by a factor of 3-4
Improve TCP by
  wo/ hidden terminal: up to 38% improvement
  w/ hidden terminal and high loss: little improvement
Improvement is largest when uplink to downlink has similar traffic
Interesting follow-on work using analog coding

## Slide 40: Reasons for Lower Improvement in TCP
COPE introduces packet re-ordering
Router queue is small  smaller coding opportunity
  TCP congestion window does not sufficiently open up due to wireless losses
TCP doesn’t provide fair allocation across different flows

## Slide 41: Discussion
Wired vs. wireless coding
Traffic patterns
Scale

## Slide 42: Outline
MIMO
Opportunistic forwarding (ExOR)
Network coding (COPE)
Combining the two (MORE)

## Slide 43: Use Opportunistic Routing
Best single path  loss prob. 50%
In opp. routing [ExOR’05], any router that hears the packet can forward it  loss prob. 0.54 = 6%
Opportunistic routing promises large increase in throughput
src
R1
dst
R4
R2
R3
50%
100%
50%
100%
100%
100%
50%
50%
Notes: BUT we realize that when the source transmits, the packet is actually broadcast over the radio..
Hence, even if it doesn’t reach a specific router, another one might get lucky and receive it.
So why discard these fortunate receptions, when we can exploit them?
2 years ago, there was this cool SIGCOMM paper on opportunistic routing that proposed a protocol called ExOR.
In opportunistic routing, any router that receives the transmission can participate in forwarding.
And because, we first broadcast, and then look at who receives the transmission,
The probability that the source must retransmit is greatly reduced to just 6%.
Thus, opp. routing promises significant improvement in throughput

## Slide 44: But
src
R1
dst
Overlap in received packets  Routers forward duplicates
R2
P1
P2
P10
P1
P2
P1
P2
Notes: Let’s see this on an example.
The source wants to deliver 10 packets, P1 throgh P10,
So it broadcasts them,
And let’s say that among other things,
The two routers R1 and R2, both receive P! And P2.
If both forward these packets, the destination receives two copies of each,
..so we wasted valuable wireless bandwidth.

## Slide 45: ExOR
State-of-the-art opp. routing, ExOR imposes a global scheduler:
Requires full coordination; every node must know who received what
Only one node transmits at a time, others listen

## Slide 46: Global Scheduling
Global coordination is too hard
One transmitter  You lost spatial reuse!
src
dst
Notes: (Furthermore, if the coordination requires that only one node transmits at a time...)
...then we cannot benefit from spatial reuse of the medium.
For example, in this network, up to 4 nodes could transmit at the same time without colliding,
So if we allow only one, then we give up a lot of wireless bandwidth.
So here’s what we thought…
Opportunistic routing is a really neat idea, so does it really have to be that complicated?
Do we really need global coordination, global scheduling, __and__ to give up spatial reuse?
Could we do it in a simpler way?
The answer is yes!

## Slide 47: MORE (Sigcomm07)
Opportunistic routing with no global scheduler and no coordination
Uses random network coding
Experiments show that randomness outperforms both current routing and ExOR
Notes: The rest of this talk is about how to do opportunistic routing without global scheduling and without global coordination.
The key idea is to use random network coding.
Our experiments show that this randomness actually outperforms both current single-path routing and ExOR

## Slide 48: Go Random
src
R1
dst
R2
α P1+ ß P2
γ P1+ δ P2
Each router forwards random combinations of packets
Randomness prevents duplicates
No scheduler; No coordination
Simple and exploits spatial reuse
P1
P2
P1
P2
Notes: Getting back to our example. -- Routers R1 and R2 had both received P1 and P2.
Now without any coordination,
...R1 picks two random numbers alpha and beta,
...multiplies the bytes in the packets by these numbers to create a coded packet
R2 does the same, picking some other random numbers…
When the destination receives two such combinations
...it actually gets 2 linear equations that it can solve to find the unknown packets P1 and P2.
This works, because we picked the numbers at random, so they are very unlikely duplicates.
So we don’t need the scheduler, because we don’t need the coordination!
This very simple idea allows us to do opportunistic routing _and_ exploit spatial reuse

## Slide 49: Random Coding Benefits Multicast
src
dst1
dst2
dst3
P1
P2
P3
P4
P1
P2
P2
P3
P3
P4
P3
P4
P1
P4
P1
P2
Without coding  source retransmits all 4 packets
Notes: But there is more to it --- With random coding we can extend opportunistic routing to multicast!
Suppose that the source wants to multicast 4 packets, P1 through P4
..to a group of 3 destinations.
The source bcast these 4 packets, --- And because wireless losses are independent, it’s likely that each destination loses different packets.
In particular in this scenario, every packet is lost at some destination,
So even if source had global knowledge, it would have to retransmit each packet ( and so we would need 4 transmissions )

## Slide 50: Random Coding Benefits Multicast
src
dst1
dst2
dst3
P1
P2
P3
P4
P1
P2
P2
P3
P3
P4
8 P1+5 P2+ P3+3 P4
7 P1+3 P2+6 P3+ P4
P3
P4
P1
P4
P1
P2
Without coding  source retransmits all 4 packets
With random coding  2 packets are sufficient
Random combinations
Notes: But WITH random coding, we can satisfy all destinations with just 2 packets. Let’s see how.
create two __completely random__ combinations of all 4 packets and broadcast them.
Destination 1 has already received P1 and P2,
…so it can substitute them in these two equations, and solve for (missing) P3 and P4.
Similarly destination 2 and 3 can retrieve their missing packets.
So this ex. shows that
Random coding is not just about removing the scheduler.
It’s actually more efficient than global coordination…

## Slide 51: MORE
Source sends packets in batches
Forwarders keep all heard packets in a buffer
Nodes transmit linear combinations of buffered packets
src
A
B
dst
P1
P2
P3
P1
P2
P3
=
+ b
+ c
a
a,b,c
4,1,3
0,2,1
4,1,3
P1
P2
P3
=
+ 1
+ 3
4
4,1,3
P1
P2
P3
=
+ 2
+ 1
0
0,2,1
Notes: Similarly to ExOR, in MORE, the source sends packets in batches…
Rather than the standard FIFO queue, the forwarders keep a buffer for incoming packets.
Whenever any node wants to transmit, it creates a random linear combinations of (all) the packets in its buffer.
Let me illustrate.
So here we have the source, destinatoin and two routers in between.
You can see their buffers for incoming packets. And you can also see that the source has a batch of 3 packets...
We put these numbers in the header of the packet, so that we know what equation it stands for.
In case you worry about this, as we show in the paper, we can compute such linear combinations and sustain high throughput.

## Slide 52: MORE
src
A
B
dst
P1
P2
P3
P1
P2
P3
=
+ b
+ c
a
a,b,c
4,1,3
0,2,1
4,1,3
=
2
+ 1
0,2,1
8,4,7
4,1,3
8,4,7
8,4,7
Source sends packets in batches
Forwarders keep all heard packets in a buffer
Nodes transmit linear combinations of buffered packets

## Slide 53: MORE
Destination decodes once it receives enough combinations
  Say batch is 3 packets
1,3,2
5,4,5
4,5,5
P1
P2
P3
=
+ 3
+ 2
1
P1
P2
P3
=
+ 4
+ 5
5
P1
P2
P3
=
+ 5
+ 5
4
Destination acks batch, and source moves to next batch
Source sends packets in batches
Forwarders keep all heard packets in a buffer
Nodes transmit linear combinations of buffered packets
Notes: At some point the destination wil have enough combinations to decode the batch.
How much is enough? Let’s say that as in our example the batch is 3 packets.
Then once the destination gather 3 combinations, since each of them is actually a linear equation,
The destination can solve this set (of 3 lin.) equations to find the 3 unknown packets (with simple algebra)
But this is just a method, ...let’s not forget about our objective...

## Slide 54: But How Do We Get the Most Throughput?
Naïve approach transmits whenever 802.11 allows
If A and B have same information, it is more efficient for B to send it
Need a Method to Our Madness
A
B
dst
Notes: `How can we get the most throughput?
A naive approach is to just stand there and keep creating linear combinations and spitting them out in the air…
… but that won’t work!
Let’s take a simple example..
Suppose that B is located very close to the destination, A is much farther off.
If A and B have the same information it is more efficient for B to send it, because it is more likely to reach the destination…
Clearly, we need a method to this maddness...

## Slide 55: Probabilistic Forwarding
A
B
dst
Notes: And that method is probabilistic forwarding
How does it work?

## Slide 56: Probabilistic Forwarding
e1
e1
e2
A
B
dst
Src
P1
P2
Loss rate 50%
Loss rate 0%
Notes: Getting back to our example.
Let’s add the source to the picture.
Suppose it has a batch of just 2 packets and it broadcasts 2 combinations ...
Because A is closer to the source, it has a very good link and receives both of them,
While B is farther and one of the packets is lost...

## Slide 57: Probabilistic Forwarding
e1
A
B
dst
Src
P1
P2
e1
?
50% of buffer
e1
e2
e1
How many packets should I forward?
Notes: A and B have shared information, and as we said, it’s more efficient for B to forward the common information, [ANIM]
Now, A is going to forward random combinations, but __how many__?
-- in this case, the batch has just 2 packets, so the destination can decode it from 2 combinations...
B is going to deliver one, so we only need one more...
In other terms, A should forward only 50% of its buffer, because the other 50% overlaps with B.

## Slide 58: Probabilistic Forwarding
e1
A
B
dst
Src
P1
P2
50%
0%
e1
e1
e2
Pr = 0.5
Pr = 1
Compute forwarding probabilities without coordination using loss rates
Notes: We could also say, that
FOR EVERY PACKET IT RECEIVES,
...A should forward one packet with probability 0.5.
...While B should forward one packet with probability 1.0
But, how do we compute these probabilities?
Easily!
We can predict these probabilities by looking at the loss rates on the links.
Here, for every packet that A receives from src, with probability 50%, B also received it, so we predict 50% overlap.
[BANNER]
Note that any routing protocol needs to know the loss rates…
…and in fact, the actual computation of the forwarding probabilities,
…is as easy as computing the shortest path in the network...
As we show in the paper.

## Slide 59: Can ExOR Use Probabilistic Forwarding To Remove Coordination?
A
B
dst
Pr = 0.5
Pr = 1
P1
P2
P1
P1
P1
Without random coding  need to know the exact packets to forward every time
With random coding  need to know only the average amount of overlap
Probability of duplicates is 50%
Notes: It’s then natural to ask can’t we just use these probabilities in ExOR and get rid of the coordination?
But we can’t. So A knows that it should forward 1 packet, but it has to pick one or the other.
Without coordinating with B, it could just as well choose wrongly and forward P1.
[BANNER]
So the basic issue is that
.. Without coding, we need to know __exactly__ the right packet to forward every time
.. This is much harder, than
…with random coding, when we only need to know the __average_ amount of overlap…

## Slide 60: Adapting to Short-term Dynamics
Need to balance sent information with received information
MORE triggers transmission by receptions
A node has a credit counter
  Upon reception, increment the counter using forwarding probabilities
  Upon transmission, decrement the counter
Source stops  No triggers  Flow is done
Notes: “Intuitiviely, there should be a balance between how much you send and how much you receive,
In the long-term this is achieved with probabilistic forwarding”
But in the short term, if you receive less than expected, because someone turned on microwave next to you,
Then you should send less, because you have less information.
This way, you will free up the medium for other nodes.
And if you received more, because the wireless medium in your area has improved, then you should send more.
The way to do that is to trigger transmissions by receptions..
So in MORE, every node has a credit counter…
A nice benefit of this credit mechanism, is that it brings a logical stop to a flow…
When the source stops …There are no more triggers in the network…

## Slide 61: Opportunistic Coding
Three ways to get neighbor state
  Reception report
  Guess
    Based on ETX metric (delivery probability)
    Estimate the probability that packets are overheard
  The neighbor is the previous hop of the packet
Notes: But how does a node know what packets its neighbors have?
Report to its neighbors the packets it stores.
However, at times of severe congestion, report may get lost in collisions. They also may arrive too late after the coding decision
The first way and the third way are reliable.

## Slide 62: COPE Design
Pseudo Broadcast
  Cons of broadcast
    Unreliable due to no ACK
    Lack of backoff
  Piggy back on unicast
    Set one of intended node as Mac address
    List all others in COPE header (between MAC and IP header)
    Receiver: if it is on the list, decode the packet, else store the packet in its pool