## Slide 1: Data Representation
Recitation 3: Monday, September 14th, 2015
Dhruven Shah, Ben Spinelli

## Slide 2: Welcome to Recitation
Recitation is a place for interaction
  If you have questions, please ask.
  If you want to go over an example not planned for recitation, let me know.
We’ll cover:
  A quick recap of topics from class, especially ones we have found students struggled with in the past
  Example problems to reinforce those topics and prepare for exams
  Demos, tips, and questions for labs

## Slide 3: News
Course Website: www.cs.cmu.edu/~213
Access to Autolab
Office hours in GHC 5207
  Sunday – Thursday 6:00-9:00 pm
  Additional office hours near due dates, see website for schedule
Linux boot camp this Saturday, 2:00-4:00 pm in Gates 4401
Data lab due September 17, 11:59 pm EDT

## Slide 4: Agenda
How do I Data Lab?
Integers
  Biasing division
  Endianness
Floating point
  Binary fractions
  IEEE standard
  Example problem

## Slide 5: How do I Data Lab?
Step 1: Download lab files
  All lab files are on Autolab
  Remember to also read the lab handout (“view writeup” link)
Step 2: Work on the right machines
  Remember to do all your lab work on Andrew or Shark machines
    Some later labs will restrict you to just the shark machines (bomb lab, for example)
  This includes untaring the handout. Otherwise, you may lose some permissions bits
  If you get a permission denied error, try “chmod +x filename”

## Slide 6: How do I Data Lab?
Step 3: Edit and test
  bits.c is the file you’re looking for
  Remember you have 3 ways to test your solutions.
    btest
    dlc
    BDD checker
  driver.pl runs the same tests as Autolab
Step 4: Submit
  Unlimited submissions, but please don’t use Autolab in place of driver.pl
  Must submit via web form
  To package/download files to your computer, use “tar -cvzf out.tar.gz in1 in2 …” and your favorite file transfer protocol

## Slide 7: How do I Data Lab?
Tips
  Write C like it’s 1989
    Declare variable at top of function
    Make sure closing brace (“}”) is in 1st column
    We won’t be using the dlc compiler for later labs
  Be careful of operator precedence
    Do you know what order ~a+1+b*c<<3*2 will execute in?
    Neither do I. Use parentheses: (~a)+1+(b*(c<<3)*2)
  Take advantage of special operators and values like !, 0, and Tmin
  Reducing ops once you’re under the threshold won’t get you extra points.
  Undefined behavior
    Like shifting by >31. See Anita’s rant.

## Slide 8: Anita’s Rant
From the Intel x86 Reference:
  “These instructions shift the bits in the first operand (destination operand) to the left or right by the number of bits specified in the second operand (count operand). Bits shifted beyond the destination operand boundary are first shifted into the CF flag, then discarded. At the end of the shift operation, the CF flag contains the last bit shifted out of the destination operand.
  The destination operand can be a register or a memory location. The count operand can be an immediate value or register CL. The count is masked to five bits, which limits the count range to 0 to 31. A special opcode encoding is provided for a count of 1.”

## Slide 9: Integers - Biasing
Can multiply/divide powers of 2 with shift
  Multiply:
    Left shift by k to multiply by 2k
  Divide:
    Right shift by k to divide by 2k
    … for positive numbers
    Shifting rounds towards -inf, but we want to round to 0
    Solution: biasing when negative

## Slide 10: Integers – Endianness
Endianness describes which bit is most significant in a binary number
You won’t need to work with this until bomb lab
Big endian:
  First byte (lowest address) is the most significant
  This is how we typically talk about binary numbers
Little endian:
  First byte (lowest address) is the least significant
  Intel x86 (shark/andrew linux machines) implement this

## Slide 11: Floating Point – Fractions in Binary
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 12: Floating Point – IEEE Standard
Single precision: 32 bits
Double precision: 64 bits
Extended precision: 80 bits (Intel only)
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits
s | exp | frac
1 | 15-bits | 63 or 64-bits

## Slide 13: Floating Point – IEEE Standard
What does this mean?
  We can think of floating point as binary scientific notation
    IEEE format includes a few optimizations to increase range for our given number of bits
  The number represented is essentially (sign * frac * 2exp)
    There are a few steps I left out there
Example:
  Assume our floating point format has no sign bit, k = 3 exponent bits, and n=2 fraction bits
  What does 10010 represent?

## Slide 14: Floating Point – IEEE Standard
What does this mean?
  We can think of floating point as binary scientific notation
    IEEE format includes a few optimizations to increase range for our given number of bits
  The number represented is essentially (sign * frac * 2exp)
    There are a few steps I left out there
Example:
  Assume our floating point format has no sign bit, k = 3 exponent bits, and n=2 fraction bits
  What does 10010 represent? 3

## Slide 15: Floating Point – IEEE Standard
Bias
  exp is unsigned; needs a bias to represent negative numbers
  Bias = 2k-1 - 1, where k is the number of exponent bits
  Can also be thought of as bit pattern 0b011…111
  When converting frac/int => float, assume normalized until proven otherwise
Normalized | Denormalized
 | exp = 0
Implied leading 1 | 
E = exp - Bias | 
Denser near origin | 
 | Represents small numbers

## Slide 16: Floating Point – IEEE Standard
Bias
  exp is unsigned; needs a bias to represent negative numbers
  Bias = 2k-1 - 1, where k is the number of exponent bits
  Can also be thought of as bit pattern 0b011…111
  When converting frac/int => float, assume normalized until proven otherwise
Normalized | Denormalized
0 < exp < (2k-1) | exp = 0
Implied leading 1 | Leading 0
E = exp - Bias | E = 1 - Bias. Why?
Denser near origin | Evenly spaced
Represents large numbers | Represents small numbers

## Slide 17: Floating Point – IEEE Standard
Special Cases (exp = 2k-1)
  Infinity
    Result of an overflow during calculation or division by 0
    exp = 2k-1, frac = 0
  Not a Number (NaN)
    Result of illegal operation (sqrt(-1), inf – inf, inf * 0)
    exp = 2k-1, frac != 0
  Keep in mind these special cases are not the same

## Slide 18: Floating Point – IEEE Standard
Round to even
  Why? Avoid statistical bias of rounding up or down on half.
  How? Like this:
1.01002 | truncate | 1.012
1.01012 | below half; round down | 1.012
1.01102 | interesting case; round to even | 1.102
1.01112 | above half; round up | 1.102
1.10002 | truncate | 1.102
1.10012 | below half; round down | 1.102
1.10102 | Interesting case; round to even | 1.102
1.10112 | above half; round up | 1.112
1.11002 | truncate | 1.112

## Slide 19: Rounding
Round up conditions
  Round = 1, Sticky = 1 ➙ > 0.5
  Guard = 1, Round = 1, Sticky = 0 ➙ Round to even
  Value Fraction GRS Incr? Rounded
  128 1.0000000 000 N 1.000
  15 1.1010000 100 N 1.101
  17 1.0001000 010 N 1.000
  19 1.0011000 110 Y 1.010
  138 1.0001010 011 Y 1.001
  63 1.1111100 111 Y 10.000
1.BBGRXXX
Guard bit: LSB of result
Round bit: 1st bit removed
Sticky bit: OR of remaining bits
Notes: This slide is stolen from the end of floating point notes. May be helpful if you just want case-by-case rules.

## Slide 20: Floating Point – Example
Consider the following 5‐bit floating point representation based on the IEEE floating point format. This format does not have a sign bit – it can only represent nonnegative numbers.
  There are k=3 exponent bits.
  There are n=2 fraction bits.
What is the…
  Bias?
  Largest denormalized number?
  Smallest normalized number?
  Largest finite number it can represent?
  Smallest non-zero value it can represent?
4 | 3 | 2 | 1 | 0
exp |  |  | frac | 

## Slide 21: Floating Point – Example
Consider the following 5‐bit floating point representation based on the IEEE floating point format. This format does not have a sign bit – it can only represent nonnegative numbers.
  There are k=3 exponent bits.
  There are n=2 fraction bits.
What is the…
  Bias? 0112 = 3
  Largest denormalized number? 000 112 = 0.00112 = 3/16
  Smallest normalized number? 001 002 = 0.01002 = 1/4
  Largest finite number it can represent? 110 112 = 1110.02 = 14
  Smallest non-zero value it can represent? 000 012 = 0.00012 = 1/16
4 | 3 | 2 | 1 | 0
exp |  |  | frac | 

## Slide 22: Floating Point – Example
For the same problem, complete the following table:
Value | Floating Point Bits | Rounded Value
9/32 |  | 
8 |  | 
9 |  | 
 | 000 10 | 
19 |  | 

## Slide 23: Floating Point – Example
For the same problem, complete the following table:
Value | Floating Point Bits | Rounded Value
9/32 | 001 00 | 1/4
8 | 110 00 | 8
9 | 110 00 | 8
1/8 | 000 10 | 
19 | 111 00 | inf

## Slide 24: Floating Point Recap
Floating point = (-1)s M 2E
MSB is sign bit s
Bias = 2(k-1) – 1 (k is num of exp bits)
Normalized (larger numbers, denser towards 0)
  exp ≠ 000…0 and exp ≠ 111…1
  M = 1.frac
  E = exp - Bias
Denormalized (smaller numbers, evenly spread)
  exp = 000….0
  M = 0.frac
  E = - Bias + 1

## Slide 25: Floating Point Recap
Special Cases
  +/- Infinity: exp = 111…1 and frac = 000…0
  +/- NaN: exp = 111…1 and frac ≠ 000…0
  +0: s = 0, exp = 000…0 and frac = 000…0
  -0: s = 1, exp = 000…0 and frac = 000…0
Round towards even when half way (lsb of frac = 0)

## Slide 26: Questions?