## Slide 1: Bits, Bytes and Integers – Part 1 15-213/14-513/15-513: Introduction to Computer Systems 2nd Lecture, September 1, 2022
Instructors:
Dave Andersen (15-213)
Zack Weinberg (15-213)
Brian Railing (15-513)
David Varodayan (14-513)

## Slide 2: Waitlist questions
15-213: Mary Widom (marwidom@cs.cmu.edu)
15-513: Mary Widom (marwidom@cs.cmu.edu)
14-513: INI Enrollment (ini-academic@andrew.cmu.edu)
Please don’t contact the instructors with waitlist questions.

## Slide 3: Reminder: Lab Deadlines
C Programming Lab: Came out Tuesday, due Sep. 6
Data Lab: Comes out today, due Sep. 15
Start early, start often

## Slide 4: Roadmap – Inside a Computer
You may have seen this block diagram, or one like it, before.
For the first half of the course we’ll be concentrating on the CPU and RAM
Second half discusses disk and network I/O
Graphics? Take 462
CPU
RAM
GPU
Display
GPU
RAM
Network Adapter
Hard
Disk
Controller
The Internet
Disks
…
Bus

## Slide 5: Course Teaser (Things You May Know Already)
What value do you get if you arithmetic right-shift the hexadecimal number 0x466db400 by eight bits?
Hexadecimal is just like decimal … if you have sixteen fingers.
“Eight bits” is two hex digits.
“Arithmetic right shift” is division by a power of two.
4 | 6 | 6 | d | b | 4 | 0 | 0
0 | 0 | 4 | 6 | 6 | d | b | 4

## Slide 6: Course Teaser (Things You May Know Already)
On an x86-64 machine, how much space does this C struct take? That is, what is the value of sizeof(struct S)?
struct S {
char c[2];
char *p;
int z;
}
2 bytes
8 bytes
4 bytes
6 bytes wasted space
4 bytes wasted space
24 bytes total

## Slide 7: Course Teaser (Things You May Know Already)
What’s wrong with this program?
/* a.c */
#include <stdio.h>
extern long x;
int main(void)
{
printf("%ld\n", x);
return 0;
}
/* b.c */
double x = 3.14159;

## Slide 8: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 9: Everything is bits
Each bit is 0 or 1
By encoding/interpreting sets of bits in various ways
  Computers determine what to do (instructions)
  … and represent and manipulate numbers, sets, strings, etc…
Why bits? Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.2V
0.9V
1.1V
0
1
0

## Slide 10: For example, can count in binary
Base 2 Number Representation
  Represent 1521310 as 111011011011012
  Represent 1.2010 as 1.0011001100110011[0011]…2
  Represent 1.5213 × 104 as 1.11011011011012 × 213

## Slide 11: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary
15213: 0011 1011 0110 1101
3
B
6
D

## Slide 12: Preview: Combining bytes…
C Data Type | Typical 32-bit | Typical 64-bit
char | 1 | 1
short | 2 | 2
int | 4 | 4
long | 4 | 8
float | 4 | 4
double | 8 | 8
pointer | 4 | 8

## Slide 13: Preview: … to make integers
UMax = where w is the number of bits (“word size”)
UMin = 0
TMax =
TMin =
  Asymmetric!
  Because of zero

## Slide 14: Activity: binary, hexadecimal, twos complement
https://canvas.cmu.edu/courses/30386/assignments/524495
https://www.cs.cmu.edu/~213/activities/bits-and-bytes.pdf
Form groups of three or four people
  Three is probably easier in this room, since the chairs don’t move
Person in the middle of each group, bring up the PDF in a program that lets you scribble on it
  If you can’t do that, swap chairs with someone in your group who can
Work through the activity as a group
  Today, we just go start to finish at your own pace
  Faculty and TAs will be walking around to help
When you’re done, upload your annotated PDF to Canvas