## Slide 1: Recitation 1: ILP, SIMD, and Thread Parallelism
15-418 Parallel Computer Architecture and Programming
CMU 15-418/15-618, Spring 2020

## Slide 2: Goals for today
Topic is parallelism models: ILP, SIMD, threading
Solve some exam-style problems
Walk through example code
Most of all,
ANSWER YOUR QUESTIONS!

## Slide 3: Recall: Taylor expansion of
How fast is this code?
Where should we focus optimization efforts?
What is the bottleneck?
void sinx(int N, int terms, float * x,
float *result) {
for (int i=0; i<N; i++) {
float value = x[i];
float numer = x[i]*x[i]*x[i];
int denom = 6; // 3!
int sign = -1;
for (int j=1; j<=terms; j++) {
value += sign * numer / denom;
numer *= x[i] * x[i];
denom *= (2*j+2) * (2*j+3);
sign *= -1;
}
result[i] = value;
}
}

## Slide 4: Recall: Taylor expansion of
How fast is this code?
On ghc machines: 7.2 ns / element 23 cycles / element
Not very good 
void sinx(int N, int terms, float * x,
float *result) {
for (int i=0; i<N; i++) {
float value = x[i];
float numer = x[i]*x[i]*x[i];
int denom = 6; // 3!
int sign = -1;
for (int j=1; j<=terms; j++) {
value += sign * numer / denom;
numer *= x[i] * x[i];
denom *= (2*j+2) * (2*j+3);
sign *= -1;
}
result[i] = value;
}
}

## Slide 5: Recall: Taylor expansion of
Where should we focus optimization efforts?
A: Where most of the time is spent
void sinx(int N, int terms, float * x,
float *result) {
for (int i=0; i<N; i++) {
float value = x[i];
float numer = x[i]*x[i]*x[i];
int denom = 6; // 3!
int sign = -1;
for (int j=1; j<=terms; j++) {
value += sign * numer / denom;
numer *= x[i] * x[i];
denom *= (2*j+2) * (2*j+3);
sign *= -1;
}
result[i] = value;
}
}

## Slide 6: Recall: Taylor expansion of
What is the bottleneck?
void sinx(int N, int terms, float * x,
float *result) {
for (int i=0; i<N; i++) {
float value = x[i];
float numer = x[i]*x[i]*x[i];
int denom = 6; // 3!
int sign = -1;
for (int j=1; j<=terms; j++) {
value += sign * numer / denom;
numer *= x[i] * x[i];
denom *= (2*j+2) * (2*j+3);
sign *= -1;
}
result[i] = value;
}
}

## Slide 7: Takeaways from today
Focus your effort on the performance bottleneck
Usually, you do not need to model processor in detail to find the performance bottleneck

## Slide 8: Dataflow for a single iteration
OK, but how does this perform on a real machine?
sign
numer
denom
x[i]
numer’
LD
value
value’
-1
sign’
j
2
3
denom’
1
j’

## Slide 9: Superscalar OOO Processor
What in microarchitecture should we worry about?
CPU
Fetch
Decode
Execute
Commit
Execute
Execute
Instruction Buffer
In-order
In-order
Out-of-order
Fetch
Decode
Commit

## Slide 10: GHC Machine Microarchitecture
What in microarchitecture should we worry about?
  Fetch & Decode?
  Execution?
  Commit?
NO. Any reasonable machine will have sufficient frontend throughput to keep execution busy + all branches in this code are easy to predict (not always the case!).
YES. This is where dataflow + most structural hazards will limit our performance.
NO. Again, any reasonable machine will have sufficient commit throughput to keep execution busy.

## Slide 11: Intel Skylake (GHC machines) Execution Microarchitecture
 | Integer |  |  | Floating Point |  | 
 | Latency | Pipelined? | Number | Latency | Pipelined? | Number
Add | 1 |  | 4 | 4* |  | 2
Multiply | 3 |  | 1 | 4 |  | 2
Divide | 21-83 |  | 1 | 13-14 | ** | 1
Load | 2 |  | 2 |  |  | 
* 3 cycles if using x87 instructions
** Can issue another operation after 4 cycles
Source: Search for “Skylake” in
https://www.agner.org/optimize/microarchitecture.pdf
https://www.agner.org/optimize/instruction_tables.pdf

## Slide 12: What is our throughput bound?
sign
numer
denom
x[i]
numer’
LD
value
value’
-1
sign’
j
2
3
denom’
1
j’
Op | # Code | Arch | Thput bound
Int Add | 3 | 4 | 0.75
Int Mul | 4 | 1 | 4
Int Div | 0 | 1 | -
FP Add | 1 | 1 | 1
FP Mul | 3 | 2 | 1.5
FP Div | 1 | 1 | 3-15
Load | 1 | 2 | 0.5
Op | # Code |  | Thput bound
Int Add | 3 | 4 | 0.75
Int Mul | 4 | 1 | 4
Int Div | 0 | 1 | -
FP Add | 1 | 1 | 1
FP Mul | 3 | 2 | 1.5
FP Div | 1 | 1 | 3-15
Load | 1 | 2 | 0.5
THPUT BOUND!
Throughput bound: Ignore data hazards, think only about max issue rate due to structural hazards

## Slide 13: What is our latency bound?
Latency bound: Ignore structural hazards, think only about the critical path through data hazards
sign
numer
denom
x[i]
numer’
LD
value
value’
-1
sign’
j
2
3
denom’
1
j’
3+1+3+3=10
3
1+3+3=7
1
3+(3/15)+3=9 to 21
LATENCY BOUND!

## Slide 14: Takeaways
Observe performance of 23 cycles / element
Latency bound dominates throughput bound  We are latency bound!
Notes
  This analysis can often be “eyeballed” w/out full dataflow
  Actual execution is more complicated, but latency/thput bounds are good approximation
  (Also, avoid division!!!)

## Slide 15: Speeding up : Attempt #1
What if we eliminate unnecessary work?
void sinx_better(int N, int terms, float * x,
float *result) {
for (int i=0; i<N; i++) {
float value = x[i];
float x2 = x[i]*x[i];
float numer = x2*x[i];
int denom = 6; // 3!
int sign = -1;
for (int j=1; j<=terms; j++) {
value += sign * numer / denom;
numer *= x2;
denom *= (2*j+2) * (2*j+3);
sign = -sign;
}
result[i] = value;
}
}
A: Small improvement. 6ns / element 18 cycles / element
Why not better?

## Slide 16: What is our latency bound?
Find the critical path in the dataflow graph
sign
numer
denom
x2
numer’
value
value’
NEG
sign’
j
2
3
denom’
1
j’
3+1+3+3=10
1
3
1
3+(3/15)+3=9 to 21
LATENCY BOUND!

## Slide 17: Attempt #1 Takeaways
First attempt didn’t change latency bound
To get real speedup, we need to focus on the performance bottleneck
Q: Why did we get any speedup at all?
A: Actual dynamic scheduling is complicated; would need to simulate execution in more detail

## Slide 18: Speeding up : Attempt #2
Let’s focus on that pesky division…
void sinx_predenom(int N, int terms, float * x, float *result) {
float rdenom[MAXTERMS];
int denom = 6;
for (int j = 1; j <= terms; j++) {
rdenom[j] = 1.0/denom;
denom *= (2*j+2) * (2*j+3);
}
for (int i=0; i<N; i++) {
float value = x[i];
float x2 = value * value;
float numer = x2 * value;
int sign = -1;
for (int j=1; j<=terms; j++) {
value += sign * numer * rdenom[j];
numer *= x2;
sign = -sign;
}
result[i] = value;
}
}
A: Big improvement! 2.4ns / element 7.7 cycles / element

## Slide 19: What is our latency bound?
Find the critical path in the dataflow graph
sign
numer
rdenom[j]
x2
numer’
value
+ &
LD
value’
NEG
sign’
j
1
j’
1
3
1
3+3=6
LATENCY BOUND!

## Slide 20: Attempt #2 Takeaways
Here we go! Attacking the bottleneck got nearly 3!
…But performance is still near the latency bound, can we do better?

## Slide 21: Speeding up : Attempt #3
Don’t need sign in inner-loop either
void sinx_predenoms(int N, int terms, float * x, float *result) {
float rdenom[MAXTERMS];
int denom = 6;
float sign = -1.0;
for (int j = 1; j <= terms; j++) {
rdenom[j] = sign/denom;
denom *= (2*j+2) * (2*j+3);
sign = -sign;
}
for (int i=0; i<N; i++) {
float value = x[i];
float x2 = value * value;
float numer = x2 * value;
for (int j=1; j<=terms; j++) {
value += numer * rdenom[j];
numer *= x2;
}
result[i] = value;
}
}
1.1ns / element 3.5 cycles / element

## Slide 22: What is our latency bound?
Find the critical path in the dataflow graph
numer
rdenom[j]
x2
numer’
value
+ &
LD
value’
j
1
j’
3
1
3 (LD will be executed speculatively, only depends on j)
LATENCY BOUND!

## Slide 23: Attempt #3 Takeaways
We’re down to the latency of a single, fast operation per iteration
+ Observed performance is very close to this latency bound, so throughput isn’t limiting
 We’re done optimizing individual iterations
How to optimize multiple iterations?
  Eliminate dependence chains across iterations
  A) Loop unrolling (ILP)
  B) Explicit parallelism (SIMD, threading)

## Slide 24: Speeding up : Loop unrolling
Compute multiple elements per iteration
void sinx_unrollx2(int N, int terms, float * x, float *result) {
// same predom stuff as before…
for (int i=0; i<N; i++) {
float value = x[i];
float x2 = value * value;
float x4 = x2 * x2;
float numer = x2 * value;
for (int j=1; j<=terms; j+=2) {
value += numer * rdenom[j];
value += numer * x2 * redom[j+1];
numer *= x4;
}
result[i] = value;
}
}
Correct? Not yet…

## Slide 25: Speeding up : Loop unrolling
Compute multiple elements per iteration
void sinx_unrollx2(int N, int terms, float * x, float *result) {
// same predom stuff as before…
for (int i=0; i<N; i++) {
float value = x[i];
float x2 = value * value;
float x4 = x2 * x2;
float numer = x2 * value;
int j;
for (j=1; j<=terms-1; j+=2) {
value += numer * rdenom[j];
value += numer * x2 * redom[j+1];
numer *= x4;
}
for (; j<=terms; j++) {
value += numer * rdenom[j];
numer *= x2;
}
result[i] = value;
}
}
0.99 ns / element 3.2 cycles / element
Didn’t change 

## Slide 26: What is our latency bound?
Find the critical path in the dataflow graph
numer
rdenom[j]
x4
numer’
value
+ &
LD
LD
j
2
j’
3/2=1.5
1/2=0.5
6/2=3 (LD will be executed speculatively, only depends on j)
rdenom[j+1]
x2
+ &
value’
LATENCY BOUND!

## Slide 27: Speeding up : Loop unrolling #2
What if floating point associated + distributed?
void sinx_unrollx2(int N, int terms, float * x, float *result) {
// same predom stuff as before…
for (int i=0; i<N; i++) {
float value = x[i];
float x2 = value * value;
float x4 = x2 * x2;
float numer = x2 * value;
int j;
for (j=1; j<=terms-1; j++) {
value += numer * (rdenom[j] + x2 * redom[j+1]);
numer *= x4;
}
for (; j<=terms; j++) {
value += numer * rdenom[j];
numer *= x2;
}
result[i] = value;
}
}
0.69 ns / element 2.2 cycles / element

## Slide 28: What is our latency bound?
Find the critical path in the dataflow graph
numer
rdenom[j]
x4
numer’
value
+ &
LD
LD
j
2
j’
3/2=1.5
1/2=0.5
3/2=1.5 (LD will be executed speculatively, only depends on j)
rdenom[j+1]
x2
+ &
value’
LATENCY BOUND!

## Slide 29: Loop unrolling takeaways
Need to break dependencies across iterations to get speedup
  Unrolling by itself doesn’t help
We are now seeing throughput effects
  Latency bound = 1.5 vs. observed = 2.2
Can unroll loop 3x, 4x to improve further, but…
…Diminishing returns (1.65 cycles / element at 4x)

## Slide 30: Speeding up : Going parallel (explicitly)
Use ISPC to vectorize the code
export void sinx_reference(uniform int N, uniform int terms,
uniform float x[],
uniform float result[]) {
foreach (i=0 ... N) {
float value = x[i];
float numer = x[i]*x[i]*x[i];
uniform int denom = 6; // 3!
uniform int sign = -1;
for (uniform int j=1; j<=terms; j++) {
value += sign * numer / denom;
numer *= x[i] * x[i];
denom *= (2*j+2) * (2*j+3);
sign *= -1;
}
result[i] = value;
}
}
1.0 ns / element 3.2 cycles / element

## Slide 31: Speeding up : Going parallel (explicitly) + optimize
export void sinx_unrollx2a(uniform int N, uniform int terms,
uniform float x[],
uniform float result[]) {
uniform float rdenom[MAXTERMS];
uniform int denom = 6;
uniform float sign = -1;
for (uniform int j = 1; j <= terms; j++) {
rdenom[j] = sign/denom;
denom *= (2*j+2) * (2*j+3);
sign = -sign;
}
foreach (i=0 ... N) {
float value = x[i];
float x2 = value * value;
float x4 = x2 * x2;
float numer = x2 * value;
uniform int j;
for (j=1; j<=terms-1; j+=2) {
value +=
numer * (rdenom[j] +
x2 * rdenom[j+1]);
numer *= x4;
}
for (; j <= terms; j++) {
value += numer * rdenom[j];
numer *= x2;
}
result[i] = value;
}
}
0.14 ns / element 0.45 cycles / element

## Slide 32: SIMD takeaways
Well, that was easy! (Thanks ISPC)
Cycles per element:
Speedup
 | Scalar | Vector
Unoptimized | 23 | 3.2
Unrolled | 2.2 | 0.45
Original
Unrolled
Vector
Vector + Unrolled
4.9
7
7.2
10
51
Maximum speedup requires hand tuning + explicit parallelism!

## Slide 33: What if? #1 Impact of structural hazards
Q: What would happen to if we only had a single, unpipelined floating-point multiplier?
A1: Performance will be much worse
A2: We will hit throughput bound much earlier
A3: Loop unrolling will help by reducing multiplies

## Slide 34: What if? #2 Impact of structural hazards
Q: What would happen to if LDs (cache hits) took 2 cycles instead of 1 cycle?
A: Nothing. This program is latency bound, and LDs are not on the critical path.

## Slide 35: Loads do not limit
Consider just the slice of the program that generates the subexpression:
What is this program’s latency + throughput bound?
Latency bound: 1 cycle / iteration!
  Through computation, not the subexpression computation – there is no cross-iteration dependence in the subexpression!)
Throughput bound: also 1 cycle / iteration
  1 add / 4 adders; 2 LDs / 2 LD units; 1 FP FMA / 1 FP unit
  (This will change to 2 cycles if we add the value FMA)
j
2
j’
rdenom[j]
+ &
LD
LD
rdenom[j+1]
x2
subexp

## Slide 36: Loads do not limit : Visualization
Consider just the slice of the program that generates the subexpression:
Subexpressions are off the critical path + we have enough throughput to produce next subexpression each cycle (excluding value FMA)
0
2
j
2
j’
2
j’’
2
j’’’
2
j’’’’
LD
LD
+ &
subexp
LD
LD
+ &
subexp’
LD
LD
+ &
subexp’’
LD
LD
+ &
subexp’’’
LD
LD
+ &
subexp’’’’

## Slide 37: Loads do not limit : Example execution
INT ADD | j=0 | j=2 | j=4 | j=6 | j=8 | ... |  |  |  |  |  |  |  |  |  |  |  | 
LD1 |  | rdenom[0] |  | rdenom[4] |  | rdenom[8] |  | ... |  |  |  |  |  |  |  |  |  | 
 |  |  | rdenom[2] |  | rdenom[6] |  | ... |  |  |  |  |  |  |  |  |  |  | 
LD2 |  | rdenom[1] |  | rdenom[5] |  | rdenom[9] |  | ... |  |  |  |  |  |  |  |  |  | 
 |  |  | rdenom[3] |  | rdenom[7] |  | ... |  |  |  |  |  |  |  |  |  |  | 
FP FMA |  |  |  | subexp’ |  |  | value’ |  |  | value’’ |  |  | value’’’ |  |  | value’’’’ |  | 
 |  |  |  |  |  | subexp’’’ |  |  | subexp’’’’’ |  |  |  |  |  |  |  |  | 
 |  |  |  |  | subexp’’ |  |  | subexp’’’’ |  |  |  |  |  |  |  |  |  | 
FP MUL |  |  | numer’=x^4 |  |  | numer’’=x^8 |  |  | numer’’’=x^12 |  |  | numer’’’’=x^16 |  |  | numer’’’’’=x^20 |  |  | ...
Note: Throughput limit is 2 cycles / iteration once we add value FMA, but this is dominated by the latency bound of 3 cycles / iteration (also from value FMA). Regardless, 2-cycle LDs are not the bottleneck.

## Slide 38: What if? #3 Vector vs. multicore
Q: What would happen to if the vector width was doubled?
A1: If we’re using ISPC, we would expect roughly 2 performance (slightly less would be realized in practice).
Q: Can we do this forever & expect same results?
A: No. Computing rdenom will limit gains (Amdahl’s Law).
Q: For this program, would you prefer larger vector or more cores?
A: Either should give speedup, but this program maps easily to SIMD, and adding vector lanes is much cheaper (area + energy) than adding cores. (Remember GPU vs CPU pictures.)

## Slide 39: What if? #4 Benefits(?) of SMT
Q: How should we schedule threads on a dual-core processor with SMT, running these two apps, each of which have 2 threads?
  The function
  A program that is copying large amounts of data with very little computation
(Note: There are four “cores” and four threads)
A: We want to schedule one thread and one memcpy() thread on each core, since SMT is most beneficial when threads use different execution units

## Slide 40: What if? #5 Limits of speculation
Q: What will limit the “performance” of this (silly) program on a superscalar OOO processor? int foo() { int i = 0; while (i < 100000) { // assume single-cycle rand instruction if (rand() % 2 == 0) { i++; } else { i--; } } }
A: Unpredictable branch in if-else will cause frequent pipeline flushes

## Slide 41: What if? #6 Benefits(?) of SMT
Q: Would the previous program benefit from running on multiple SMT threads on a single core?
A: Yes! Its performance is limited by the CPU frontend, which is replicated in SMT