## Slide 1: Lecture 2: Instruction-Level Parallelism
15-418 Parallel Computer Architecture and Programming
CMU 15-418/15-618, Spring 2020

## Slide 2: Many kinds of processors
Why so many? What differentiates these processors?
CPU
GPU
FPGA
Etc.

## Slide 3: Why so many kinds of processors?
Each processor is designed for different kinds of programs
CPUs
  “Sequential” code – i.e., single / few threads
GPUs
  Programs with lots of independent work  “Embarrassingly parallel”
Many others: Deep neural networks, Digital signal processing, Etc.
TODAY

## Slide 4: Parallelism pervades architecture
Speeding up programs is all about parallelism
  1) Find independent work
  2) Execute it in parallel
  3) Profit
Key questions:
  Where is the parallelism?
  Whose job is it to find parallelism?

## Slide 5: Where is the parallelism?
Different processors take radically different approaches
CPUs: Instruction-level parallelism
  Implicit
  Fine-grain
GPUs: Thread- & data-level parallelism
  Explicit
  Coarse-grain

## Slide 6: Whose job to find parallelism?
Different processors take radically different approaches
CPUs: Hardware dynamically schedules instructions
  Expensive, complex hardware  Few cores (tens)
  (Relatively) Easy to write fast software
GPUs: Software makes parallelism explicit
  Simple, cheap hardware  Many cores (thousands)
  (Often) Hard to write fast software

## Slide 7: Visualizing these differences
Pentium 4 “Northwood” (2002)

## Slide 8: Visualizing these differences
Pentium 4 “Northwood” (2002)
Highlighted areas actually execute instructions  Most area spent on scheduling (not on executing the program)

## Slide 9: Visualizing these differences
AMD Fiji (2015)

## Slide 10: Visualizing these differences
AMD Fiji (2015)
Highlighted areas actually execute instructions  Most area spent executing the program
  (Rest is mostly I/O & memory, not scheduling)

## Slide 11: Today you will learn…
How CPUs exploit ILP to speed up sequential code
Key ideas:
  Pipelining & Superscalar: Work on multiple instructions at once
  Out-of-order execution: Dynamically schedule instructions whenever they are “ready”
  Speculation: Guess what the program will do next to discover more independent work, “rolling back” incorrect guesses
CPUs must do all of this while preserving the illusion that instructions execute in-order, one-at-a-time

## Slide 12: In other words… Today is about:

## Slide 13: Buckle up! …But please ask questions!

## Slide 14: Example: Polynomial evaluation
int poly(int *coef,
int terms, int x) {
int power = 1;
int value = 0;
for (int j = 0; j < terms; j++) {
value += coef[j] * power;
power *= x;
}
return value;
}

## Slide 15: Example: Polynomial evaluation
Compiling on ARM
int poly(int *coef,
int terms, int x) {
int power = 1;
int value = 0;
for (int j = 0; j < terms; j++) {
value += coef[j] * power;
power *= x;
}
return value;
}
poly:
cmp r1, #0
ble .L4
push {r4, r5}
mov r3, r0
add r1, r0, r1, lsl #2
movs r4, #1
movs r0, #0
.L3:
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
pop {r4, r5}
bx lr
.L4:
movs r0, #0
bx lr
r0: value
r1: &coef[terms]
r2: x
r3: &coef[0]
r4: power
r5: coef[j]

## Slide 16: Example: Polynomial evaluation
Compiling on ARM
int poly(int *coef,
int terms, int x) {
int power = 1;
int value = 0;
for (int j = 0; j < terms; j++) {
value += coef[j] * power;
power *= x;
}
return value;
}
poly:
cmp r1, #0
ble .L4
push {r4, r5}
mov r3, r0
add r1, r0, r1, lsl #2
movs r4, #1
movs r0, #0
.L3:
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
pop {r4, r5}
bx lr
.L4:
movs r0, #0
bx lr
r0: value
r1: &coef[terms]
r2: x
r3: &coef[j]
r4: power
r5: coef[j]
Preamble
Iteration
Fini

## Slide 17: Example: Polynomial evaluation
Compiling on ARM
for (int j = 0; j < terms; j++) {
value += coef[j] * power;
power *= x;
}
.L3:
ldr r5, [r3], #4 // r5 <- coef[j]; j++ (two operations)
cmp r1, r3 // compare: j < terms?
mla r0, r4, r5, r0 // value += r5 * power (mul + add)
mul r4, r2, r4 // power *= x
bne .L3 // repeat?
r0: value
r1: &coef[terms]
r2: x
r3: &coef[j]
r4: power
r5: coef[j]

## Slide 18: Example: Polynomial evaluation
Executing poly(A, 3, x)
cmp r1, #0
ble .L4
push {r4, r5}
mov r3, r0
add r1, r0, r1, lsl #2
movs r4, #1
movs r0, #0
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...

## Slide 19: Example: Polynomial evaluation
Executing poly(A, 3, x)
cmp r1, #0
ble .L4
push {r4, r5}
mov r3, r0
add r1, r0, r1, lsl #2
movs r4, #1
movs r0, #0
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
J=0 iteration
Preamble

## Slide 20: Example: Polynomial evaluation
Executing poly(A, 3, x)
cmp r1, #0
ble .L4
push {r4, r5}
mov r3, r0
add r1, r0, r1, lsl #2
movs r4, #1
movs r0, #0
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
...
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
pop {r4, r5}
bx lr
J=0 iteration
Preamble
J=1 iteration
J=2 iteration
Fini

## Slide 21: Example: Polynomial evaluation
Executing poly(A, 3, x)
cmp r1, #0
ble .L4
push {r4, r5}
mov r3, r0
add r1, r0, r1, lsl #2
movs r4, #1
movs r0, #0
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
...
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
pop {r4, r5}
bx lr
J=0 iteration
J=1 iteration
J=2 iteration
Preamble
Fini

## Slide 22: The software-hardware boundary
The instruction set architecture (ISA) is a functional contract between hardware and software
  It says what each instruction does, but not how
  Example: Ordered sequence of x86 instructions
A processor’s microarchitecture is how the ISA is implemented
Arch : Arch :: Interface : Implementation

## Slide 23: Simple CPU model
Execute instructions in program order
Divide instruction execution into stages, e.g.:
  1. Fetch – get the next instruction from memory
  2. Decode – figure out what to do & read inputs
  3. Execute – perform the necessary operations
  4. Commit – write the results back to registers / memory
  (Real processors have many more stages)

## Slide 24: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit

## Slide 25: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
ldr
1. Read “ldr r5, [r3] #4” from memory

## Slide 26: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
ldr
2. Decode “ldr r5, [r3] #4” and read input regs

## Slide 27: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
ldr
3. Load memory at r3 and compute r3 + 4

## Slide 28: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
ldr
4. Write values into regs r5 and r3

## Slide 29: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
cmp

## Slide 30: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
cmp

## Slide 31: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
cmp

## Slide 32: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
cmp

## Slide 33: Evaluating polynomial on the simple CPU model
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
mla

## Slide 34: Evaluating polynomial on the simple CPU model
Fetch | ldr |  |  |  | cmp |  |  |  | mla | 
Decode |  | ldr |  |  |  | cmp |  |  |  | mla
Execute |  |  | ldr |  |  |  | cmp |  |  | 
Commit |  |  |  | ldr |  |  |  | cmp |  | 
…
Latency = 4 ns / instr
TIME
How fast is this processor?
Latency? Throughput?
1 ns
Throughput = 1 instr / 4 ns

## Slide 35: Simple CPU is very wasteful
Fetch | ldr |  |  |  | cmp |  |  |  | mla | 
Decode |  | ldr |  |  |  | cmp |  |  |  | mla
Execute |  |  | ldr |  |  |  | cmp |  |  | 
Commit |  |  |  | ldr |  |  |  | cmp |  | 
…
TIME
1 ns
Idle Hardware

## Slide 36: Pipelining

## Slide 37: Pipelining keeps CPU busy through instruction-level parallelism
Idea: Start on the next instr’n immediately
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
ldr

## Slide 38: Pipelining keeps CPU busy through instruction-level parallelism
Idea: Start on the next instr’n immediately
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
cmp
ldr

## Slide 39: Pipelining keeps CPU busy through instruction-level parallelism
Idea: Start on the next instr’n immediately
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
mla
cmp
ldr

## Slide 40: Pipelining keeps CPU busy through instruction-level parallelism
Idea: Start on the next instr’n immediately
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
mul
mla
cmp
ldr

## Slide 41: Pipelining keeps CPU busy through instruction-level parallelism
Idea: Start on the next instr’n immediately
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
bne
mul
mla
cmp

## Slide 42: Pipelining keeps CPU busy through instruction-level parallelism
Idea: Start on the next instr’n immediately
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
ldr
bne
mul
mla

## Slide 43: Evaluating polynomial on the pipelined CPU
Fetch | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul | bne
Decode |  | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul
Execute |  |  | ldr | cmp | mla | mul | bne | ldr | cmp | mla
Commit |  |  |  | ldr | cmp | mla | mul | bne | ldr | cmp
…
Latency = 4 ns / instr
TIME
How fast is this processor?
Latency? Throughput?
1 ns
Throughput = 1 instr / ns 4X speedup!

## Slide 44: Speedup achieved through pipeline parallelism
Fetch | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul | bne
Decode |  | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul
Execute |  |  | ldr | cmp | mla | mul | bne | ldr | cmp | mla
Commit |  |  |  | ldr | cmp | mla | mul | bne | ldr | cmp
…
TIME
Processor works on 4 instructions at a time

## Slide 45: Limitations of pipelining
Parallelism requires independent work
Q: Are instructions independent?
A: No! Many possible hazards limit parallelism…

## Slide 46: Data hazards
ldr ra, [rb], #4 // ra  Memory[rb]; rb  rb + 4 cmp rc, rd // rc  rd + re Q: When can the CPU pipeline the cmp behind ldr?
Fetch | ldr | cmp | … | … | … | …
Decode |  | ldr | cmp | … | … | …
Execute |  |  | ldr | cmp | … | …
Commit |  |  |  | ldr | cmp | …
A: When they use different registers
  Specifically, when cmp does not read any data written by ldr
  E.g., rb != rd

## Slide 47: Dealing with data hazards: Stalling the pipeline
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
ldr
Cannot pipeline cmp (ldr writes r3)

## Slide 48: Dealing with data hazards: Stalling the pipeline
Cannot pipeline cmp (ldr writes r3)
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
cmp
ldr
??

## Slide 49: Dealing with data hazards: Stalling the pipeline
Cannot pipeline cmp (ldr writes r3)
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
mla
cmp
ldr

## Slide 50: Dealing with data hazards: Stalling the pipeline
Cannot pipeline cmp (ldr writes r3)
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
mla
cmp
ldr
Inject a “bubble” (NOP) into the pipeline

## Slide 51: Dealing with data hazards: Stalling the pipeline
Cannot pipeline cmp (ldr writes r3)
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
CPU
Fetch
Decode
Execute
Commit
mla
cmp
mul
cmp proceeds once ldr has committed

## Slide 52: Stalling degrades performance
But stalling is sometimes unavoidable
  E.g., long-latency instructions (divide, cache miss)
Fetch | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul | bne
Decode |  | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul
Execute |  |  | ldr |  | cmp | mla | mul | bne | ldr | 
Commit |  |  |  | ldr |  | cmp | mla | mul | bne | ldr
…
TIME
Processor works on 3 instructions at a time

## Slide 53: Dealing with data hazards: Forwarding data
Wait a second… data is available after Execute!
Forwarding eliminates many (not all) pipeline stalls
CPU
Fetch
Decode
Execute
Commit
mla
cmp
ldr
mul
r3+4
r3
r1

## Slide 54: Speedup achieved through pipeline parallelism
Fetch | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul | bne
Decode |  | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul
Execute |  |  | ldr | cmp | mla | mul | bne | ldr | cmp | mla
Commit |  |  |  | ldr | cmp | mla | mul | bne | ldr | cmp
…
TIME
Processor works on 4 instructions at a time 

## Slide 55: Pipelining is not free!
Q: How well does forwarding scale?
A: Not well… many forwarding paths in deep & complex pipelines
CPU
Fetch
Decode
Execute
Commit
Mem
Execute

## Slide 56: Control hazards + Speculation
Programs must appear to execute in program order  All instructions depend on earlier ones
Most instructions implicitly continue at the next…
But branches redirect execution to new location

## Slide 57: Dealing with control hazards: Flushing the pipeline
What if we always fetch the next instruction?
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
pop {r4, r5}
bx lr
CPU
Fetch
Decode
Execute
Commit
bne
mul
mla
cmp
Static instruction sequence (i.e., program layout in memory)

## Slide 58: Dealing with control hazards: Flushing the pipeline
What if we always fetch the next instruction?
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
pop {r4, r5}
bx lr
CPU
Fetch
Decode
Execute
Commit
pop
bne
mul
mla
Static instruction sequence (i.e., program layout in memory)

## Slide 59: Dealing with control hazards: Flushing the pipeline
What if we always fetch the next instruction?
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
pop {r4, r5}
bx lr
CPU
Fetch
Decode
Execute
Commit
bx
pop
bne
mul
Static instruction sequence (i.e., program layout in memory)
Whoops! We fetched the wrong instructions! (Loop not finished)

## Slide 60: Dealing with control hazards: Flushing the pipeline
What if we always fetch the next instruction?
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
pop {r4, r5}
bx lr
CPU
Fetch
Decode
Execute
Commit
ldr
bne
Static instruction sequence (i.e., program layout in memory)
Whoops! We fetched the wrong instructions! (Loop not finished)
(Next loop iteration)

## Slide 61: Pipeline flushes destroy performance
Penalty increases with deeper pipelines
Fetch | ldr | cmp | mla | mul | bne |  |  | ldr | cmp | mla
Decode |  | ldr | cmp | mla | mul | bne |  |  | ldr | cmp
Execute |  |  | ldr | cmp | mla | mul | bne |  |  | ldr
Commit |  |  |  | ldr | cmp | mla | mul | bne |  | 
…
TIME
Processor works on 2 or 3 instructions at a time

## Slide 62: Dealing with control hazards: Speculation!
Processors do not wait for branches to execute
Instead, they speculate (i.e., guess) where to go next + start fetching
Modern processors use very sophisticated mechanisms
  E.g., speculate in Fetch stage—before processor even knows instrn is a branch!
  >95% prediction accuracy
  Still, branch mis-speculation is major problem

## Slide 63: Pipelining Summary
Pipelining is a simple, effective way to improve throughput
  -stage pipeline gives up to speedup
Pipelining has limits
  Hard to keep pipeline busy because of hazards
  Forwarding is expensive in deep pipelines
  Pipeline flushes are expensive in deep pipelines
 Pipelining is ubiquitous, but tops out at

## Slide 64: Software Takeaways
Processors with a simple “in-order” pipeline are very sensitive to running “good code”
  Compiler should target a specific model of CPU
  Low-level assembly hacking
…But very few CPUs are in-order these days
  E.g., embedded, ultra-low-power applications
Instead, all modern CPUs are “out-of-order”
  Even in classic “low-power domains” (like mobile)

## Slide 65: Out-of-Order Execution

## Slide 66: Increasing parallelism via dataflow
Parallelism limited by many false dependencies, particularly sequential program order
Dataflow tracks how instructions actually depend on each other
  True dependence: read-after-write
Dataflow increases parallelism by eliminating unnecessary dependences

## Slide 67: Example: Dataflow in polynomial evaluation
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
ldr
cmp
mla
mul
bne
Loop iteration

## Slide 68: Example: Dataflow in polynomial evaluation
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
...
ldr
cmp
mla
mul
bne
Loop iteration
ldr
cmp
mla
mul
bne
ldr
mul
cmp
bne

## Slide 69: Example: Dataflow polynomial execution
Execution only, with perfect scheduling & unlimited execution units
  ldr, mul execute in 2 cycles
  cmp, bne execute in 1 cycle
  mla executes in 3 cycles
Q: Does dataflow speedup execution? By how much?
Q: What is the performance bottleneck?

## Slide 70
ldr |  |  |  |  |  |  |  | 
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 71
ldr |  |  |  |  |  |  |  | 
 |  | cmp |  |  |  |  |  | 
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 72
ldr |  |  |  |  |  |  |  | 
 |  | cmp |  |  |  | mla |  | 
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 73
ldr |  |  |  |  |  |  |  | mul
 |  | cmp |  |  |  | mla |  | 
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 74
ldr |  |  |  |  |  |  |  | mul
 |  | cmp |  |  |  | mla |  | 
 |  |  |  | bne |  |  |  | 
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 75
ldr |  |  |  |  |  |  |  | mul
ldr |  | cmp |  |  |  | mla |  | mul
 |  |  |  | bne |  |  |  | 
 |  | cmp |  |  |  |  |  | 
 |  |  |  | bne |  | mla |  | 
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 76
ldr |  |  |  |  |  |  |  | mul
ldr |  | cmp |  |  |  | mla |  | mul
 |  |  |  | bne |  |  |  | 
ldr |  | cmp |  |  |  |  |  | mul
 |  |  |  | bne |  | mla |  | 
 |  | cmp |  |  |  |  |  | 
 |  |  |  | bne |  |  |  | 
 |  |  |  |  |  | mla |  | 
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
TIME

## Slide 77
ldr |  |  |  |  |  |  |  | mul
ldr |  | cmp |  |  |  | mla |  | mul
 |  |  |  | bne |  |  |  | 
ldr |  | cmp |  |  |  |  |  | mul
 |  |  |  | bne |  | mla |  | 
ldr |  | cmp |  |  |  |  |  | mul
 |  |  |  | bne |  |  |  | 
ldr |  | cmp |  |  |  | mla |  | mul
 |  |  |  | bne |  |  |  | 
ldr |  | cmp |  |  |  |  |  | mul
 |  |  |  | bne |  | mla |  | 
ldr |  | cmp |  |  |  |  |  | mul
 |  |  |  | bne |  |  |  | 
ldr |  | cmp |  |  |  | mla |  | mul
 |  |  |  | bne |  |  |  | 
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
TIME

## Slide 78: Example: Dataflow polynomial execution
Q: Does dataflow speedup execution? By how much?
  Yes! 3 cycles / loop iteration
  Instructions per cycle (IPC) = 5/3 1.67 (vs. 1 for perfect pipelining)
Q: What is the performance bottleneck?
  mla: Each mla depends on previous mla & takes 3 cycles
   This program is latency-bound

## Slide 79: Latency Bound
What is the “critical path” of the computation?
  Longest path across iterations in dataflow graph
  E.g., mla in last slide (but could be multiple ops)
Critical path limits maximum performance
Real CPUs may not achieve latency bound, but useful mental model + tool for program analysis

## Slide 80: Out-of-order (OoO) execution uses dataflow to increase parallelism
Idea: Execute programs in dataflow order, but give the illusion of sequential execution
This is a “restricted dataflow” model
  Restricted to instructions near those currently committing
  (Pure dataflow processors also exist that expose dataflow to software)

## Slide 81: High-level OoO microarchitecture
CPU
Fetch
Decode
Commit
Execute
Instruction Buffer
In-order
In-order
Out-of-order

## Slide 82: OoO is hidden behind in-order frontend & commit
CPU
Instructions only enter & leave instruction buffer in program order; all bets are off in between!
Fetch
Decode
Commit
Execute
Instruction Buffer
A
B
C

## Slide 83: Example: OoO polynomial evaluation
Q: Does OoO speedup execution? By how much?
Q: What is the performance bottleneck?
Assume perfect forwarding & branch prediction

## Slide 84: Example: OoO polynomial evaluation pipeline diagram
Fetch & Decode | ldr |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commit |  |  |  | ldr |  |  |  |  |  |  |  |  |  |  |  | 
TIME

## Slide 85: Example: OoO polynomial evaluation pipeline diagram
Fetch & Decode | ldr | cmp |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  | cmp |  |  |  |  |  |  |  |  |  |  |  | 
Commit |  |  |  | ldr | cmp |  |  |  |  |  |  |  |  |  |  | 
TIME

## Slide 86: Example: OoO polynomial evaluation pipeline diagram
Fetch & Decode | ldr | cmp | mla |  |  |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  | cmp | mla |  |  |  |  |  |  |  |  |  |  | 
Commit |  |  |  | ldr | cmp |  |  | mla |  |  |  |  |  |  |  | 
TIME

## Slide 87: Example: OoO polynomial evaluation pipeline diagram
Fetch & Decode | ldr | cmp | mla | mul |  |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  | cmp | mla |  |  | mul |  |  |  |  |  |  |  | 
Commit |  |  |  | ldr | cmp |  |  | mla |  | mul |  |  |  |  |  | 
TIME

## Slide 88: Example: OoO polynomial evaluation pipeline diagram
Fetch & Decode | ldr | cmp | mla | mul | bne |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  | cmp | mla |  |  | mul |  | bne |  |  |  |  |  | 
Commit |  |  |  | ldr | cmp |  |  | mla |  | mul | bne |  |  |  |  | 
TIME

## Slide 89: Example: OoO polynomial evaluation pipeline diagram
Fetch & Decode | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul | bne | ldr
Execute |  | ldr |  | cmp | mla |  |  | mul |  | bne | ldr |  | cmp | mla |  | 
Commit |  |  |  | ldr | cmp |  |  | mla |  | mul | bne |  | ldr | cmp |  | 
TIME

## Slide 90: Example: OoO polynomial evaluation pipeline diagram
Wait a minute… this isn’t OoO… or even faster than a simple pipeline!
Q: What went wrong?
A: We’re throughput-limited: can only exec 1 instrn
Fetch & Decode | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul | bne | ldr | cmp | mla | mul | bne | ldr
Execute |  | ldr |  | cmp | mla |  |  | mul |  | bne | ldr |  | cmp | mla |  | 
Commit |  |  |  | ldr | cmp |  |  | mla |  | mul | bne |  | ldr | cmp |  | 
TIME

## Slide 91: High-level Superscalar OoO microarchitecture
Must increase pipeline width to increase ILP > 1
CPU
Fetch
Decode
Execute
Commit
Execute
Execute
Instruction Buffer
In-order
In-order
Out-of-order
Fetch
Decode
Commit

## Slide 92: Focus on Execution, not Fetch & Commit
Goal of OoO design is to only be limited by dataflow execution
Fetch and commit are over-provisioned so that they (usually) do not limit performance  Programmers can (usually) ignore fetch/commit
Big Caveat: Programs with inherently unpredictable control flow will often be limited by fetch stalls (branch misprediction)
  E.g., branching based on random data

## Slide 93: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | cmp |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Execute |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 94: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr | mla | bne | cmp | mul |  |  |  |  |  |  |  |  |  |  | 
 | cmp | mul | ldr | mla | bne |  |  |  |  |  |  |  |  |  |  | 
Execute |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 95: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr | mla | bne | cmp | mul |  |  |  |  |  |  |  |  |  |  | 
 | cmp | mul | ldr | mla | bne |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 96: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr | mla | bne | cmp | mul |  |  |  |  |  |  |  |  |  |  | 
 | cmp | mul | ldr | mla | bne |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | mul |  |  |  |  |  |  |  |  |  |  |  |  | 
Commit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 97: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr | mla | bne | cmp | mul |  |  |  |  |  |  |  |  |  |  | 
 | cmp | mul | ldr | mla | bne |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  | cmp |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | mla |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | mul |  |  |  |  |  |  |  |  |  |  |  |  | 
Commit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 98: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr | mla | bne | cmp | mul |  |  |  |  |  |  |  |  |  |  | 
 | cmp | mul | ldr | mla | bne |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  | cmp | bne |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | mla |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | mul |  | ldr |  |  |  |  |  |  |  |  |  |  | 
Commit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 99: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr | mla | bne | cmp | mul |  |  |  |  |  |  |  |  |  |  | 
 | cmp | mul | ldr | mla | bne |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  | cmp | bne | mul |  |  |  |  |  |  |  |  |  | 
 |  |  |  | mla |  |  | mla |  |  |  |  |  |  |  |  | 
 |  |  | mul |  | ldr |  | cmp | bne |  |  |  |  |  |  |  | 
Commit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 100: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr | mla | bne | cmp | mul |  |  |  |  |  |  |  |  |  |  | 
 | cmp | mul | ldr | mla | bne |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  | cmp | bne | mul |  |  |  |  |  |  |  |  |  | 
 |  |  |  | mla |  |  | mla |  |  |  |  |  |  |  |  | 
 |  |  | mul |  | ldr |  | cmp | bne |  |  |  |  |  |  |  | 
Commit |  |  |  | ldr | cmp |  | mla | bne | cmp | mla | bne |  |  |  |  | 
 |  |  |  |  |  |  | mul | ldr |  | mul |  |  |  |  |  | 
TIME
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3
ldr r5, [r3], #4
cmp r1, r3
mla r0, r4, r5, r0
mul r4, r2, r4
bne .L3

## Slide 101: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr | mla | bne | cmp | mul |  |  |  |  |  |  |  |  |  |  | 
 | cmp | mul | ldr | mla | bne |  |  |  |  |  |  |  |  |  |  | 
Execute |  | ldr |  | cmp | bne | mul |  |  |  |  |  |  |  |  |  | 
 |  |  |  | mla |  |  | mla |  |  |  |  |  |  |  |  | 
 |  |  | mul |  | ldr |  | cmp | bne |  |  |  |  |  |  |  | 
Commit |  |  |  | ldr | cmp |  | mla | bne | cmp | mla | bne |  |  |  |  | 
 |  |  |  |  |  |  | mul | ldr |  | mul |  |  |  |  |  | 
TIME
Observe:
Front-end & commit in-order (i.e., left-to-right)
Execute out-of-order

## Slide 102: Example: Superscalar OoO polynomial evaluation
Fetch & Decode | ldr | mla | bne | cmp | mul | ldr | mla | bne | cmp | mul | ldr | mla | bne | cmp | mul | ldr
 | cmp | mul | ldr | mla | bne | cmp | mul | ldr | mla | bne | cmp | mul | ldr | mla | bne | cmp
Execute |  | ldr |  | cmp | bne | mul |  | ldr |  | cmp | bne | mul |  | ldr |  | cmp
 |  |  |  | mla |  |  | mla |  |  | mla |  |  | mla |  |  | mla
 |  |  | mul |  | ldr |  | cmp | bne | mul |  | ldr |  | cmp | bne | mul | 
Commit |  |  |  | ldr | cmp |  | mla | bne | cmp | mla | bne | cmp | mla | bne | cmp | mla
 |  |  |  |  |  |  | mul | ldr |  | mul | ldr |  | mul | ldr |  | mul
TIME
One loop iteration / 3 cycles!

## Slide 103: Structural hazards: Other throughput limitations
Execution units are specialized
  Floating-point (add/multiply)
  Integer (add/multiply/compare)
  Memory (load/store)
Processor designers must choose which execution units to include and how many
Structural hazard: Data is ready, but instr’n cannot issue because no hardware is available

## Slide 104: Example: Structural hazards can severely limit performance
Fetch & Decode | ldr | mla | bne | cmp | mul | ldr | mla | bne | cmp | mul | ldr | mla | bne | cmp | mul | ldr
 | cmp | mul | ldr | mla | bne | cmp | mul | ldr | mla | bne | cmp | mul | ldr | mla | bne | cmp
Mem Execute |  | ldr |  | ldr |  |  | ldr |  | ldr |  |  | ldr |  | ldr |  | 
Int Execute |  |  |  | cmp | bne | cmp | bne |  | cmp | bne | cmp | bne |  | cmp | bne | cmp
Mult Execute |  |  | mla |  |  | mul |  | mla |  |  | mul |  | mla |  |  | mul
Commit |  |  |  | ldr | cmp | mla |  | mul | ldr |  | mla |  | mul | ldr |  | mla
 |  |  |  |  |  |  |  | bne | cmp |  |  |  | bne | cmp |  | 
One loop iteration / 5 cycles 

## Slide 105: Throughput Bound
Ingredients:
  Number of operations to perform (of each type)
  Number & issue rate of “execution ports”/“functional units” (of each type)
Throughput bound = ops / issue rate
  E.g., (1 mla + 1 mul) / (2 + 3 cycles)
Again, a real CPU might not exactly meet this bound

## Slide 106: Software Takeaway
OoO is much less sensitive to “good code”
  Better performance portability
  Of course, compiler still matters
OoO makes performance analysis much simpler
  Throughput bound: Availability of execution ports
  Latency bound: “Critical path” latency
  Slowest gives good approximation of program perf

## Slide 107: Out-of-Order Execution: Under the Hood

## Slide 108: OoO x86: Microcoding
Each x86 instruction describes several operations
  E.g., add [esp+4], 5 means: 1. Load Mem[esp+4] 2. Add 5 to it 3. Store result to Mem[esp+4]
This is too much for (fast) hardware
Instead, hardware decodes instr’ns into micro-ops  Rest of pipeline uses micro-ops

## Slide 109: Register Renaming
“False dependences” can severely limit parallelism
  Write-after-read
  Write-after-write
OoO processors eliminate false dependences by transparently renaming registers
  CPU has many more “physical” than “architectural” registers
  Each time register is written, it is allocated to a new physical register
  Physical registers freed when instructions commit

## Slide 110: Memory Disambiguation
CPU must respect store  load ordering
  E.g., a later instruction reads a value from memory written by an earlier instruction
But what if the OoO CPU executes the load first?
  Must “rollback” + execute the load again (next slide)
Corollary: OoO CPU must track the order of all loads & stores, and only write memory when a store commits

## Slide 111: Rollback & Recovery
OoO CPUs speculate constantly to improve performance
  E.g., even guessing the results of a computation (“value prediction”)
Need mechanisms to “rollback” to an earlier point in execution when speculation goes awry
  Complex: Need to recover old register names, flush pending memory operations, etc
Very expensive: Up to hundreds of instrns of work lost!

## Slide 112: …But wait, there’s more!
Many issues we could not touch on
How to eliminate false dependences
  E.g., write-after-read / write-after-write
How to track dependences through memory
  E.g., storeload forwarding
How to rollback mis-speculations

## Slide 113: Scaling Instruction-Level Parallelism

## Slide 114: Recall from last time: ILP & pipelining tapped out… why?

## Slide 115: Superscalar scheduling is complex & hard to scale
Q: When is it safe to issue two instructions?
A: When they are independent
  Must compare all pairs of input and output registers
Scalability: comparisons where is “issue width” of processor
  Not great!

## Slide 116: Limitations of ILP
4-wide superscalar 20-stage pipeline 80 instrns in flight
High-performance OoO buffers hundreds of instructions
Programs have limited ILP
  Even with perfect scheduling, >8-wide issue doesn’t help
Pipelines can only go so deep
  Branch misprediction penalty grows
  Frequency (GHz) limited by power
Dynamic scheduling overheads are significant
Out-of-order scheduling is expensive

## Slide 117: Limitations of ILP  Multicore
ILP works great! …But is complex + hard to scale
From hardware perspective, multicore is much more efficient, but…
Parallel software is hard!
  Industry resisted multicore for as long as possible
  When multicore finally happened, CPU arch simplified  more cores
  Many program(mer)s still struggle to use multicore effectively