## Slide 1
14-513
18-613

## Slide 2: Machine-Level Programming III: Procedures 18-213/18-613: Introduction to Computer Systems 6th Lecture, May 22, 2025

## Slide 3: If you’re struggling with assembly
Chapter 3 of the textbook is your friend
  More detailed explanations of everything in these lectures
  Work through the practice problems
  Ask for help with the practice problems
  Today’s lecture will take us to the end of 3.7
Lots of tips, tricks, and guides have been posted on Piazza
Talk it out with a friend
  “Help me understand what jmp *.L32(,%rdx,8) does in general” is an OK discussion to have; not an AIV
  “Help me understand what jmp *.L32(,%rdx,8) does in phase 8 of this binary bomb”, on the other hand, is an AIV
  If you haven’t got a friend handy, try a rubber duck. Really!

## Slide 4: Recap: Finding Jump Table in Binary
00000000004005e0 <switch_eg>:
. . .
4005e9: ff 24 fd f0 07 40 00 jmpq *0x4007f0(,%rdi,8)
. . .
% gdb switch
(gdb) x /8xg 0x4007f0
0x4007f0: 0x0000000000400614 0x00000000004005f0
0x400800: 0x00000000004005f8 0x0000000000400602
0x400810: 0x0000000000400614 0x000000000040060b
0x400820: 0x000000000040060b 0x2c646c25203d2078
(gdb)

## Slide 5: Switch Statements on the Shark Machines
Nuance: It is desirable for addresses to be relative rather than absolute.
  Since offsets can be smaller than whole addresses, the code takes up less memory
  Relative vs absolute addresses also make it easier to link code by making it “position independent”. We’ll talk more about that later.
  To this end, x86-64 has an addressing mode which provides hardware support for managing addresses relative to the %rip.
Nuance: Loads and stores with 64-bit displacement are available only via %eax.
  Why? Its all wires! (See Prof. Nace in 18-240 for details!)

## Slide 6: Switch Statements on the Shark Machines
To make things work nicely with the constraints on the prior page:
  Rather than keeping absolute addresses, the jump table address is kept relative to the %rip.
  The address of the target code is placed into the %rax, because only that register can contain a 64-bit target address

## Slide 7: Switch Statements on the Shark Machines
The code that does the jumping looks like this:
# Handle the cases too small or too large for the switch
# Negative cases look large to ja and offsets can be used
# to shift the smallest case to 0.
0x00000000004017e9 <+41>: cmp $0xc,%esi
0x00000000004017ec <+44>: ja 0x401818 <foo+88>
# Get a pointer to the jump table
# %rip points to next addr, so %rdx becomes 0x498018 (jump table)
0x00000000004017ee <+46>: lea 0x96823(%rip),%rdx
# Get offset from %rsi-th index of jump table
0x00000000004017f5 <+53>: movslq (%rdx,%rsi,4),%rax
# Add that offset to the address of the jump table
0x00000000004017f9 <+57>: add %rdx,%rax
# Jump to that address, ultimately an offset from %rip
0x00000000004017fc <+60>: jmp *%rax

## Slide 8: Switch Statements on the Shark Machines
The jump table contains offsets relative to the start of the jump table
(gdb) x/20dw 0x498008
0x498018: -616376 -616448 -616448 -616448
0x498028: -616472 -616448 -616461 -616448
0x498038: -616392 -616448 -616416 -616448
0x498048: -616416 0 0 0
(gdb) x/20xw 0x498008
0x498008: 0x74636e75 0x206e6f69 0x216f6f66 0x00000000
0x498018: 0xfff69848 0xfff69800 0xfff69800 0xfff69800
0x498028: 0xfff697e8 0xfff69800 0xfff697f3 0xfff69800
0x498038: 0xfff69838 0xfff69800 0xfff69820 0xfff69800
0x498048: 0xfff69820 0x00000000 0x00000000 0x00000000

## Slide 9: Switch Statements on the Shark Machines
Ultimately, the target address is equal to the %rip + the offset to the start of jump table, plus an offset (possibly negative) from the start of the jump table to the target code.
  This target address is computed, placed into the %rax, and jumped to
# Get a pointer to the jump table
# %rip points to next addr, so %rdx becomes 0x498018 (jump table)
0x00000000004017ee <+46>: lea 0x96823(%rip),%rdx
# Get offset from %rsi-th index of jump table
0x00000000004017f5 <+53>: movslq (%rdx,%rsi,4),%rax
# Add that offset to the address of the jump table
0x00000000004017f9 <+57>: add %rdx,%rax
# Jump to that address, ultimately an offset from %rip
0x00000000004017fc <+60>: jmp *%rax

## Slide 10: Today
Procedures
  Mechanisms CSAPP 3.7 preamble
  Stack Structure CSAPP 3.7.1
  Calling Conventions
    Passing control CSAPP 3.7.2
    Passing data CSAPP 3.7.3
    Managing local data CSAPP 3.7.4 – 3.7.5
  Illustration of Recursion CSAPP 3.7.6
Notes: ~half the slides are for the “Managing local data” part.

## Slide 11: Procedures

## Slide 12: Mechanisms in Procedures
What’s needed?
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}
Notes: Ask the students what’s needed, before revealing the answer

## Slide 13: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 14: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 15: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 16: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 17: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}
Machine instructions implement the mechanisms, but the choices are determined by designers. These choices make up the Application Binary Interface (ABI).

## Slide 18: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 19: x86-64 Stack
Carnegie Mellon
Region of memory managed with stack discipline
Memory viewed as array of bytes.
Different regions have different purposes.
(Like ABI, a policy decision)
code
stack
memory

## Slide 20: x86-64 Stack
Carnegie Mellon
Region of memory managed with stack discipline
Stack Pointer: %rsp
Stack “Top”
Stack “Bottom”
code
stack

## Slide 21: x86-64 Stack
Region of memory managed with stack discipline
Grows toward lower addresses
Register %rsp contains lowest stack address
  address of “top” element
Stack Pointer: %rsp
Stack Grows
Down
(toward lower addresses)
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 22: x86-64 Stack: Push
pushq Src
  Fetch operand at Src
  Decrement %rsp by 8
  Write operand at address given by %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Bottom”
Stack Pointer: %rsp
Stack “Top”
val

## Slide 23: x86-64 Stack: Push
pushq Src
  Fetch operand at Src
  Decrement %rsp by 8
  Write operand at address given by %rsp
-8
Stack Grows
Down
Increasing
Addresses
Stack “Bottom”
Stack Pointer: %rsp
Stack “Top”
val

## Slide 24: x86-64 Stack: Pop
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (usually a register)
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Carnegie Mellon
val
Stack “Bottom”

## Slide 25: x86-64 Stack: Pop
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (usually a register)
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
+8
val
Stack “Bottom”

## Slide 26: x86-64 Stack: Pop
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (usually a register)
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
val
(The memory doesn’t change, only the value of %rsp)
Stack “Bottom”
Stack “Top”

## Slide 27: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 28: Code Examples
long mult2(long a, long b)
{
long s = a * b;
return s;
}
void multstore(long x, long y, long *dest)
{
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
400557: retq # Return
0000000000400540 <multstore>:
400540: push %rbx # Save %rbx
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
400549: mov %rax,(%rbx) # Save at dest
40054c: pop %rbx # Restore %rbx
40054d: retq # Return
Notes: Will cover in detail shortly

## Slide 29: Procedure Control Flow
Use stack to support procedure call and return
Procedure call: call label
  Push return address on stack
  Jump to label
Return address:
  Address of the next instruction right after call
  Example from disassembly
Procedure return: ret
  Pop address from stack
  Jump to address

## Slide 30: Control Flow Example #1
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400544
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip

## Slide 31: Control Flow Example #2
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400550
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip
Notes: 0x120-0x118 = 8

## Slide 32: Control Flow Example #3
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400557
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip

## Slide 33: Control Flow Example #4
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400549
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip

## Slide 34: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustrations of Recursion & Pointers

## Slide 35: Procedure Data Flow
Registers
First 6 integer arguments
Return value
Stack
Only allocate stack space when needed
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax
Arg 7
• • •
Arg 8
Arg n
• • •

## Slide 36: Data Flow Examples
long mult2
(long a, long b)
{
long s = a * b;
return s;
}
void multstore
(long x, long y, long *dest) {
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
# a in %rdi, b in %rsi
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
# s in %rax
400557: retq # Return
0000000000400540 <multstore>:
# x in %rdi, y in %rsi, dest in %rdx
• • •
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
# t in %rax
400549: mov %rax,(%rbx) # Save at dest
• • •
Notes: Rdi, rsi outer => x,y; rdi,rsi inner => a,b. Change names without moving data.
Mov rdx, rbx => defer until caller/callee save

## Slide 37: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 38: Stack-Based Languages
Languages that support recursion
  e.g., C, Pascal, Java
  Code must be “Reentrant”
    Multiple simultaneous instantiations of single procedure
  Need some place to store state of each instantiation
    Arguments
    Local variables
    Return address
Stack discipline
  State for given procedure needed for limited time
    From when called to when return
  Callee returns before caller does
Stack allocated in Frames
  state for single procedure instantiation

## Slide 39: Call Chain Example
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
yoo
who
amI
amI
amI
Example
Call Chain
amI
Procedure amI() is recursive

## Slide 40: Stack Frames
Frame Pointer: %rbp
Contents
  Return information
  Local storage (if needed)
  Temporary space (if needed)
Management
  Space allocated when enter procedure
    “Set-up” code
    Includes push by call instruction
  Deallocated when return
    “Tear-down” code
    Includes pop by ret instruction
Stack Pointer: %rsp
Stack “Top”
Previous Frame
Frame for proc
(Optional) x
Notes: When rbp not optional? Variable arity argument passing – need to track extents of args on stack to allow deallocation during tear-down

## Slide 41: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 42: Example
yoo(…)
{
•
•
who();
•
•
}
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 43: Example
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI(…)
{
•
•
amI();
•
•
}

## Slide 44: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 45: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 46: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 47: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 48: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 49: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 50: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 51: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 52: x86-64/Linux Stack Frame
Current Stack Frame (“Top” to Bottom)
  “Argument build:” Parameters for function about to call
  Local variables If can’t keep in registers
  Saved register context
  Old frame pointer (optional)
Caller Stack Frame
  Return address
    Pushed by call instruction
  Arguments for this call
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
(Optional)
Old %rbp
Arguments
7+
Caller
Frame
Frame pointer %rbp
Stack pointer
%rsp
(Optional)

## Slide 53: Example: incr
long incr(long *p, long val) {
long x = *p;
long y = x + val;
*p = y;
return x;
}
incr:
movq (%rdi), %rax
addq %rax, %rsi
movq %rsi, (%rdi)
ret
Register | Use(s)
%rdi | Argument p
%rsi | Argument val, y
%rax | x, Return value

## Slide 54: Example: Calling incr #1
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Notes: Why the unused bytes? Could be alignment. Or space to spill something later.

## Slide 55: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000
Notes: Leaq: stash known address of “15213” for use in function. Will be safely there until return to call_incr

## Slide 56: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000
Aside 1: movl $3000, %esi
Note: movl -> %exx zeros out high order 32 bits.
Why use movl instead of movq? 1 byte shorter.

## Slide 57: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000
Aside 2: leaq 8(%rsp), %rdi
Computes %rsp+8
Actually, used for what it is meant!

## Slide 58: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 59: Example: Calling incr #3a
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 60: Example: Calling incr #3b
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 61: Example: Calling incr #4
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rax | Return value, 15213

## Slide 62: Example: Calling incr #5a
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rax | Return value
%rsp
Updated Stack Structure
. . .
Rtn address

## Slide 63: Example: Calling incr #5b
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
Register | Use(s)
%rax | Return value
%rsp
Updated Stack Structure
. . .
Rtn address
%rsp
Final Stack Structure
. . .

## Slide 64: Register Saving Conventions
When procedure yoo calls who:
  yoo is the caller
  who is the callee
Can a register be used for temporary storage?
  Contents of register %rdx overwritten by who
  If a callee clobbers your register, its value is lost!
    Need coordination between caller/callee
yoo:
• • •
movq $15213, %rdx
call who
addq %rdx, %rax
• • •
ret
who:
• • •
subq $18213, %rdx
• • •
ret

## Slide 65: Register Saving Conventions
When procedure yoo calls who:
  yoo is the caller
  who is the callee
Can a register be used for temporary storage?
Conventions
  “Caller Saved”
    Caller must save values in its stack frame before call
  “Callee Saved”
    Callee saves values in its frame before using
    Callee restores values before returning

## Slide 66: x86-64 Linux Register Usage #1
%rax
  Return value
  Also caller-saved
  Can be modified by procedure
%rdi, ..., %r9
  Integer arguments
  Also caller-saved
  Can be modified by procedure
%r10, %r11
  Caller-saved
  Can be modified by procedure
%rax
%rdx
%rcx
Caller-saved
Return value
%r8
%r9
%r10
%r11
%rdi
%rsi
Caller-saved
Arguments
Caller-saved
Temporaries

## Slide 67: x86-64 Linux Register Usage #2
%rbx, %r12, %r13, %r14
  Callee-saved
  Callee must save & restore
%rbp
  Callee-saved
  Callee must save & restore
  May be used as frame pointer
  Compiler decides use of rbp
%rsp
  Special form of callee save
  Restored to original value upon exit from procedure
%rbx
%rsp
Callee-saved
Temporaries
Special
%rbp
%r12
%r13
%r14

## Slide 68: Quiz Time!
Canvas Quiz: Day 6 - Machine Procedures

## Slide 69: Callee-Saved Example #1
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
x comes in register %rdi.
We need %rdi for the call to incr.
Where should be put x, so we can use it after the call to incr?
Notes: Note that call_incr2 differs from call_incr that we saw earlier, in returning x+v2 instead of v1+v2.

## Slide 70: Callee-Saved Example #2
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
%rsp
Resulting Stack Structure
. . .
Rtn address
Saved %rbx
Notes: We are a callee, must save %rbx (to stack)

## Slide 71: Callee-Saved Example #3
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
Initial Stack Structure
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
%rsp
. . .
Rtn address
Saved %rbx

## Slide 72: Callee-Saved Example #4
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
x is saved in %rbx, a callee saved register
Notes: Rdi is x;

## Slide 73: Callee-Saved Example #5
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
x is saved in %rbx, a callee saved register

## Slide 74: Callee-Saved Example #6
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
Upon return from incr:
x safe in %rbx
Return val v2 in %rax
Compute x+v2: addq %rbx, %rax
Notes: If incr() used rbx, it had to restore call_incr2()’s rbx value before returning

## Slide 75: Callee-Saved Example #7
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
Saved %rbx
Return result in %rax

## Slide 76: Callee-Saved Example #8
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
18213
Unused
%rsp
Initial Stack Structure
. . .
Rtn address
Saved %rbx
18213
Unused
%rsp
. . .
Rtn address
Saved %rbx
final Stack Structure
Notes: Remember: we saved %rbx onto stack earlier. Need to restore.

## Slide 77: Today
Procedures
  Mechanisms
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 78: Recursive Function
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret

## Slide 79: Recursive Function Terminal Case
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rax | Return value | Return value
Notes: Load up 0 return, test rdi for 0, jump to L6. rep;ret -> no-op padding that is more efficient than actual nop.

## Slide 80: Recursive Function Register Save
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rsp
. . .
Rtn address
Saved %rbx

## Slide 81: Recursive Function Call Setup
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x >> 1 | Recursive argument
%rbx | x & 1 | Callee-saved
Notes: Put x into rbx; (safe – callee-saved) and with 1 to get addend, shift rdi to make new arg.

## Slide 82: Recursive Function Call
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Recursive call return value | 

## Slide 83: Recursive Function Result
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Return value | 
Notes: Remember rbx is save because the callee had to restore it before returning.

## Slide 84: Recursive Function Completion
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rax | Return value | Return value
%rsp
. . .

## Slide 85: Observations About Recursion
Handled Without Special Consideration
  Stack frames mean that each function call has private storage
    Saved registers & local variables
    Saved return pointer
  Register saving conventions prevent one function call from corrupting another’s data
    Unless the C code explicitly does so (e.g., buffer overflow in later Lecture)
  Stack discipline follows call / return pattern
    If P calls Q, then Q returns before P
    Last-In, First-Out
Also works for mutual recursion
  P calls Q; Q calls P

## Slide 86: x86-64 Procedure Summary
Important Points
  Stack is the right data structure for procedure call/return
    If P calls Q, then Q returns before P
Recursion (& mutual recursion) handled by normal calling conventions
  Can safely store values in local stack frame and in callee-saved registers
  Put function arguments 7+ at top of stack
  Result return in %rax
Pointers are addresses of values
  On stack or global
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %rbp
Arguments
7+
Caller
Frame
%rbp
(Optional)
%rsp

## Slide 87: Small Exercise
long add5(long b0, long b1, long b2, long b3, long b4) {
return b0+b1+b2+b3+b4;
}
long add10(long a0, long a1, long a2, long a3, long a4, long a5,
long a6, long a7, long a8, long a9) {
return add5(a0, a1, a2, a3, a4)+
add5(a5, a6, a7, a8, a9);
}
Where are a0,…, a9 passed?
Where are b0,…, b4 passed?
rdi, rsi, rdx, rcx, r8, r9, stack
rdi, rsi, rdx, rcx, r8
Which registers do we need to save?
Ill-posed question. Need assembly.
Notes: 1)Rdi, rsi, rdx, rcx, r8, r9, stack
2)rdi,rsi,rdx,rcx,r8

## Slide 88: Small Exercise
long add5(long b0, long b1, long b2, long b3, long b4) {
return b0+b1+b2+b3+b4;
}
long add10(long a0, long a1, long a2, long a3, long a4, long a5,
long a6, long a7, long a8, long a9) {
return add5(a0, a1, a2, a3, a4)+
add5(a5, a6, a7, a8, a9);
}
add5:
addq %rsi, %rdi
addq %rdi, %rdx
addq %rdx, %rcx
leaq (%rcx,%r8), %rax
ret
add10:
pushq %rbp
pushq %rbx
movq %r9, %rbp
call add5
movq %rax, %rbx
movq 48(%rsp), %r8
movq 40(%rsp), %rcx
movq 32(%rsp), %rdx
movq 24(%rsp), %rsi
movq %rbp, %rdi
call add5
addq %rbx, %rax
popq %rbx
popq %rbp
ret