## Slide 1
14-513
18-613

## Slide 2: Cache Memories 18-213/18-613: Introduction to Computer Systems 11th Lecture, February 17th, 2022

## Slide 3: Announcements
Lab 3 (attacklab) due today
Lab 4 (cachelab) out today
Homework continues on the usual schedule
Looking ahead: Midterm is not next week, but the week after
  Take-home
  Counts 25% toward midterm grade
  Out Monday and due Friday (the week after next)
  Counts as a 2x homework toward final grade
  VM will be covered on the midterm this semester
    Covered next week in class
    Wasn’t covered until the final last fall, so keep that in mind when looking at the F21 exam
    Tons of good problems on other old exams
  Ints, Floats, and Assembly will be condensed to make room.

## Slide 4: Today
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 5: Recall: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 6: Recall: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers.
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 7: Recall: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4

## Slide 8: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 9: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 10: Recall: General Caching Concepts: 3 Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache starts empty and this is the first reference to the block.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.
Conflict miss
  Occurs when the cache is large enough, but too many data objects all map (by the placement policy) to the same limited set of blocks
    E.g., if the placement policy maps both 0 and 8 to the same block, then referencing 0, 8, 0, 8, 0, 8, ... would miss every time.

## Slide 11: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware
  Hold frequently accessed blocks of main memory
CPU looks first for data in cache
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memory

## Slide 12: What it Really Looks Like
Bus interface
ALU
Register file
CPU chip
Cache
memory
Core i7-3960X
AMD FX 8150
Nehalem

## Slide 13: What it Really Looks Like (Cont.)
Intel Tiger Lake
Processor Die
(4 core version)
CPU caches
L1 per core: 32KB Instruction
+ 48KB Data
L2 per core: 1.25MB
Shared L3: 12MB (8 core version has 24MB)
L3
L3
L3
L3
Notes: Latest generation Intel processor, launched in 2020

## Slide 14: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size
= S x E x B data bytes
valid bit

## Slide 15: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 16: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 17: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes (= hit)
valid? +
block offset
tag

## Slide 18: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes (= hit)
valid? +
int (4 Bytes) is here
block offset
If tag doesn’t match (= miss): old line is evicted and replaced

## Slide 19: Direct-Mapped Cache Simulation
4-bit addresses (address space size M=16 bytes)
S=4 sets, E=1 Blocks/set, B=2 bytes/block
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
v
Tag
Block
0
0
0
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
0
M[0-1]
Set 0
Set 1
Set 2
Set 3
(cold)
(cold)
(cold)
(conflict)
Notes: Pause at the end of this slide to consider that M[0] and M[8] have nothing to do with one another, but that they interfere with one anothers’ existences in the cache.

## Slide 20: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
2 lines per set
S sets

## Slide 21: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes (= hit)
block offset
tag

## Slide 22: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes (= hit)
block offset
tag
5
4
short int (2 Bytes) is here
No match or not valid (= miss):
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 23: 2-Way Set Associative Cache Simulation
4-bit addresses (M=16 bytes)
S=2 sets, E=2 blocks/set, B=2 bytes/block
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1
Notes: For the same trace as before, we get a hit for the second 0 with a 2-way set associative cache (instead of a miss with a direct-mapped cache).

## Slide 24: What about writes?
Multiple copies of data exist:
  L1, L2, L3, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Each cache line needs a dirty bit (set if data differs from memory)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location will follow
  No-write-allocate (writes straight to memory, does not load into cache)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate
0
1
2
B-1
tag
d
B = 2b bytes
dirty bit
v
valid bit

## Slide 25: Why Index Using Middle Bits?
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
t bits
0…01
100
Address of int:
find set
Standard Method:
Middle bit indexing
t bits
1…11
100
Address of int:
find set
Alternative Method:
High bit indexing

## Slide 26: Illustration of Indexing Approaches
64-byte memory
  6-bit addresses
16 byte, direct-mapped cache
Block size = 4. (Thus, 4 sets; why?)
2 bits tag, 2 bits index, 2 bits offset
Set 0
Set 1
Set 2
Set 3
1111xx
1110xx
1101xx
1100xx
1011xx
1010xx
1001xx
1000xx
0111xx
0110xx
0101xx
0100xx
0011xx
0010xx
0001xx
0000xx
Notes: 16byte direct mapped $, 4B blocks -> must be 4 sets to account for all 16B of cache

## Slide 27: Middle Bit Indexing
Addresses of form TTSSBB
  TT Tag bits
  SS Set index bits
  BB Offset bits
Makes good use of spatial locality
Set 0
Set 1
Set 2
Set 3
1111xx
1110xx
1101xx
1100xx
1011xx
1010xx
1001xx
1000xx
0111xx
0110xx
0101xx
0100xx
0011xx
0010xx
0001xx
0000xx

## Slide 28: High Bit Indexing
Addresses of form SSTTBB
  SS Set index bits
  TT Tag bits
  BB Offset bits
Program with high spatial locality would generate lots of conflicts
Set 0
Set 1
Set 2
Set 3
1111xx
1110xx
1101xx
1100xx
1011xx
1010xx
1001xx
1000xx
0111xx
0110xx
0101xx
0100xx
0011xx
0010xx
0001xx
0000xx
Notes: Go from block with set index bits 00 to 01, displace the line sitting in set 0 from the block with set index 00.

## Slide 29: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.

## Slide 30: Example: Core i7 L1 Data Cache
B =
S = , s =
E = , e =
C =
Block offset: . bits
Set index: . bits
Tag: . bits
Stack Address: 0x00007f7262a1e010
Block offset: 0x??
Set index: 0x??
Tag: 0x??
32 kB 8-way set associative
64 bytes/block
47 bit address range
Notes: B = 64 (2^6)
E = 8 (2^3)
S = 64 (2^6) [need to infer from B, E, and Cache Size]
Cache Size = 2^15 (32768)

## Slide 31: Example: Core i7 L1 Data Cache
B = 64
S = 64, s = 6
E = 8, e = 3
C = 64 x 64 x 8 = 32,768
Block offset: 6 bits
Set index: 6 bits
Tag: 35 bits
Stack Address: 0x00007f7262a1e010
Block offset: 0x??
Set index: 0x??
Tag: 0x??
32 kB 8-way set associative 64 bytes/block
47 bit address range

## Slide 32: Example: Core i7 L1 Data Cache
B = 64
S = 64, s = 6
E = 8, e = 3
C = 64 x 64 x 8 = 32,768
Block offset: 6 bits
Set index: 6 bits
Tag: 35 bits
Stack Address: 0x00007f7262a1e010
Block offset: 0x10
Set index: 0x0
Tag: 0x7f7262a1e
32 kB 8-way set associative 64 bytes/block
47 bit address range
0000 0001 0000
Notes: 0x010 => 0000 0001 0000, say that it awkwardly segments the bits, but that’s ok

## Slide 33: Cache Performance Metrics
Miss Rate
  Fraction of memory accesses not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (as %):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a cached block to the processor
    includes time to determine whether line is in cache
  Typical numbers:
    4 clock cycle for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 34: How Bad Can a Few Cache Misses Be?
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider this simplified example: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 x 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 x 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 35: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories

## Slide 36: Quiz Time!
Check out:
Canvas > Day 10 – Cache Memories

## Slide 37: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 38: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 39: Memory Mountain Test Function
long data[MAXELEMS]; /* Global array to traverse */
/* test - Iterate over first "elems" elements of
* array "data" with stride of "stride“,
* using 4x4 loop unrolling.
*/
int test(int elems, int stride) {
long i, sx2=stride*2, sx3=stride*3, sx4=stride*4;
long acc0 = 0, acc1 = 0, acc2 = 0, acc3 = 0;
long length = elems, limit = length - sx4;
/* Combine 4 elements at a time */
for (i = 0; i < limit; i += sx4) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+stride];
acc2 = acc2 + data[i+sx2];
acc3 = acc3 + data[i+sx3];
}
/* Finish any remaining elements */
for (; i < length; i++) {
acc0 = acc0 + data[i];
}
return ((acc0 + acc1) + (acc2 + acc3));
}
Call test() with many combinations of elems
and stride.
For each elems and stride:
1. Call test() once to warm up the caches.
2. Call test() again and measure the read throughput(MB/s)
mountain/mountain.c

## Slide 40: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Notes: Slopes of spatial locality – increase stride, degrade throughput because burn through blocks faster
Ridges of temporal – As increase size, can’t fit in level of cache any more, drop to next one down. Data in cache because of warm up before test run.
Prefetching – do better than we expect.

## Slide 41: Closer Look at Stride Effects
Chart: Stride
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
8 elems per cache block
128K
Chart: Throughput for size = 128K
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
Measured | 30896 | 25024 | 24135 | 20391 | 17199 | 14634 | 12670 | 11274 | 11248 | 11262 | 11294 | 11251
Miss rate = stride/8
Miss rate = 1.0
stride

## Slide 42: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 43: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  Matrix elements are doubles (8 bytes)
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register
matmult/mm.c

## Slide 44: Miss Rate Analysis for Matrix Multiply
Assume:
  Block size = 32B (big enough for four doubles)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j
=
x

## Slide 45: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > sizeof(aij) bytes, exploit spatial locality
    miss rate = sizeof(aij) / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    miss rate = 1 (i.e. 100%)

## Slide 46: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Miss rate for inner loop iterations:
  A B C
  0.25 1.0 0.0
matmult/mm.c
Block size = 32B (four doubles)

## Slide 47: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0
matmult/mm.c
Block size = 32B (four doubles)
Same analysis as ijk
Notes: Can go quickly through this slide. Only point is that the outer loop order doesn’t change the analysis

## Slide 48: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Miss rate for inner loop iterations:
  A B C
  0.0
matmult/mm.c
Block size = 32B (four doubles)
0.25
0.25

## Slide 49: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Miss rate for inner loop iterations:
  A B C
  0.0
matmult/mm.c
Block size = 32B (four doubles)
1.0
1.0

## Slide 50: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  avg misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  avg misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  avg misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 51: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700
jki | 4.8 | 4.68 | 4.65 | 4.8 | 6.84 | 15.03 | 22.78 | 29.39 | 40.39 | 57.06 | 60.54 | 63.33 | 65.61 | 67.49
kji | 4.83 | 4.72 | 4.64 | 4.69 | 6.83 | 15.1 | 22.68 | 29.18 | 40.26 | 57.02 | 60.53 | 63.34 | 65.62 | 67.53
ijk | 3.75 | 4.08 | 4.33 | 4.45 | 4.45 | 4.45 | 4.45 | 4.47 | 7.73 | 18.77 | 20.36 | 21.67 | 22.76 | 23.71
jik | 3.93 | 4.14 | 4.36 | 4.47 | 4.52 | 4.56 | 4.57 | 4.6 | 7.96 | 19.05 | 20.59 | 21.86 | 22.92 | 23.82
kij | 1.86 | 1.78 | 2.14 | 2.3 | 2.23 | 2.18 | 2.14 | 2.12 | 2.12 | 2.13 | 2.13 | 2.14 | 2.16 | 2.22
ikj | 1.78 | 1.8 | 2.12 | 2.03 | 1.96 | 1.92 | 1.89 | 1.86 | 1.86 | 1.88 | 1.89 | 1.9 | 1.91 | 1.95
ijk / jik (1.25)
jki / kji (2.0)
kij / ikj (0.5)
Cycles per inner loop iteration

## Slide 52: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 53: Example: Matrix Multiplication
a
b
i
j
x
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n + j] += a[i*n + k] * b[k*n + j];
}

## Slide 54: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache line = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
x
=
n
x
=
8 wide
Notes: n/8 – comes from taking n and doing it in chunks of 8 that fit in a cache line, with perfect stride 1 accesses across the row
N – comes from missing on everything but the 1 double needed going down a column

## Slide 55: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache line = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 n2 = (9/8) n3
n
x
=
8 wide

## Slide 56: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=L)
for (j = 0; j < n; j+=L)
for (k = 0; k < n; k+=L)
/* L x L mini matrix multiplications */
for (i1 = i; i1 < i+L; i1++)
for (j1 = j; j1 < j+L; j1++)
for (k1 = k; k1 < k+L; k1++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
x
c
=
c
+
Block size L x L
matmult/bmm.c

## Slide 57: Cache Miss Analysis
Assume:
  Cache line = 8 doubles. Blocking size L ≥ 8
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3L2 < C
First (block) iteration:
  Misses per block: L2/8
  Blocks per Iteration: 2n/L
  (omitting matrix c)
  Misses per Iteration:
  2n/L x L2/8 = nL/4
  Afterwards in cache (schematic)
x
=
x
=
Block size L x L
n/L blocks
Notes: L^2 / 8 comes from taking L^2 bytes per block and perfectly caching them 8 doubles at a time.
2n/L comes from doing n/L blocks of size L^2 in each source matrix

## Slide 58: Cache Miss Analysis
Assume:
  Cache line = 8 doubles. Blocking size L ≥ 8
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3L2 < C
Second (block) iteration:
  Same misses as
  first iteration
  2n/L x L2/8 = nL/4
Total misses:
  nL/4 misses per iteration x (n/L)2 iterations = n3/(4L) misses
x
=
Block size L x L
n/L blocks
Notes: n/L is the dimension of the matrix in blocks. (n/L)^2 is the number of iterations.
nL/4 is the misses per iteration. N^3/4L is the total miss count.

## Slide 59: Blocking Summary
No blocking: (9/8) n3 misses
Blocking: (1/(4L)) n3 misses
Use largest block size L, such that L satisfies 3L2 < C
  Fit three blocks in cache! Two input, one output.
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly
Notes: 3L^2 to accommodate M3 = M1 x M2, with M1,2,3 all supplying blocks of dim L^2

## Slide 60: Cache Summary
Cache memories can have significant performance impact
You can write your programs to exploit this!
  Focus on the inner loops, where bulk of computations and memory accesses occur.
  Try to maximize spatial locality by reading data objects sequentially with stride 1.
  Try to maximize temporal locality by using a data object as often as possible once it’s read from memory.

## Slide 61: Supplemental slides

## Slide 62: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
128m | 16636 | 8966 | 5846 | 4298 | 3403 | 2789 | 2348 | 2055 | 1904 | 1786 | 1693 | 1607
64m | 16925 | 9080 | 5860 | 4307 | 3408 | 2795 | 2352 | 2058 | 1912 | 1791 | 1695 | 1608
32m | 17168 | 9212 | 5897 | 4331 | 3431 | 2822 | 2375 | 2078 | 1924 | 1809 | 1713 | 1628
16m | 17405 | 9559 | 6027 | 4458 | 3520 | 2899 | 2465 | 2179 | 2049 | 1952 | 1883 | 1825
8m | 19339 | 11837 | 8045 | 6079 | 4927 | 4246 | 3745 | 3289 | 3131 | 3026 | 2899 | 2924
4m | 20728 | 16852 | 13212 | 10371 | 8542 | 7259 | 6345 | 5627 | 5396 | 5228 | 5090 | 4977
2m | 29025 | 19350 | 13735 | 10550 | 8610 | 7308 | 6361 | 5648 | 5417 | 5241 | 5094 | 4978
1024k | 29291 | 19543 | 13689 | 10508 | 8597 | 7281 | 6354 | 5628 | 5388 | 5218 | 5071 | 4956
512k | 29290 | 19411 | 13779 | 10594 | 8667 | 7390 | 6438 | 5684 | 5453 | 5325 | 5213 | 5128
256k | 29762 | 21456 | 16905 | 13504 | 11044 | 9359 | 8175 | 7240 | 7082 | 6889 | 6858 | 6835
128k | 30042 | 23953 | 22661 | 18952 | 15706 | 13602 | 11761 | 10409 | 10184 | 10137 | 10158 | 9875
64k | 29468 | 23044 | 21501 | 19208 | 15955 | 13551 | 11784 | 10516 | 10364 | 10320 | 10262 | 10132
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Core i5 Haswell
3.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size

## Slide 63: Cache Capacity Effects from Memory Mountain
Chart: Working set size (bytes)
| 128m | 64m | 32m | 16m | 8m | 4m | 2m | 1024k | 512k | 256k | 128k | 64k | 32k | 16k
s8 | 2055 | 2058 | 2078 | 2179 | 3289 | 5627 | 5648 | 5628 | 5684 | 7240 | 10409 | 10516 | 26110 | 27746
Core i7 Haswell
3.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slice through memory mountain with stride=8
L1
L2
L3
Main Memory

## Slide 64: Modeling Block Size Effects from Memory Mountain
Chart: Throughput for size = 128K
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
Measured | 30896 | 25024 | 24135 | 20391 | 17199 | 14634 | 12670 | 11274 | 11248 | 11262 | 11294 | 11251
Model | 30896 | 24743.7642 | 20634.8109 | 17696.1805 | 15490.2007 | 13773.2479 | 12398.9348 | 11274 | 11274 | 11274 | 11274 | 11274
Core i7 Haswell
2.26 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Stride s

## Slide 65: 2008 Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
128m | 5427 | 2757 | 1939 | 1455 | 1151 | 951 | 803 | 701 | 672 | 646 | 626 | 610
64m | 5496 | 2760 | 1936 | 1459 | 1149 | 949 | 803 | 703 | 666 | 644 | 621 | 610
32m | 5498 | 2758 | 1938 | 1454 | 1151 | 934 | 811 | 704 | 671 | 645 | 625 | 611
16m | 5506 | 2769 | 1941 | 1460 | 1153 | 953 | 811 | 705 | 672 | 646 | 626 | 614
8m | 5657 | 2977 | 2090 | 1586 | 1251 | 1035 | 882 | 766 | 777 | 836 | 1018 | 1365
4m | 10401 | 8422 | 7522 | 6468 | 5469 | 4809 | 4284 | 3894 | 3900 | 3899 | 3898 | 3897
2m | 10401 | 8418 | 7517 | 6468 | 5465 | 4804 | 4284 | 3898 | 3896 | 3897 | 3893 | 3897
1024k | 10479 | 8469 | 7578 | 6508 | 5510 | 4854 | 4326 | 3935 | 3939 | 3945 | 3951 | 3963
512k | 10486 | 8465 | 7578 | 6508 | 5514 | 4854 | 4330 | 3938 | 3945 | 3952 | 3956 | 3969
256k | 10479 | 8456 | 7578 | 6503 | 5510 | 4850 | 4322 | 3931 | 3935 | 3938 | 3944 | 3958
128k | 10473 | 8443 | 7552 | 6488 | 5496 | 4833 | 4307 | 3920 | 3912 | 3922 | 3923 | 3938
64k | 10460 | 8414 | 7537 | 6463 | 5474 | 4817 | 4295 | 3902 | 3897 | 3899 | 3893 | 3905
No prefetching
Core 2 Duo
2.4 GHz
32 KB L1 d-cache
6MB L2 cache
64 B block size

## Slide 66: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
matmult/mm.c
Block size = 32B (four doubles)

## Slide 67: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c
Block size = 32B (four doubles)

## Slide 68: Recap: Stack and instruction pointers
The stack pointer (%rsp) points to the top of the stack
The instruction pointer (%rip) points to the next instruction to be executed
They are independent
  But linked by call and ret instructions
Stack
Text
Data
Heap
Shared
Libraries
rsp
rip

## Slide 69: Recap: stack operations
push %rax =
more stuff
rsp

## Slide 70: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
more stuff
rax
rsp

## Slide 71: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
more stuff
rax
rsp

## Slide 72: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
more stuff
rax
rip
rsp

## Slide 73: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
ret =
more stuff
rax
rip
rsp

## Slide 74: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
ret =
  mov (%rsp), %rip
  add %rsp, 8
more stuff
rax
rsp

## Slide 75: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
ret =
  mov (%rsp), %rip
  add %rsp, 8
pop %rax =
more stuff
rax
rsp

## Slide 76: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
ret =
  mov (%rsp), %rip
  add %rsp, 8
pop %rax =
  mov (%rsp), %rax
  add %rsp, 8
more stuff
rsp