## Slide 1
14-513
18-613

## Slide 2: Machine-Level Programming II: Control 18-213/18-613: Introduction to Computer Systems 5th Lecture, Spring 2026

## Slide 3: Today
Control: Condition codes CSAPP 3.6.1 - 3.6.2
Conditional branches CSAPP 3.6.3 - 3.6.6
Loops CSAPP 3.6.7
Switch Statements CSAPP 3.6.8

## Slide 4: Processor State (x86-64, Partial)
Information about currently executing program
  Temporary data ( %rax, … )
  Location of runtime stack ( %rsp )
  Location of current code control point ( %rip, … )
  Status of recent tests ( CF, ZF, SF, OF )
%rip
Registers
Current stack top
Instruction pointer
CF
ZF
SF
OF
Condition codes
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 5: Condition Codes (Implicit Setting)
Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Implicitly set (as side effect) of arithmetic operations
  Example: addq Src,Dest ↔ t = a+b
  CF set if carry/borrow out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by lea instruction

## Slide 6: ZF set when
000000000000…00000000000

## Slide 7: SF set when
yxxxxxxxxxxxx...
yxxxxxxxxxxxx...
+
1xxxxxxxxxxxx...
For signed arithmetic, this reports when result is a negative number

## Slide 8: CF set when
1xxxxxxxxxxxx...
1xxxxxxxxxxxx...
+
xxxxxxxxxxxxx...
1
For unsigned arithmetic, this reports overflow
0xxxxxxxxxxxx...
1xxxxxxxxxxxx...
-
1xxxxxxxxxxxx...
1
Carry
Borrow

## Slide 9: OF set when
yxxxxxxxxxxxx...
yxxxxxxxxxxxx...
+
zxxxxxxxxxxxx...
z = ~y
For signed arithmetic, this reports overflow
  (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
a
b
t
yxxxxxxxxxxxx...
zxxxxxxxxxxxx...
-
zxxxxxxxxxxxx...
  (a>0 && b<0 && t<0) || (a<0 && b>0 && t>0)
a
b
t
Positive
Overflow
Negative
Overflow

## Slide 10: Condition Codes (Explicit Setting: Compare)
Explicit Setting by Compare Instruction
  cmpq Src2, Src1
  cmpq b,a like computing a-b without setting destination
  CF set if carry/borrow out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)
Notes: OF: 1st case: positive number (a) minus negative number (b) should be like a – (-b) = a+b > 0; if < 0, then OF
OF: 2nd case: negative number (a) minus positive number (b) should be like (-a) – b = -(a+b) < 0; if > 0 then OF

## Slide 11: Condition Codes (Explicit Setting: Test)
Explicit Setting by Test instruction
  testq Src2, Src1
    testq b,a like computing a&b without setting destination
  Sets condition codes based on value of Src1 & Src2
  Useful to have one of the operands be a mask
  ZF set when a&b == 0
  SF set when a&b < 0
Very often:
testq %rax,%rax
Notes: Very often the compiler just repeats the same register twice – ANDing a register with itself doesn’t change the value – so this tests whether the value in that register is zero, or negative.

## Slide 12: Condition Codes (Explicit Reading: Set)
Explicit Reading by Set Instructions
  setX Dest: Set low-order byte of destination Dest to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes of Dest
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (signed)
setge | ~(SF^OF) | Greater or Equal (signed)
setl | SF^OF | Less (signed)
setle | (SF^OF)¦ZF | Less or Equal (signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 13: Explicit Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setl %al # Set when <
  movzbl %al, %eax # Zero rest of %rax
ret
SetX Instructions:
  Set single byte based on combination of condition codes
One of addressable byte registers
  Does not alter remaining bytes
  Typically use movzbl to finish job
    32-bit instructions also set upper 32 bits to 0
int lt (long x, long y)
{
return x < y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 14: Example: setl (Signed <)
Condition: SF^OF
SF | OF | SF ^ OF | Implication
0 | 0 | 0 | 
1 | 0 | 1 | 
0 | 1 | 1 | 
1 | 1 | 0 | 
1xxxxxxxxxxxx...
0xxxxxxxxxxxx...
-
0xxxxxxxxxxxx...
a
b
t
negative overflow case
No overflow, so SF implies not <
No overflow, so SF implies a < b
Overflow, so SF implies negative overflow, i.e. a < b
Overflow, so SF implies positive overflow, i.e. not <
OF set if
(a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)
Notes: Case 0: no overflow, trust sign bit: a-b >= 0 (i.e., !(a<b))
Case 1: no overflow, trust sign bit: a-b < 0 (i.e., (a<b))
Case 2: overflow with 0 sign bit, i.e., (-a) – (+b) > 0 (i.e., a < b) => a negative, b positive, so a < b
Case 3: overflow with 1 sign bit, i.e., (+a) – (-b) < 0 (i.e., !(a < b)) => a positive, b negative, so a >=b

## Slide 15: x86-64 Integer Registers
%rsp
  Can reference low-order byte
%al
%bl
%cl
%dl
%sil
%dil
%spl
%bpl
%r8b
%r9b
%r10b
%r11b
%r12b
%r13b
%r14b
%r15b
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 16: An x86-64 quirk to watch out for
Most instructions with a 32-bit destination zero the upper 32 bits of the register!
movzbl %al, %eax
%al
%eax
%rax
%al
00 00 00
00 00 00 00
Zero extended from %al
Zapped to 0
Notes: This seems perfectly sensible for movzbl, but imagine if instead we had movsbl - *sign* extend al to eax – and al was a negative number, we’d get 00 00 00 00 FF FF FF al which probably wasn’t what we wanted. Should have used movsbq %al, %rax instead.

## Slide 17: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 18: Jumping
jX Instructions
  Jump to different part of code depending on condition codes
  Implicit reading of condition codes
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (signed)
jge | ~(SF^OF) | Greater or Equal (signed)
jl | SF^OF | Less (signed)
jle | (SF^OF)¦ZF | Less or Equal (signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 19: Conditional Branch Example (Old Style)
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
absdiff:
cmpq %rsi, %rdi # x:y, x-y
jle .L4
movq %rdi, %rax
subq %rsi, %rax
ret
.L4: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
Generation
  shark> gcc –Og -S –fno-if-conversion control.c
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
Get to this shortly

## Slide 20: Expressing with Goto Code
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
C allows goto statement
Jump to position designated by label
long absdiff_j
(long x, long y)
{
long result;
int ntest = (x <= y);
if (ntest) goto Else;
result = x-y;
goto Done;
Else:
result = y-x;
Done:
return result;
}
if-conversion

## Slide 21: General Conditional Expression Translation (Using Branches)
C Code
val = Test ? Then_Expr : Else_Expr;
Goto Version
ntest = !Test;
if (ntest) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
  Create separate code regions for then & else expressions
  Execute appropriate one
val = x>y ? x-y : y-x;

## Slide 22: Using Conditional Moves
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
result = Then_Expr;
eval = Else_Expr;
nt = !Test;
if (nt) result = eval;
return result;
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC tries to use them
    But, only when known to be safe
Why?
  Branches are very disruptive to instruction flow through pipelines
  Conditional moves do not require control transfer

## Slide 23: Conditional Move Example
absdiff:
movq %rdi, %rax # x
subq %rsi, %rax # result = x-y
movq %rsi, %rdx
subq %rdi, %rdx # eval = y-x
cmpq %rsi, %rdi # x:y
cmovle %rdx, %rax # if <=, result = eval
ret
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
When is
this bad?

## Slide 24: Bad Cases for Conditional Move
Expensive Computations
Both values get computed
Only makes sense when computations are very simple
val = Test(x) ? Hard1(x) : Hard2(x);
Risky Computations
Both values get computed
May have undesirable effects
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x*=7 : x+=3;
Bad Performance
Unsafe
Illegal

## Slide 25: Exercise
xorq %rax, %rax
subq $1, %rax
cmpq $2, %rax
setl %al
movzbl %al, %eax
%rax | SF | CF | OF | ZF
0x0000 0000 0000 0000 | 0 | 0 | 0 | 1
0xFFFF FFFF FFFF FFFF | 1 | 1 | 0 | 0
0xFFFF FFFF FFFF FFFF | 1 | 0 | 0 | 0
0xFFFF FFFF FFFF FF01 | 1 | 0 | 0 | 0
0x0000 0000 0000 0001 | 1 | 0 | 0 | 0
cmpq b,a like computing a-b w/o setting dest
CF set if carry/borrow out from most significant bit (used for unsigned comparisons)
ZF set if a == b
SF set if (a-b) < 0 (as signed)
OF set if two’s-complement (signed) overflow
Note: setl and movzbl do not modify condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (signed)
setge | ~(SF^OF) | Greater or Equal (signed)
setl | SF^OF | Less (signed)
setle | (SF^OF)¦ZF | Less or Equal (signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 26: Exercise
xorq %rax, %rax
subq $1, %rax
cmpq $2, %rax
setl %al
movzbl %al, %eax
%rax | SF | CF | OF | ZF
0x0000 0000 0000 0000 | 0 | 0 | 0 | 1
0xFFFF FFFF FFFF FFFF | 1 | 1 | 0 | 0
0xFFFF FFFF FFFF FFFF | 1 | 0 | 0 | 0
0xFFFF FFFF FFFF FF01 | 1 | 0 | 0 | 0
0x0000 0000 0000 0001 | 1 | 0 | 0 | 0
cmpq b,a like computing a-b w/o setting dest
CF set if carry/borrow out from most significant bit (used for unsigned comparisons)
ZF set if a == b
SF set if (a-b) < 0 (as signed)
OF set if two’s-complement (signed) overflow
Note: setl and movzbl do not modify condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (signed)
setge | ~(SF^OF) | Greater or Equal (signed)
setl | SF^OF | Less (signed)
setle | (SF^OF)¦ZF | Less or Equal (signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 27: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 28: “Do-While” Loop Example
C Code
long pcount_do
(unsigned long x) {
long result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Count number of 1’s in argument x (“popcount”)
Use conditional branch to either continue looping or to exit loop

## Slide 29: “Do-While” Loop Compilation
movl $0, %eax # result = 0
.L2: # loop:
movq %rdi, %rdx
andl $1, %edx # t = x & 0x1
addq %rdx, %rax # result += t
shrq %rdi # x >>= 1
jne .L2 # if(x) goto loop
rep; ret
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Register | Use(s)
%rdi | Argument x
%rax | result

## Slide 30: General “Do-While” Translation
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 31: General “While” Translation #1
While version
while (Test)
Body
“Jump-to-middle” translation
Used with -Og
Goto Version
goto test;
loop:
Body
test:
if (Test)
goto loop;
done:

## Slide 32: While Loop Example
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Jump to Middle Version
long pcount_goto_jtm
(unsigned long x) {
long result = 0;
goto test;
loop:
result += x & 0x1;
x >>= 1;
test:
if(x) goto loop;
return result;
}
Compare to do-while version of function
Initial goto starts loop at test

## Slide 33: General “While” Translation #2
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
“Do-while” conversion
Used with –O1
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 34: While Loop Example #2
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Do-While Version
long pcount_goto_dw
(unsigned long x) {
long result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
done:
return result;
}
Initial conditional guards entrance to loop
Compare to do-while version of function
  Removes jump to middle. When is this good or bad?
Notes: If more often not entering loop, then skip unnecessary unconditional jump to the middle, which just evaluates to done.

## Slide 35: “For” Loop Form
for (Init; Test; Update )
Body
General Form
#define WSIZE 8*sizeof(int)
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 36: “For” Loop  Do-While Loop
For version
Do-While Version
if (!Test)
goto done;
do {
Body
Update
} while(Test);
done:
Goto Version
if (!Test)
goto done;
loop:
Body
Update
if (Test)
goto loop;
done:
for (Init; Test; Update )
Body
Initial test can often be optimized away – why?
Notes: Can optimize initial test away when Test is known to be true first time because of initial condition Init. E.g., for(i=0, i < 8; i++)

## Slide 37: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 38: Switch Statement Example
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
long my_switch
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 39: Jump Table Structure
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
jtab:
goto *JTab[x];
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Translation (Extended C)
Jump Table
Jump Targets

## Slide 40: Switch Statement Example
long my_switch
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
.L3:
.L5:
.L9:
.L7:
.L8:
my_switch:
cmpq $6, %rdi # x:6
ja .L8 # if x > 6 jump # to default
jmp *.L4(,%rdi,8)

## Slide 41: Assembly Setup Explanation
Table Structure
  Each target requires 8 bytes
  Base address at .L4
Jumping
  Direct: jmp .L8
  Jump target is denoted by label .L8
  Indirect: jmp *.L4(,%rdi,8)
  Start of jump table: .L4
  Must scale by factor of 8 (addresses are 8 bytes)
  Fetch target from effective Address .L4 + x*8
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6

## Slide 42: Code Blocks (x == 1)
.L3:
movq %rsi, %rax # y
imulq %rdx, %rax # y*z
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 43: Handling Fall-Through
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
case 3:
w = 1;
case 2:
w = y/z;
goto merge;
merge:
w += z;

## Slide 44: Code Blocks (x == 2, x == 3)
.L5: # Case 2
movq %rsi, %rax
cqto # sign extend
# rax to rdx:rax
idivq %rcx # y/z
jmp .L6 # goto merge
.L9: # Case 3
movl $1, %eax # w = 1
.L6: # merge:
addq %rcx, %rax # w += z
ret
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rcx | z
%rax | Return value

## Slide 45: Code Blocks (x == 5, x == 6, default)
.L7: # Case 5,6
movl $1, %eax # w = 1
subq %rdx, %rax # w -= z
ret
.L8: # Default:
movl $2, %eax # 2
ret
switch(x) {
. . .
case 5: // .L7
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 46: Switch Statement Example
Setup
long my_switch(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
my_switch:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8
jmp *.L4(,%rdi,8)
What range of values takes default?
Note that w not initialized here
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value
Notes: Cmpq 6 rdi  go to default if above all case values
w is not initialized until it is sure to be used.

## Slide 47: Switch Statement Example
long my_switch(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Setup
Setup
my_switch:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8 # use default
jmp *.L4(,%rdi,8) # goto *Jtab[x]
Notes: *.L4(,rdi,8) is L4 + rdi * addrsize  go to *Jtab[x], with x in rdi

## Slide 48: Jump Table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}

## Slide 49: Finding Jump Table in Binary
00000000004005e0 <switch_eg>:
4005e0: 48 89 d1 mov %rdx,%rcx
4005e3: 48 83 ff 06 cmp $0x6,%rdi
4005e7: 77 2b ja 400614 <switch_eg+0x34>
4005e9: ff 24 fd f0 07 40 00 jmpq *0x4007f0(,%rdi,8)
4005f0: 48 89 f0 mov %rsi,%rax
4005f3: 48 0f af c2 imul %rdx,%rax
4005f7: c3 retq
4005f8: 48 89 f0 mov %rsi,%rax
4005fb: 48 99 cqto
4005fd: 48 f7 f9 idiv %rcx
400600: eb 05 jmp 400607 <switch_eg+0x27>
400602: b8 01 00 00 00 mov $0x1,%eax
400607: 48 01 c8 add %rcx,%rax
40060a: c3 retq
40060b: b8 01 00 00 00 mov $0x1,%eax
400610: 48 29 d0 sub %rdx,%rax
400613: c3 retq
400614: b8 02 00 00 00 mov $0x2,%eax
400619: c3 retq

## Slide 50: Finding Jump Table in Binary (cont.)
00000000004005e0 <switch_eg>:
. . .
4005e9: ff 24 fd f0 07 40 00 jmpq *0x4007f0(,%rdi,8)
. . .
% gdb switch
(gdb) x /8xg 0x4007f0
0x4007f0: 0x0000000000400614 0x00000000004005f0
0x400800: 0x00000000004005f8 0x0000000000400602
0x400810: 0x0000000000400614 0x000000000040060b
0x400820: 0x000000000040060b 0x2c646c25203d2078
(gdb)

## Slide 51: Finding Jump Table in Binary (cont.)
% gdb switch
(gdb) x /8xg 0x4007f0
0x4007f0: 0x0000000000400614 0x00000000004005f0
0x400800: 0x00000000004005f8 0x0000000000400602
0x400810: 0x0000000000400614 0x000000000040060b
0x400820: 0x000000000040060b 0x2c646c25203d2078
. . .
4005f0: 48 89 f0 mov %rsi,%rax
4005f3: 48 0f af c2 imul %rdx,%rax
4005f7: c3 retq
4005f8: 48 89 f0 mov %rsi,%rax
4005fb: 48 99 cqto
4005fd: 48 f7 f9 idiv %rcx
400600: eb 05 jmp 400607 <switch_eg+0x27>
400602: b8 01 00 00 00 mov $0x1,%eax
400607: 48 01 c8 add %rcx,%rax
40060a: c3 retq
40060b: b8 01 00 00 00 mov $0x1,%eax
400610: 48 29 d0 sub %rdx,%rax
400613: c3 retq
400614: b8 02 00 00 00 mov $0x2,%eax
400619: c3 retq

## Slide 52: Switch Statements on the Shark Machines
Nuance: It is desirable for addresses to be relative rather than absolute.
  Since offserts can be smaller than whole addresses, the code takes up less memory
  Relative vs absolute addresses also make it easier to link code by making it “position independent”. We’ll talk more about that later.
  To this end, x86-64 has an addressing mode which provides hardware support for managing addresses relative to the %rip.
Nuance: Loads and stores with 64-bit displacement are available only via %eax.
  Why? Its all wires! (See Prof. Nace in 18-240 for details!)

## Slide 53: Switch Statements on the Shark Machines
To make things work nicely with the constraints on the prior page:
  Rather than keeping absolute addresses, the jump table address is kept relative to the %rip.
  The address of the target code is placed into the %rax, because only that register can contain a 64-bit target address

## Slide 54: Switch Statements on the Shark Machines
The code that does the jumping looks like this:
# Handle the cases too small or too large for the switch
# Negative cases look large to ja and offsets can be used
# to shift the smallest case to 0.
0x00000000004017e9 <+41>: cmp $0xc,%esi
0x00000000004017ec <+44>: ja 0x401818 <foo+88>
# Get a pointer to the jump table
# %rip points to next addr, so %rdx becomes 0x498018 (jump table)
0x00000000004017ee <+46>: lea 0x96823(%rip),%rdx
# Get offset from %rsi-th index of jump table
0x00000000004017f5 <+53>: movslq (%rdx,%rsi,4),%rax
# Add that offset to the address of the jump table
0x00000000004017f9 <+57>: add %rdx,%rax
# Jump to that address, ultimately an offset from %rip
0x00000000004017fc <+60>: jmp *%rax

## Slide 55: Switch Statements on the Shark Machines
The jump table contains offsets relative to the start of the jump table
(gdb) x/20dw 0x498008
0x498018: -616376 -616448 -616448 -616448
0x498028: -616472 -616448 -616461 -616448
0x498038: -616392 -616448 -616416 -616448
0x498048: -616416 0 0 0
(gdb) x/20xw 0x498008
0x498008: 0x74636e75 0x206e6f69 0x216f6f66 0x00000000
0x498018: 0xfff69848 0xfff69800 0xfff69800 0xfff69800
0x498028: 0xfff697e8 0xfff69800 0xfff697f3 0xfff69800
0x498038: 0xfff69838 0xfff69800 0xfff69820 0xfff69800
0x498048: 0xfff69820 0x00000000 0x00000000 0x00000000

## Slide 56: Switch Statements on the Shark Machines
Ultimately, the target address is equal to the %rip + the offset to the start of jump table, plus an offset (possibly negative) from the start of the jump table to the target code.
  This target address is computed, placed into the %rax, and jumped to
# Get a pointer to the jump table
# %rip points to next addr, so %rdx becomes 0x498018 (jump table)
0x00000000004017ee <+46>: lea 0x96823(%rip),%rdx
# Get offset from %rsi-th index of jump table
0x00000000004017f5 <+53>: movslq (%rdx,%rsi,4),%rax
# Add that offset to the address of the jump table
0x00000000004017f9 <+57>: add %rdx,%rax
# Jump to that address, ultimately an offset from %rip
0x00000000004017fc <+60>: jmp *%rax

## Slide 57: Summarizing
C Control
  if-then-else
  do-while
  while, for
  switch
Assembler Control
  Conditional jump
  Conditional move
  Indirect jump (via jump tables)
  Compiler generates code sequence to implement more complex control
Standard Techniques
  Loops converted to do-while or jump-to-middle form
  Large switch statements use jump tables
  Sparse switch statements may use decision trees (if-elseif-elseif-else)

## Slide 58: Summary
Today
  Control: Condition codes
  Conditional branches & conditional moves
  Loops
  Switch statements
Next Time
  Stack
  Call / return
  Procedure call discipline