## Slide 1: Run-time support for adaptive heavyweight services
Julio López & David O’Hallaron {jclopez,droh}@cs.cmu.edu
Carnegie Mellon University
Notes: TODO:
Outline
Scheduling code
Active frame interface
Tables with results
Graphs

## Slide 2: Main points
Need for flexible scheduling.
Feasible framework.
Reasonable cost.

## Slide 3: Outline
Motivation.
  Heavyweight services.
  Quakeviz.
Active frame.
Scheduling with active frames.
Evaluation.

## Slide 4: Motivation
Lightweight services: Small amounts of computation at the servers.
Heavyweight services:
  Advanced information retrieval algorithms.
  Data mining.
  Remote visualization.

## Slide 5: Quakeviz
Jacobo Bielak and Omar Ghattas (CMU CE)
David O’Hallaron (CMU CS and ECE)
Jonathan Shewchuk (UC-Berkeley)
Steven Day (SDSU Geology)
http://www.cs.cmu.edu/~quake
Visualization of datasets generated by the Quake project at CMU.
Simulation data of the ground motion of large basins during strong earthquakes.
40 GB - 6 TB depending on degree of downsampling.
Notes: The quake project developed a methodology to simulate earthquakes.
produces enormous data-sets .
In order to to debug the simulation process, analyze the data (detect patterns, behavior, etc) it is useful to visualize the data.
We want to visualize them.

## Slide 6: Visualization
remote
database
Extract ROI
isosurface
extraction
scene
synthesis
local
display
and
input
rendering
reading
solver
engine
materials
database
Seq. #
ROI
contours
scene
vtk routines
Structure
Displacement data

## Slide 7: Quakeviz scenario
Best-effort WAN
Dataset
Compute server
Remote site
High end workstation
Local site
Desktop
Local site
Laptop
Resources are limited.
Resources are heterogeneous.

## Slide 8: Approaches for providing remote viz services
Ultrahigh
Bandwidth
Link
Low-end remote server
Powerful local workstation
Do everything at the local site.
  Pros: low latency, easy to grid-enable existing packages.
  Cons: requires high-bandwidth link between sites, requires powerful compute and graphics resources at the local site.

## Slide 9: Approaches for providing remote viz services
Do everything on the remote server:
  Pros: very simple to grid enable existing packages.
  Cons: high latency, eliminates possibility of proxying and caching at local site, can overuse remote site, not appropriate for smaller datasets.
Moderate
Bandwidth
Link
Very high-end remote server
Local
machine

## Slide 10: Approaches for providing remote viz services
Do everything but the rendering on the remote server:
  Pros: fairly simply to grid-enable existing packages, removes some load from the remote site, in most cases it minimizes the bandwidth requirements between the local and the remote site.
  Cons: requires every local site to have good rendering power.
High-end remote
server
Machine with good rendering power
Moderate
bandwidth
Link

## Slide 11: Approaches for providing remote viz services
High
bandwidth
link
High-end remote
server
Low-end local
PC or PDA
Moderate
bandwidth
link
Powerful local proxy server
Use a local proxy for the rendering:
  Pros: offloads work from the remote site, allows local sites to contribute additional resources.
  Cons: local sites may not have sufficiently powerful proxy resources, application is more complex, requires high bandwidth between local and remote sites.

## Slide 12: Challenges
Resources are:
  Limited.
  Heterogeneous.
  Dynamic.
Application’s resource usage is dynamic.

## Slide 13: Heavyweight service requirements
Best-effort WAN
Local site
Dataset
Local site
Remote site
High end workstation
Contribute and aggregate resources.
Performance-portable.

## Slide 14: Main points
Need for flexible scheduling.
Feasible framework.
Reasonable cost.

## Slide 15: Active frame
interface ActiveFrame { HostAddress execute(ServerState state); }
Form of mobile object that carries data and a program to operate on the data.
Frame
data
Frame
program

## Slide 16: Active frame
Active
Frame
Server
Frame
Active
Frame
Server
Active
Frame
Server
Frame
Frame
Execute frame
Frame
Transfer frame
Frame
Transfer frame
TCP stream
TCP stream

## Slide 17: Active frame
Input Active Frame
Frame
data
Frame
program
Frame thread
Active frame
interpreter
Application libraries
e.g, vtk
Active Frame Server
Host
Control thread
Frame thread
Output Active Frame
Frame
data
Frame
program
Frame thread
Frame
data
Frame
program
Execute
TCP stream

## Slide 18: Remote viz service with active frames
Best-effort WAN
Local site
Dataset
Local site
Remote site
Request
Response
Response
Response

## Slide 19: Overview of a Dv visualization service
Dv
Server
Remote DV Active Frame Servers
Local DV Active Frame Servers
Response
frames
Dv
Server
Dv
Server
Response
frames
...
Request frames
Response
frames
User
inputs/
Display
Response
frames
Dv
Server
Local
Dv
client
Remote
datasets

## Slide 20: Dv frames processing
reader
local
Dv
client
response frames (to other Dv servers)
[app. data, scheduler, flowgraph,control ]
request frame
[request server, scheduler, flowgraph, data reader ]
request server
remote machine
...
local
Dv
server
scheduler
result
...
local machine
(Dv client)

## Slide 21: Scheduling active frames
interface Scheduler { HostAddress getHost(int hopCount); }
Returns the host’s address to execute a task.
Application defined scheduling policies.
Can use resource information: CMU’s Remos/RPS or UCSD/Tennessee’s Network Weather Service.

## Slide 22: Scheduling active frames
Output Active Frame
Frame thread
Frame
data
Frame
program
Scheduler
Active frame
interpreter
Application libraries
e.g, vtk
Active Frame Server
Host
Control thread
TCP stream
Frame thread
Input Active Frame
Frame
data
Frame
program
Scheduler
Frame thread
Frame
data
Frame
program
Scheduler
getHost()
?
Execute
Frame
data
Frame
program
Scheduler

## Slide 23: Static scheduling
Best-effort WAN
Local site
Dataset
Local site
Remote site
Same host assignment for all frames.
Exploits application-specific info.
Cannot adapt to dynamic resource changes.
Frame
Frame
Frame
Frame
Frame
Frame
?
Request

## Slide 24: Scheduling at frame creation time
Best-effort WAN
Local site
Dataset
Local site
Remote site
Use dynamic resource data.
Adaptation occurs at the source.
Frame
Frame
Frame
Frame
Frame
Frame
?
?
Request

## Slide 25: Scheduling at frame delivery time
Best-effort WAN
Local site
Dataset
Local site
Remote site
React to changing conditions even in flight.
Highest degree of adaptation.
Added complexity, might introduce significant overhead.
Frame
Frame
Frame
Frame
Frame
Request
Frame
?
Frame
?
Frame
?
Frame
?

## Slide 26: Main points
Need for flexible scheduling.
Feasible framework.
Reasonable cost.

## Slide 27: Evaluation

## Slide 28: Dataset
183.equake (SPEC CPU2000) ground motion dataset.
Unstructured tetrahedral mesh.
30,000 nodes (points).
151,000 tetrahedral elements.
165 frames with ground displacement data (aprox. 40 secs of shaking).
Each data frame = 120 KB.

## Slide 29: Single host setup
Read
Extract
ROI
Isosurfaces
Simulation output
Scene
Rendering
Display
Local machine
Animation of the earthquake data.
Single host Sequential C++ version.
Pentium III/450 MHz.
512 MB RAM.
Real 3D Starfighter AGP/8MB video accelarator.
NT 4.0/ OpenGL.

## Slide 30: Single host setup
Isosurfaces | 10 | 20 | 50
Operation | (ms) | (ms) | (ms)
Read frame data | 584.35 | 582.65 | 586.13
Isosurface extraction | 1044.37 | 1669.73 | 3562.36
Rendering | 55.72 | 63.73 | 125.77
Total | 1684.44 | 2316.11 | 4274.26
FPS | 0.59 | 0.43 | 0.23

## Slide 31: Single host elapsed time
100% CPU usage.
No I/O to overlap with.
Isosurface extraction accounts for 60 – 80% total time.
Application parameters determine resource usage.

## Slide 32: Single host frames per second
Not a smooth animation.
Does not allow for interaction.
Insufficient resources.

## Slide 33: Pipeline setup
Extract
ROI
Isosurfaces
Simulation output
Source server
100 Mb Switched Ethernet
10 Mb Ethernet
Read
Scene
Rendering
Display
Compute server
Dv client
Same display client and datasets.
Servers:
  Pentium III/550 MHz.
  256 MB RAM.
  Linux kernel 2.0.36.
  Blackdown JDK 1.2 RC1.

## Slide 34: Pipeline elapsed times
Isosurfaces Operation | 10 (ms) | 20 (ms) | 50 (ms)
Read Frame Data | 286.21 | 285.98 | 287.11
Program transfer (s-s) | 110.14 | 94.47 | 86.51
Data transfer (s-s) | 118.88 | 116.92 | 119.52
Isosurface extraction | 696.43 | 1152.03 | 2561.41
Program transfer (s-c) | 39.54 | 44.13 | 46.40
Polys transfer (s-c) | 175.10 | 435.66 | 1700.59
Render | 64.99 | 162.32 | 340.40
Total | 1491.29 | 2291.51 | 5141.95

## Slide 35: Pipeline elapsed times
Need to exploit dynamic application-level information.
Automate resource selection.
Compute server is heavily loaded.
Program transfer 5-10% .
Reasonable cost.

## Slide 36: Pipeline Throughput
 | Processing time |  |  | Frames per second |  | 
#isos | 10 | 20 | 50 | 10 | 20 | 50
Source | 515.23 | 497.37 | 493.15 | 1.94 | 2.01 | 2.03
Server | 1140.09 | 1843.21 | 4514.44 | 0.88 | 0.54 | 0.22
Client | 279.63 | 642.11 | 2087.40 | 3.58 | 1.56 | 0.48
Max frame rate |  |  |  | 0.88 | 0.54 | 0.22

## Slide 37: Frames per second
Significant improvement for 10 and 20 isosurfaces.
Added bonus: user interaction.
Resource aggregation.
Scheduling matters.

## Slide 38: Fan setup
Isosurfaces
Source server
100 Mb Switched Ethernet
10 Mb Ethernet
Read
Rendering
Display
Compute server
Dv client
Extract
ROI
Scene
Isosurfaces
Compute server
Isosurfaces
Compute server
Simulation output

## Slide 39: Fan elapsed times
Isosurfaces Operation | 10 (ms) | 20 (ms) | 50 (ms)
Read Frame Data | 283.46 | 283.58 | 284.52
Program transfer (s-s) | 13.61 | 15.09 | 17.73
Data transfer (s-s) | 116.36 | 116.18 | 115.99
Isosurface extraction | 677.09 | 1098.01 | 2384.19
Program transfer (s-c) | 65.26 | 83.47 | 173.76
Polys transfer (s-c) | 337.45 | 434.13 | 1899.29
Render | 123.24 | 183.44 | 271.99
Total | 1616.47 | 2213.88 | 5147.48

## Slide 40: Fan elapsed times
Client is busy receiving and rendering frames.
Program transfer below 5%.
Reasonable cost.

## Slide 41: Fan Throughput
 | Processing time |  |  | Frames per second |  | 
#isos | 10 | 20 | 50 | 10 | 20 | 50
Source | 413.43 | 414.85 | 418.24 | 2.42 | 2.41 | 2.39
Server | 1209.77 | 1746.87 | 4590.96 | 2.48 | 1.72 | 0.65
Client | 525.96 | 701.03 | 2345.04 | 1.90 | 1.43 | 0.43
Max frame rate |  |  |  | 1.90 | 1.43 | 0.43

## Slide 42: Frames per second
Improvement in all cases.
Smother animations.
Benefits of resource aggregation.
Scheduling matters.

## Slide 43: Summary
In order to provide heavyweight services we must build them so they are performance-portable.
It is feasible to build a flexible mechanism to support heavyweight services.
Active frames supports various levels of adaptivity.
Services obtain the benefits of resource aggregation.

## Slide 44: Related work
AppLeS (SDSC/UCSD).
Active messages (Berkeley). Active networks (MIT).
Remos/RPS (CMU). NWS (SDSC/UCSD).

## Slide 45: Conclusions
Need for flexible scheduling.
Feasible framework.
Reasonable cost.
Need to:
  Exploit application-level dynamic data.
  Use resource dynamic data.
  Automate resource selection.
http://www.cs.cmu.edu/~dv

## Slide 46: More information
http://www.cs.cmu.edu/~dv