## Slide 1: Machine Learning for Signal Processing Lecture 1: Introduction Representing sound and images
Class 1. 20 Jan 2015
Instructor: Bhiksha Raj
TA: Pallavi Baljekar

## Slide 2: What is a signal
A mechanism for conveying information
  Semaphores, gestures, traffic lights..
Electrical engineering: currents, voltages
Digital signals: Ordered collections of numbers that convey information
  from a source to a destination
  about a real world phenomenon
    Sounds, images

## Slide 3: Signal Examples: Audio
A sequence of numbers
  [n1 n2 n3 n4 …]
  The order in which the numbers occur is important
    Ordered
    In this case, a time series
  Represent a perceivable sound

## Slide 4: Example: Images
A rectangular arrangement (matrix) of numbers
  Or sets of numbers (for color images)
Each pixel represents a visual representation of one of these numbers
  0 is minimum / black, 1 is maximum / white
  Position / order is important
Pixel = 0.5

## Slide 5: Example: Biosignals
Biosignals
  MRI: “k-space”  3D Fourier transform
    Invert to get image
  EEG: Many channels of brain electrical activity
  ECG: Cardiac activity
  OCT, Ultrasound, Echo cardiogram: Echo-based imaging
  Others..
Challenges: denoising, prediction, classification..
MRI
EEG
ECG
Optical Coherence Tomography

## Slide 6: Financial Data
Stocks, options, other derivatives
Analyze trends and make predictions
Recent special issue:
  IEEE Journal of Selected Topics in Signal Processing, Aug 2012: Introduction to the Issue on Signal Processing Methods in Finance and Electronic Trading

## Slide 7: Ebb and flow of Movie revenues
Link to NYT page

## Slide 8: 4D signal

## Slide 9: Sinusoids

## Slide 10: Human Vocal Tract

## Slide 11: Physical Model

## Slide 12: Newer Physical Model

## Slide 13: Many others
Network data..
Weather..
Any stochastic time series
Etc.

## Slide 14: What is Signal Processing
Acquisition, Analysis, Interpretation, and Manipulation of signals.
  Acquisition: Sampling, sensing
  Decomposition: Fourier transforms, wavelet transforms, dictionary-based representations, PCA/NMF/ICA/PLSA/..
  Denoising signals
  Coding: GSM, Jpeg, Mpeg, Ogg Vorbis
  Detection: Radars, Sonars
  Pattern matching: Biometrics, Iris recognition, finger print recognition
  Prediction
  Etc.

## Slide 15: The Tasks in a typical Signal Processing Paradigm
Capture: Recovery, enhancement
Channel: Coding-decoding, compression-decompression, storage
Regression: Prediction, classification
Signal Capture
Feature Extraction
Channel
Modeling/Regression
sensor

## Slide 16: What is Machine Learning
The science that deals with the development of algorithms that can learn from data
  Learning patterns in data
    Automatic categorization of text into categories; Market basket analysis
  Learning to classify between different kinds of data
    Spam filtering: Valid email or junk?
  Learning to predict data
    Weather prediction, movie recommendation
Statistical analysis and pattern recognition when performed by a computer scientist..

## Slide 17: MLSP
Application of Machine Learning techniques to the analysis of signals
Can be applied to each component of the chain
Signal Capture
Feature Extraction
Channel
Modeling/Regression
sensor

## Slide 18: MLSP
Application of Machine Learning techniques to the analysis of signals
Can be applied to each component of the chain
Sensing
  Compressed sensing, dictionary based representations
Denoising
  ICA, filtering, separation
Signal Capture
Feature Extraction
Channel
Modeling/Regression
sensor

## Slide 19: MLSP
Application of Machine Learning techniques to the analysis of signals
Can be applied to each component of the chain
Channel: Compression, coding
Signal Capture
Feature Extraction
Channel
Modeling/Regression
sensor

## Slide 20: MLSP
Application of Machine Learning techniques to the analysis of signals
Can be applied to each component of the chain
Feature Extraction:
  Dimensionality reduction
    Linear models, non-linear models
Signal Capture
Feature Extraction
Channel
Modeling/Regression
sensor

## Slide 21: MLSP
Application of Machine Learning techniques to the analysis of signals
Can be applied to each component of the chain
Classification, Modelling and Interpretation, Prediction
Signal Capture
Feature Extraction
Channel
Modeling/Regression
sensor

## Slide 22: In this course
Jetting through fundamentals:
  Linear Algebra, Signal Processing, Probability
Machine learning concepts
  Methods of modelling, estimation, classification, prediction
Applications:
  Representation
  Sensing and recovery
  Prediction and Classification
  Sounds, Images, Other forms of data
Topics covered are representative

## Slide 23: Recommended Background
DSP
  Fourier transforms, linear systems, basic statistical signal processing
Linear Algebra
  Definitions, vectors, matrices, operations, properties
Probability
  Basics: what is an random variable, probability distributions, functions of a random variable
Machine learning
  Learning, modelling and classification techniques

## Slide 24: Schedule of Other Lectures
Tentative Schedule on Website
http://mlsp.cs.cmu.edu/courses/spring2015

## Slide 25: Grading
Homework assignments : 50%
  Mini projects
  Will be assigned during course
  Minimum 3, Maximum 4
  You will not catch up if you slack on any homework
    Those who didn’t slack will also do the next homework
  Attendance counts..
Final project: 50%
  Will be assigned early in course
  May 5: Poster presentation for all projects, with demos (if possible)

## Slide 26: Instructor and TA
Instructor: Prof. Bhiksha Raj
  Room 6705 Hillman Building
  bhiksha@cs.cmu.edu
  412 268 9826
TA:
  Pallavi Baljekar
    pbaljeka@cs.cmu.edu
Office Hours:
  Bhiksha Raj: Wed 1-2.00
  TA: TBD
Hillman
Windows
My office
Forbes

## Slide 27: Additional Administrivia
Website:
  http://mlsp.cs.cmu.edu/courses/spring2015/
  Lecture material will be posted on the day of each class on the website
  Reading material and pointers to additional information will be on the website
Mailing list: Piazza

## Slide 28: Representing Data
Audio
Images
  Video
Other types of signals
  In a manner similar to one of the above

## Slide 29: What is an audio signal
A typical digital audio signal
  It’s a sequence of points

## Slide 30: Where do these numbers come from?
Any sound is a pressure wave: alternating highs and lows of air pressure moving through the air
When we speak, we produce these pressure waves
  Essentially by producing puff after puff of air
  Any sound producing mechanism actually produces pressure waves
These pressure waves move the eardrum
  Highs push it in, lows suck it out
  We sense these motions of our eardrum as “sound”
Pressure highs
Spaces between arcs show pressure
lows

## Slide 31: SOUND PERCEPTION

## Slide 32: Storing pressure waves on a computer
The pressure wave moves a diaphragm
  On the microphone
The motion of the diaphragm is converted to continuous variations of an electrical signal
  Many ways to do this
A “sampler” samples the continuous signal at regular intervals of time and stores the numbers

## Slide 33: Are these numbers sound?
How do we even know that the numbers we store on the computer have anything to do with the recorded sound really?
  Recreate the sense of sound
The numbers are used to control the levels of an electrical signal
The electrical signal moves a diaphragm back and forth to produce a pressure wave
  That we sense as sound
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*

## Slide 34: Are these numbers sound?
How do we even know that the numbers we store on the computer have anything to do with the recorded sound really?
  Recreate the sense of sound
The numbers are used to control the levels of an electrical signal
The electrical signal moves a diaphragm back and forth to produce a pressure wave
  That we sense as sound
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*

## Slide 35: How many samples a second
Convenient to think of sound in terms of sinusoids with frequency
Sounds may be modelled as the sum of many sinusoids of different frequencies
  Frequency is a physically motivated unit
  Each hair cell in our inner ear is tuned to specific frequency
Any sound has many frequency components
  We can hear frequencies up to 16000Hz
    Frequency components above 16000Hz can be heard by children and some young adults
    Nearly nobody can hear over 20000Hz.
0
10
20
30
40
50
60
70
80
90
100
-1
-0.5
0
0.5
1
Pressure 
A sinusoid

## Slide 36: Signal representation - Sampling
Sampling frequency (or sampling rate) refers to the number of samples taken a second
Sampling rate is measured in Hz
  We need a sample rate twice as high as the highest frequency we want to represent (Nyquist freq)
For our ears this means a sample rate of at least 40kHz
  Because we hear up to 20kHz
*
*
*
*
*
*
*
*
*
*
*
*
*
Time in secs.

## Slide 37: Aliasing
Low sample rates result in aliasing
  High frequencies are misrepresented
  Frequency f1 will become (sample rate – f1 )
  In video also when you see wheels go backwards

## Slide 38: Aliasing examples
Time
Frequency
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
0
0.5
1
1.5
2
x 10
4
Time
Frequency
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
0
2000
4000
6000
8000
10000
Time
Frequency
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
0
1000
2000
3000
4000
5000
Sinusoid sweeping from 0Hz to 20kHz
44.1kHz SR, is ok
22kHz SR, aliasing!
11kHz SR, double aliasing!
On real sounds
at 44kHz
at 22kHz
at 11kHz
at 5kHz
at 4kHz
at 3kHz
On video
On images

## Slide 39: Avoiding Aliasing
Sound naturally has all perceivable frequencies
  And then some
  Cannot control the rate of variation of pressure waves in nature
Sampling at any rate will result in aliasing
Solution: Filter the electrical signal before sampling it
  Cut off all frequencies above sampling.frequency/2
  E.g., to sample at 44.1Khz, filter the signal to eliminate all frequencies above 22050 Hz
Antialiasing Filter
Sampling
Analog signal
Digital signal

## Slide 40: Typical Sampling Rates
Common sample rates
  For speech 8kHz to 16kHz
  For music 32kHz to 44.1kHz
  Pro-equipment 96kHz

## Slide 41: Storing numbers on the Computer
Sound is the outcome of a continuous range of variations
  The pressure wave can take any value (within limits)
  The diaphragm can also move continuously
  The electrical signal from the diaphragm has continuous variations
A computer has finite resolution
  Numbers can only be stored to finite resolution
  E.g. a 16-bit number can store only 65536 values, while a 4-bit number can store only 16 values
  To store the sound wave on the computer, the continuous variation must be “mapped” on to the discrete set of numbers we can store

## Slide 42: Mapping signals into bits
Example of 1-bit sampling table
Signal Value | Bit sequence | Mapped to
S > 2.5v | 1 | 1 * const
S <=2.5v | 0 | 0
Original Signal
Quantized approximation

## Slide 43: Mapping signals into bits
Example of 2-bit sampling table
Signal Value | Bit sequence | Mapped to
S >= 3.75v | 11 | 3 * const
3.75v > S >= 2.5v | 10 | 2 * const
2.5v > S >= 1.25v | 01 | 1 * const
1.25v > S >= 0v | 0 | 0
Original Signal
Quantized approximation

## Slide 44: Storing the signal on a computer
The original signal
8 bit quantization
3 bit quantization
2 bit quantization
1 bit quantization

## Slide 45: Tom Sullivan Says his Name
16 bit sampling
5 bit sampling
4 bit sampling
3 bit sampling
1 bit sampling

## Slide 46: A Schubert Piece
16 bit sampling
5 bit sampling
4 bit sampling
3 bit sampling
1 bit sampling

## Slide 47: Quantization Formats
Sampling can be uniform
  Sample values equally spaced out
Or nonuniform
Signal Value | Bits | Mapped to
S >= 3.75v | 11 | 3 * const
3.75v > S >= 2.5v | 10 | 2 * const
2.5v > S >= 1.25v | 01 | 1 * const
1.25v > S >= 0v | 0 | 0
Signal Value | Bits | Mapped to
S >= 4v | 11 | 4.5 * const
4v > S >= 2.5v | 10 | 3.25 * const
2.5v > S >= 1v | 01 | 1.25 * const
1.0v > S >= 0v | 0 | 0.5 * const

## Slide 48: Uniform Quantization
At the sampling instant, the actual value of the waveform is rounded off to the nearest level permitted by the quantization
Values entirely outside the range are quantized to either the highest or lowest values

## Slide 49: Non-uniform Quantiztion
Quantization levels are non-uniformly spaced
At the sampling instant, the actual value of the waveform is rounded off to the nearest level permitted by the quantization
Values entirely outside the range are quantized to either the highest or lowest values
Original
Uniform
Nonuniform

## Slide 50: Uniform Quantization
UPON BEING SAMPLED AT ONLY 3 BITS (8 LEVELS)

## Slide 51: Uniform Quantization
There is a lot more action in the central region than outside.
Assigning only four levels to the busy central region and four entire levels to the sparse outer region is inefficient
Assigning more levels to the central region and less to the outer region can give better fidelity
  for the same storage

## Slide 52: Non-uniform Quantization
Assigning more levels to the central region and less to the outer region can give better fidelity for the same storage

## Slide 53: Non-uniform Quantization
Assigning more levels to the central region and less to the outer region can give better fidelity for the same storage
Uniform
Non-uniform

## Slide 54: Non-uniform Sampling
Uniform sampling maps uniform widths of the analog signal to units steps of the quantized signal
In “standard” non-uniform sampling the step sizes are smaller near 0 and wider farther away
  The curve that the steps are drawn on follow a logarithmic law:
    Mu Law: Y = C. log(1 + mX/C)/(1+m)
    A Law: Y = C. (1 + log(a.X)/C)/(1+a)
One can get the same perceptual effect with 8bits of non-uniform sampling as 12bits of uniform sampling
Nonlinear
Uniform
Analog value
quantized value
Analog value
quantized value

## Slide 55: Dealing with audio
Capture / read audio in the format provided by the file or hardware
  Linear PCM, Mu-law, A-law,
Convert to 16-bit PCM value
  I.e. map the bits onto the number on the right column
  This mapping is typically provided by a table computed from the sample compression function
  No lookup for data stored in PCM
Conversion from Mu law:
  http://www.speech.cs.cmu.edu/comp.speech/Section2/Q2.7.html
Signal Value | Bits | Mapped to
S >= 3.75v | 11 | 3
3.75v > S >= 2.5v | 10 | 2
2.5v > S >= 1.25v | 01 | 1
1.25v > S >= 0v | 0 | 0
Signal Value | Bits | Mapped to
S >= 4v | 11 | 4.5
4v > S >= 2.5v | 10 | 3.25
2.5v > S >= 1v | 01 | 1.25
1.0v > S >= 0v | 0 | 0.5

## Slide 56: Images

## Slide 57: Images

## Slide 58: The Eye
Basic Neuroscience: Anatomy and Physiology Arthur C. Guyton, M.D. 1987 W.B.Saunders Co.
Retina

## Slide 59: The Retina
http://www.brad.ac.uk/acad/lifesci/optometry/resources/modules/stage1/pvp1/Retina.html

## Slide 60: Rods and Cones
Separate Systems
Rods
  Fast
  Sensitive
  Grey scale
  predominate in the periphery
Cones
  Slow
  Not so sensitive
  Fovea / Macula
  COLOR!
Basic Neuroscience: Anatomy and Physiology Arthur C. Guyton, M.D. 1987 W.B.Saunders Co.

## Slide 61: The Eye
The density of cones is highest at the fovea
  The region immediately surrounding the fovea is the macula
    The most important part of your eye: damage == blindness
Peripheral vision is almost entirely black and white
Eagles are bifoveate
Dogs and cats have no fovea, instead they have an elongated slit

## Slide 62: Spatial Arrangement of the Retina
(From Foundations of Vision, by Brian Wandell, Sinauer Assoc.)

## Slide 63: Three Types of Cones (trichromatic vision)
Wavelength in nm
Normalized reponse

## Slide 64: Trichromatic Vision
So-called “blue” light sensors respond to an entire range of frequencies
  Including in the so-called “green” and “red” regions
The difference in response of “green” and “red” sensors is small
  Varies from person to person
    Each person really sees the world in a different color
  If the two curves get too close, we have color blindness
    Ideally traffic lights should be red and blue

## Slide 65: White Light

## Slide 66
Response to White Light
?

## Slide 67: Response to White Light

## Slide 68: Response to Sparse Light
?

## Slide 69: Response to Sparse Light

## Slide 70: Human perception anomalies
The same intensity of monochromatic light will result in different perceived brightness at different wavelengths
Many combinations of wavelengths can produce the same sensation of colour.
Yet humans can distinguish 10 million colours
Dim
Bright

## Slide 71: Representing Images
Utilize trichromatic nature of human vision
  Sufficient to trigger each of the three cone types in a manner that produces the sensation of the desired color
    A tetrachromatic animal would be very confused by our computer images
      Some new-world monkeys are tetrachromatic
The three “chosen” colors are red (650nm), green (510nm) and blue (475nm)
  By appropriate combinations of these colors, the cones can be excited to produce a very large set of colours
    Which is still a small fraction of what we can actually see
  How many colours? …

## Slide 72: The “CIE” colour space
From experiments done in the 1920s by W. David Wright and John Guild
  Subjects adjusted x,y,and z on the right of a circular screen to match a colour on the left
X, Y and Z are normalized responses of the three sensors
  X + Y + Z is 1.0
    Normalized to have to total net intensity
The image represents all colours we can see
  The outer curve represents monochromatic light
    X,Y and Z as a function of l
  The lower line is the line of purples
    End of visual spectrum
The CIE chart was updated in 1960 and 1976
  The newer charts are less popular
International council on illumination, 1931

## Slide 73: What is displayed
The RGB triangle
  Colours outside this area cannot be matched by additively combining only 3 colours
    Any other set of monochromatic colours would have a differently restricted area
    TV images can never be like the real world
Each corner represents the (X,Y,Z) coordinate of one of the three “primary” colours used in images
In reality, this represents a very tiny fraction of our visual acuity
  Also affected by the quantization of levels of the colours

## Slide 74: Representing Images on Computers
Greyscale: a single matrix of numbers
  Each number represents the intensity of the image at a specific location in the image
  Implicitly, R = G = B at all locations
Color: 3 matrices of numbers
  The matrices represent different things in different representations
  RGB Colorspace: Matrices represent intensity of Red, Green and Blue
  CMYK Colorspace: Cyan, Magenta, Yellow
  YIQ Colorspace..
  HSV Colorspace..

## Slide 75: Computer Images: Grey Scale
Picture Element (PIXEL)
Position & gray value (scalar)
R = G = B. Only a single number need be stored per pixel

## Slide 76
10
10
What we see
What the computer “sees”

## Slide 77: Color Images
Picture Element (PIXEL)
Position & color value (red, green, blue)

## Slide 78: RGB Representation
original
R
B
G
R
B
G

## Slide 79: RGB Manipulation Example: Color Balance
original
R
B
G
R
B
G

## Slide 80: The CMYK color space
Represent colors in terms of cyan, magenta, and yellow
  The “K” stands for “Key”, not “black”
Blue

## Slide 81: CMYK is a subtractive representation
RGB is based on composition, i.e. it is an additive representation
  Adding equal parts of red, green and blue creates white
What happens when you mix red, green and blue paint?
  Clue – paint colouring is subtractive..
CMYK is based on masking, i.e. it is subtractive
  The base is white
  Masking it with equal parts of C, M and Y creates Black
  Masking it with C and Y creates Green
    Yellow masks blue
  Masking it with M and Y creates Red
    Magenta masks green
  Masking it with M and C creates Blue
    Cyan masks green
  Designed specifically for printing
    As opposed to rendering

## Slide 82: An Interesting Aside
Paints create subtractive coloring
  Each paint masks out some colours
  Mixing paint subtracts combinations of colors
  Paintings represent subtractive colour masks
In the 1880s Georges-Pierre Seurat pioneered an additive-colour technique for painting based on “pointilism”
  How do you think he did it?

## Slide 83: Quantization and Saturation
Captured images are typically quantized to N-bits
Standard value: 8 bits
8-bits is not very much < 1000:1
Humans can easily accept 100,000:1
And most cameras will give you 6-bits anyway…

## Slide 84: Processing Colour Images
Typically work only on the Grey Scale image
  Decode image from whatever representation to RGB
  GS = R + G + B
For specific algorithms that deal with colour, individual colours may be maintained
  Or any linear combination that makes sense may be maintained.

## Slide 85: Other Signals
Direct measurement (like sound):
  ECG, EMG, EKG
Indirect measurement (through a transform)
  MRI
    Takes measurements in the Fourier domain

## Slide 86: The General Theory of Sensing
Actual signal : y( j)
  j may be time, position, etc..
  Usually continuously valued
Captured value:
  ; Q is the space of all j
  K( j) is a measurement kernel
  Ideally a delta (which takes non-zero value only at the desired j)
    Captures actual snapshots
  But in reality not
    More on this later..

## Slide 87: Next Class..
Review of linear algebra..