## Slide 1: Radiometry and reflectance
16-385 Computer Vision
Spring 2019, Lecture 13
http://www.cs.cmu.edu/~16385/

## Slide 2: Course announcements
Homework 3 has been posted and is due on March 10th.
- Any questions about the homework?
- How many of you have looked at/started/finished homework 3?
Extra office hours today: Wednesday 6-8 pm, graphics lounge.

## Slide 3: Computer vision talks at CMU
VASC Seminar: https://www.ri.cmu.edu/events/category/vasc-seminar/month/
- VASC stands for Vision and Autonomous Systems Center (no idea).
- One of the longest-running and best-known departmental vision seminars.
Faculty candidate talks: https://www.ri.cmu.edu/events/
- Many vision talks this year.
- Some of the best our field has to offer – the rising stars of computer vision.
Jiajun Wu 3/7 10am NSH 3305
Jun-Yan Zhu 3/19 noon GHC 6115
Angjoo Kanazawa 3/21 10am GHC 6115
Abe Davis 3/25 2pm GHC 6115
Matthias Niessner 3/27 noon GHC 6115
Angela Dai 3/28 noon GHC 6115
Robotics Institute Seminar: https://www.ri.cmu.edu/events/category/robotics-seminar/month/
- Most of the time about robotic, but sometimes about vision.
Talks in other departments (MLD, CSD).

## Slide 4: Computer vision talks at CMU
Find all events: https://www.ri.cmu.edu/events/
I will be sending notifications on Piazza about vision talks.
I will also be starting discussion threads on Piazza about vision talks.
Attending and commenting on talks regularly can count towards an extra 5% credit.

## Slide 5: Overview of today’s lecture
Appearance phenomena.
Measuring light and radiometry.
Reflectance and BRDF.
Light sources.

## Slide 6: Slide credits
Most of these slides were adapted from:
Srinivasa Narasimhan (16-385, Spring 2014).
Todd Zickler (Harvard University).
Steven Gortler (Harvard University).

## Slide 7: Appearance

## Slide 8: Appearance
Notes: The problem becomes especially difficult when we allow ourselves to consider the full diversity of the materials that surround us.
Different materials reflect light in different ways, and while these differences in color, sheen, gloss, haze, and so on are what makes many pictures beautiful, they are also what makes them very hard to analyze radiometrically.

## Slide 9: “Physics-based” computer vision (a.k.a “inverse optics”)
reflectance
illumination
shape
shape
, reflectance
, illumination
Our challenge: Invent computational representations of shape, lighting, and reflectance that are efficient: simple enough to make inference tractable, yet general enough to capture the world’s most important phenomena
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 10: Example application: Photometric Stereo

## Slide 11: Why study the physics (optics) of the world? Lets see some pictures!

## Slide 12: Light and Shadows

## Slide 15: Reflections

## Slide 19: Refractions

## Slide 23: Interreflections

## Slide 25: Scattering

## Slide 29: More Complex Appearances

## Slide 35: Measuring light and radiometry

## Slide 36: Solid angle
The solid angle subtended by a small surface patch with respect to point O is the area of its central projection onto the unit sphere about O
Depends on:
  orientation of patch
  distance of patch

## Slide 37: Solid angle
The solid angle subtended by a small surface patch with respect to point O is the area of its central projection onto the unit sphere about O
Depends on:
  orientation of patch
  distance of patch
One can show:
Units: steradians [sr]

## Slide 38: Solid angle
The solid angle subtended by a small surface patch with respect to point O is the area of its central projection onto the unit sphere about O
Depends on:
  orientation of patch
  distance of patch
One can show:
“surface foreshortening”
Units: steradians [sr]

## Slide 39: Solid angle
To calculate solid angle subtended by a surface S relative to O you must add up (integrate) contributions from all tiny patches (nasty integral)
One can show:
“surface foreshortening”
Units: steradians [sr]

## Slide 40: Question
Suppose surface S is a hemisphere centered at O. What is the solid angle it subtends?

## Slide 41: Question
Suppose surface S is a hemisphere centered at O. What is the solid angle it subtends?
Answer: 2\pi (area of sphere is 4\pi*r^2; area of unit sphere is 4\pi; half of that is 2\pi)

## Slide 42: Quantifying light: flux, irradiance, and radiance
Imagine a sensor that counts photons passing through planar patch X in directions within angular wedge W
It measures radiant flux [watts = joules/sec]: rate of photons hitting sensor area
Measurement depends on sensor area |X|
radiant flux
* shown in 2D for clarity; imagine three dimensions

## Slide 43: Quantifying light: flux, irradiance, and radiance
Irradiance: A measure of incoming light that is independent of sensor area |X|
Units: watts per square meter [W/m2]

## Slide 44: Quantifying light: flux, irradiance, and radiance
Irradiance: A measure of incoming light that is independent of sensor area |X|
Units: watts per square meter [W/m2]

## Slide 45: Quantifying light: flux, irradiance, and radiance
Irradiance: A measure of incoming light that is independent of sensor area |X|
Units: watts per square meter [W/m2]
Depends on sensor direction normal.
We keep track of the normal because a planar sensor with distinct orientation would converge to a different limit
In the literature, notations n and W are often omitted, and values are implied by context

## Slide 46: Quantifying light: flux, irradiance, and radiance
Radiance: A measure of incoming light that is independent of sensor area |X|, orientation n, and wedge size (solid angle) |W|
Units: watts per steradian per square meter [W/(m2∙sr)]
Has correct units, but still depends on sensor orientation
To correct this, convert to measurement that would have been made if sensor was perpendicular to direction ω

## Slide 47: Quantifying light: flux, irradiance, and radiance
Radiance: A measure of incoming light that is independent of sensor area |X|, orientation n, and wedge size (solid angle) |W|
Units: watts per steradian per square meter [W/(m2∙sr)]
Has correct units, but still depends on sensor orientation
To correct this, convert to measurement that would have been made if sensor was perpendicular to direction ω
“foreshortened area”

## Slide 48: Quantifying light: flux, irradiance, and radiance
Radiance: A measure of incoming light that is independent of sensor area |X|, orientation n, and wedge size (solid angle) |W|
Units: watts per steradian per square meter [W/(m2∙sr)]
Has correct units, but still depends on sensor orientation
To correct this, convert to measurement that would have been made if sensor was perpendicular to direction ω

## Slide 49: Quantifying light: flux, irradiance, and radiance
Radiance: A measure of incoming light that is independent of sensor area |X|, orientation n, and wedge size (solid angle) |W|
Units: watts per steradian per square meter [W/(m2∙sr)]
Has correct units, but still depends on sensor orientation
To correct this, convert to measurement that would have been made if sensor was perpendicular to direction ω
“foreshortened in the direction of travel”

## Slide 50: Quantifying light: flux, irradiance, and radiance
Attractive properties of radiance:
  Allows computing the radiant flux measured by any finite sensor
Notes: \Phi(W,X)=\int_X\int_W L(\hat{\boldsymbol{\omega}},x)d\boldsymbol{\omega}dA

## Slide 51: Quantifying light: flux, irradiance, and radiance
Attractive properties of radiance:
  Allows computing the radiant flux measured by any finite sensor
Notes: \Phi(W,X)=\int_X\int_W L(\hat{\boldsymbol{\omega}},x)d\boldsymbol{\omega}dA

## Slide 52: Quantifying light: flux, irradiance, and radiance
Attractive properties of radiance:
  Allows computing the radiant flux measured by any finite sensor
  Constant along a ray in free space

## Slide 53: Quantifying light: flux, irradiance, and radiance
Attractive properties of radiance:
  Allows computing the radiant flux measured by any finite sensor
  Constant along a ray in free space
  A camera measures radiance (after a one-time radiometric calibration). So RAW pixel values are proportional to radiance.
  - “Processed” images (like PNG and JPEG) are not linear radiance measurements!!
Notes: Possible classroom question: A Lambertian planar light source (e.g., a heated metal sheet) is one whose radiant intensity is J(\omega)=J_o<N,\omega>. Show that emitted radiance is independent of \omega (and thus that the sheet looks equally bright from all directions)

## Slide 54: Question
Most light sources, like a heated metal sheet, follow Lambert’s Law
radiant intensity [W/sr]
“Lambertian area source”
What is the radiance of an infinitesimal patch [W/sr･m2]?
Notes: %%% latexit code
J(\hat{\boldsymbol{\omega}})=J_o\langle\hat{\boldsymbol{\omega}},\hat{\boldsymbol{n}}\rangle=J_o\cos\theta

## Slide 55: Question
Most light sources, like a heated metal sheet, follow Lambert’s Law
radiant intensity [W/sr]
“Lambertian area source”
Answer:
(independent of direction)
What is the radiance of an infinitesimal patch [W/sr･m2]?
Notes: %%% latexit code
J(\hat{\boldsymbol{\omega}})=J_o\langle\hat{\boldsymbol{\omega}},\hat{\boldsymbol{n}}\rangle=J_o\cos\theta

## Slide 56: Question
Most light sources, like a heated metal sheet, follow Lambert’s Law
radiant intensity [W/sr]
“Lambertian area source”
What is the radiance of an infinitesimal patch [W/sr･m2]?
Answer:
(independent of direction)
“Looks equally bright when viewed from any direction”
Notes: %%% latexit code
J(\hat{\boldsymbol{\omega}})=J_o\langle\hat{\boldsymbol{\omega}},\hat{\boldsymbol{n}}\rangle=J_o\cos\theta

## Slide 57
Radiometric concepts – boring…but, important!
(1) Solid Angle :
( steradian )
What is the solid angle subtended by a hemisphere?
(solid angle subtended by )
(foreshortened area)
(surface area)
(2) Radiant Intensity of Source :
Light Flux (power) emitted per unit solid angle
( watts / steradian )
(3) Surface Irradiance :
( watts / m )
Light Flux (power) incident per unit surface area.
Does not depend on where the light is coming from!
source
2
(4) Surface Radiance (tricky) :
(watts / m steradian )
Flux emitted per unit foreshortened area
per unit solid angle.
L depends on direction
Surface can radiate into whole hemisphere.
L depends on reflectance properties of surface.

## Slide 58: Appearance
Notes: The problem becomes especially difficult when we allow ourselves to consider the full diversity of the materials that surround us.
Different materials reflect light in different ways, and while these differences in color, sheen, gloss, haze, and so on are what makes many pictures beautiful, they are also what makes them very hard to analyze radiometrically.

## Slide 59: “Physics-based” computer vision (a.k.a “inverse optics”)
reflectance
illumination
shape
shape
, reflectance
, illumination
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 60: Reflectance and BRDF

## Slide 61: Reflectance
Ratio of outgoing energy to incoming energy at a single point
Want to define a ratio such that it:
  converges as we use smaller and smaller incoming and outgoing wedges
  does not depend on the size of the wedges (i.e. is intrinsic to the material)
Notes: f_{x,\hat{\bf n}}(W_\text{in},\hat{\boldsymbol{\omega}}_\text{out})=\frac{L^\text{out}(x,\hat{\boldsymbol{\omega}}_\text{out})}{E_{\hat{\bf n}}^\text{in}(W_\text{in},x)}
\lim_{W_\text{in}\longrightarrow \hat{\boldsymbol{w}}_\text{in}}
f_{x,\hat{\bf n}}(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})

## Slide 62: Reflectance
Ratio of outgoing energy to incoming energy at a single point
Want to define a ratio such that it:
  converges as we use smaller and smaller incoming and outgoing wedges
  does not depend on the size of the wedges (i.e. is intrinsic to the material)
Notations x and n often implied by context and omitted; directions \omega are expressed in local coordinate system defined by normal n (and some chosen tangent vector)
Units: sr-1
Called Bidirectional Reflectance Distribution Function (BRDF)
Notes: f_{x,\hat{\bf n}}(W_\text{in},\hat{\boldsymbol{\omega}}_\text{out})=\frac{L^\text{out}(x,\hat{\boldsymbol{\omega}}_\text{out})}{E_{\hat{\bf n}}^\text{in}(W_\text{in},x)}
\lim_{W_\text{in}\longrightarrow \hat{\boldsymbol{w}}_\text{in}}
f_{x,\hat{\bf n}}(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})

## Slide 63
BRDF: Bidirectional Reflectance Distribution Function
x
y
z
source
viewing
direction
surface
element
normal
incident
direction
Irradiance at Surface in direction
Radiance of Surface in direction
BRDF :

## Slide 64: Reflectance: BRDF
Units: sr-1
Real-valued function defined on the double-hemisphere
Has many useful properties
Notes: f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})
f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})=f(\hat{\boldsymbol{\omega}}_\text{out},\hat{\boldsymbol{\omega}}_\text{in})
\forall \hat{\boldsymbol{\omega}}_\text{in},\ \ \int_{\Omega_\text{out}} f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})\cos\theta_\text{out}d\hat{\boldsymbol{\omega}}_\text{out}\le 1

## Slide 65
Important Properties of BRDFs
x
y
z
source
viewing
direction
surface
element
normal
incident
direction
Conservation of Energy:
Why smaller than or equal?

## Slide 66: Property: “Helmholtz reciprocity”
Helmholtz Reciprocity: (follows from 2nd Law of Thermodynamics)
BRDF does not change when source and viewing directions are swapped.
Notes: For example, a useful property of most opaque materials is that their reflectance function has a symmetry property known as reciprocity.
Reciprocity states that the BRDF is symmetric in terms of its input and output directions, so if we swap these directions, the BRDF value remain unchanged.

## Slide 67: Common assumption: Isotropy
Bi-directional Reflectance Distribution Function (BRDF)
4D → 3D
[Matusik et al., 2003]
Can be written as a function of 3 variables :
BRDF does not change when surface is rotated about the normal.
Notes: An isotropic BRDF is one that is:
- unchanged when the input is spun around the surface normal, and
- symmetric across the incident plane,
These symmetry conditions imply that the domain of an isotropic BRDF is three dimensional instead of four.
<animate> Returning to our problem...

## Slide 68: Useful re-parameterization of double-hemisphere
Notes: An isotropic BRDF is one that is:
- unchanged when the input is spun around the surface normal, and
- symmetric across the incident plane,
These symmetry conditions imply that the domain of an isotropic BRDF is three dimensional instead of four.
<animate> Returning to our problem...

## Slide 69: Useful re-parameterization of double-hemisphere
reciprocity
Notes: An isotropic BRDF is one that is:
- unchanged when the input is spun around the surface normal, and
- symmetric across the incident plane,
These symmetry conditions imply that the domain of an isotropic BRDF is three dimensional instead of four.
<animate> Returning to our problem...

## Slide 70: Useful re-parameterization of double-hemisphere
reciprocity
isotropy:
Notes: An isotropic BRDF is one that is:
- unchanged when the input is spun around the surface normal, and
- symmetric across the incident plane,
These symmetry conditions imply that the domain of an isotropic BRDF is three dimensional instead of four.
<animate> Returning to our problem...

## Slide 71: Reflectance: BRDF
Units: sr-1
Real-valued function defined on the double-hemisphere
Has many useful properties
Allows computing output radiance (and thus pixel value) for any configuration of lights and viewpoint
reflectance equation
Why is there a cosine in the reflectance equation?
Notes: f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})
f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})=f(\hat{\boldsymbol{\omega}}_\text{out},\hat{\boldsymbol{\omega}}_\text{in})
\forall \hat{\boldsymbol{\omega}}_\text{in},\ \ \int_{\Omega_\text{out}} f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})\cos\theta_\text{out}d\hat{\boldsymbol{\omega}}_\text{out}\le 1

## Slide 72
Derivation of the Reflectance Equation
From the definition of BRDF:

## Slide 73
Derivation of the Scene Radiance Equation
From the definition of BRDF:
Write Surface Irradiance in terms of Source Radiance:
Integrate over entire hemisphere of possible source directions:
Convert from solid angle to theta-phi representation:

## Slide 75: BRDF
Bi-directional Reflectance Distribution Function (BRDF)

## Slide 76: BRDF
Bi-directional Reflectance Distribution Function (BRDF)
Lambertian (diffuse) BRDF: energy equally distributed in all directions
What does the BRDF equal in this case?
Notes: At the other end, as I already mentioned is something that is ideally diffuse.

## Slide 77
Diffuse Reflection and Lambertian BRDF
viewing
direction
surface
element
normal
incident
direction
Lambertian BRDF is simply a constant :
albedo
Surface appears equally bright from ALL directions! (independent of )
Most commonly used BRDF in Vision and Graphics!
source intensity I

## Slide 78: BRDF
Bi-directional Reflectance Distribution Function (BRDF)
Specular BRDF: all energy concentrated in mirror direction
What does the BRDF equal in this case?
Notes: In the limit, something that is a perfect mirror reflects light in only one direction and the reflectance is a delta function.

## Slide 79
Specular Reflection and Mirror BRDF
source intensity I
viewing
direction
surface
element
normal
incident
direction
specular/mirror
direction
Mirror BRDF is simply a double-delta function :
Valid for very smooth surfaces.
All incident light energy reflected in a SINGLE direction (only when = ).
specular albedo

## Slide 80
Example Surfaces
Body Reflection:
Diffuse Reflection
Matte Appearance
Non-Homogeneous Medium
Clay, paper, etc
Surface Reflection:
Specular Reflection
Glossy Appearance
Highlights
Dominant for Metals
Many materials exhibit
both Reflections:

## Slide 81: BRDF
Bi-directional Reflectance Distribution Function (BRDF)
Glossy BRDF: more energy concentrated in mirror direction than elsewhere
Notes: something that is more glossy will have a substantially different reflectance function -- one in which more of the energy is concentrated in the mirror direction

## Slide 82: Trick for dielectrics (non-metals)
BRDF is a sum of a Lambertian diffuse component and non-Lambertian specular components
The two components differ in terms of color and polarization, and under certain conditions, this can be exploited to separate them.
Notes: Before we continue, I want to clarify what I mean by separability, or the idea that SV-BRDF can be separated into distinct diffuse and specular components.

## Slide 83: Trick for dielectrics (non-metals)
Often called the dichromatic BRDF:
Diffuse term varies with wavelength, constant with polarization
Specular term constant with wavelength, varies with polarization
BRDF is a sum of a Lambertian diffuse component and non-Lambertian specular components
The two components differ in terms of color and polarization, and under certain conditions, this can be exploited to separate them.
Notes: Before we continue, I want to clarify what I mean by separability, or the idea that SV-BRDF can be separated into distinct diffuse and specular components.

## Slide 84: Trick for dielectrics (non-metals)
DIFFUSE
=
+
SPECULAR
In this example, the two components were separated using linear polarizing filters on the camera and light source.

## Slide 85: Trick for dielectrics (non-metals)
DIFFUSE
=
+
SPECULAR

## Slide 86: Tabulated 4D BRDFs (hard to measure)
[Ngan et al., 2005]
Gonioreflectometer
Notes: At the other end, as I already mentioned is something that is ideally diffuse.

## Slide 87: Low-parameter (non-linear) BRDF models
Blinn:
Lafortune:
Ward:
Phong:
A small number of parameters define the (2D,3D, or 4D) function
Except for Lambertian, the BRDF is non-linear in these parameters
Examples:
Lambertian:
Where do these constants come from?
α is called the albedo

## Slide 88: Reflectance Models
Reflection: An Electromagnetic Phenomenon
Two approaches to derive Reflectance Models:
  Physical Optics (Wave Optics)
  Geometrical Optics (Ray Optics)
  Geometrical models are approximations to physical models
  But they are easier to use!

## Slide 89: Reflectance that Require Wave Optics

## Slide 90: Summary of some useful lighting models
plenoptic function (function on 5D domain)
far-field illumination (function on 2D domain)
low-frequency far-field illumination (nine numbers)
directional lighting (three numbers = direction and strength)
point source (four numbers = location and strength)

## Slide 91: References
Basic reading:
Szeliski, Section 2.2.
Gortler, Chapter 21.
This book by Steven Gortler has a great introduction to radiometry, reflectance, and their use for image formation.
Additional reading:
Arvo, “Analytic Methods for Simulated Light Transport,” Yale 1995.
Veach, “Robust Monte Carlo Methods for Light Transport Simulation,” Stanford 1997.
These two thesis are foundational for modern computer graphics. Among other things, they include a thorough derivation (starting from wave optics and measure theory) of all radiometric quantities and associated integro- differential equations. You can also look at them if you are interested in physics-based rendering.
Dutre et al., “Advanced Global Illumination,” 2006.
A book discussing modeling and simulation of other appearance effects beyond single-bounce reflectance.
Weyrich et al., “Principles of Appearance Acquisition and Representation,” FTCGV 2009.
A very thorough review of everything that has to do with modeling and measuring BRDFs.
Walter et al., “Microfacet models for refraction through rough surfaces,” EGSR 2007.
This paper has a great review of physics-based models for reflectance and refraction.
Matusik, “A data-driven reflectance model,” MIT 2003.
This thesis introduced the largest measured dataset of 4D reflectances. It also provides detailed discussion of many topics relating to modelling reflectance.
Rusinkiewicz, “A New Change of Variables for Efficient BRDF Representation,” 1998.
Romeiro and Zickler, “Inferring reflectance under real-world illumination,” Harvard TR 2010.
These two papers discuss the isotropy and other properties of common BRDFs, and how one can take advantage of them using alternative parameterizations.
Shafer, “Using color to separate reflection components,” 1984.
The paper introducing the dichromatic reflectance model.
Stam, “Diffraction Shaders,” SIGGRAPH 1999.
Levin et al., “Fabricating BRDFs at high spatial resolution using wave optics,” SIGGRAPH 2013.
Cuypers et al., “Reflectance model for diffraction,” TOG 2013.
These three papers describe reflectance effects that can only be modeled using wave optics (and in particular diffraction).
Notes: Ch