## Slide 1: Radiometry and reflectance
16-385 Computer Vision
Spring 2019, Lecture 14
http://www.cs.cmu.edu/~16385/

## Slide 2: Course announcements
Lot’s of grades posted during spring break.
- Mid-semester grades.
- Comments for HW1.
- Grades and comments for HW2.
Homework 4 will be posted tonight and will be due on March 3rd.
- It’s another shorter homework, based on material from this and the next lecture.
Talk tomorrow: Jun-Yan Zhu, “Learning to synthesize images,” noon-1 pm, GHC 6115

## Slide 3: Overview of today’s lecture
Measuring light and radiometry.
Reflectance and BRDF.
Light sources.

## Slide 4: Slide credits
Most of these slides were adapted from:
Srinivasa Narasimhan (16-385, Spring 2014).
Todd Zickler (Harvard University).
Steven Gortler (Harvard University).

## Slide 5: Appearance

## Slide 6: Appearance
Notes: The problem becomes especially difficult when we allow ourselves to consider the full diversity of the materials that surround us.
Different materials reflect light in different ways, and while these differences in color, sheen, gloss, haze, and so on are what makes many pictures beautiful, they are also what makes them very hard to analyze radiometrically.

## Slide 7: “Physics-based” computer vision (a.k.a “inverse optics”)
reflectance
illumination
shape
shape
, reflectance
, illumination
Our challenge: Invent computational representations of shape, lighting, and reflectance that are efficient: simple enough to make inference tractable, yet general enough to capture the world’s most important phenomena
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 8: Example application: Photometric Stereo

## Slide 9: Why study the physics (optics) of the world? Lets see some pictures!

## Slide 10: Light and Shadows

## Slide 13: Reflections

## Slide 17: Refractions

## Slide 21: Interreflections

## Slide 23: Scattering

## Slide 27: More Complex Appearances

## Slide 33: Measuring light and radiometry

## Slide 34: Solid angle
The solid angle subtended by a small surface patch with respect to point O is the area of its central projection onto the unit sphere about O
Depends on:
  orientation of patch
  distance of patch

## Slide 35: Solid angle
The solid angle subtended by a small surface patch with respect to point O is the area of its central projection onto the unit sphere about O
Depends on:
  orientation of patch
  distance of patch
One can show:
Units: steradians [sr]

## Slide 36: Solid angle
The solid angle subtended by a small surface patch with respect to point O is the area of its central projection onto the unit sphere about O
Depends on:
  orientation of patch
  distance of patch
One can show:
“surface foreshortening”
Units: steradians [sr]

## Slide 37: Solid angle
To calculate solid angle subtended by a surface S relative to O you must add up (integrate) contributions from all tiny patches (nasty integral)
One can show:
“surface foreshortening”
Units: steradians [sr]

## Slide 38: Question
Suppose surface S is a hemisphere centered at O. What is the solid angle it subtends?

## Slide 39: Question
Suppose surface S is a hemisphere centered at O. What is the solid angle it subtends?
Answer: 2\pi (area of sphere is 4\pi*r^2; area of unit sphere is 4\pi; half of that is 2\pi)

## Slide 40: Quantifying light: flux, irradiance, and radiance
Imagine a sensor that counts photons passing through planar patch X in directions within angular wedge W
It measures radiant flux [watts = joules/sec]: rate of photons hitting sensor area
Measurement depends on sensor area |X|
radiant flux
* shown in 2D for clarity; imagine three dimensions

## Slide 41: Quantifying light: flux, irradiance, and radiance
Irradiance: A measure of incoming light that is independent of sensor area |X|
Units: watts per square meter [W/m2]

## Slide 42: Quantifying light: flux, irradiance, and radiance
Irradiance: A measure of incoming light that is independent of sensor area |X|
Units: watts per square meter [W/m2]

## Slide 43: Quantifying light: flux, irradiance, and radiance
Irradiance: A measure of incoming light that is independent of sensor area |X|
Units: watts per square meter [W/m2]
Depends on sensor direction normal.
We keep track of the normal because a planar sensor with distinct orientation would converge to a different limit
In the literature, notations n and W are often omitted, and values are implied by context

## Slide 44: Quantifying light: flux, irradiance, and radiance
Radiance: A measure of incoming light that is independent of sensor area |X|, orientation n, and wedge size (solid angle) |W|
Units: watts per steradian per square meter [W/(m2∙sr)]
Has correct units, but still depends on sensor orientation
To correct this, convert to measurement that would have been made if sensor was perpendicular to direction ω

## Slide 45: Quantifying light: flux, irradiance, and radiance
Radiance: A measure of incoming light that is independent of sensor area |X|, orientation n, and wedge size (solid angle) |W|
Units: watts per steradian per square meter [W/(m2∙sr)]
Has correct units, but still depends on sensor orientation
To correct this, convert to measurement that would have been made if sensor was perpendicular to direction ω
“foreshortened area”

## Slide 46: Quantifying light: flux, irradiance, and radiance
Radiance: A measure of incoming light that is independent of sensor area |X|, orientation n, and wedge size (solid angle) |W|
Units: watts per steradian per square meter [W/(m2∙sr)]
Has correct units, but still depends on sensor orientation
To correct this, convert to measurement that would have been made if sensor was perpendicular to direction ω

## Slide 47: Quantifying light: flux, irradiance, and radiance
Radiance: A measure of incoming light that is independent of sensor area |X|, orientation n, and wedge size (solid angle) |W|
Units: watts per steradian per square meter [W/(m2∙sr)]
Has correct units, but still depends on sensor orientation
To correct this, convert to measurement that would have been made if sensor was perpendicular to direction ω
“foreshortened in the direction of travel”

## Slide 48: Quantifying light: flux, irradiance, and radiance
Attractive properties of radiance:
  Allows computing the radiant flux measured by any finite sensor
Notes: \Phi(W,X)=\int_X\int_W L(\hat{\boldsymbol{\omega}},x)d\boldsymbol{\omega}dA

## Slide 49: Quantifying light: flux, irradiance, and radiance
Attractive properties of radiance:
  Allows computing the radiant flux measured by any finite sensor
Notes: \Phi(W,X)=\int_X\int_W L(\hat{\boldsymbol{\omega}},x)d\boldsymbol{\omega}dA

## Slide 50: Quantifying light: flux, irradiance, and radiance
Attractive properties of radiance:
  Allows computing the radiant flux measured by any finite sensor
  Constant along a ray in free space

## Slide 51: Quantifying light: flux, irradiance, and radiance
Attractive properties of radiance:
  Allows computing the radiant flux measured by any finite sensor
  Constant along a ray in free space
  A camera measures radiance (after a one-time radiometric calibration). So RAW pixel values are proportional to radiance.
  - “Processed” images (like PNG and JPEG) are not linear radiance measurements!!
Notes: Possible classroom question: A Lambertian planar light source (e.g., a heated metal sheet) is one whose radiant intensity is J(\omega)=J_o<N,\omega>. Show that emitted radiance is independent of \omega (and thus that the sheet looks equally bright from all directions)

## Slide 52: Question
Most light sources, like a heated metal sheet, follow Lambert’s Law
radiant intensity [W/sr]
“Lambertian area source”
What is the radiance of an infinitesimal patch [W/sr･m2]?
Notes: %%% latexit code
J(\hat{\boldsymbol{\omega}})=J_o\langle\hat{\boldsymbol{\omega}},\hat{\boldsymbol{n}}\rangle=J_o\cos\theta

## Slide 53: Question
Most light sources, like a heated metal sheet, follow Lambert’s Law
radiant intensity [W/sr]
“Lambertian area source”
Answer:
(independent of direction)
What is the radiance of an infinitesimal patch [W/sr･m2]?
Notes: %%% latexit code
J(\hat{\boldsymbol{\omega}})=J_o\langle\hat{\boldsymbol{\omega}},\hat{\boldsymbol{n}}\rangle=J_o\cos\theta

## Slide 54: Question
Most light sources, like a heated metal sheet, follow Lambert’s Law
radiant intensity [W/sr]
“Lambertian area source”
What is the radiance of an infinitesimal patch [W/sr･m2]?
Answer:
(independent of direction)
“Looks equally bright when viewed from any direction”
Notes: %%% latexit code
J(\hat{\boldsymbol{\omega}})=J_o\langle\hat{\boldsymbol{\omega}},\hat{\boldsymbol{n}}\rangle=J_o\cos\theta

## Slide 55
Radiometric concepts – boring…but, important!
(1) Solid Angle :
( steradian )
What is the solid angle subtended by a hemisphere?
(solid angle subtended by )
(foreshortened area)
(surface area)
(2) Radiant Intensity of Source :
Light Flux (power) emitted per unit solid angle
( watts / steradian )
(3) Surface Irradiance :
( watts / m )
Light Flux (power) incident per unit surface area.
Does not depend on where the light is coming from!
source
2
(4) Surface Radiance (tricky) :
(watts / m steradian )
Flux emitted per unit foreshortened area
per unit solid angle.
L depends on direction
Surface can radiate into whole hemisphere.
L depends on reflectance properties of surface.

## Slide 56: Appearance
Notes: The problem becomes especially difficult when we allow ourselves to consider the full diversity of the materials that surround us.
Different materials reflect light in different ways, and while these differences in color, sheen, gloss, haze, and so on are what makes many pictures beautiful, they are also what makes them very hard to analyze radiometrically.

## Slide 57: “Physics-based” computer vision (a.k.a “inverse optics”)
reflectance
illumination
shape
shape
, reflectance
, illumination
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 58: Reflectance and BRDF

## Slide 59: Reflectance
Ratio of outgoing energy to incoming energy at a single point
Want to define a ratio such that it:
  converges as we use smaller and smaller incoming and outgoing wedges
  does not depend on the size of the wedges (i.e. is intrinsic to the material)
Notes: f_{x,\hat{\bf n}}(W_\text{in},\hat{\boldsymbol{\omega}}_\text{out})=\frac{L^\text{out}(x,\hat{\boldsymbol{\omega}}_\text{out})}{E_{\hat{\bf n}}^\text{in}(W_\text{in},x)}
\lim_{W_\text{in}\longrightarrow \hat{\boldsymbol{w}}_\text{in}}
f_{x,\hat{\bf n}}(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})

## Slide 60: Reflectance
Ratio of outgoing energy to incoming energy at a single point
Want to define a ratio such that it:
  converges as we use smaller and smaller incoming and outgoing wedges
  does not depend on the size of the wedges (i.e. is intrinsic to the material)
Notations x and n often implied by context and omitted; directions \omega are expressed in local coordinate system defined by normal n (and some chosen tangent vector)
Units: sr-1
Called Bidirectional Reflectance Distribution Function (BRDF)
Notes: f_{x,\hat{\bf n}}(W_\text{in},\hat{\boldsymbol{\omega}}_\text{out})=\frac{L^\text{out}(x,\hat{\boldsymbol{\omega}}_\text{out})}{E_{\hat{\bf n}}^\text{in}(W_\text{in},x)}
\lim_{W_\text{in}\longrightarrow \hat{\boldsymbol{w}}_\text{in}}
f_{x,\hat{\bf n}}(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})

## Slide 61
BRDF: Bidirectional Reflectance Distribution Function
x
y
z
source
viewing
direction
surface
element
normal
incident
direction
Irradiance at Surface in direction
Radiance of Surface in direction
BRDF :

## Slide 62: Reflectance: BRDF
Units: sr-1
Real-valued function defined on the double-hemisphere
Has many useful properties
Notes: f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})
f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})=f(\hat{\boldsymbol{\omega}}_\text{out},\hat{\boldsymbol{\omega}}_\text{in})
\forall \hat{\boldsymbol{\omega}}_\text{in},\ \ \int_{\Omega_\text{out}} f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})\cos\theta_\text{out}d\hat{\boldsymbol{\omega}}_\text{out}\le 1

## Slide 63
Important Properties of BRDFs
x
y
z
source
viewing
direction
surface
element
normal
incident
direction
Conservation of Energy:
Why smaller than or equal?

## Slide 64: Property: “Helmholtz reciprocity”
Helmholtz Reciprocity: (follows from 2nd Law of Thermodynamics)
BRDF does not change when source and viewing directions are swapped.
Notes: For example, a useful property of most opaque materials is that their reflectance function has a symmetry property known as reciprocity.
Reciprocity states that the BRDF is symmetric in terms of its input and output directions, so if we swap these directions, the BRDF value remain unchanged.

## Slide 65: Common assumption: Isotropy
Bi-directional Reflectance Distribution Function (BRDF)
4D → 3D
[Matusik et al., 2003]
Can be written as a function of 3 variables :
BRDF does not change when surface is rotated about the normal.
Notes: An isotropic BRDF is one that is:
- unchanged when the input is spun around the surface normal, and
- symmetric across the incident plane,
These symmetry conditions imply that the domain of an isotropic BRDF is three dimensional instead of four.
<animate> Returning to our problem...

## Slide 66: Useful re-parameterization of double-hemisphere
Notes: An isotropic BRDF is one that is:
- unchanged when the input is spun around the surface normal, and
- symmetric across the incident plane,
These symmetry conditions imply that the domain of an isotropic BRDF is three dimensional instead of four.
<animate> Returning to our problem...

## Slide 67: Useful re-parameterization of double-hemisphere
reciprocity
Notes: An isotropic BRDF is one that is:
- unchanged when the input is spun around the surface normal, and
- symmetric across the incident plane,
These symmetry conditions imply that the domain of an isotropic BRDF is three dimensional instead of four.
<animate> Returning to our problem...

## Slide 68: Useful re-parameterization of double-hemisphere
reciprocity
isotropy:
Notes: An isotropic BRDF is one that is:
- unchanged when the input is spun around the surface normal, and
- symmetric across the incident plane,
These symmetry conditions imply that the domain of an isotropic BRDF is three dimensional instead of four.
<animate> Returning to our problem...

## Slide 69: Reflectance: BRDF
Units: sr-1
Real-valued function defined on the double-hemisphere
Has many useful properties
Allows computing output radiance (and thus pixel value) for any configuration of lights and viewpoint
reflectance equation
Why is there a cosine in the reflectance equation?
Notes: f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})
f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})=f(\hat{\boldsymbol{\omega}}_\text{out},\hat{\boldsymbol{\omega}}_\text{in})
\forall \hat{\boldsymbol{\omega}}_\text{in},\ \ \int_{\Omega_\text{out}} f(\hat{\boldsymbol{\omega}}_\text{in},\hat{\boldsymbol{\omega}}_\text{out})\cos\theta_\text{out}d\hat{\boldsymbol{\omega}}_\text{out}\le 1

## Slide 70
Derivation of the Reflectance Equation
From the definition of BRDF:

## Slide 71
Derivation of the Scene Radiance Equation
From the definition of BRDF:
Write Surface Irradiance in terms of Source Radiance:
Integrate over entire hemisphere of possible source directions:
Convert from solid angle to theta-phi representation:

## Slide 73: BRDF
Bi-directional Reflectance Distribution Function (BRDF)

## Slide 74: BRDF
Bi-directional Reflectance Distribution Function (BRDF)
Lambertian (diffuse) BRDF: energy equally distributed in all directions
What does the BRDF equal in this case?
Notes: At the other end, as I already mentioned is something that is ideally diffuse.

## Slide 75
Diffuse Reflection and Lambertian BRDF
viewing
direction
surface
element
normal
incident
direction
Lambertian BRDF is simply a constant :
albedo
Surface appears equally bright from ALL directions! (independent of )
Most commonly used BRDF in Vision and Graphics!
source intensity I

## Slide 76: BRDF
Bi-directional Reflectance Distribution Function (BRDF)
Specular BRDF: all energy concentrated in mirror direction
What does the BRDF equal in this case?
Notes: In the limit, something that is a perfect mirror reflects light in only one direction and the reflectance is a delta function.

## Slide 77
Specular Reflection and Mirror BRDF
source intensity I
viewing
direction
surface
element
normal
incident
direction
specular/mirror
direction
Mirror BRDF is simply a double-delta function :
Valid for very smooth surfaces.
All incident light energy reflected in a SINGLE direction (only when = ).
specular albedo

## Slide 78
Example Surfaces
Body Reflection:
Diffuse Reflection
Matte Appearance
Non-Homogeneous Medium
Clay, paper, etc
Surface Reflection:
Specular Reflection
Glossy Appearance
Highlights
Dominant for Metals
Many materials exhibit
both Reflections:

## Slide 79: BRDF
Bi-directional Reflectance Distribution Function (BRDF)
Glossy BRDF: more energy concentrated in mirror direction than elsewhere
Notes: something that is more glossy will have a substantially different reflectance function -- one in which more of the energy is concentrated in the mirror direction

## Slide 80: Trick for dielectrics (non-metals)
BRDF is a sum of a Lambertian diffuse component and non-Lambertian specular components
The two components differ in terms of color and polarization, and under certain conditions, this can be exploited to separate them.
Notes: Before we continue, I want to clarify what I mean by separability, or the idea that SV-BRDF can be separated into distinct diffuse and specular components.

## Slide 81: Trick for dielectrics (non-metals)
Often called the dichromatic BRDF:
Diffuse term varies with wavelength, constant with polarization
Specular term constant with wavelength, varies with polarization
BRDF is a sum of a Lambertian diffuse component and non-Lambertian specular components
The two components differ in terms of color and polarization, and under certain conditions, this can be exploited to separate them.
Notes: Before we continue, I want to clarify what I mean by separability, or the idea that SV-BRDF can be separated into distinct diffuse and specular components.

## Slide 82: Trick for dielectrics (non-metals)
DIFFUSE
=
+
SPECULAR
In this example, the two components were separated using linear polarizing filters on the camera and light source.

## Slide 83: Trick for dielectrics (non-metals)
DIFFUSE
=
+
SPECULAR

## Slide 84: Tabulated 4D BRDFs (hard to measure)
[Ngan et al., 2005]
Gonioreflectometer
Notes: At the other end, as I already mentioned is something that is ideally diffuse.

## Slide 85: Low-parameter (non-linear) BRDF models
Blinn:
Lafortune:
Ward:
Phong:
A small number of parameters define the (2D,3D, or 4D) function
Except for Lambertian, the BRDF is non-linear in these parameters
Examples:
Lambertian:
Where do these constants come from?
α is called the albedo

## Slide 86: Reflectance Models
Reflection: An Electromagnetic Phenomenon
Two approaches to derive Reflectance Models:
  Physical Optics (Wave Optics)
  Geometrical Optics (Ray Optics)
  Geometrical models are approximations to physical models
  But they are easier to use!

## Slide 87: Reflectance that Require Wave Optics

## Slide 88: Light sources

## Slide 89: “Physics-based” computer vision (a.k.a “inverse optics”)
reflectance
illumination
shape
shape
, reflectance
, illumination
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 90: Lighting models: Plenoptic function
Radiance as a function of position and direction
Radiance as a function of position, direction, and time
Spectral radiance as a function of position, direction, time and wavelength
[Adelson and Bergen, 1991]

## Slide 91: Lighting models: far-field (or directional) approximation
Assume that, over the observed region of interest, all source of incoming flux are relatively far away
[Debevec, 1998]
ignores close
inter-reflections
radiance only depends on direction; not location

## Slide 92: Application: augmented reality
[Debevec, 1998]

## Slide 93: Application: augmented reality
[Debevec, 1998]

## Slide 94: Application: augmented reality
http://gl.ict.usc.edu/LightStages/

## Slide 95: Application: augmented reality
[https://developers.google.com/ar/]
[https://developer.apple.com/arkit/]

## Slide 96: Lighting models: far-field approximation
[http://gl.ict.usc.edu/Data/HighResProbes/]
One can download far-field lighting environments that have been captured by others
A number of apps and software exist to help you capture capture your own environments using a light probe

## Slide 97: Application: inferring outdoor illumination
[Lalonde et al., 2009]

## Slide 98: A further simplification: Low-frequency illumination
First nine basis functions are sufficient for re-creating Lambertian appearance
[Ramamoorthi and Hanrahan, 2001; Basri and Jacobs, 2003]

## Slide 99: Low-frequency illumination
[Ramamoorthi and Hanrahan, 2001; Basri and Jacobs, 2003]

## Slide 100: Low-frequency illumination
[Ramamoorthi and Hanrahan, 2001; Basri and Jacobs, 2003]
Truncate to first 9 terms

## Slide 101: Application: Trivial rendering
Capture light probe
Low-pass filter (truncate to first nine SHs)
Rendering a (convex) diffuse object in this environment simply requires a lookup based on the surface normal at each pixel

## Slide 102
White-out: Snow and Overcast Skies
CAN’T perceive the shape of the snow covered terrain!
CAN perceive shape in regions
lit by the street lamp!!
WHY?

## Slide 103
Diffuse Reflection from Uniform Sky
Assume Lambertian Surface with Albedo = 1 (no absorption)
Assume Sky radiance is constant
Substituting in above Equation:
Radiance of any patch is the same as Sky radiance !! (white-out condition)

## Slide 104: Even simpler: Directional lighting
Assume that, over the observed region of interest, all source of incoming flux is from one direction
Convenient representation
“light direction”
“light strength”
Notes: & L(x,\omega,t,\lambda)\longrightarrow L(x,t,\lambda)\longrightarrow s(t,\lambda)\delta(\omega=\omega_o(t))\\
& L(x,\omega)\longrightarrow L(\omega)\longrightarrow s\delta(\omega=\omega_o)
\vec{\boldsymbol{\ell}}=(\ell_x,\ell_y,\ell_z)
\hat{\boldsymbol{\ell}}=\frac{\vec{\boldsymbol{\ell}}}{||\vec{\boldsymbol{\ell}}||}

## Slide 105: Simple shading
ASSUMPTION 1:
LAMBERTIAN
ASSUMPTION 2:
DIRECTIONAL LIGHTING
Notes: I=a\hat{\bf n}^\top\vec{\boldsymbol{\ell}}

## Slide 106: “N-dot-l” shading
ASSUMPTION 1:
LAMBERTIAN
ASSUMPTION 2:
DIRECTIONAL LIGHTING
Notes: I=a\hat{\bf n}^\top\vec{\boldsymbol{\ell}}

## Slide 107: An ideal point light source
Think of this as a spatially-varying directional source where
the direction is away from x_o
the strength is proportional to 1/(distance)^2

## Slide 108: Summary of some useful lighting models
plenoptic function (function on 5D domain)
far-field illumination (function on 2D domain)
low-frequency far-field illumination (nine numbers)
directional lighting (three numbers = direction and strength)
point source (four numbers = location and strength)

## Slide 109: References
Basic reading:
Szeliski, Section 2.2.
Gortler, Chapter 21.
This book by Steven Gortler has a great introduction to radiometry, reflectance, and their use for image formation.
Additional reading:
Arvo, “Analytic Methods for Simulated Light Transport,” Yale 1995.
Veach, “Robust Monte Carlo Methods for Light Transport Simulation,” Stanford 1997.
These two thesis are foundational for modern computer graphics. Among other things, they include a thorough derivation (starting from wave optics and measure theory) of all radiometric quantities and associated integro- differential equations. You can also look at them if you are interested in physics-based rendering.
Dutre et al., “Advanced Global Illumination,” 2006.
A book discussing modeling and simulation of other appearance effects beyond single-bounce reflectance.
Weyrich et al., “Principles of Appearance Acquisition and Representation,” FTCGV 2009.
A very thorough review of everything that has to do with modeling and measuring BRDFs.
Walter et al., “Microfacet models for refraction through rough surfaces,” EGSR 2007.
This paper has a great review of physics-based models for reflectance and refraction.
Matusik, “A data-driven reflectance model,” MIT 2003.
This thesis introduced the largest measured dataset of 4D reflectances. It also provides detailed discussion of many topics relating to modelling reflectance.
Rusinkiewicz, “A New Change of Variables for Efficient BRDF Representation,” 1998.
Romeiro and Zickler, “Inferring reflectance under real-world illumination,” Harvard TR 2010.
These two papers discuss the isotropy and other properties of common BRDFs, and how one can take advantage of them using alternative parameterizations.
Shafer, “Using color to separate reflection components,” 1984.
The paper introducing the dichromatic reflectance model.
Stam, “Diffraction Shaders,” SIGGRAPH 1999.
Levin et al., “Fabricating BRDFs at high spatial resolution using wave optics,” SIGGRAPH 2013.
Cuypers et al., “Reflectance model for diffraction,” TOG 2013.
These three papers describe reflectance effects that can only be modeled using wave optics (and in particular diffraction).
Notes: Ch