## Slide 1: Photometric stereo
16-385 Computer Vision
Spring 2019, Lecture 15
http://www.cs.cmu.edu/~16385/

## Slide 2: Course announcements
Homework 4 has been posted tonight and is due on March 27th.
- How many of you have looked at/started/finished the homework?
- Any questions?
How many of you attended Jun-Yan Zhu talk?
Another talk tomorrow: Angjoo Kanazawa, “Perceiving Humans in the 3D World,” 10-11 am, GHC 6115

## Slide 3: Overview of today’s lecture
Leftover about light sources.
Some notes about radiometry.
Photometric stereo.
Uncalibrated photometric stereo.
Generalized bas-relief ambiguity.
Shape from shading.
Start image processing pipeline.

## Slide 4: Slide credits
Many of these slides were adapted from:
Srinivasa Narasimhan (16-385, Spring 2014).
Todd Zickler (Harvard University).
Steven Gortler (Harvard University).
Kayvon Fatahalian (Stanford University; CMU 15-462, Fall 2015).

## Slide 5: Some notes about radiometry

## Slide 6: What about color?
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 7: Spectral radiance
Distribution of radiance as a function of wavelength.
All of the phenomena we described in this lecture can be extended to take into account color, by considering separate radiance and BRDF functions independently for each wavelength.
spectral reflectance
illuminant spectrum
spectral radiance
retinal color

## Slide 8: Spectral radiance
Distribution of radiance as a function of wavelength.
All of the phenomena we described in this lecture can be extended to take into account color, by considering separate radiance and BRDF functions independently for each wavelength.
Does this view of color ignore any important phenomena?

## Slide 9: Spectral radiance
Distribution of radiance as a function of wavelength.
All of the phenomena we described in this lecture can be extended to take into account color, by considering separate radiance and BRDF functions independently for each wavelength.
Does this view of color ignore any important phenomena?
Things like fluorescence and any other phenomena where light changes color.

## Slide 10: Spectral Sensitivity Function (SSF)
Any light sensor (digital or not) has different sensitivity to different wavelengths.
This is described by the sensor’s spectral sensitivity function .
When measuring light of a some SPD , the sensor produces a scalar response:
sensor response
light SPD
sensor SSF
Weighted combination of light’s SPD: light contributes more at wavelengths where the sensor has higher sensitivity.
The spectral sensitivity function converts radiometric units (radiance, irradiance) defined per wavelength, to radiometric quantities where wavelength has been averaged out.

## Slide 11: Radiometry versus photometry
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 12: Radiometry versus photometry
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 13: Radiometry versus photometry
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 14
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 15: Quiz 1: Measurement of a sensor using a thin lens
What integral should we write for the power measured by infinitesimal pixel p?
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 16: Quiz 1: Measurement of a sensor using a thin lens
What integral should we write for the power measured by infinitesimal pixel p?
Can I transform this integral over the hemisphere to an integral over the aperture area?
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 17: Quiz 1: Measurement of a sensor using a thin lens
What integral should we write for the power measured by infinitesimal pixel p?
Can I transform this integral over the hemisphere to an integral over the aperture area?
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 18: Quiz 1: Measurement of a sensor using a thin lens
Can I write the denominator in a more convenient form?
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 19: Quiz 1: Measurement of a sensor using a thin lens
What does this say about the image I am capturing?
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 20: Vignetting
Four types of vignetting:
Mechanical: light rays blocked by hoods, filters, and other objects.
Lens: similar, but light rays blocked by lens elements.
Natural: due to radiometric laws (“cosine fourth falloff”).
Pixel: angle-dependent sensitivity of photodiodes.
Fancy word for: pixels far off the center receive less light
white wall under uniform light
more interesting example of vignetting

## Slide 21: Quiz 2: BRDF of the moon
What BRDF does the moon have?
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 22: Quiz 2: BRDF of the moon
What BRDF does the moon have?
Can it be diffuse?
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 23: Quiz 2: BRDF of the moon
What BRDF does the moon have?
Can it be diffuse?
Even though the moon appears matte, its edges remain bright.
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 24: Rough diffuse appearance
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 25: Five important equations/integrals to remember
Flux measured by a sensor of area X and directional receptivity W:
Reflectance equation:
Radiance under directional lighting and Lambertian BRDF (“n-dot-l shading”):
Conversion of a (hemi)-spherical integral to a surface integral:
Computing (hemi)-spherical integrals:
and
Notes: Our work addresses the problem of inferring scene properties from image data.
Specifically, we want to relate observed image intensities to object shape, scene illumination, and material properties, or surface reflectance.
The task is made difficult by the fact that shape, lighting, and reflectance information are all tightly coupled in the image data so that we cannot typically draw conclusions about one of them without making restrictive assumptions about the others.

## Slide 26: Photometric stereo

## Slide 27: Image Intensity and 3D Geometry
Shading as a cue for shape reconstruction
What is the relation between intensity and shape?

## Slide 28: “N-dot-l” shading
ASSUMPTION 1:
LAMBERTIAN
ASSUMPTION 2:
DIRECTIONAL LIGHTING
Why do we call these normal “shape”?
Notes: I=a\hat{\bf n}^\top\vec{\boldsymbol{\ell}}

## Slide 29: Surfaces and normals
x
z
what is a camera like this called?
viewing rays for different pixels
imaged surface
Notes: I=a\hat{\bf n}^\top\vec{\boldsymbol{\ell}}

## Slide 30: Surfaces and normals
x
z
viewing rays for different pixels
imaged surface
Surface representation as a depth field (also known as Monge surface):
pixel coordinates on image place
depth at each pixel
How does surface normal relate to this representation?
orthographic camera
Notes: I=a\hat{\bf n}^\top\vec{\boldsymbol{\ell}}

## Slide 31: Surfaces and normals
x
z
orthographic camera
viewing rays for different pixels
imaged surface
Surface representation as a depth image (also known as Monge surface):
pixel coordinates on image place
depth at each pixel
Unnormalized normal:
Actual normal:
Normals are scaled spatial derivatives of depth image!
Notes: I=a\hat{\bf n}^\top\vec{\boldsymbol{\ell}}

## Slide 32: Shape from a Single Image?
Given a single image of an object with known surface reflectance taken under a known light source, can we recover the shape of the object?

## Slide 33: Human Perception

## Slide 34
Examples of the classic bump/dent stimuli used to test lighting assumptions when judging shape from shading, with shading orientations (a) 0° and (b) 180° from the vertical.
Thomas R et al. J Vis 2010;10:6
Notes: Examples of the classic bump/dent stimuli used to test lighting assumptions when judging shape from shading, with shading orientations (a) 0° and (b) 180° from the vertical.

## Slide 35: Human Perception
by V. Ramachandran
Our brain often perceives shape from shading.
Mostly, it makes many assumptions to do so.
For example:
Light is coming from above (sun).
Biased by occluding contours.

## Slide 36: Single-lighting is ambiguous
ASSUMPTION 1:
LAMBERTIAN
ASSUMPTION 2:
DIRECTIONAL LIGHTING
Notes: I=a\hat{\bf n}^\top\vec{\boldsymbol{\ell}}

## Slide 37: Lambertian photometric stereo
Assumption: We know the lighting directions.
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 38: Lambertian photometric stereo
define “pseudo-normal”
solve linear system
for pseudo-normal
What are the dimensions of these matrices?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 39: Lambertian photometric stereo
define “pseudo-normal”
solve linear system
for pseudo-normal
What are the knowns and unknowns?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 40: Lambertian photometric stereo
define “pseudo-normal”
solve linear system
for pseudo-normal
How many lights do I need for unique solution?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 41: Lambertian photometric stereo
define “pseudo-normal”
solve linear system
for pseudo-normal
once system is solved, b gives normal direction and albedo
How do we solve this system?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 42: Solving the Equation with three lights
inverse
Is there any reason to use more than three lights?

## Slide 43: More than Three Light Sources
Get better SNR by using more lights
Least squares solution:
Solve for as before
Moore-Penrose pseudo inverse

## Slide 44: Computing light source directions
Trick: place a chrome sphere in the scene
  the location of the highlight tells you the source direction

## Slide 45: Limitations
Big problems
  Doesn’t work for shiny things, semi-translucent things
  Shadows, inter-reflections
Smaller problems
  Camera and lights have to be distant
  Calibration requirements
    measure light source directions, intensities
    camera response function

## Slide 46: Depth from normals
Solving the linear system per-pixel gives us an estimated surface normal for each pixel
How can we compute depth from normals?
  Normals are like the “derivative” of the true depth
Input photo
Estimated normals
Estimated normals (needle diagram)

## Slide 47: Surfaces and normals
x
z
orthographic camera
viewing rays for different pixels
imaged surface
Surface representation as a depth image (also known as Monge surface):
pixel coordinates in image space
depth at each pixel
Unnormalized normal:
Actual normal:
Normals are scaled spatial derivatives of depth image!
Notes: I=a\hat{\bf n}^\top\vec{\boldsymbol{\ell}}

## Slide 48: Normal Integration
Integrating a set of derivatives is easy in 1D
  (similar to Euler’s method from diff. eq. class)
Could just integrate normals in each column / row separately
Instead, we formulate as a linear system and solve for depths that best agree with the surface normals

## Slide 49: Depth from normals
Get a similar equation for V2
  Each normal gives us two linear constraints on z
  compute z values by solving a matrix equation
V1
V2
N

## Slide 50: Results
Estimate light source directions
Compute surface normals
Compute albedo values
Estimate depth from surface normals
Relight the object (with original texture and uniform albedo)

## Slide 51
Results: Lambertian Sphere
Input Images
Estimated Albedo
Estimated Surface Normals
Needles are projections
of surface normals on
image plane

## Slide 52: Lambertain Mask

## Slide 53: Results – Albedo and Surface Normal

## Slide 54: Results – Shape of Mask

## Slide 55
Results: Lambertian Toy
Input Images
Estimated Surface Normals
Estimated Albedo
I.2

## Slide 56: Non-idealities: interreflections

## Slide 57: Non-idealities: interreflections
Shallow reconstruction
(effect of interreflections)
Accurate reconstruction
(after removing interreflections)

## Slide 58: What if the light directions are unknown?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 59: Uncalibrated photometric stereo

## Slide 60: What if the light directions are unknown?
define “pseudo-normal”
solve linear system
for pseudo-normal
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 61: What if the light directions are unknown?
define “pseudo-normal”
solve linear system
for pseudo-normal at each image pixel
M: number of pixels
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 62: What if the light directions are unknown?
define “pseudo-normal”
solve linear system
for pseudo-normal at each image pixel
How do we solve this system without knowing light matrix L?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 63: Factorizing the measurement matrix
Lights
Pseudonormals
What are the dimensions?

## Slide 64: Factorizing the measurement matrix
Singular value decomposition:
This decomposition minimizes |I-LB|2

## Slide 65
Are the results unique?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 66
Are the results unique?
I = L B = (L Q-1) (Q B)
We can insert any 3x3 matrix Q in the decomposition and get the same images:
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 67
Are the results unique?
I = L B = (L Q-1) (Q B)
We can insert any 3x3 matrix Q in the decomposition and get the same images:
Can we use any assumptions to remove some of these 9 degrees of freedom?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 68: Generalized bas-relief ambiguity

## Slide 69
Enforcing integrability
What does the matrix B correspond to?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 70
Enforcing integrability
What does the matrix B correspond to?
Surface representation as a depth image (also known as Monge surface):
pixel coordinates in image space
depth at each pixel
Unnormalized normal:
Actual normal:
Pseudo-normal:
Rearrange into 3xN matrix B.
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 71
Enforcing integrability
What does the integrability constraint correspond to?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 72
Enforcing integrability
What does the integrability constraint correspond to?
Differentiation order should not matter:
Can you think of a way to express the above using pseudo-normals b?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 73
Enforcing integrability
What does the integrability constraint correspond to?
Differentiation order should not matter:
Can you think of a way to express the above using pseudo-normals b?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 74
Enforcing integrability
What does the integrability constraint correspond to?
Differentiation order should not matter:
Can you think of a way to express the above using pseudo-normals b?
Simplify to:
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 75
Enforcing integrability
What does the integrability constraint correspond to?
Differentiation order should not matter:
Can you think of a way to express the above using pseudo-normals b?
Simplify to:
If Be is the pseudo-normal matrix we get from SVD, then find the 3x3 transform D such that B=D⋅Be is the closest to satisfying integrability in the least-squares sense.
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 76
Enforcing integrability
Does enforcing integrability remove all ambiguities?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 77
Generalized Bas-relief ambiguity
If B is integrable, then:
B’=G-T⋅B is also integrable for all G of the form ( ≠ 0)
Combined with transformed lights S’=G⋅S, the transformed pseudonormals produce the same images as the original pseudonormals.
This ambiguity cannot be removed using shadows.
This ambiguity can be removed using interreflections or additional assumptions.
This ambiguity is known as the generalized bas-relief ambiguity.
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 78
Generalized Bas-relief ambiguity
When = = 0, G is equivalent to the transformation employed by relief sculptures.
Otherwise, includes shearing.
When = = 0 and = +-1, top/down ambiguity.
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 79: What assumptions have we made for all this?
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 80: What assumptions have we made for all this?
Lambertian BRDF
Directional lighting
No interreflections or scattering
Notes: %%% latexit
I_1=a\hat{\boldsymbol{n}}^\top\vec{\boldsymbol{\ell}}_1
\vec{\boldsymbol{b}}\triangleq a\hat{\boldsymbol{n}}
\left[\begin{array}{c}
I_1 \\ I_2 \\ \vdots \\ I_N
\end{array}\right]_{N\times 1}\!\!\!\!\!
=\left[\begin{array}{c}
\vec{\boldsymbol{\ell}}_1^\top \\
\vec{\boldsymbol{\ell}}_2^\top \\
\vdots \\
\vec{\boldsymbol{\ell}}_N^\top \\
\end{array}\right]_{N\times 3}\!\!\!\!\!\!\!\!\!
\left[\begin{array}{c}
\vec{\boldsymbol{b}}
\end{array}\right]_{3\times 1}

## Slide 81: Shape independent of BRDF via reciprocity: “Helmholtz Stereopsis”
[Zickler et al., 2002]

## Slide 82: Shape from shading

## Slide 83: Single-lighting is ambiguous
ASSUMPTION 1:
LAMBERTIAN
ASSUMPTION 2:
DIRECTIONAL LIGHTING
[Prados, 2004]
Notes: I=a\hat{\bf n}^\top\vec{\boldsymbol{\ell}}

## Slide 84: Stereographic Projection
(p,q)-space (gradient space)
(f,g)-space
Problem
(p,q) can be infinite when
Redefine reflectance map as

## Slide 85: Image Irradiance Constraint
Image irradiance should match the reflectance map
Minimize
(minimize errors in image irradiance in the image)

## Slide 86: Smoothness Constraint
Used to constrain shape-from-shading
Relates orientations (f,g) of neighboring surface points
: surface orientation under stereographic projection
Minimize
(penalize rapid changes in surface orientation f and g over the image)

## Slide 87: Shape-from-Shading
Find surface orientations (f,g) at all image points that minimize
smoothness
constraint
weight
image irradiance
error
Minimize

## Slide 88: Numerical Shape-from-Shading
Smoothness error at image point (i,j)
Of course you can consider more neighbors (smoother results)
Image irradiance error at image point (i,j)
Find and that minimize
(Ikeuchi & Horn 89)

## Slide 89: Numerical Shape-from-Shading
Find and that minimize
If and minimize , then
where and are 4-neighbors average around image point (k,l)
(Ikeuchi & Horn 89)

## Slide 90: Numerical Shape-from-Shading
Use known values on the occluding boundary to constrain the solution (boundary conditions)
Compare with for convergence test
As the solution converges, increase to remove the smoothness constraint
Update rule
(Ikeuchi & Horn 89)

## Slide 91: Results

## Slide 92: Results

## Slide 93: More modern results

## Slide 94: References
Basic reading:
Szeliski, Section 2.2.
Gortler, Chapter 21.
This book by Steven Gortler has a great introduction to radiometry, reflectance, and their use for image formation.
Additional reading:
Oren and Nayar, “Generalization of the Lambertian model and implications for machine vision,” IJCV 1995.
The paper introducing the most common model for rough diffuse reflectance.
Debevec, “Rendering Synthetic Objects into Real Scenes,” SIGGRAPH 1998.
The paper that introduced the notion of the environment map, the use of chrome spheres for measuring such maps, and the idea that they can be used for easy rendering.
Lalonde et al., “Estimating the Natural Illumination Conditions from a Single Outdoor Image,” IJCV 2012.
A paper on estimating outdoors environment maps from just one image.
Basri and Jacobs, “Lambertian reflectance and linear subspaces,” ICCV 2001.
Ramamoorthi and Hanrahan, “A signal-processing framework for inverse rendering,” SIGGRAPH 2001.
Sloan et al., “Precomputed radiance transfer for real-time rendering in dynamic, low-frequency lighting environments,” SIGGRAPH 2002.
Three papers describing the use of spherical harmonics to model low-frequency illumination, as well as the low-pass filtering effect of Lambertian reflectance on illumination.
Zhang et al., “Shape-from-shading: a survey,” PAMI 1999.
A review of perceptual and computational aspects of shape from shading.
Woodham, “Photometric method for determining surface orientation from multiple images,” Optical Engineering 1980.
The paper that introduced photometric stereo.
Yuille and Snow, “Shape and albedo from multiple images using integrability,” CVPR 1997.
Belhumeur et al., “The bas-relief ambiguity,” IJCV 1999.
Papadhimitri and Favaro, “A new perspective on uncalibrated photometric stereo,” CVPR 2013.
Three papers discussing uncalibrated photometric stereo. The first paper shows that, when the lighting directions are not known, by assuming integrability, one can reduce unknowns to the bas-relief ambiguity. The second paper discusses the bas-relief ambiguity in a more general context. The third paper shows that, if instead of an orthographic camera one uses a perspective camera, this is further reduced to just a scale ambiguity.
Alldrin et al., “Resolving the generalized bas-relief ambiguity by entropy minimization,” CVPR 2007.
A popular technique for resolving the bas-relief ambiguity in uncalibrated photometric stereo.
Zickler et al., “Helmholtz stereopsis: Exploiting reciprocity for surface reconstruction,” IJCV 2002.
A method for photometric stereo reconstruction under arbitrary BRDF.
Nayar et al., “Shape from interreflections,” IJCV 1991.
Chandraker et al., “Reflections on the generalized bas-relief ambiguity,” CVPR 2005.
Two papers discussing how one can perform photometric stereo (calibrated or otherwise) in the presence of strong interreflections.
Frankot and Chellappa, “A method for enforcing integrability in shape from shading algorithms,” PAMI 1988.
Agrawal et al., “What is the range of surface reconstructions from a gradient field?,” ECCV 2006.
Two papers discussing how one can integrate a normal field to reconstruct a surface.
Notes: Ch