## Slide 1
14-513
18-613

## Slide 2: Virtual Memory: Systems 18-213/18-613: Introduction to Computer Systems 13th Lecture, June 9, 2026

## Slide 3: Review: Virtual Memory & Physical Memory
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
A page table contains page table entries (PTEs) that map virtual pages to physical pages.

## Slide 4: Review: Translating with a k-level Page Table
Page table base register
(part of the process’ context)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
VIRTUAL ADDRESS
PHYSICAL ADDRESS
...
...
the Level 1
page table
a Level 2
page table
a Level k
page table
Having multiple levels greatly reduces total page table size
Notes: A heads up: One of the quiz questions requires understanding this structure.

## Slide 5: Review: Translation Lookaside Buffer (TLB)
MMU
Cache/
Memory
CPU
VA
1
PA
4
Data
5
Typically, a TLB hit eliminates the k memory accesses required to do a page table lookup.
TLB
2
VPN
PTE
3
A small cache of page table entries with fast access by MMU

## Slide 6: Recall: Set Associative Cache
B = 2b bytes per cache block (the data)
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
t bits
s bits
b bits
Address of word:
CT tag
CI index
CO offset
data begins at this offset
Steps for a READ:
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 7: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag
(bits per field for our simple example)

## Slide 8: Today
Simple memory system example CSAPP 9.6.4
Case study: Core i7/Linux memory system CSAPP 9.7
Memory mapping CSAPP 9.8

## Slide 9: Simple Memory System Example
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
VPO
PPO
PPN
VPN
Virtual Page Number
Virtual Page Offset
Physical Page Number
Physical Page Offset
Why is the VPO 6 bits?
Why is the VPN 8 bits?
Why is the
VPN 8 bits?
Notes: Understanding these Why questions will be relevant for today’s quiz.

## Slide 10: Simple Memory System TLB
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
0
0
0
1
1
0
1
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Translation Lookaside Buffer (TLB)
VPN = 0b1101 = 0x0D

## Slide 11: Simple Memory System Page Table
Only showing the first 16 entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN
0x0D → 0x2D

## Slide 12: Simple Memory System Cache
16 lines, 4-byte cache line size
Physically addressed
Direct mapped
V[0b00001101101001] = V[0x369]
P[0b101101101001] = P[0xB69] = 0x15
1
11
0
10
1
9
1
8
0
7
1
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx
1
0
1
0
0
1
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx
Notes: Click to reveal PPO. Then run through lookup that retrieves 0x15 before clicking again to reveal the answer.

## Slide 13: Address Translation Example
TLB
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0x0F
0x3
0x03
Y
N
0x0D
Virtual Address: 0x03D4
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
0
0
0
1
0
1
0
1
1
0
1
0
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
0D
03
1

## Slide 14: Address Translation Example
Cache
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
1
0
1
0
1
1
0
1
0
0
0x5
0x0D
Y
0x36
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx

## Slide 15: Address Translation Example: TLB/Cache Miss
Virtual Address: 0x0020
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN
Page table
Notes: We are not showing the TLB on the slide, but by assumption it’s a TLB miss, so we need to look at the Page Table for the translation.

## Slide 16: Address Translation Example: TLB/Cache Miss
Cache
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
N
Mem
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx

## Slide 17: Virtual Memory Exam Question
------
------
0x4C20
------
Exam: http://www.cs.cmu.edu/~213/oldexams/exam2b-s11.pdf (solution)
13
12
11
10
9
8
7
6
5
4
3
2
1
0
TLBI
TLBT
15
14
0x7E85
0x7E85
TLBI = 0x2
TLBT = 0x1F
0x7E85  0x9585
0x9585
0
1
1
1
1
1
1
0
1
0
0
0
0
1
1
0
= 0x0111111010000101
PPN
Notes: Brandon: I find this slide confusing and unintuitive and not good as an exercise, so I am hiding it for now.

## Slide 18: Today
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 19: Intel Core i7 Memory System
L1 d-cache
32 KB, 8-way
L2 unified cache
256 KB, 8-way
L3 unified cache
8 MB, 16-way
(shared by all cores)
Main memory
Registers
L1 d-TLB
64 entries, 4-way
L1 i-TLB
128 entries, 4-way
L2 unified TLB
512 entries, 4-way
L1 i-cache
32 KB, 8-way
MMU
(addr translation)
Instruction
fetch
Core x4
DDR3 Memory controller
3 x 64 bit @ 10.66 GB/s
32 GB/s total (shared by all cores)
Processor package
QuickPath interconnect
4 links @ 25.6 GB/s each
To other
cores
To I/O
bridge

## Slide 20: End-to-end Core i7 Address Translation
CPU
VPN
VPO
36
12
TLBT
TLBI
4
32
...
L1 d-TLB (16 sets, 4 entries/set)
VPN1
VPN2
9
9
PTE
CR3
PPN
PPO
40
12
Page tables
TLB
miss
TLB
hit
Physical
address
(PA)
Result
32/64
...
CT
CO
40
6
CI
6
L2, L3, and
main memory
L1 d-cache
(64 sets, 8 lines/set)
L1
hit
L1
miss
Virtual address (VA)
VPN3
VPN4
9
9
PTE
PTE
PTE
Notes: 1. 48-bit virtual addresses and 52-bit physical addresses. Why would one ever need *more* DRAM than a complete virtual address space? Hold working sets for *many* concurrent processes.
2. 9-bit VPNi implies 8 byte PTEs

## Slide 21: Core i7 Level 1-3 Page Table Entries
Page table physical base address
Unused
G
PS
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page table. Significant fields:
P: Child page table present in physical memory (1) or not (0).
R/W: Read-only or read-write access access permission for all reachable pages.
U/S: user or supervisor (kernel) mode access permission for all reachable pages.
WT: Write-through or write-back cache policy for the child page table.
A: Reference bit (set by MMU on reads and writes, cleared by software).
PS: Page size either 4 KB or 4 MB (defined for Level 1 PTEs only).
Page table physical base address: 40 most significant bits of physical page table address (forces page tables to be 4KB aligned)
XD: Disable or enable instruction fetches from all pages reachable from this PTE.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page table location on disk)
P=0
52
62
63
Notes: Reference bit – used in LRU. G = Global page (don’t evict from TLB on task switch). CD = Caching disabled for the child page table.

## Slide 22: Core i7 Level 4 Page Table Entries
Page physical base address
Unused
G
D
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page. Significant fields:
P: Child page is present in memory (1) or not (0)
R/W: Read-only or read-write access permission for child page
U/S: User or supervisor mode access
WT: Write-through or write-back cache policy for this page
A: Reference bit (set by MMU on reads and writes, cleared by software)
D: Dirty bit (set by MMU on writes, cleared by software)
G: Global page (don’t evict from TLB on task switch)
Page physical base address: 40 most significant bits of physical page address (forces pages to be 4KB aligned)
XD: Disable or enable instruction fetches from this page.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page location on disk)
P=0
52
62
63
Notes: CD = Cache disabled or enabled

## Slide 23: Core i7 Page Table Translation
CR3
Physical
address
of page
Physical
address
of L1 PT
9
VPO
9
12
Virtual
address
L4 PT
Page
table
L4 PTE
PPN
PPO
40
12
Physical
address
Offset into
physical and
virtual page
VPN 3
VPN 4
VPN 2
VPN 1
L3 PT
Page middle
directory
L3 PTE
L2 PT
Page upper
directory
L2 PTE
L1 PT
Page global
directory
L1 PTE
9
9
40
/
40
/
40
/
40
/
40
/
12
/
512 GB
region
per entry
1 GB
region
per entry
2 MB
region
per entry
4 KB
region
per entry

## Slide 24: Cute Trick for Speeding Up L1 Access
Observation
  Bits that determine CI identical in virtual and physical address
  Can index into cache while address translation taking place
  Generally we hit in TLB, so PPN bits (CT bits) available quickly
  “Virtually indexed, physically tagged”
  Cache carefully sized to make this possible
Physical
address
(PA)
CT
CO
40
6
CI
6
Virtual
address
(VA)
VPN
VPO
36
12
PPO
PPN
Address
Translation
No
Change
CI
L1 Cache
CT
Tag Check

## Slide 25: Virtual Address Space of a Linux Process
Kernel code and data
Memory mapped region
for shared libraries
Runtime heap (malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
%rsp
Process
virtual
memory
brk
Physical memory
Identical for each process
Process-specific data
structs (ptables,
task and mm structs, kernel stack)
Kernel
virtual
memory
0x00400000
Different for each process

## Slide 26: Linux Organizes VM as Collection of “Areas”
vm_next
vm_next
task_struct
mm_struct
pgd
mm
mmap
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
Text
Data
Shared libraries
0
pgd:
  Page global directory address
  Points to L1 page table
vm_prot:
  Read/write permissions for this area
vm_flags
  Pages shared with other processes or private to this process
vm_flags
vm_flags
vm_flags
Each process has own task_struct, etc

## Slide 27: Linux Page Fault Handling
read
1
write
2
read
3
vm_next
vm_next
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
text
data
shared libraries
vm_flags
vm_flags
vm_flags
Segmentation fault:
accessing a non-existing page
Normal page fault
Protection exception:
e.g., violating permission by writing to a read-only page (Linux reports as Segmentation fault)

## Slide 28: Today
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 29: Memory Mapping
VM areas initialized by associating them with disk objects.
  Called memory mapping
Area can be backed by (i.e., get its initial values from) :
  Regular file on disk (e.g., an executable object file)
    Initial page bytes come from a section of a file
  Anonymous file (e.g., nothing)
    First fault will allocate a physical page full of 0's (demand-zero page)
    Once the page is written to (dirtied), it is like any other page
Dirty pages are copied back and forth between memory and a special swap file.

## Slide 30: Review: Memory Management & Protection
Code and data can be isolated or shared among processes
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 31: Sharing Revisited: Shared Objects
Process 1 maps the shared object (on disk).
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory

## Slide 32: Sharing Revisited: Shared Objects
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Process 2 maps the same shared object.
Notice how the virtual addresses can be different.
But, difference must be multiple of page size.

## Slide 33: Sharing Revisited: Private Copy-on-write (COW) Objects
Two processes mapping a private copy-on-write (COW) object
Area flagged as private copy-on-write
PTEs in private areas are flagged as read-only
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Private
copy-on-write
area

## Slide 34: Sharing Revisited: Private Copy-on-write (COW) Objects
Instruction writing to private page triggers protection fault.
Handler creates new R/W page.
Instruction restarts upon handler return.
Copying deferred as long as possible!
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Copy-on-write
Write to private
copy-on-write
page

## Slide 35: Finding Shareable Pages
Kernel Same-Page Merging
  OS scans through all of physical memory, looking for duplicate pages
  When found, merge into single copy, marked as copy-on-write
  Implemented in Linux kernel in 2009
  Limited to pages marked as likely candidates
  Especially useful when processor running many virtual machines
    A virtual machine is an abstraction for an entire computer, including its OS & I/O devices (beyond the scope of this course)

## Slide 36: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
Map len bytes starting at offset offset of the file specified by file description fd, preferably at address start
  start: may be 0 for “pick an address”
  prot: PROT_READ, PROT_WRITE, PROT_EXEC, ...
  flags: MAP_ANON, MAP_PRIVATE, MAP_SHARED, ...
Return a pointer to start of mapped area (may not be start)
Notes: PROT_READ = ok to read pages
PROT_WRITE = ok to read or write
PROT_EXEC = ok to execute
MAP_ANON = backing store is anonymous object & pages are demand-zeroed
MAP_PRIVATE = copy-on-write object
MAP_SHARED = shared object

## Slide 37: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
len bytes
start
(or address
chosen by kernel)
Process virtual memory
Disk file specified by
file descriptor fd
len bytes
offset
(bytes)
0
0

## Slide 38: Uses of mmap
Reading big files
  Uses paging mechanism to bring files into memory
Shared data structures
  When call with MAP_SHARED flag
    Multiple processes have access to same region of memory
    Risky!
File-based data structures
  E.g., database
  Give prot argument PROT_READ | PROT_WRITE
  When unmap region, file will be updated via write-back
  Can implement load from file / update / write back to file

## Slide 39: Example: Using mmap to Support Attack Lab
Problem
  Want students to be able to perform code injection attacks
  Shark machine stacks are not executable
Solution
  Suggested by Sam King (now at UC Davis)
  Use mmap to allocate region of memory marked executable
  Divert stack to new region
  Execute student attack code
  Restore back to original stack
  Use munmap to remove mapped region

## Slide 40: Using mmap to Support Attack Lab
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%rsp
(stack
pointer)
Memory
invisible to
user code
0x40000000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)

## Slide 41: Using mmap to Support Attack Lab
0x55586000
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%rsp
(stack
pointer)
Memory
invisible to
user code
0x40000000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)
Region created by mmap
0x55586000
Notes: Save a copy of the original %rsp, before update %rsp to point to start of mmap region.

## Slide 42: Using mmap to Support Attack Lab
0x55586000
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%rsp
(stack
pointer)
Memory
invisible to
user code
0x40000000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)
Region created by mmap
0x55586000
Frame for launch
Frame for test
Frame for getbuf

## Slide 43: Using mmap to Support Attack Lab
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%rsp
(stack
pointer)
Memory
invisible to
user code
0x40000000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)
Restore original %rsp
Use munmap to remove mapped region

## Slide 44: Summary
VM requires hardware support
  Exception handling mechanism
  TLB
  Various control registers
VM requires OS support
  Managing page tables
  Implementing page replacement policies
  Managing file system
VM enables many capabilities
  Loading programs from memory
  Providing memory protection

## Slide 45: Using mmap to Support Attack Lab
stack_top = new_stack + STACK_SIZE - 8;
asm("movq %%rsp,%%rax ; movq %1,%%rsp ; movq %%rax,%0"
: "=r" (global_save_stack) // %0
: "r" (stack_top) // %1
);
launch(global_offset);
void *new_stack = mmap(START_ADDR, STACK_SIZE, PROT_EXEC|PROT_READ|PROT_WRITE,
MAP_PRIVATE | MAP_GROWSDOWN | MAP_ANONYMOUS | MAP_FIXED,
0, 0);
if (new_stack != START_ADDR) {
munmap(new_stack, STACK_SIZE);
exit(1);
}
asm("movq %0,%%rsp"
:
: "r" (global_save_stack) // %0
);
munmap(new_stack, STACK_SIZE);
Allocate new region
Divert stack to new region & execute attack code
Restore stack and remove region