## Slide 1: Parallelism and the Memory Hierarchy Todd C. Mowry & Dave Eckhardt
Brief History of Parallel Processing
Impact of Parallelism on Memory Protection
Cache Coherence

## Slide 2: A Brief History of Parallel Processing
Initial Focus (starting in 1970’s): “Supercomputers” for Scientific Computing
C.mmp at CMU (1971)
16 PDP-11 processors
Cray XMP (circa 1984)
4 vector processors
Thinking Machines CM-2 (circa 1987)
65,536 1-bit processors +
2048 floating-point co-processors
SGI UV 1000cc-NUMA (today)
4096 processor cores
Blacklight at the Pittsburgh Supercomputer Center

## Slide 3: A Brief History of Parallel Processing
Initial Focus (starting in 1970’s): “Supercomputers” for Scientific Computing
Another Driving Application (starting in early 90’s): Databases
Sun Enterprise 10000 (circa 1997)
64 UltraSPARC-II processors
Oracle SuperCluster M6-32 (today)
32 SPARC M2 processors

## Slide 4: A Brief History of Parallel Processing
Initial Focus (starting in 1970’s): “Supercomputers” for Scientific Computing
Another Driving Application (starting in early 90’s): Databases
Inflection point in 2004: Intel hits the Power Density Wall
Pat Gelsinger, ISSCC 2001

## Slide 5: Impact of the Power Density Wall
The real “Moore’s Law” continues
  i.e. # of transistors per chip continues to increase exponentially
But thermal limitations prevent us from scaling up clock rates
  otherwise the chips would start to melt, given practical heat sink technology
How can we deliver more performance to individual applications?
  increasing numbers of cores per chip
Caveat:
  in order for a given application to run faster, it must exploit parallelism

## Slide 6: Parallel Machines Today
Examples from Apple’s product line:
(Images from apple.com)
iPhone 6
2 A8 cores
iPad Air 2
3 A8X cores
MacBook Pro Retina 15”
4 Intel Core i7 cores
iMac
4 Intel Core i5 cores
Mac Pro
12 Intel Xeon E5 cores

## Slide 7: Example “Multicore” Processor: Intel Core i7
Cores: six 3.33 GHz Nahelem processors (with 2-way “Hyper-Threading”)
Caches: 64KB L1 (private), 256KB L2 (private), 12MB L3 (shared)
Intel Core i7-980X (6 cores)

## Slide 8: Impact of Parallel Processing on the Kernel (vs. Other Layers)
Kernel itself becomes a parallel program
  avoid bottlenecks when accessing data structures
    lock contention, communication, load balancing, etc.
  use all of the standard parallel programming tricks
Thread scheduling gets more complicated
  parallel programmers usually assume:
    all threads running simultaneously
      load balancing, avoiding synchronization problems
    threads don’t move between processors
      for optimizing communication and cache locality
Primitives for naming, communicating, and coordinating need to be fast
  Shared Address Space: virtual memory management across threads
  Message Passing: low-latency send/receive primitives
Programmer
Programming Language
Compiler
User-Level Run-Time SW
Kernel
Hardware
System Layers

## Slide 9: Case Study: Protection
One important role of the OS:
  provide protection so that buggy processes don’t corrupt other processes
Shared Address Space:
  access permissions for virtual memory pages
    e.g., set pages to read-only during copy-on-write optimization
Message Passing:
  ensure that target thread of send() message is a valid recipient

## Slide 10: How Do We Propagate Changes to Access Permissions?
What if parallel machines (and VM management) simply looked like this:
  (assume that this is a parallel program, deliberately sharing pages)
Updates to the page tables (in shared memory) could be read by other threads
But this would be a very slow machine!
  Why?
CPU 0
CPU 1
CPU 2
CPU N
…
Memory
Page Table
Read-Write
Read-Only
f029
f835
Set Read-Only
Read-Only
(No caches or TLBs.)

## Slide 11: VM Management in a Multicore Processor
“TLB Shootdown”:
  relevant entries in the TLBs of other processor cores need to be flushed
CPU 0
CPU 1
CPU 2
CPU N
…
Memory
Page Table
Read-Write
Read-Only
f029
f835
Read-Only
TLB 0
TLB 1
TLB 2
TLB N
L3 Cache
L2 $
L1 $
L2 $
L1 $
L2 $
L1 $
L2 $
L1 $
Set Read-Only

## Slide 12: TLB Shootdown (Example Design)
Initiating core triggers OS to lock the corresponding Page Table Entry (PTE)
OS generates a list of cores that may be using this PTE (erring conservatively)
Initiating core sends an Inter-Processor Interrupt (IPI) to those other cores
  requesting that they invalidate their corresponding TLB entries
Initiating core invalidates local TLB entry; waits for acknowledgements
Other cores receive interrupts, execute interrupt handler which invalidates TLBs
  send an acknowledgement back to the initiating core
Once initiating core receives all acknowledgements, it unlocks the PTE
CPU 0
CPU 1
CPU 2
CPU N
…
TLB 0
TLB 1
TLB 2
TLB N
Page Table
Read-Write
Read-Only
f029
f835
Read-Only
Lock PTE
0 1 2 N

## Slide 13: TLB Shootdown Timeline
Image from: Villavieja et al, “DiDi: Mitigating the Performance Impact of TLB Shootdowns Using a Shared TLB Directory.” In Proceedings of PACT 2011.

## Slide 14: Performance of TLB Shootdown
  Expensive operation
    e.g., over 10,000 cycles on 8 or more cores
  Gets more expensive with increasing numbers of cores
Image from: Baumann et al,“The Multikernel: a New OS Architecture for Scalable Multicore Systems.” In Proceedings of SOSP ‘09.

## Slide 15: Now Let’s Consider Consistency Issues with the Caches
CPU 0
CPU 1
CPU 2
CPU N
…
Memory
TLB 0
TLB 1
TLB 2
TLB N
L3 Cache
L2 $
L1 $
L2 $
L1 $
L2 $
L1 $
L2 $
L1 $

## Slide 16: Caches in a Single-Processor Machine (Review from 213)
Ideally, memory would be arbitrarily fast, large, and cheap
  unfortunately, you can’t have all three (e.g., fast  small, large  slow)
  cache hierarchies are a hybrid approach
    if all goes well, they will behave as though they are both fast and large
Cache hierarchies work due to locality
  temporal locality  even relatively small caches may have high hit rates
  spatial locality  move data in blocks (e.g., 64 bytes)
Locating the data:
  Main memory: directly (geographically) addressed
    we know exactly where to look:
      at the unique location corresponding to the address
  Cache: may or may not be somewhere in the cache
    need tags to identify the data
    may need to check multiple locations, depending on the degree of associativity

## Slide 17: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 18: Intel Quad Core i7 Cache Hierarchy
Regs
L1
D-cache
L1
I-cache
L2 unified cache
Core 0
Regs
L1
D-cache
L1
I-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 I-cache and D-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Block size: 64 bytes for all caches.

## Slide 19: Simple Multicore Example: Core 0 Loads X
L1-D
L2
Core 0
Core 3
…
L3
Main memory
load r1  X
(1) Miss
(2) Miss
(3) Miss
X: 17
(r1 = 17)
(4) Retrieve from memory, fill caches
X
17
X
17
X
17
L1-D
L2

## Slide 20: Example Continued: Core 3 Also Does a Load of X
L1-D
L2
Core 0
Core 3
…
L3
Main memory
load r2  X
(3) Hit! (fill L2 & L1)
X: 17
(r2 = 17)
X
17
X
17
X
17
L1-D
L2
(1) Miss
(2) Miss
X
17
X
17
Fairly straightforward with only loads. But what happens when stores occur?
Example of constructive sharing:
Core 3 benefited from Core 0 bringing X into the L3 cache

## Slide 21: Review: How Are Stores Handled in Uniprocessor Caches?
L1-D
L2
L3
Main memory
X: 17
X
17
X
17
X
17
store 5  X
17  5
What happens here?
We need to make sure we don’t have a consistency problem

## Slide 22: Options for Handling Stores in Uniprocessor Caches
L1-D
L2
L3
Main memory
X: 17
X
17
X
17
X
17
store 5  X
Option 1: Write-Through Caches
17  5
17  5
17  5
17  5
 propagate “immediately”
What are the advantages and disadvantages
of this approach?
(1)
(2)
(3)

## Slide 23: Options for Handling Stores in Uniprocessor Caches
L1-D
L2
L3
Main memory
X: 17
X
17
X
17
X
17
store 5  X
Option 1: Write-Through Caches
17  5
17  5
17  5
17  5
propagate immediately
L1-D
L2
L3
Main memory
X: 17
X
17
X
17
X
17
Option 2: Write-Back Caches
17  5
defer propagation until eviction
keep track of dirty status in tags
Dirty
Upon eviction,
if data is dirty, write it back.
Write-back is more commonly used in practice (due to bandwidth limitations)
(Analogous to
PTE dirty bit.)

## Slide 24: Resuming Multicore Example
L1-D
L2
Core 0
Core 3
…
L3
Main memory
X: 17
X
17
X
17
X
17
L1-D
L2
X
17
X
17
What is supposed to happen in this case?
Is it incorrect behavior for r2 to equal 17?
if not, when would it be?
(Note: core-to-core communication often takes tens of cycles.)
1. store 5  X
17  5
Dirty
2. load r2  X
(r2 = 17) Hmm…
Hit!

## Slide 25: What is Correct Behavior for a Parallel Memory Hierarchy?
Note: side-effects of writes are only observable when reads occur
  so we will focus on the values returned by reads
Intuitive answer:
  reading a location should return the latest value written (by any thread)
Hmm… what does “latest” mean exactly?
  within a thread, it can be defined by program order
  but what about across threads?
    the most recent write in physical time?
      hopefully not, because there is no way that the hardware can pull that off
        e.g., if it takes >10 cycles to communicate between processors, there is no way that processor 0 can know what processor 1 did 2 clock ticks ago
    most recent based upon something else?
      Hmm…

## Slide 26: Refining Our Intuition
What would be some clearly illegal combinations of (A,B,C)?
How about:
What can we generalize from this?
  writes from any particular thread must be consistent with program order
    in this example, observed even numbers must be increasing (ditto for odds)
  across threads: writes must be consistent with a valid interleaving of threads
    not physical time! (programmer cannot rely upon that)
// write evens to X
for (i=0; i<N; i+=2) {
X = i;
…
}
Thread 0
// write odds to X
for (j=1; j<N; j+=2) {
X = j;
…
}
Thread 1
…
A = X;
…
B = X;
…
C = X;
…
Thread 2
(Assume: X=0 initially, and these are the only writes to X.)
(4,8,1)?
(9,12,3)?
(7,19,31)?

## Slide 27: Visualizing Our Intuition
Each thread proceeds in program order
Memory accesses interleaved (one at a time) to a single-ported memory
  rate of progress of each thread is unpredictable
// write evens to X
for (i=0; i<N; i+=2) {
X = i;
…
}
Thread 0
// write odds to X
for (j=1; j<N; j+=2) {
X = j;
…
}
Thread 1
…
A = X;
…
B = X;
…
C = X;
…
Thread 2
CPU 0
CPU 1
CPU 2
Memory
Single port to memory

## Slide 28: Correctness Revisited
Recall: “reading a location should return the latest value written (by any thread)”
  “latest” means consistent with some interleaving that matches this model
  this is a hypothetical interleaving; the machine didn’t necessary do this!
// write evens to X
for (i=0; i<N; i+=2) {
X = i;
…
}
Thread 0
// write odds to X
for (j=1; j<N; j+=2) {
X = j;
…
}
Thread 1
…
A = X;
…
B = X;
…
C = X;
…
Thread 2
CPU 0
CPU 1
CPU 2
Memory
Single port to memory

## Slide 29: Two Parts to Memory Hierarchy Correctness
“Cache Coherence”
  do all loads and stores to a given cache block behave correctly?
    i.e. are they consistent with our interleaving intuition?
    important: separate cache blocks have independent, unrelated interleavings!
“Memory Consistency Model”
  do all loads and stores, even to separate cache blocks, behave correctly?
    builds on top of cache coherence
    especially important for synchronization, causality assumptions, etc.

## Slide 30: Cache Coherence (Easy Case)
One easy case: a physically shared cache
L1-D
L2
Core 0
Core 3
…
L3
L1-D
L2
L3 cache is physically shared by on-chip cores
Intel Core i7
X
17

## Slide 31: Cache Coherence (Easy Case)
One easy case: a physically shared cache
L1-D
L2
Core 0
…
2-way Hyperthreading
Thread 1
Thread 0
Intel Core i7
L1 cache (plus L2, L3) is physically shared by Thread 0 and Thread 1

## Slide 32: Cache Coherence: Beyond the Easy Case
How do we implement L1 & L2 cache coherence between the cores?
Common approaches: update or invalidate protocols
L1-D
L2
Core 0
Core 3
…
L3
L1-D
L2
X
17
X
17
X
17
X
17
X
17
???
store 5  X

## Slide 33: One Approach: Update Protocol
Basic idea: upon a write, propagate new value to shared copies in peer caches
L1-D
L2
Core 0
Core 3
…
L3
L1-D
L2
X
17
X
17
X
17
X
17
X
17
store 5  X
17  5
17  5
17  5
17  5
17  5
X = 5
update

## Slide 34: Another Approach: Invalidate Protocol
Basic idea: to perform a write, first delete any shared copies in peer caches
L1-D
L2
Core 0
Core 3
…
L3
L1-D
L2
X
17
X
17
X
17
X
17
X
17
store 5  X
17  5
17  5
17  5
Delete X
invalidate
X
17
X
17
Invalid
Invalid

## Slide 35: Update vs. Invalidate
When is one approach better than the other?
  (hint: the answer depends upon program behavior)
Key question:
  Is a block written by one processor read by others before it is rewritten?
  if so, then update may win:
    readers that already had copies will not suffer cache misses
  if not, then invalidate wins:
    avoids useless updates (including to dead copies)
Which one is used in practice?
  invalidate (due to hardware complexities of update)
    although some machines have supported both (configurable per-page by the OS)

## Slide 36: How Invalidation-Based Cache Coherence Works (Short Version)
Cache tags contain additional coherence state (“MESI” example below):
  Invalid:
    nothing here (often as the result of receiving an invalidation message)
  Shared (Clean):
    matches the value in memory; other processors may have shared copies also
    I can read this, but cannot write it until I get an exclusive/modified copy
  Exclusive (Clean):
    matches the value in memory; I have the only copy
    I can read or write this (a write causes a transition to the Modified state)
  Modified (aka Dirty):
    has been modified, and does not match memory; I have the only copy
    I can read or write this; I must supply the block if another processor wants to read
The hardware keeps track of this automatically
  using either broadcast (if interconnect is a bus) or a directory of sharers
(Not “Messi”)

## Slide 37: Performance Impact of Invalidation-Based Cache Coherence
Invalidations result in a new source of cache misses!
Recall that uniprocessor cache misses can be categorized as:
  (i) cold/compulsory misses, (ii) capacity misses, (iii) conflict misses
Due to the sharing of data, parallel machines also have misses due to:
  (iv) true sharing misses
    e.g., Core A reads X  Core B writes X  Core A reads X again (cache miss)
      nothing surprising here; this is true communication
  (v) false sharing misses
    e.g., Core A reads X  Core B writes Y  Core A reads X again (cache miss)
      What???
      where X and Y unfortunately fell within the same cache block

## Slide 38: Beware of False Sharing!
It can result in a devastating ping-pong effect with a very high miss rate
  plus wasted communication bandwidth
Pay attention to data layout:
  the threads above appear to be working independently, but they are not
while (TRUE) {
X += …
…
}
L1-D
Core 0
Core 1
L1-D
while (TRUE) {
Y += …
…
}
X
…
Y
…
X
…
Y
…
X
…
Y
…
1 block
invalidations,
cache misses
Thread 1
Thread 0

## Slide 39: How False Sharing Might Occur in the OS
Operating systems contain lots of counters (to count various types of events)
  many of these counters are frequently updated, but infrequently read
Simplest implementation: a centralized counter
  Perfectly reasonable on a sequential machine.
But it performs very poorly on a parallel machine. Why?
  each update of get_tid_ctr invalidates it from other processor’s caches
// Number of calls to get_tid
int gettid_ctr = 0;
int gettid(void) {
atomic_add(&gettid_ctr,1);
return (running->tid);
}
int get_gettid_events(void) {
return (gettid_ctr);
}

## Slide 40: “Improved” Implementation: An Array of Counters
Each processor updates its own counter
To read the overall count, sum up the counter array
Eliminates lock contention, but may still perform very poorly. Why?
  False sharing!
int gettid_ctr[NUM_CPUs]= {0};
int gettid(void) {
// exact coherence not required
gettid_ctr[running->CPU]++;
return (running->tid);
}
int get_gettid_events(void) {
int cpu, total = 0;
for (cpu = 0; CPU < NUM_CPUs; cpu++)
total += gettid_ctr[cpu];
return (total);
}
No longer need a
lock around this.

## Slide 41: Faster Implementation: Padded Array of Counters
Put each private counter in its own cache block.
  (any downsides to this?)
struct {
int get_tid_ctr;
int PADDING[INTS_PER_CACHE_BLOCK-1];
} ctr_array[NUM_CPUs];
int get_tid(void) {
ctr_array[running->CPU].get_tid_ctr++;
return (running->tid);
}
int get_tid_count(void) {
int cpu, total = 0;
for (cpu = 0; CPU < NUM_CPUs; cpu++)
total += ctr_array[cpu].get_tid_ctr;
return (total);
}
Even better:
replace PADDING
with other useful
per-CPU counters.

## Slide 42: Parallel Counter Implementation Summary
Centralized:
Simple Array:
Padded Array:
Clustered Array:
CPU 0
CPU 1
CPU 2
CPU 3
…
CPU 0
CPU 1
CPU 2
CPU 3
…
…
Cache Block
CPU 0
CPU 1
CPU 2
CPU 3
…
Cache Block
Cache Block
Cache Block
…
CPU 0
CPU 1
CPU 2
CPU 3
…
Cache Block
Cache Block
Cache Block
…
Mutex
contention?
False
sharing?
Wasted space?
(If there are multiple counters to pack together.)

## Slide 43: True Sharing Can Benefit from Spatial Locality
With true sharing, spatial locality can result in a prefetching benefit
Hence data layout can help or harm sharing-related misses in parallel software
X = …
Y = …
…
…
L1-D
Core 0
Core 1
L1-D
…
…
r1 = X;
r2 = Y;
X
…
Y
…
X
…
Y
…
X
…
Y
…
1 block
both X and Y
sent in 1 miss
Thread 1
Thread 0
Cache Hit!
Cache Miss

## Slide 44: Options for Building Even Larger Shared Address Machines
Tradeoffs?
NUMA is more commonly used at large scales (e.g., Blacklight at the PSC)
…
CPU 0
Memory 0
Memory 1
Memory N
Interconnection Network
CPU 1
CPU N
…
Symmetric Multiprocessor (SMP):
…
CPU 0
Memory 0
CPU 1
Memory 1
CPU N
Memory N
Interconnection Network
Non-Uniform Memory Access (NUMA):

## Slide 45: Summary
Case study: memory protection on a parallel machine
  TLB shootdown
    involves Inter-Processor Interrupts to flush TLBs
Part 1 of Memory Correctness: Cache Coherence
  reading “latest” value does not correspond to physical time!
    corresponds to latest in hypothetical interleaving of accesses
  new sources of cache misses due to invalidations:
    true sharing misses
    false sharing misses
Looking ahead: Part 2 of Memory Correctness, plus Scheduling Revisited

## Slide 46: Omron Luna88k Workstation
From circa 1991: ran a parallel Mach kernel (on the desks of lucky CMU CS Ph.D. students) four years before the Pentium/Windows 95 era began.
Jan 1 00:28:40 luna88k vmunix: CPU0 is attached
Jan 1 00:28:40 luna88k vmunix: CPU1 is attached
Jan 1 00:28:40 luna88k vmunix: CPU2 is attached
Jan 1 00:28:40 luna88k vmunix: CPU3 is attached
Jan 1 00:28:40 luna88k vmunix: LUNA boot: memory from 0x14a000 to 0x2000000
Jan 1 00:28:40 luna88k vmunix: Kernel virtual space from 0x00000000 to 0x79ec000.
Jan 1 00:28:40 luna88k vmunix: OMRON LUNA-88K Mach 2.5 Vers 1.12 Thu Feb 28 09:32 1991 (GENERIC)
Jan 1 00:28:40 luna88k vmunix: physical memory = 32.00 megabytes.
Jan 1 00:28:40 luna88k vmunix: available memory = 26.04 megabytes.
Jan 1 00:28:40 luna88k vmunix: using 819 buffers containing 3.19 megabytes of memory
Jan 1 00:28:40 luna88k vmunix: CPU0 is configured as the master and started.