## Slide 1: Control of Instantaneously Coupled Systems Applied to Humanoid Walking
Eric C. Whitman & Christopher G. Atkeson
Carnegie Mellon University

## Slide 2: Related Work
Trajectory generation + trajectory tracking
  Takanishi 1990, Kajita 2003
Online regeneration of trajectories
  Nishiwaki 2006
Model Predictive Control/Receding Horizon Control
  Wieber 2006
Optimize footstep locations
  Diedam 2008

## Slide 3: Dynamic Programming
Bellman Equation:
x1
x2
Christopher G. Atkeson, “Randomly sampling actions in dynamic programming”, IEEE Symposium on Approximate Dynamic Programming and Reinforcement Learning, 2007.

## Slide 4: Dynamic Programming Output
Inverted Pendulum:
Swing-up

## Slide 5: A Dynamic Programming Solution
Offline computation
Can optimize CoM motion and footstep timing/location
Even a simple model has a 10-D state space
  Too high for DP
Decouple to reduce dimensionality
Add coordination variables to maintain optimality
10010=1020 >> 1004+1004+1003+1003+1003=2.03x108

## Slide 6: Simplify the System
DOFS:
12 + 6 = 18
DOFS:
12 + 6 – 3 = 15
Origin at foot
DOFS:
12 + 6 – 3 – 2*3 = 9
Origin at foot
Feet don’t rotate
DOFS:
12 + 6 – 3 – 2*3 – 3 = 6
Origin at foot
Feet don’t rotate
Torso doesn’t rotate
DOFS:
12 + 6 – 3 – 2*3 – 3 – 1 = 5
Origin at foot
Feet don’t rotate
Torso doesn’t rotate
Constant height CoM

## Slide 7: The Simple System
3D LIPM
- 2 DOFS
Fully Controllable Swing Foot
- 3 DOFS
Kajita et. Al., “The 3d Linear Inverted Pendulum Model: A simple modeling for biped walking pattern generation”, ICRA 2001.

## Slide 8: Instantaneously Coupled Systems (ICS)
Partition the state and action space
Normally dynamics are independent
Dynamics are coupled at specific instants
Additive cost -> Independent Policies

## Slide 9: Decoupling the System
X
Y
Z
X
Z
Y
Z
Panne et. Al., “A controller for the dynamic walk of a biped across variable terrain”, Conference on Decision and Control, 1992.
Yin et. Al., “Simbicon: simple biped locomotion control”, SIGGRAPH 2007.
Sagittal Subsystem
Coronal Subsystem
Z
Swing-Z
Subsystem

## Slide 10: Adding Coordination Variables
Solve for all possible and pick the best later
Add as an additional state to all sub-systems
  Trivial dynamics:
DP produces
At run-time, we have , so we get

## Slide 11: Value: V(ttd)

## Slide 12: ttd

## Slide 13: Coordinating Footstep Time & Location
Split up stance & swing legs
  5 Policies – one for each DoF
Replace with
  Drop/combine unnecessary variables
DP produces
At run-time, we have , so we get
Pick optimal by minimizing

## Slide 14: Full Controller
System
State
Subsystem Value
Functions
Subsystem Policies
Stance Ankle Torque
Swing Foot Acceleration
Dynamic Balance
Force Control
Joint
Torques
Benjamin J. Stephens, “Dynamic balance force control for compliant
humanoid robots”, IROS 2010.
Optimize Coordination Variables

## Slide 15: Results – Push Recovery Video

## Slide 16: Results – Push Recovery
Rightward Pushes
Forward Pushes
Rearward Pushes
Leftward Pushes

## Slide 17: Results – Push Recovery

## Slide 18: Results – Speed Control Video

## Slide 19: Results – Speed Control

## Slide 20: Future Work
Implement on hardware
Increase capability
  Turning
  Rough/uneven ground
Improve performance
  Torso rotation
  Non-LIPM walking
  Arm swing
  Toe off / Heel strike

## Slide 21: Conclusion/Key Points
Dynamic programming is valid for large regions of state space and fast at run-time
Splitting the system into subsystems makes dynamic programming feasible
Augmenting the subsystems with coordination variables restores optimality
Simultaneously optimizes CoM motion, footstep timing, and footstep location
React in real-time to unexpected disturbances

## Slide 22: Questions?

## Slide 23: Walking as an ICS
Sagittal
Coronal
Swing-Z
States:
Actions:
X
Z
Y
Z
Z

## Slide 24: Separate Policies for Stance & Swing Legs
States:
Actions:

## Slide 25: The System
Bentivegna et. Al., “Compliant control of a compliant humanoid joint”, Humanoids 2007.

## Slide 26: ttd/tlo as a State
Trivial Dynamics:

## Slide 27: Forward Push Video

## Slide 28: Backward Push Videos