## Slide 1: Lecture 18 Deformable / Non-Rigid Registration ch. 11 of Insight into Images edited by Terry Yoo, et al.
Notes: Note: To print these slides in grayscale (e.g., on a laser printer), first change the Theme Background to “Style 1” (i.e., dark text on white background), and then tell PowerPoint’s print dialog that the “Output” is “Grayscale.” Everything should be clearly legible then. This is how I also generate the .pdf handouts.

## Slide 2: Registration: “Rigid” vs. Deformable
Rigid Registration:
  Uses a simple transform, uniformly applied
  Rotations, translations, etc.
Deformable Registration:
  Allows a non-uniform mapping between images
  Measure and/or correct small, varying discrepancies by deforming one image to match the other
  Usually only tractable for deformations of small spatial extent!

## Slide 3: Deformable, i.e. Non-Rigid, Registration (NRR)
Vector field (aka deformation field) T is computed from A to B
Inverse warp transforms B into A’s coordinate system
Not only do we get correspondences, but…
We also get shape differences (from T)
A
B
B(T)

## Slide 4: NRR Clinical Background
Internal organs are non-rigid
The body can change posture
  Even skeletal arrangement can change
Single-patient variations:
  Normal
  Pathological
  Treatment-related
Inter-subject mapping: People are different!
  Atlas-based segmentation typically requires NRR

## Slide 5: More Clinical Examples
Physical brain deformation during neurosurgery
Normal squishing, shifting and emptying of abdominal/pelvic organs and soft tissues
  Digestion, excretion, heart-beat, breathing, etc.
Lung motion during respiration can be huge!
Patient motion during image scanning

## Slide 6: Optical Flow
Traditionally for determining motion in video—assumes 2 sequential images
Detects small shifts of small intensity patterns from one image to the next
Output is a vector field, one vector for each small image patch/intensity pattern
Basic gradient-based formulation assumes intensity values are conserved over time

## Slide 7: Optical Flow Assumptions
Images are a function of space and time
After short time dt, the image has moved dx
Velocity vector v = dx/dt is the optical flow
  I(x, t) = I(x+dx, t+dt) = I(x+vdt, t+dt)
Resulting optical flow constraint:
  Cof = Ixv + It = 0
Image spatial gradient
Image temporal derivative

## Slide 8: Optical Flow Constraint
Optical flow constraint dictates that when an image patch is spatially shifted over time, that it will retain its intensity values
Let image A = I(x, t =0) and let B = I(x, t =1)
Then It = A(T) – B
This alone is not a sufficient constraint!

## Slide 9: NRR Is Ill-Posed
Review of well-posed problems:
  A solution exists, is unique, and depends continuously on the data
  Otherwise, a problem is ill-posed
Ambiguity within homogenous regions:
A
B
?
Notes: So, solution is NOT unique!

## Slide 10: Very Ill-Posed Problem
NRR answer is not unique, and…
NRR Search-space is often ∞-dimensional!
Solution: Regularization
  Adding a regularization term can provide provable uniqueness and a computable subspace
Regularization usually based on continuum mechanics
  T is restricted to be physically admissible
  We’re typically deforming physical anatomy, after all
  Optimum T should deform “just enough” for alignment
Notes: But what about Inter-subject mapping?

## Slide 11: NRR Regularization Methods
Numerous continuum mechanical models available for regularization priors
  Elastic
  Diffusion
  Viscous
  Flow
  Curvature
Optimization is then physical simulation over time, t, of trying to deform one image shape to match another
This optimization has 3 equivalent formulations:
  Global potential energy minimization
  Variational or weak form, as used in finite-element methods
  Euler-Lagrangian (E-L) equations, as used in finite-difference techniques

## Slide 12: Langrangian View
Elastic physical model:
  How much have we stretched, etc., from our original image coordinates?
  Simulation calculates the physical model’s resistance to deformation based on the total deformation from time t=0 to t=now.
T is the final vector field ūf :
  ūf = ū( t=tfinal )
  A(X + ūf) ~ B(x)
  X = x - ūf
Deformation at time t:
Deformation at time t + dt:
A( X )
A( X+ū(t) )
A( X )
A( X+ū(t+dt) )
Notes: Note: Capital X for A’s original coordinates
Lowercase x for B’s original coordinates

## Slide 13: Eulerian View
A( x+v(t) )
Viscous-flow physical model:
  How much have we flowed from our immediately previous simulation state?
  Simulation calculates the physical model’s resistance to deformation based on the incremental deformation from time t=(now-1) to t=now.
T is the aggregate flow of x(t), based on accumulated optical flow (i.e. velocity) v(t):
  x(t) = x + v(t)
  A( x(t=tfinal) ) ~ B(x)
Deformation at time t:
Deformation at time t + dt:
A( x )
A( x+v(t) )
A( x+v(t+dt) )
Notes: Note: Lowercase x for B’s original coordinates

## Slide 14: Comparison of Regularization Reference Frames
Langrangian
  The entire deformation is regularized
    Well constrained for “normal” physical deformation
    Too constrained to achieve “large” deformations
  Not ideal for many inter-subject mapping tasks
Eulerian
  Only the incremental updates are regularized
    Underconstrained for “normal” physical deformation
    Readily achieves large, inter-subject deformations
  Unrealistic transformations can result

## Slide 15: Transient Quadratic (TQ) Approach
Enables better-constrained large deformations
Uses Lagrangian regularization for specified time interval, followed by a re-gridding strategy
  After an interval’s deformation reaches a threshold, we begin a new interval for which the last deformation becomes the new starting point
  TQ thus resets the coordinate system while permanently storing the past state of the algorithm
Results in a hybrid E+L physical model, resembling soft, stretchable plastic
  Maintains the elastic regularization for a given time then takes on a new shape until new stresses are applied

## Slide 16: Optical Flow Regularized
Goal: Minimize global potential energy, ED
First term adjusts v to make the images match (wants Cof = 0 within the bounded domain Ω)
Second term adds a stabilizing function Ψ, typically a regulator operator L applied to v

## Slide 17: Optical Flow E-L Regularized
After deriving the E-L equations & setting their derivative = 0, we find that the…
Potential energy minimum will occur when:
First term minimizes optical flow constraint
Second term minimizes Laplacian (i.e. roughness) of velocity field v
Note that this equation is evaluated locally
  Allows for efficient implementation

## Slide 18: Demons Algorithm: Math
Very efficient gradient-descent NRR algorithm
Originally conceived as having “demons” push image level sets around, but is also…
Based on E-L regularized optical flow
Alternates between minimizing each half of the previous equation:
  Descent in optical flow direction, based on:
  Smoothing, which estimates vxx=0 with a difference-of-Gaussian filter, by applying a Gaussian on each iteration

## Slide 19: Demons Algorithm: Code
Initialize solution (i.e. total vector field) = Identity
Loop:
  Estimate vector field update
    Use (stabilized) optical flow
  Add update to total vector field
  Blur total vector field (for regularization)
Allows much larger deformation fields than optical flow alone.
Langrangian registration: blur the total vector field (as above)
Eulerian registration: blur the individual vector-field updates

## Slide 20: Choices & Details
There are many more NRR algorithms available
Almost all of them are slower than demons, but they may give you better results
See the text for details, and lots of helpful pictures