## Slide 1: RouteBricks: Exploiting Parallelism To Scale Software Routers
Mihai Dobrescu et al.
SOSP 2009 Best Paper
Presentor : Hun Namkung

## Slide 2: Contents
Introduction
Parallelizing Across Servers
Parallelizing Within Servers
Evaluation
Conclusion
HW Router
RouteBricks
Many of the contents are from SOSP 2009 Slides

## Slide 3: Contents
Introduction
Parallelizing Across Servers
Parallelizing Within Servers
Evaluation
Conclusion
HW Router
RouteBricks
Many of the contents are from SOSP 2009 Slides

## Slide 4: 1. Introduction
HW router
  Fast
  Throughput : Tbps
  No programmability
SW router
  Throughput < 10Gbps
  General-purpose CPUs
  Programmable
    New network services / Research innovation / Management / etc
1.1 HW router vs SW router

## Slide 5: 1. Introduction
Off-the-shelf PCs
  Uses Purely general purpose CPUs, purely software router
Advantage
  Familiar programming environment
  Large-volume manufacturers, thus low cost
  Rapid advances in technology/features
Can this approach achieve Tbps?
  Goal : achieve performance/scalability as much as possible
1.2 RouteBricks
RouteBricks

## Slide 6: 2. Parallelizing Across Servers
2.1 Requirements
Internal link rates < R (low cost)
Per-server processing rate : c x R (where c > 1, independent from N, scalability)
Per-server fanout : constant (scalability)

## Slide 7: 2. Parallelizing Across Servers
2.2 A Naïve Solution
internal links of capacity R, not cost efficient.

## Slide 8: 2. Parallelizing Across Servers
2.3 Better Solution – VLB(Valiant Load Balancing)
L. Valiant et al. Universal Schemes for Parallel Communication. (STOC), 1981.
One more layer
Link capacity R -> R/N

## Slide 9: 2. Parallelizing Across Servers
2 x internal links of R/N, more cost efficient
Does not solve limited fanout problem
2.3 Better Solution – VLB(Valiant Load Balancing)

## Slide 10: 2. Parallelizing Across Servers
2.4 Extend VLB
1. Single server handle multiple ports
2. Add more layer as you need
Off-the-shelf PCs-> limited number of PCIe slots (i.e 5 NICs)
By combining both techniques, any number of ports(ie, N=32 or N=1024) can be supported
Tradeoff : throughput will be degraded (each server need increased capacity)

## Slide 11: 3. Parallelizing Within Servers
3.1 NUMA architecture
Sheer forwarding

## Slide 12: 3. Parallelizing Within Servers
3.2 Result

## Slide 13: 3. Parallelizing Within Servers
3.3 Batch Processing
Result : 1.3Gbps -> 3Gbps

## Slide 14: 3. Parallelizing Within Servers
3.4 Multiple Queues

## Slide 15: 3. Parallelizing Within Servers
3.4 Multiple Queues
1 port, 2 cores
Synchronization overhead
1 packet , 2 cores
Cache misses

## Slide 16: 3. Parallelizing Within Servers
3.4 Multiple Queues
Rule1. 1 core per packet
Rule2. 1 core per queue
Result : 3Gbps -> 9.7Gbps

## Slide 17: 4. Evaluation
4.1 Single-server performance
Need to divide by three because there are 3 layers

## Slide 18: 4. Evaluation
4.2 With upcoming servers

## Slide 19: 5. Conclusion
Scalable and fast software switch utilizing the state of the art HW(NUMA, multiple queue NIC cards)
Programmable with click
Performance is not close to HW router, but it shows SW router’s future potential.