## Slide 1: 15-744: Computer Networking
L-13 Data Center Networking I

## Slide 2: Overview
Data Center Overview
DC Topologies
Routing in the DC

## Slide 3: Why study DCNs?
Scale
  Google: 0 to 1B users in ~15 years
  Facebook: 0 to 1B users in ~10 years
  Must operate at the scale of O(1M+) users
Cost:
  To build: Google ($3B/year), MSFT ($15B/total)
  To operate: 1-2% of global energy consumption*
  Must deliver apps using efficient HW/SW footprint
* LBNL, 2013.
Notes: http://www.wired.com/wiredenterprise/2013/02/microsofts-data-center/
Koomey, Jonathan. 2008. "Worldwide electricity used in data centers." Environmental Research Letters. vol. 3, no. 034008. September 23. <http://stacks.iop.org/1748-9326/3/034008>
Masanet,! E.,! Shehabi,! A.,! Ramakrishnan,! L.,! Liang,! J.,! Ma,! X.,! Walker,! B.,! Hendrix,! V.,! and! P.! Mantha! (2013).!The)Energy)Efficiency)Potential)of)CloudABased)Software:)A)U.S.)Case)Study.!Lawrence!Berkeley!National!Laboratory,!Berkeley,!California.!!

## Slide 4: Datacenter Arms Race
Amazon, Google, Microsoft, Yahoo!, … race to build next-gen mega-datacenters
Industrial-scale Information Technology
100,000+ servers
Located where land, water, fiber-optic connectivity, and cheap power are available

## Slide 5: Google Oregon Datacenter

## Slide 6: Computers + Net + Storage + Power + Cooling

## Slide 7: What defines a data center network?
The Internet | Data Center Network (DCN)
Many autonomous systems (ASes) | One administrative domain
Distributed control/routing | Centralized control and route selection
Single shortest-path routing | Many paths from source to destination
Hard to measure | Easy to measure, but lots of data…
Standardized transport (TCP and UDP) | Many transports (DCTCP, pFabric, …)
Innovation requires consensus (IETF) | Single company can innovate
“Network of networks” | “Backplane of giant supercomputer”

## Slide 8: DCN research “cheat sheet”
How would you design a network to support 1M endpoints?
If you could…
  Control all the endpoints and the network?
  Violate layering, end-to-end principle?
  Build custom hardware?
  Assume common OS, dataplane functions?
Top-to-bottom rethinking of the network

## Slide 9: Overview
Data Center Overview
DC Topologies
Routing in the DC

## Slide 10: Layer 2 vs. Layer 3 for Data Centers

## Slide 11: Data Center Costs
Amortized Cost* | Component | Sub-Components
~45% | Servers | CPU, memory, disk
~25% | Power infrastructure | UPS, cooling, power distribution
~15% | Power draw | Electrical utility costs
~15% | Network | Switches, links, transit
  *3 yr amortization for servers, 15 yr for infrastructure; 5% cost of money
The Cost of a Cloud: Research Problems in Data Center Networks. Sigcomm CCR 2009. Greenberg, Hamilton, Maltz, Patel.

## Slide 12: Server Costs
30% utilization considered “good” in most data centers!
Uneven application fit
  Each server has CPU, memory, disk: most applications exhaust one resource, stranding the others
Uncertainty in demand
  Demand for a new service can spike quickly
Risk management
  Not having spare servers to meet demand brings failure just when success is at hand

## Slide 13: Goal: Agility – Any service, Any Server
Turn the servers into a single large fungible pool
  Dynamically expand and contract service footprint as needed
Benefits
  Lower cost (higher utilization)
  Increase developer productivity
  Achieve high performance and reliability
Notes: Increase productivity because services can be deployed much faster

## Slide 14: Achieving Agility
Workload management
  Means for rapidly installing a service’s code on a server
  Virtual machines, disk images, containers
Storage Management
  Means for a server to access persistent data
  Distributed filesystems (e.g., HDFS, blob stores)
Network
  Means for communicating with other servers, regardless of where they are in the data center

## Slide 15: Datacenter Networks
10,000s of ports
Compute
Storage (Disk, Flash, …)
Provide the illusion of
“One Big Switch”

## Slide 16: Datacenter Traffic Growth
Source: “Jupiter Rising: A Decade of Clos Topologies and Centralized Control in Google’s Datacenter Network”, SIGCOMM 2015.
Today: Petabits/s in one DC
More than core of the Internet!
Notes: Today’s datacenter networks carry more traffic than the entire core of the Internet!

## Slide 17: Tree-based network topologies
100,000 x 10 Gb/s = 1 Pb/s
Can’t buy sufficiently fast core switches!
Notes: My first exposure to real networks was in 1994, when I worked for a large ISP called Neosoft, in Houston
At that time, our network was structured as a tree topology, which was quite common at the time and is still widely used
In a tree topology, groups of nodes are aggregated behind network switches, which connect to switches at higher branches of the tree
As you go up the tree, these switches get increasingly power and fast, to support the growth in aggregated bandwidth in subtrees
But they have the property that...
This means that as you add nodes to the leaves, you can overwhelm the root
Here are 100k nodes at 10G, however even today, the fastest switch is 100 Gb/s

## Slide 18: Folded-Clos multi-rooted trees
10 Gb/s
Switches
10 Gb/s
servers
Al Fares, et al., Sigcomm’08
Bandwidth needs met by massive multipathing

## Slide 19: PortLand: Main Assumption
Hierarchical structure of data center networks:
  They are multi-level, multi-rooted trees

## Slide 20: Background: Fat-Tree
Inter-connect racks (of servers) using a fat-tree topology
Fat-Tree: a special type of Clos Networks (after C. Clos) K-ary fat tree: three-layer topology (edge, aggregation and core)
  each pod consists of (k/2)2 servers & 2 layers of k/2 k-port switches
  each edge switch connects to k/2 servers & k/2 aggr. switches
  each aggr. switch connects to k/2 edge & k/2 core switches
  (k/2)2 core switches: each connects to k pods
Fat-tree
with K=4

## Slide 21: Why Fat-Tree?
Fat tree has identical bandwidth at any bisections
Each layer has the same aggregated bandwidth
Can be built using cheap devices with uniform capacity
  Each port supports same speed as end host
  All devices can transmit at line speed if packets are distributed uniform along available paths
Great scalability: k-port switch supports k3/4 servers
Fat tree network with K = 3 supporting 54 hosts

## Slide 22: Data Center Network

## Slide 23: Overview
Data Center Overview
DC Topologies
Routing in the DC

## Slide 24: Flat vs. Location Based Addresses
Commodity switches today have ~640 KB of low latency, power hungry, expensive on chip memory
  Stores 32 – 64 K flow entries
Assume 10 million virtual endpoints in 500,000 servers in datacenter
Flat addresses  10 million address mappings  ~100 MB on chip memory  ~150 times the memory size that can be put on chip today
Location based addresses  100 – 1000 address mappings  ~10 KB of memory  easily accommodated in switches today

## Slide 25: Hierarchical Addresses

## Slide 26: Hierarchical Addresses

## Slide 27: Hierarchical Addresses

## Slide 28: Hierarchical Addresses

## Slide 29: Hierarchical Addresses

## Slide 30: Hierarchical Addresses

## Slide 31: PortLand: Location Discovery Protocol
Location Discovery Messages (LDMs) exchanged between neighboring switches
Switches self-discover location on boot up

## Slide 32: Location Discovery Protocol

## Slide 33: Location Discovery Protocol

## Slide 34: Location Discovery Protocol

## Slide 35: Location Discovery Protocol

## Slide 36: Location Discovery Protocol

## Slide 37: Location Discovery Protocol

## Slide 38: Location Discovery Protocol

## Slide 39: Location Discovery Protocol

## Slide 40: Location Discovery Protocol

## Slide 41: Location Discovery Protocol

## Slide 42: Location Discovery Protocol

## Slide 43: Location Discovery Protocol

## Slide 44: Name Resolution

## Slide 45: Name Resolution

## Slide 46: Name Resolution

## Slide 47: Name Resolution

## Slide 48: Fabric Manager

## Slide 49: Name Resolution

## Slide 50: Name Resolution

## Slide 51: Name Resolution

## Slide 52: Other Schemes
SEATTLE [SIGCOMM ‘08]:
  Layer 2 network fabric that works at enterprise scale
  Eliminates ARP broadcast, proposes one-hop DHT
  Eliminates flooding, uses broadcast based LSR
  Scalability limited by
    Broadcast based routing protocol
    Large switch state
VL2 [SIGCOMM ‘09]
  Network architecture that scales to support huge data centers
  Layer 3 routing fabric used to implement a virtual layer 2
  Scale Layer 2 via end host modifications
    Unmodified switch hardware and software
    End hosts modified to perform enhanced resolution to assist routing and forwarding

## Slide 53: VL2: Name-Location Separation
VL2
payload
ToR3
. . .
. . .
y
x
Servers use flat names
Switches run link-state routing and maintain only switch-level topology
Cope with host churns with very little overhead
y
z
payload
ToR4
z
ToR2
ToR4
ToR1
ToR3
y, z
payload
ToR3
z
. . .
Directory Service
…
x  ToR2
y  ToR3
z  ToR4
…
Lookup &
Response
…
x  ToR2
y  ToR3
z  ToR3
…
Allows to use low-cost switches
Protects network and hosts from host-state churn
Obviates host and switch reconfiguration

## Slide 54: VL2: Random Indirection
x
y
payload
T3
y
z
payload
T5
z
IANY
IANY
IANY
IANY
Cope with arbitrary TMs with very little overhead
Links used for up paths
Links used for down paths
T1
T2
T3
T4
T5
T6
[ ECMP + IP Anycast ]
Harness huge bisection bandwidth
Obviate esoteric traffic engineering or optimization
Ensure robustness to failures
Work with switch mechanisms available today

## Slide 55: Next Lecture
Data center topology
Data center scheduling
Required reading
  Efficient Coflow Scheduling with Varys
  c-Through: Part-time Optics in Data Centers

## Slide 56: Energy Proportional Computing
Figure 1. Average CPU utilization of more than 5,000 servers during a six-month period. Servers
are rarely completely idle and seldom operate near their maximum utilization, instead operating
most of the time at between 10 and 50 percent of their maximum
It is surprisingly hard to achieve high levels of utilization of typical servers (and your home PC or laptop is even worse)
“The Case for
Energy-Proportional
Computing,”
Luiz André Barroso,
Urs Hölzle,
IEEE Computer
December 2007

## Slide 57: Energy Proportional Computing
Figure 2. Server power usage and energy efficiency at varying utilization levels, from idle to
peak performance. Even an energy-efficient server still consumes about half its full power
when doing virtually no work.
“The Case for
Energy-Proportional
Computing,”
Luiz André Barroso,
Urs Hölzle,
IEEE Computer
December 2007
Doing nothing well … NOT!

## Slide 58: Energy Proportional Computing
Figure 4. Power usage and energy efficiency in a more energy-proportional server. This
server has a power efficiency of more than 80 percent of its peak value for utilizations of
30 percent and above, with efficiency remaining above 50 percent for utilization levels as
low as 10 percent.
“The Case for
Energy-Proportional
Computing,”
Luiz André Barroso,
Urs Hölzle,
IEEE Computer
December 2007
Design for
wide dynamic
power range and
active low power
modes
Doing nothing
VERY well

## Slide 59: Thermal Image of Typical Cluster
Rack
Switch
M. K. Patterson, A. Pratt, P. Kumar, “From UPS to Silicon: an end-to-end evaluation of datacenter efficiency”, Intel Corporation

## Slide 60: DC Networking and Power
Within DC racks, network equipment often the “hottest” components in the hot spot
Network opportunities for power reduction
  Transition to higher speed interconnects (10 Gbs) at DC scales and densities
  High function/high power assists embedded in network element (e.g., TCAMs)

## Slide 61: DC Networking and Power
96 x 1 Gbit port Cisco datacenter switch consumes around 15 kW -- approximately 100x a typical server @ 150 W
High port density drives network element design, but such high power density makes it difficult to tightly pack them with servers
Alternative distributed processing/communications topology under investigation by various research groups

## Slide 62: Summary
Energy Consumption in IT Equipment
  Energy Proportional Computing
  Inherent inefficiencies in electrical energy distribution
Energy Consumption in Internet Datacenters
  Backend to billions of network capable devices
  Enormous processing, storage, and bandwidth supporting applications for huge user communities
  Resource Management: Processor, Memory, I/O, Network to maximize performance subject to power constraints: “Do Nothing Well”
  New packaging opportunities for better optimization of computing + communicating + power + mechanical

## Slide 64: Containerized Datacenters
Sun Modular Data Center
  Power/cooling for 200 KW of racked HW
  External taps for electricity, network, water
  7.5 racks: ~250 Servers, 7 TB DRAM, 1.5 PB disk
Notes: 64
2 slides imply many more devices to manage

## Slide 65: Containerized Datacenters

## Slide 66: Aside: Disk Power
IBM Microdrive (1inch)
writing 300mA (3.3V) 1W
standby 65mA (3.3V) .2W
IBM TravelStar (2.5inch)
read/write 2W
spinning 1.8W
low power idle .65W
standby .25W
sleep .1W
startup 4.7 W
seek 2.3W

## Slide 67: Spin-down Disk Model
Not Spinning
Spinning
& Ready
Spinning
& Access
Spinning
& Seek
Spinning up
Spinning down
Request
Trigger: request or predict
Predictive
.2W
.65-1.8W
2W
2.3W
4.7W
Inactivity Timeout threshold*

## Slide 68: Disk Spindown
Disk Power Management – Oracle (off-line)
Disk Power Management – Practical scheme (on-line)
access1
access2
IdleTime > BreakEvenTime
Idle for BreakEvenTime
Wait time
Source: from the presentation slides of the authors
Notes: 68
There are two disk power management schemes, one is called oracle scheme, the other is practical scheme. The oracle scheme is an offline scheme, which know ahead of time the length of upcoming idle period. If the idle time is larger than the breakeven time, the disk will spindown and spinup right in time before the next request. The practical scheme has no such future knowledge. If the disk is idle for a threshold of time, then the disk will spin down and spin up upon the arrival of next request. The previous work show if we set the threshold to be the breakeven time, the practical scheme is 2-compitative compared to the oracle scheme.

## Slide 69: Spin-Down Policies
Fixed Thresholds
  Tout = spin-down cost s.t. 2*Etransition = Pspin*Tout
Adaptive Thresholds: Tout = f (recent accesses)
  Exploit burstiness in Tidle
Minimizing Bumps (user annoyance/latency)
  Predictive spin-ups
Changing access patterns (making burstiness)
  Caching
  Prefetching

## Slide 70: Google
Since 2005, its data centers have been composed of standard shipping containers--each with 1,160 servers and a power consumption that can reach 250 kilowatts
Google server was 3.5 inches thick--2U, or 2 rack units, in data center parlance. It had two processors, two hard drives, and eight memory slots mounted on a motherboard built by Gigabyte

## Slide 71: Google's PUE
In the third quarter of 2008, Google's PUE was 1.21, but it dropped to 1.20 for the fourth quarter and to 1.19 for the first quarter of 2009 through March 15
Newest facilities have 1.12