## Slide 1: 15-744: Computer Networking
L-15 Data Center Networking III

## Slide 2: Announcements
Midterm – next Wednesday 3/7
Project meeting slots – will be posted on Piazza by Wednesday
  Slots mostly during lecture time on Friday

## Slide 3: Overview
DCTCP
Pfabric
RDMA

## Slide 4: Data Center Packet Transport
Large purpose-built DCs
  Huge investment: R&D, business
Transport inside the DC
  TCP rules (99.9% of traffic)
How’s TCP doing?

## Slide 5: TCP in the Data Center
We’ll see TCP does not meet demands of apps.
  Suffers from bursty packet drops, Incast [SIGCOMM ‘09], ...
  Builds up large queues:
    Adds significant latency.
    Wastes precious buffers, esp. bad with shallow-buffered switches.
Operators work around TCP problems.
  Ad-hoc, inefficient, often expensive solutions
  No solid understanding of consequences, tradeoffs

## Slide 6: Partition/Aggregate Application Structure
TLA
MLA
MLA
Worker Nodes
………
Picasso
“Everything you can imagine is real.”
“Bad artists copy.
Good artists steal.”
“It is your work in life that is the ultimate seduction.“
“The chief enemy of creativity is good sense.“
“Inspiration does exist,
but it must find you working.”
“I'd like to live as a poor man
with lots of money.“
“Art is a lie that makes us
realize the truth.
“Computers are useless.
They can only give you answers.”
1.
2.
3.
…..
1. Art is a lie…
2. The chief…
3.
…..
1.
2. Art is a lie…
3.
…..
Art is…
Picasso
Time is money
  Strict deadlines (SLAs)
Missed deadline
  Lower quality result
Deadline = 250ms
Deadline = 50ms
Deadline = 10ms

## Slide 7: Generality of Partition/Aggregate
The foundation for many large-scale web applications.
  Web search, Social network composition, Ad selection, etc.
Example: Facebook
  Partition/Aggregate ~ Multiget
  Aggregators: Web Servers
  Workers: Memcached Servers
Memcached Servers
Internet
Web
Servers
Memcached Protocol

## Slide 8: Workloads
Partition/Aggregate
(Query)
Short messages [50KB-1MB]
(Coordination, Control state)
Large flows [1MB-50MB]
(Data update)
Delay-sensitive
Delay-sensitive
Throughput-sensitive
Notes: Replace PDF

## Slide 9: Incast: Cluster-based Storage Systems
Client
Switch
Storage
Servers
R
R
R
R
1
2
Data Block
Server
Request Unit
(SRU)
3
4
Synchronized Read
Client now sends
next batch of requests
1
2
3
4
Notes: Data is striped across multiple servers for reliability (coding/replication) and performance. Also aids in incremental scalability.
To read this data a client performs a “Synchronized Read” operation.
The client reads data one data-block at a time. The portion of a data block stored by each server is called a SRU (in our terminology)
- mention that this setting is simplistic
- could have multiple clients, multiple outstanding blocks,
- describe sending of requests, responses
- the client sends out the next batch of requests only after it has received the entire data block (barrier synchronized)
To test how this read operation performs in the real world as we increase the number of servers on which we stripe data … (next slide)

## Slide 10: Incast
TCP timeout
Worker 1
Worker 2
Worker 3
Worker 4
Aggregator
RTOmin = 300 ms
Synchronized mice collide.
  Caused by Partition/Aggregate.

## Slide 11: Incast in Bing
Requests are jittered over 10ms window.
Jittering switched off around 8:30 am.
MLA Query Completion Time (ms)
Jittering trades of median for high percentiles
Notes: 1. Incast really happens – see this actual screenshot from production tool
2. People care, they’ve solved it at application by jittering.
3. They care about the 99.9th percentile, 1-1000 customers

## Slide 12: Queue Buildup
Sender 1
Sender 2
Receiver
Big flows buildup queues.
  Increased latency for short flows.
Measurements in Bing cluster
  For 90% packets: RTT < 1ms
  For 10% packets: 1ms < RTT < 15ms

## Slide 13: Data Center Transport Requirements
High Burst Tolerance
  Incast due to Partition/Aggregate is common.
Low Latency
  Short flows, queries
3. High Throughput
  Continuous data updates, large file transfers
The challenge is to achieve these three together.

## Slide 14: Tension Between Requirements
High Burst Tolerance
High Throughput
Low Latency
Deep Buffers:
Queuing Delays
Increase Latency
Shallow Buffers:
Bad for Bursts &
Throughput
Reduced RTOmin (SIGCOMM ‘09)
Doesn’t Help Latency
AQM – RED:
Avg Queue Not Fast
Enough for Incast
Objective:
Low Queue Occupancy & High Throughput
Notes: Deep Buffers – bad for latency
Shallow Buffers – bad for bursts & throughput
Reduce RTOmin – no good for latency
AQM – Difficult to tune, not fast enough for incast-style micro-bursts, lose throughput in low stat-mux

## Slide 15: Review: The TCP/ECN Control Loop
Sender 1
Sender 2
Receiver
ECN Mark (1 bit)
ECN = Explicit Congestion Notification
Notes: DCTCP is based on the existing Explicit Congestion Notification framework in TCP.

## Slide 16: Two Key Ideas
React in proportion to the extent of congestion, not its presence.
  Reduces variance in sending rates, lowering queuing requirements.
Mark based on instantaneous queue length.
  Fast feedback to better deal with bursts.
ECN Marks | TCP | DCTCP
1 0 1 1 1 1 0 1 1 1 | Cut window by 50% | Cut window by 40%
0 0 0 0 0 0 0 0 0 1 | Cut window by 50% | Cut window by 5%

## Slide 17: Data Center TCP Algorithm
Switch side:
  Mark packets when Queue Length > K.
  Sender side:
  Maintain running average of fraction of packets marked (α).
  In each RTT:
Adaptive window decreases:
  Note: decrease factor between 1 and 2.
B
K
Mark
Don’t
Mark
Notes: very simple marking mechanism
not all the tunings other aqms have
on the source side, the source is tryign to estimate the fraction of packets getting marked
using the obs that there is a stream of ecn marks coming back – more info in the stream than in any single bit
trying to maintain smooth rate variations to operate well even when using shallow buffers, and only a few flows (no stat mux)
F over the last RTT. In TCP there is always a way to get the next RTT from the window size. Comes from the self-clocking of TCP.
Only changing the decrease. Simplest version – makes a lot of sense. So generic could apply it to any algorithm – CTCP, CUBIC – how to cut its window leaving increase part to what it already does. Have to be careful here.

## Slide 18: DCTCP in Action
Setup: Win 7, Broadcom 1Gbps Switch
Scenario: 2 long-lived flows, K = 30KB
(Kbytes)
Notes: Not ns2.

## Slide 19: Why it Works
High Burst Tolerance
  Large buffer headroom → bursts fit.
  Aggressive marking → sources react before packets are dropped.
Low Latency
  Small buffer occupancies → low queuing delay.
3. High Throughput
  ECN averaging → smooth rate adjustments, low variance.

## Slide 20: Conclusions
DCTCP satisfies all our requirements for Data Center packet transport.
  Handles bursts well
  Keeps queuing delays low
  Achieves high throughput
Features:
  Very simple change to TCP and a single switch parameter.
  Based on mechanisms already available in Silicon.

## Slide 21: Overview
DCTCP
Pfabric
RDMA

## Slide 22: DC Fabric: Just a Giant Switch
H1
H2
H3
H4
H5
H6
H7
H8
H9

## Slide 23: DC Fabric: Just a Giant Switch
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX

## Slide 24: DC Fabric: Just a Giant Switch
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX

## Slide 25
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
Objective?
Minimize avg FCT
DC transport = Flow scheduling on giant switch
ingress & egress
capacity constraints
TX
RX

## Slide 26: “Ideal” Flow Scheduling
Problem is NP-hard  [Bar-Noy et al.]
  Simple greedy algorithm: 2-approximation
1
2
3
1
2
3
Notes: State explicitly that you can’t actually build this in practice the way it is described
Central, etc

## Slide 27: Key Insight
Decouple flow scheduling from rate control
H1
H2
H3
H4
H5
H6
H7
H8
H9
Switches implement flow
scheduling via local mechanisms
Hosts implement simple rate control to avoid high packet loss
Notes: “you should not use rate control to implement flow scheduling… decouple”

## Slide 28: pFabric Switch
Switch Port
7
1
9
4
3
Priority Scheduling send highest priority packet first
Priority Dropping drop lowest priority packets first
6
3
2
5
small “bag” of packets per-port
prio = remaining flow size
H1
H2
H3
H4
H5
H6
H7
H8
H9

## Slide 29: pFabric Switch Complexity
Buffers are very small (~2×BDP per-port)
  e.g., C=10Gbps, RTT=15µs → Buffer ~ 30KB
  Today’s switch buffers are 10-30x larger
  Priority Scheduling/Dropping
  Worst-case: Minimum size packets (64B)
  51.2ns to find min/max of ~600 numbers
  Binary comparator tree: 10 clock cycles
  Current ASICs: clock ~ 1ns
Notes: Use small buffers as an advantage (not as a requirement)

## Slide 30: pFabric Rate Control
With priority scheduling/dropping, queue buildup doesn’t matter
Greatly simplifies rate control
H1
H2
H3
H4
H5
H6
H7
H8
H9
50% Loss
Only task for RC:
Prevent congestion collapse when elephants collide

## Slide 31: pFabric Rate Control
Minimal version of TCP algorithm
Start at line-rate
  Initial window larger than BDP
No retransmission timeout estimation
  Fixed RTO at small multiple of round-trip time
Reduce window size upon packet drops
  Window increase same as TCP (slow start, congestion avoidance, …)
H1
H2
H3
H4
H5
H6
H7
H8
H9

## Slide 32: Why does this work?
Key invariant for ideal scheduling:
At any instant, have the highest priority packet (according to ideal algorithm) available at the switch.
Priority scheduling
  High priority packets traverse fabric as quickly as possible
What about dropped packets?
  Lowest priority → not needed till all other packets depart
  Buffer > BDP → enough time (> RTT) to retransmit
Notes: If we step back, what are we trying to do? And tie to the conceptual ideal scheduelr
When might this invariant break?
This might happen if at an earlier point in time we dropped this packet because earlier high priority packets caused it to be dropped
Can this happen in pfabric’s design?
It cannot because…

## Slide 33: Overview
DCTCP
Pfabric
RDMA

## Slide 35: RDMA
RDMA performance typically better than TCP
Key assumption  lossless network
Need Priority Flow Control (PFC) in Ethernet

## Slide 38: “Congestion Spreading” in Lossless Networks (Priority Flow Control of PFC)
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE

## Slide 39: DCQCN
Microsoft/Mellanox proposal to run congestion control for RoCEv2
Receiving NICS reflect back ECN info once per N microseconds
Sender adjusts rate in DCTCP-like fashion
Experience:
  Although tree-like topology deadlocks can occur due to broadcast
  Livelock issues if losses occur due to poor loss recovery
  Hard to use > 2 priorities due to buffer limitations  need enough buffer to accommodate delays in pause
  Simple fixes – but suggest fragile design

## Slide 40: Analysis
How low can DCTCP maintain queues without loss of throughput?
How do we set the DCTCP parameters?
Need to quantify queue size oscillations (Stability).
Time
(W*+1)(1-α/2)
W*
Window Size
W*+1

## Slide 41: Analysis
How low can DCTCP maintain queues without loss of throughput?
How do we set the DCTCP parameters?
Need to quantify queue size oscillations (Stability).
Time
(W*+1)(1-α/2)
W*
Window Size
W*+1
Packets sent in this
RTT are marked.

## Slide 42: Analysis
How low can DCTCP maintain queues without loss of throughput?
How do we set the DCTCP parameters?
Need to quantify queue size oscillations (Stability).
85% Less Buffer than TCP

## Slide 43: Evaluation
Implemented in Windows stack.
Real hardware, 1Gbps and 10Gbps experiments
  90 server testbed
  Broadcom Triumph 48 1G ports – 4MB shared memory
  Cisco Cat4948 48 1G ports – 16MB shared memory
  Broadcom Scorpion 24 10G ports – 4MB shared memory
Numerous micro-benchmarks
  – Throughput and Queue Length
  – Multi-hop
  – Queue Buildup
  – Buffer Pressure
Cluster traffic benchmark
– Fairness and Convergence
– Incast
– Static vs Dynamic Buffer Mgmt

## Slide 44: Incast Really Happens
Requests are jittered over 10ms window.
Jittering switched off around 8:30 am.
Jittering trades off median against high percentiles.
99.9th percentile is being tracked.
MLA Query Completion Time (ms)
Notes: 1. Incast really happens – see this actual screenshot from production tool
2. People care, they’ve solved it at application by jittering.
3. They care about the 99.9th percentile, 1-1000 customers

## Slide 45: Overview
Data Center Overview
Routing in the DC
Transport in the DC

## Slide 46: Cluster-based Storage Systems
Client
Switch
Storage
Servers
R
R
R
R
1
2
Data Block
Server
Request Unit
(SRU)
3
4
Synchronized Read
Client now sends
next batch of requests
1
2
3
4
Notes: Data is striped across multiple servers for reliability (coding/replication) and performance. Also aids in incremental scalability.
To read this data a client performs a “Synchronized Read” operation.
The client reads data one data-block at a time. The portion of a data block stored by each server is called a SRU (in our terminology)
- mention that this setting is simplistic
- could have multiple clients, multiple outstanding blocks,
- describe sending of requests, responses
- the client sends out the next batch of requests only after it has received the entire data block (barrier synchronized)
To test how this read operation performs in the real world as we increase the number of servers on which we stripe data … (next slide)

## Slide 47: TCP Throughput Collapse
Collapse!
Cluster Setup
1Gbps Ethernet
Unmodified TCP
S50 Switch
1MB Block Size
TCP Incast
  Cause of throughput collapse:
  coarse-grained TCP timeouts
Notes: And, here are the results of the experiment. On the Y axis we have Throughput (Goodput), and on the X axis we have the number of servers involved in the transfer. Initially the throughput is 900Mbps, close to the maximum achievable in the network. As we scale the number of servers, by around 7 servers we notice a drastic collapse in throughput down to 100Mbps (an order of magnitude lower than the max). This TCP throughput collapse is called TCP Incast, and the cause for this is coarse-grained TCP timeouts.

## Slide 48: TCP: Loss recovery comparison
Sender
Receiver
1
2
3
4
5
Ack 1
Ack 1
Ack 1
Ack 1
Retransmit
2
Seq #
Ack 5
Sender
Receiver
1
2
3
4
5
1
Retransmission
Timeout
(RTO)
Ack 1
Seq #
Timeout driven recovery is
slow (ms)
Data-driven recovery is
super fast (µs) in datacenters
Notes: So we have seen the 2 loss recovery mechanisms in TCP. The point to note is that timeouts are expensive, in ms, where as data-driven recovery is quick (us in datacenters)
But why are timeouts in milliseconds?

## Slide 49: Link Idle Time Due To Timeouts
Client
Switch
R
R
R
R
1
2
3
4
Synchronized Read
4
1
2
3
4
Server
Request Unit
(SRU)
time
Req.
sent
Rsp.
sent
4 dropped
Response
resent
1 – 3 done
Link Idle!
Notes: Let us revisit the synchronized reads scenario (in parallel filesystems) to understand why timeouts cause link idle time (and hence throughput collapse).
Setting: SRU contains only one packet worth of information for simplicity.
If 4 is dropped, when server 4 is timing out, the link is idle – no one is utilizing the available bandwidth.

## Slide 50: Client Link Utilization
200ms
Link Idle!
Notes: Another way to visualize this is to look at the client link utilization when the transfer was taking place.
Y axis = Throughput
X axis = time
Let us consider only 1 block transfer (Block 2). When servers send their responses, the client link utilization reaches a peak (all links are 1Gbps). But one of the servers experiences losses and has to fallback on timeout driven loss recovery. When the remaining servers involved in the read finish their transfers, the link is idle (for 200ms in this example), just before the timeout event occurs and the final server completes the transfer. Once the entire data block is received, the request for the next data block can be sent out.
{ This is a visualization of a simulation run }

## Slide 51: Default minRTO: Throughput Collapse
Unmodified TCP
(200ms minRTO)
Notes: Same graph as before – synchronized reads, unmodified TCP on servers.

## Slide 52: Lowering minRTO to 1ms helps
Millisecond retransmissions are not enough
Unmodified TCP
(200ms minRTO)
1ms minRTO
Notes: The blue line represents the 1ms minRTO TCP implementation.
A single line change helps! Gets rid of collapse.
But not good enough at scale. There is a drop-off close to 40-47 servers.
Based on this one might be tempted to suggest, can we just eliminate minRTO. Only eliminating minRTO will not help. And the reason for this is that RTT is still measured in milliseconds, and hence the RTO values are still in miliseconds.
This is the case for microsecond retransmissions.

## Slide 53: Solution: µsecond TCP + no minRTO
Unmodified TCP
(200ms minRTO)
more servers
1ms minRTO
microsecond TCP
+ no minRTO
High throughput for up to 47 servers

## Slide 54: Simulation: Scaling to thousands
Block Size = 80MB, Buffer = 32KB, RTT = 20us
Notes: Block size = 80MB, buffer = 32KB, RTT = 20us (next generation datacenters)

## Slide 55: Delayed-ACK (for RTO > 40ms)
Delayed-Ack: Optimization to reduce #ACKs sent
Seq #
Sender
Receiver
1
Ack 1
40ms
Sender
Receiver
1
Ack 2
Seq #
2
Sender
Receiver
1
Ack 0
Seq #
2
Notes: Explanation of Delayed ACK specification.

## Slide 56: µsecond RTO and Delayed-ACK
Premature Timeout
  RTO on sender triggers before Delayed-ACK on receiver
Sender
Receiver
1
Ack 1
Seq #
1
RTO < 40ms
Timeout
Retransmit packet
Seq #
Sender
Receiver
1
Ack 1
40ms
RTO > 40ms
Notes: Premature timeouts slow the rate of transfer (timeouts still result in {slow start + congestion avoidance}).

## Slide 57: Impact of Delayed-ACK

## Slide 58: Is it safe for the wide-area?
Stability: Could we cause congestion collapse?
  No: Wide-area RTOs are in 10s, 100s of ms
  No: Timeouts result in rediscovering link capacity (slow down the rate of transfer)
Performance: Do we timeout unnecessarily?
  [Allman99] Reducing minRTO increases the chance of premature timeouts
    Premature timeouts slow transfer rate
  Today: detect and recover from premature timeouts
  Wide-area experiments to determine performance impact
Notes: Allman et. al said that reducing minRTO results in an increase in premature timeouts.
The reason why a premature timeout would occur in such a setting would be because of a sudden jump/increase in RTT, from it steady state value. Such a jump would most probably be caused by a significant path change in the wide area. We have reason to believe that such changes are not a common occurrence in the wide area today.
Also, premature timeouts just slow the rate of transfer (timeouts still result in {slow start + congestion avoidance}).
Premature timeouts are less harmful today
Can detect them using the tcp timestamp option - if we get an ack for a seq number that we retransmitted due to a timeout, but it has a timestamp of the first packet with this seq number that we transmitted, then we know we experienced a premature timeout.
Can recover from them (F-RTO) – If we detect a premature timeout, exit slow start and enter congestion avoidance (with cwnd = cwnd_before_timeout / 2)
Both implemented widely!

## Slide 59: Wide-area Experiment
Do microsecond timeouts harm wide-area throughput?
Microsecond TCP
+
No minRTO
Standard TCP
BitTorrent
Seeds
BitTorrent
Clients

## Slide 60: Wide-area Experiment: Results
No noticeable difference in throughput

## Slide 61: Other Efforts
Topology
  Using extra links to meet traffic matrix
    60Ghz links  MSR paper in HotNets09
    Reconfigurable optical interconnects  CMU and UCSD in Sigcomm2010
Transport
  Data Center TCP  data-center only protocol that uses RED-like techniques in routers

## Slide 62: Aside: Disk Power
IBM Microdrive (1inch)
writing 300mA (3.3V) 1W
standby 65mA (3.3V) .2W
IBM TravelStar (2.5inch)
read/write 2W
spinning 1.8W
low power idle .65W
standby .25W
sleep .1W
startup 4.7 W
seek 2.3W

## Slide 63: Spin-down Disk Model
Not Spinning
Spinning
& Ready
Spinning
& Access
Spinning
& Seek
Spinning up
Spinning down
Request
Trigger: request or predict
Predictive
.2W
.65-1.8W
2W
2.3W
4.7W
Inactivity Timeout threshold*

## Slide 64: Disk Spindown
Disk Power Management – Oracle (off-line)
Disk Power Management – Practical scheme (on-line)
access1
access2
IdleTime > BreakEvenTime
Idle for BreakEvenTime
Wait time
Source: from the presentation slides of the authors
Notes: 64
There are two disk power management schemes, one is called oracle scheme, the other is practical scheme. The oracle scheme is an offline scheme, which know ahead of time the length of upcoming idle period. If the idle time is larger than the breakeven time, the disk will spindown and spinup right in time before the next request. The practical scheme has no such future knowledge. If the disk is idle for a threshold of time, then the disk will spin down and spin up upon the arrival of next request. The previous work show if we set the threshold to be the breakeven time, the practical scheme is 2-compitative compared to the oracle scheme.

## Slide 65: Spin-Down Policies
Fixed Thresholds
  Tout = spin-down cost s.t. 2*Etransition = Pspin*Tout
Adaptive Thresholds: Tout = f (recent accesses)
  Exploit burstiness in Tidle
Minimizing Bumps (user annoyance/latency)
  Predictive spin-ups
Changing access patterns (making burstiness)
  Caching
  Prefetching

## Slide 66: Google
Since 2005, its data centers have been composed of standard shipping containers--each with 1,160 servers and a power consumption that can reach 250 kilowatts
Google server was 3.5 inches thick--2U, or 2 rack units, in data center parlance. It had two processors, two hard drives, and eight memory slots mounted on a motherboard built by Gigabyte

## Slide 67: Google's PUE
In the third quarter of 2008, Google's PUE was 1.21, but it dropped to 1.20 for the fourth quarter and to 1.19 for the first quarter of 2009 through March 15
Newest facilities have 1.12