## Slide 1: 15-744: Computer Networking
L-16 Network Measurement

## Slide 2: Outline
Motivation
Three case studies:
  Internet Topology
  Bandwidth Map
  Internet Latency

## Slide 3: Why network measurement?
Help understand the network (Internet)
  E.g. Topology (ISP don’t usually publish this)
  Useful for modeling and simulation
Identify problems and bottlenecks
  Where do we need more investment?
  Which link is down (now)?
Improve application/user experience
  End-to-end performance is key to UE…
  …UE means money

## Slide 4: What to measure?
Network topology
  Connectivity, redundancy, coverage
Network performance
  Bandwidth, latency, jitter, utility
Types of protocols/applications
  TCP/UDP/ICMP, P2P/Client-server
Application specific data
  Video player: buffering time, bitrate
  Web service: page load time

## Slide 5: How to measure?
A lot of general tools
  Traceroute, ping, iperf, etc.
Components built in applications
  E.g. video player could log buffering time
ISPs knows better about their own network
  But usually not public
Passive and active
  Pure listening vs. inject traffic
  Overhead difference

## Slide 6: Outline
Motivation
Three case studies:
  Internet Topology
    Faloutsos’99, Li’04
  Bandwidth Map
  Internet Latency

## Slide 7: Why study topology?
Correctness of network protocols typically independent of topology
Performance of networks critically dependent on topology
  e.g., convergence of route information
Identifying good topologies and mechanism design for them
  Internet impossible to replicate
  Modeling of topology needed to generate test topologies

## Slide 8: Internet topologies
AT&T
SPRINT
MCI
AT&T
MCI
SPRINT
Router level
Autonomous System (AS) level

## Slide 9: Router level vs. AS level
Router level topologies reflect physical connectivity between nodes
  Inferred from tools like traceroute or well known public measurement projects like Mercator and Skitter
AS graph reflects a peering relationship between two providers/clients
  Inferred from inter-domain routers that run BGP and public projects like Oregon Route Views

## Slide 10: Hub-and-Spoke Topology
Single hub node
  Common in enterprise networks
  Main location and satellite sites
  Simple design and trivial routing
Problems
  Single point of failure
  Bandwidth limitations
  High delay between sites
  Costs to backhaul to hub

## Slide 11: Simple Alternatives to Hub-and-Spoke
Dual hub-and-spoke
  Higher reliability
  Higher cost
  Good building block
Levels of hierarchy
  Reduce backhaul cost
  Aggregate the bandwidth
  Shorter site-to-site delay
…

## Slide 12: Waxman model (Waxman 1988)
Observation: Long-range links are expensive
Nodes placed at random in 2-d space with dimension L
Probability of edge (u,v):
  ae^{-d/(bL)}, where d is Euclidean distance (u,v), a and b are constants
Models locality
v
u
d(u,v)

## Slide 13: Transit-stub model (Zegura 1997)
Observation: Real networks exhibit
  Hierarchical structure
  Specialized nodes (transit, stub..)
  Connectivity requirements
  Redundancy
Characteristics incorporated into the Georgia Tech Internetwork Topology Models (GT-ITM) simulator (E. Zegura, K.Calvert and M.J. Donahoo, 1995)

## Slide 14: Transit-stub model (Zegura 1997)
Transit domains
  placed in 2-d space
  populated with routers
  connected to each other
Stub domains
  placed in 2-d space
  populated with routers
  connected to transit domains
Models hierarchy

## Slide 15: So…are we done?
No!
In 1999, Faloutsos, Faloutsos and Faloutsos published a paper, demonstrating power law relationships in Internet graphs
Specifically, the node degree distribution exhibited power laws
That Changed Everything…..

## Slide 16: Power Law Measurement Methodology
AS level topology
  Collect BGP routing information from many routers
Router level topology
  Traceroute between a lot of pairs of nodes
  Two IP addresses correspond two the same node if the their names (inverse DNS) are the same

## Slide 17: Power laws in AS level topology

## Slide 18
A few nodes have lots of connections
Rank R(d)
Degree d
Source: Faloutsos et al. (1999)
Power Laws and Internet Topology
Router-level graph & Autonomous System (AS) graph
Led to active research in degree-based network models
Most nodes have few connections
R(d) = P (D>d) x #nodes

## Slide 19: GT-ITM abandoned..
GT-ITM did not give power law degree graphs
New topology generators and explanation for power law degrees were sought
Focus of generators to match degree distribution of observed graph

## Slide 20: Features of Degree-Based Models
Degree sequence follows a power law (by construction)
High-degree nodes correspond to highly connected central “hubs”, which are crucial to the system
Achilles’ heel: robust to random failure, fragile to specific attack
Preferential Attachment
Expected Degree Sequence

## Slide 21: Problem With Power Law
... but they're descriptive models!
Many graphs with similar distribution have different properties
No correct physical explanation, need an understanding of practical issues:
  the driving force behind deployment
  the driving force behind growth

## Slide 22: Li et al. 2004(HOT)
Consider the explicit design of the Internet
  Annotated network graphs (capacity, bandwidth)
  Technological and economic limitations
  Network performance
Seek a theory for Internet topology that is explanatory and not merely descriptive.
  Explain high variability in network connectivity
  Ability to match large scale statistics (e.g. power laws) is only secondary evidence
Notes: Why do we have the power law distribution?

## Slide 23: Router Technology Constraint
10
0
10
1
10
2
Degree
10
-1
10
0
10
1
10
2
10
3
Bandwidth (Gbps)
15 x 10 GE
15 x 3 x 1 GE
15 x 4 x OC12
15 x 8 FE
Technology constraint
Total Bandwidth
Bandwidth per Degree
Cisco 12416 GSR, circa 2002
high BW low degree
high degree low BW

## Slide 24: Aggregate Router Feasibility
approximate
aggregate
feasible region
core technologies
edge technologies
older/cheaper
technologies
Source: Cisco Product Catalog, June 2002
Notes: So what does this suggest?
Not possible to have high bw – high degree router as the hub nodes.

## Slide 25: Variability in End-User Bandwidths
Rank (number of users)
Connection Speed (Mbps)
1e-1
1e-2
1
1e1
1e2
1e3
1e4
1e2
1
1e4
1e6
1e8
Dial-up
~56Kbps
Broadband
Cable/DSL
~500Kbps
Ethernet
10-100Mbps
Ethernet
1-10Gbps
most users
have low speed connections
a few users have very high speed connections
high
performance
computing
academic
and corporate
residential and
small business
Notes: It look sat the end-user bandwidth demands, there is great variability in the availability and/or willingness-to-pay for bandwidth on the part of customers at the edge. Although a few users have very high speed connections, most users have low speed connections.
Given these facts, what will a ISP do? The goal of the ISP is to minimize cost.
The cost of links creates an economic incentive to aggregate traffic as close to the edge as possible.
The variability in edge connectivity speeds thus creates variability in the connectivity at edge routers.

## Slide 26
Heuristically Optimal Topology
Hosts
Edges
Cores
Mesh-like core of fast, low degree routers
High degree nodes are at the edges.

## Slide 27
SOX
SFGP/
AMPATH
U. Florida
U. So. Florida
Miss State
GigaPoP
WiscREN
SURFNet
Rutgers U.
MANLAN
Northern
Crossroads
Mid-Atlantic
Crossroads
Drexel U.
U. Delaware
PSC
NCNI/MCNC
MAGPI
UMD NGIX
DARPA
BossNet
GEANT
Seattle
Sunnyvale
Los Angeles
Houston
Denver
Kansas
City
Indian-
apolis
Atlanta
Wash
D.C.
Chicago
New York
OARNET
Northern Lights
Indiana GigaPoP
Merit
U. Louisville
NYSERNet
U. Memphis
Great Plains
OneNet
Arizona St.
U. Arizona
Qwest Labs
UNM
Oregon
GigaPoP
Front Range
GigaPoP
Texas Tech
Tulane U.
North Texas
GigaPoP
Texas
GigaPoP
LaNet
UT Austin
CENIC
UniNet
WIDE
AMES NGIX
Pacific
Northwest
GigaPoP
U. Hawaii
Pacific
Wave
ESnet
TransPAC/APAN
Iowa St.
Florida A&M
UT-SW
Med Ctr.
NCSA
MREN
SINet
WPI
StarLight
Intermountain
GigaPoP
Abilene Backbone
Physical Connectivity
(as of December 16, 2003)
0.1-0.5 Gbps
0.5-1.0 Gbps
1.0-5.0 Gbps
5.0-10.0 Gbps

## Slide 28: Summary Topology Measurement
Faloutsos’99 on Internet topology
  Observed “power laws” in Internet structure
    Router level, AS-level, neighborhood sizes
  Inspired degree-based topology generators
What is wrong with these topologies? Li’04
  Many graphs with similar distribution have different properties
  Should look at fundamental technology constraints and economic trade-offs
Thought
  Network measurement is a function system response. It’s always better to know what the system is like first.

## Slide 29: Outline
Motivation
Three case studies:
  Internet Topology
  Bandwidth Map
    Sun’14
  Internet Latency

## Slide 30: Motivation
Measuring BW between nodes is easy
  Iperf…
How about a real-time traffic map of Internet?
  CDNs could have better server selection
  P2P application choose the best peer
  Network diagnoses and trouble-shooting
Think about Google Map for real-world traffic

## Slide 31: Challenges
Coverage
  Need millions of vantage points
Overhead
  BW measurements usually inject non-trivial traffic to the network
(Near) real-time views
  Even bigger overhead

## Slide 32: Opportunity
Idea: infer traffic map from video player statistics
The growing volume of Internet video traffic (Coverage)
  Accounts for 30%-50% of total traffic
  30M NetFlix streaming subscribers
And the ability to instrument video players （Overhead, real-time)
  Companies are already doing this

## Slide 33: Overview of Service
Capacity & Utilization

## Slide 34: …Yet Still Challenges
Video measurements provide estimates of end-to-end throughput
  Not per link
  Not capacity/utilization
No information about background traffic
  Unobserved video & non-video traffic

## Slide 35: Problem definition

## Slide 36: Inferring Capacity
Use max observed throughput?
Simple, but not accurate
  Actually gives a lower bound
Problems
  Tend to underestimate (background traffic)
  Fails to consider confluence of flows
  Practical aspects: capacity are likely drawn from discrete set of values (e.g. 1Gbps)
  Practical aspects: ISPs tend to minimize cost

## Slide 37: Inferring Capacity Continued…
Confluence of flows & background traffic
Discrete capacities
Minimize cost

## Slide 38: Side Information to Help
Because original problem is hard to solve
Candidate side information:
  Gravity models: The traffic volumes between a s, d pair is roughly proportional to the products of the total traffic volume originating in s and d.
  Measurement vs. Background ratio: e.g., YouTube is ≈ 18% of peak traffic
  Overprovisioning: network core links are typically overprovisioned to run at γ=30-40% link utilization on average.

## Slide 39: Inferring Utilization
Need to be more real time
  Side information doesn’t hold within short time
Restate problem
  Ts,d,e,s,d,e,Cbg,e
We can estimate Ts,d,e from bg,e
  Using max-min fairness: allocate user with small demands of what it wants, and evenly divide unused resourse to big users

## Slide 40: Inferring Utilization - Example
Each A-C flow gets 1M, B-C flow gets 5M
  TA,C=1M, TB,C=5M
Suppose measured 1 AC and 1 BC link
If bga,c=4.5M, bgb,c=13.5M, then TEstA,C=0.5M, TEstB,C=1M
If bga,c=4M, bgb,c=9M, then TEstA,C=1M, TEstB,C=5M

## Slide 41: Evaluation – Simulation Setup
Synthesized traffic patterns
Sensitivity
  Number of epochs
  Background vs. measurement traffic ratio
  Accuracy of capacity inference

## Slide 42: Evaluation – Capacity Accuracy

## Slide 43: Evaluation – Utilization Accuracy

## Slide 44: Summary Bandwidth Measurement
Early stage work (Sun’14) on traffic map
  Leverage the popularity of video players
  Low overhead and high coverage
The data is straight-forward to collect, but
  Converting from end-to-end measurements to per-link number is hard
  Converting from throughput to capacity is hard
Thought
  The interesting fact may be hidden (deep) under the things we (can) measure

## Slide 45: Outline
Motivation
Three case studies:
  Internet Topology
  Bandwidth Map
  Internet Latency
    Singla’14, Li’10

## Slide 46: Value of (Very) Low Latency
User experience
  Response within 30msillusion of zero wait-time
Money
  A 100ms latency penalty for Amazon1% loss
Cloud computing & thin clients
  Desktop as a service
  Computation offload from mobile devices
New applications
  E.g. Telemedicine

## Slide 47: Latency Lags Bandwidth
The improvement of b/w has been huge
  It’s easier…
  Easier to market
  Average Internet connection is 11.5Mbps in US
Reducing latency is harder
  Usually requires structural change of network
Can we build a “speed of light” Internet?
  First let’s look at why it is slow? (Singla’14)

## Slide 48: Wait, don’t CDNs solve the problem?
They do help to some extent, but…
It doesn’t help for all applications
  E.g. telemedicine
CDNs are expensive
  Available only to larger Internet companies
Lower Internet latency also helps to reduce CDN deployment cost

## Slide 49: Latency Measurement Methodology
Fetch web pages using cURL
  just the HTML for the landing pages
  28,000 Web sites from 186 PlanetLab locations
Obtain time for
  DNS resolution
  TCP handshake: between SYN and SYN-ACK
  TCP transfer: actual data transmission
  Total

## Slide 50: Latency Measurement Methodology Cont.
Also ping the Web servers for 30 times
  Log min and median
traceroute from PlanetLab nodes to servers
  Then geolocate each router/server using commercial geolocation services
Geolocation (based on IP) is not accurate
  Use multiple services
  Results are not sensitive to specific service

## Slide 51: Important Concepts
C-latency:
  Time for light to travel between client & server (shortest path)
Router path latency:
  Time for light to travel through each router
Latency inflation:
  measured time/c-latency

## Slide 52: Result Overview
PlanetLab nodes are well-connected, so real world results are probably worse

## Slide 53: Result Overview - Summary
Total latency inflation:
  35.4 (median); 100 (80th percentile)
Protocol overhead
  DNS (7.4) and TCP handshake （3.4）
But minimum ping is also 3.2 inflated
  Suggests inefficiency in lower layers…
Very tail heavy distribution

## Slide 54: Is Congestion the Problem?
Log RTT (TCP SYN and SYN-ACK) over 24-hour time period
Variation is generally small

## Slide 55: Infrastructure Inflation
Router path is 2x inflated (median)
  Suggests inefficiency in route selection
  Not too bad since speed of light in fiber is ~2/3rd the speed of light in vacuum
Then why is pinging still 3.2x inflated?
  1) Traceroute may not yield response from all routers
  2) Physical path of links may not follow shortest path for geological and economical reasons

## Slide 56: Absolute Numbers (Li’10)
Consider client-server applications where server is running in the cloud
Methodology
  Instantiate an instance in each data center of the cloud provider
  Ping these instances from 200 PlanetLab nodes
  Record the minimum RTT
The best latency you can get with today’s cloud

## Slide 57: Latency to Closest Cloud
Using Amazon (C1), average RTT is 74ms

## Slide 58: Summary Latency Measurement
Singla’14 proposes an ambitious goal
  Cut Internet latency to the limit of speed of light
  Will likely benefit many applications
Why is today’s Internet so slow?
  Infrastructural inefficiency
  Protocol overhead
Li’10 studied the latency to cloud
  Many tens of milliseconds of latency
  Long tail distribution
Thought
  Detailed measurements are a good way to locate bottlenecks of the system