## Slide 1: 15-744: Computer Networking
L-18 Data-Oriented Networking

## Slide 2: Data-Oriented Networking Overview
In the beginning...
  First applications strictly focused on host-to-host interprocess communication:
    Remote login, file transfer, ...
  Internet was built around this host-to-host model.
  Architecture is well-suited for communication between pairs of stationary hosts.
... while today
  Vast majority of Internet usage is data retrieval and service access.
  Users care about the content and are oblivious to location. They are often oblivious as to delivery time:
    Fetching headlines from CNN, videos from YouTube, TV from Tivo
    Accessing a bank account at “www.bank.com”.

## Slide 3: To the beginning...
What if you could re-architect the way “bulk” data transfer applications worked
  HTTP
  FTP
  Email
  etc.
... knowing what we know now?

## Slide 4: Innovation in Data Transfer is Hard
Imagine: You have a novel data transfer technique
How do you deploy?
  Update HTTP. Talk to IETF. Modify Apache, IIS, Firefox, Netscape, Opera, IE, Lynx, Wget, …
  Update SMTP. Talk to IETF. Modify Sendmail, Postfix, Outlook…
  Give up in frustration
Notes: This is not because people don’t feel that data transfer is important. In fact, over the last few years, a number of projects have looked at the issue. To name just a few systems, you have protocols such as Bittorrent…
However, while a large body of work exists in the area, deploying these new techniques is hard. Most of the above systems have usually applied their new transfer technique within the context of particular system or application. Applying these techniques to a broad category of applications is harder.
Imagine you come up with a new way of efficiently transferring data. If you want to apply YOUR new technique to a a commonly used protocol such as HTTP. You would have to update the protocol to incorporate your changes, maybe talk to a standards body to incorporate those changes, and then go about modifying the host of systems that actually use the protocol so that they can benefit from your new ideas.
Now, if you wanted to apply your techniques to a completely different category of applications, say email, you would need to repeat the entire process.

## Slide 5: Overview
Bittorrent
RE
CCN

## Slide 6: Peer-to-Peer Networks: BitTorrent
BitTorrent history and motivation
  2002: B. Cohen debuted BitTorrent
  Key motivation: popular content
    Popularity exhibits temporal locality (Flash Crowds)
    E.g., Slashdot/Digg effect, CNN Web site on 9/11, release of a new movie or game
  Focused on efficient fetching, not searching
    Distribute same file to many peers
    Single publisher, many downloaders
  Preventing free-loading

## Slide 7: BitTorrent: Simultaneous Downloading
Divide large file into many pieces
  Replicate different pieces on different peers
  A peer with a complete piece can trade with other peers
  Peer can (hopefully) assemble the entire file
Allows simultaneous downloading
  Retrieving different parts of the file from different peers at the same time
  And uploading parts of the file to peers
  Important for very large files

## Slide 8: BitTorrent: Tracker
Infrastructure node
  Keeps track of peers participating in the torrent
Peers register with the tracker
  Peer registers when it arrives
  Peer periodically informs tracker it is still there
Tracker selects peers for downloading
  Returns a random set of peers
  Including their IP addresses
  So the new peer knows who to contact for data
Can have “trackerless” system using DHT

## Slide 9: BitTorrent: Chunks
Large file divided into smaller pieces
  Fixed-sized chunks
  Typical chunk size of 256 Kbytes
Allows simultaneous transfers
  Downloading chunks from different neighbors
  Uploading chunks to other neighbors
Learning what chunks your neighbors have
  Periodically asking them for a list
File done when all chunks are downloaded

## Slide 10: Self-certifying Names
A piece of data comes with a public key and a signature.
Client can verify the data did come from the principal by
  Checking the public key hashes into P, and
  Validating that the signature corresponds to the public key.
Challenge is to resolve the flat names into a location.

## Slide 11: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Web Server
.torrent

## Slide 12: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Get-announce
Web Server

## Slide 13: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Response-peer list
Web Server

## Slide 14: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Shake-hand
Web Server
Shake-hand

## Slide 15: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
pieces
pieces
Web Server

## Slide 16: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
pieces
pieces
pieces
Web Server

## Slide 17: BitTorrent: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Get-announce
Response-peer list
pieces
pieces
pieces
Web Server

## Slide 18: BitTorrent: Chunk Request Order
Which chunks to request?
  Could download in order
  Like an HTTP client does
Problem: many peers have the early chunks
  Peers have little to share with each other
  Limiting the scalability of the system
Problem: eventually nobody has rare chunks
  E.g., the chunks need the end of the file
  Limiting the ability to complete a download
Solutions: random selection and rarest first

## Slide 19: BitTorrent: Rarest Chunk First
Which chunks to request first?
  The chunk with the fewest available copies
  I.e., the rarest chunk first
Benefits to the peer
  Avoid starvation when some peers depart
Benefits to the system
  Avoid starvation across all peers wanting a file
  Balance load by equalizing # of copies of chunks

## Slide 20: Free-Riding Problem in P2P Networks
Vast majority of users are free-riders
  Most share no files and answer no queries
  Others limit # of connections or upload speed
A few “peers” essentially act as servers
  A few individuals contributing to the public good
  Making them hubs that basically act as a server
BitTorrent prevent free riding
  Allow the fastest peers to download from you
  Occasionally let some free loaders download

## Slide 21: Bit-Torrent: Preventing Free-Riding
Peer has limited upload bandwidth
  And must share it among multiple peers
Prioritizing the upload bandwidth: tit for tat
  Favor neighbors that are uploading at highest rate
Rewarding the top few (e.g. four) peers
  Measure download bit rates from each neighbor
  Reciprocates by sending to the top few peers
  Recompute and reallocate every 10 seconds
Optimistic unchoking
  Randomly try a new neighbor every 30 seconds
  To find a better partner and help new nodes startup

## Slide 22: BitTyrant: Gaming BitTorrent
Lots of altruistic contributors
High contributors take a long time to find good partners
Active sets are statically sized
  Peer uploads to top N peers at rate 1/N
  E.g., if N=4 and peers upload at 15, 12, 10, 9, 8, 3
  … then peer uploading at rate 9 gets treated quite well

## Slide 23: BitTyrant: Gaming BitTorrent
Best to be the Nth peer in the list, rather than 1st
  Distribution of BW suggests 14KB/s is enough
  Dynamically probe for this value
Use saved bandwidth to expand peer set
  Choose clients that maximize download/upload ratio
Discussion
  Is “progressive tax” so bad?
  What if everyone does this?

## Slide 24: BitTorrent and DHTs
Since 2005, BitTorrent supports the use of a Kademlia-based DHT (Mainline) for finding peers
Key = sha1(info section of torrent metafile)
get_peers(key)  gets a list of peers for a torrent
Each host also “puts” their own info into the DHT

## Slide 25: Aside: Chunk boundaries and Rabin Fingerprinting
4
7
8
2
8
File Data
Rabin Fingerprints
Given Value - 8
Natural Boundary
Natural Boundary
Hash 1
Hash 2

## Slide 26: Overview
Bittorrent
RE
CCN

## Slide 27: Redundant Traffic in the Internet
Lots of redundant traffic in the Internet
Redundancy due to…
  Identical objects
  Partial content match (e.g. page banners)
  Application-headers
  …
Same content traversing same set of links
Time T
Time T + 5

## Slide 28: Scale link capacities by suppressing duplicates
Enterprises
A key idea: suppress duplicates
  Popular objects, partial content matches, backups, app headers
  Effective capacity improves ~ 2X
Many approaches
  Application-layer caches
  Protocol-independent schemes
    Below app-layer
    WAN accelerators, de-duplication
  Content distribution
    CDNs like Akamai, CORAL
    Bittorrent
Point solutions  apply to specific link, protocol, or app
Mobile users
Home users
Video
Data centers
Web content
Other svcs (backup)
Wan Opt
Wan Opt
Dedup/ archival
Dedup/ archival
ISP HTTP
cache
CDN

## Slide 29: Universal need to scale capacities
Wan Opt
Wan Opt
Dedup/ archival
Dedup/ archival
ISP HTTP
cache
Network Redundancy Elimination Service
Point solutions inadequate
RE: A primitive operation supported inherently in the network
Applies to all links, flows (long/short), apps, unicast/multicast
Transparent network service; optional end-point modifications
How? Implications?
Architectural support to address universal need to scale capacities? Implications?
Bittorrent
Point solutions:
Little or no benefit in the core
✗ Point solutions:
Other links must re-implement specific RE mechanisms
✗ Point solutions: Only benefit system/app attached

## Slide 30: How? Ideas from WAN optimization
Cache
Cache
WAN link
Data center
Enterprise
Network must examine byte streams, remove duplicates, reinsert
Building blocks from WAN optimizers: RE agnostic to application, ports or flow semantics
Upstream cache = content table + fingerprint index
  Fingerprint index: content-based names for chunks of bytes in payload
  Fingerprints computed for content, looked up to identify redundant byte-strings
  Downstream cache: content table

## Slide 31: Redundancy Elimination
Object-level caching
  Application layer approaches like Web proxy caches
  Store static objects in local cache
  [Summary Cache: SIGCOMM 98, Co-operative Caching: SOSP 99]
Packet-level caching
  [Spring et. al: SIGCOMM 00]
  WAN Optimization Products: Riverbed, Peribit, Packeteer, ..
Packet-Cache
Packet-Cache
Access link
Internet
Enterprise
Packet-level caching is better than object-level caching

## Slide 32: Towards Universal RE
However, existing RE approaches apply only to point deployments
  E.g. at stub network access links, or between branch offices
They only benefit the system to which they are directly connected.
Why not make RE a native network service that everyone can use?

## Slide 33: Universal Redundancy Elimination At All Routers
Internet2
Total packets with universal RE= 12
(ignoring tiny packets)
Upstream router removes redundant bytes.
Downstream router reconstructs full packet
Total packets w/o RE = 18
Wisconsin
Berkeley
CMU
33%
Packet cache at every router

## Slide 34: Benefits of Universal Redundancy Elimination
Subsumes benefits of point deployments
Also benefits Internet Service Providers
  Reduces total traffic carried  better traffic engineering
  Better responsiveness to sudden overload (e.g. flash crowds)
Re-design network protocols with redundancy elimination in mind  Further enhance the benefits of universal RE

## Slide 35: Redundancy-Aware Routing
Total packets with RE + routing= 10
(Further 20% benefit )
Total packets with RE = 12
Wisconsin
Berkeley
CMU
45%
ISP needs information of traffic similarity between CMU and Berkeley
ISP needs to compute redundancy-aware routes

## Slide 36: Overview
Bittorrent
RE
CCN

## Slide 37: Google…
Biggest content source
Third largest ISP
source: ‘ATLAS’ Internet Observatory 2009 Annual Report’, C. Labovitz et.al.
Level(3)
Google
Global
Crossing

## Slide 38
1995 - 2007: Textbook Internet
2009: Rise of the
Hyper Giants
source: ‘ATLAS’ Internet Observatory 2009 Annual Report’, C. Labovitz et.al.

## Slide 39: What does the network look like…
ISP
ISP

## Slide 40: What should the network look like…
ISP
ISP

## Slide 41: CCN Model
Packets say ‘what’ not ‘who’ (no src or dst)
communication is to local peer(s)
upstream performance is measurable
memory makes loops impossible
Data

## Slide 42: Names
Like IP, CCN imposes no semantics on names.
‘Meaning’ comes from application, institution and global conventions:
/parc.com/people/van/presentations/CCN
/parc.com/people/van/calendar/freeTimeForMeeting
/thisRoom/projector
/thisMeeting/documents
/nearBy/available/parking
/thisHouse/demandReduction/2KW

## Slide 43: CCN Names/Security
Signed by nytimes.com/web/george
⎧ ⎪ ⎨ ⎪ ⎩
/nytimes.com/web/frontPage/v20100415/s0/0x3fdc96a4...
⎧ ⎪ ⎨ ⎪ ⎩
Signed by nytimes.com/web
0x1b048347
signature
key
nytimes.com/web/george/desktop public key
⎧ ⎪ ⎨ ⎪ ⎩
Signed by nytimes.com
Per-packet signatures using public key
  Packet also contain link to public key

## Slide 44: Names Route Interests
FIB lookups are longest match (like IP prefix lookups) which helps guarantee log(n) state scaling for globally accessible data.
Although CCN names are longer than IP identifiers, their explicit structure allows lookups as efficient as IP’s.
Since nothing can loop, state can be approximate (e.g., bloom filters).

## Slide 45: CCN node model

## Slide 46: CCN node model
get /parc.com/videos/WidgetA.mpg/v3/s2
/parc.com/videos/WidgetA.mpg/v3/s2 0
P

## Slide 47: Flow/Congestion Control
One Interest pkt  one data packet
All xfers are done hop-by-hop – so no need for congestion control
Sequence numbers are part of the name space

## Slide 48: “But ...
“this doesn’t handle conversations or realtime.
  Yes it does - see ReArch VoCCN paper.
“this is just Google.
  This is IP-for-content. We don’t search for data, we route to it.
“this will never scale.
  Hierarchically structured names give same log(n) scaling as IP but CCN tables can be much smaller since multi-source model allows inexact state (e.g., Bloom filter).

## Slide 49: What about connections/VoIP?
Key challenge - rendezvous
Need to support requesting ability to request content that has not yet been published
E.g., route request to potential publishers, and have them create the desired content in response

## Slide 51: Summary
Data Link
Physical
Applications
The Hourglass Model
‘Thin Waist’
Limits Application Innovation
Increases Data Delivery Flexibility
UDP
TCP
Data Link
Physical
Applications
The Hourglass Model
Innovation
Flexibility
Network (IP/Other)
Moving up the
Transport (TCP/Other)

## Slide 52: Next Lecture
DNS, Web and CDNs
Reading:
  CDN vs. ICN

## Slide 54: Outline
DTNs

## Slide 55: Unstated Internet Assumptions
Some path exists between endpoints
  Routing finds (single) “best” existing route
E2E RTT is not very large
  Max of few seconds
  Window-based flow/cong ctl. work well
E2E reliability works well
  Requires low loss rates
Packets are the right abstraction
  Routers don’t modify packets much
  Basic IP processing

## Slide 56: New Challenges
Very large E2E delay
  Propagation delay = seconds to minutes
  Disconnected situations can make delay worse
Intermittent and scheduled links
  Disconnection may not be due to failure (e.g. LEO satellite)
  Retransmission may be expensive
Many specialized networks won’t/can’t run IP

## Slide 57: IP Not Always a Good Fit
Networks with very small frames, that are connection-oriented, or have very poor reliability do not match IP very well
  Sensor nets, ATM, ISDN, wireless, etc
IP Basic header – 20 bytes
  Bigger with IPv6
Fragmentation function:
  Round to nearest 8 byte boundary
  Whole datagram lost if any fragment lost
  Fragments time-out if not delivered (sort of) quickly

## Slide 58: IP Routing May Not Work
End-to-end path may not exist
  Lack of many redundant links [there are exceptions]
  Path may not be discoverable [e.g. fast oscillations]
  Traditional routing assumes at least one path exists, fails otherwise
Insufficient resources
  Routing table size in sensor networks
  Topology discovery dominates capacity
Routing algorithm solves wrong problem
  Wireless broadcast media is not an edge in a graph
  Objective function does not match requirements
    Different traffic types wish to optimize different criteria
    Physical properties may be relevant (e.g. power)

## Slide 59: What about TCP?
Reliable in-order delivery streams
Delay sensitive [6 timers]:
  connection establishment, retransmit, persist, delayed-ACK, FIN-WAIT, (keep-alive)
Three control loops:
  Flow and congestion control, loss recovery
Requires duplex-capable environment
  Connection establishment and tear-down

## Slide 60: Performance Enhancing Proxies
Perhaps the bad links can be ‘patched up’
  If so, then TCP/IP might run ok
  Use a specialized middle-box (PEP)
Types of PEPs [RFC3135]
  Layers: mostly transport or application
  Distribution
  Symmetry
  Transparency

## Slide 61: TCP PEPs
Modify the ACK stream
  Smooth/pace ACKS  avoids TCP bursts
  Drop ACKs  avoids congesting return channel
  Local ACKs  go faster, goodbye e2e reliability
  Local retransmission (snoop)
  Fabricate zero-window during short-term disruption
Manipulate the data stream
  Compression, tunneling, prioritization

## Slide 62: Architecture Implications of PEPs
End-to-end “ness”
  Many PEPs move the ‘final decision’ to the PEP rather than the endpoint
  May break e2e argument [may be ok]
Security
  Tunneling may render PEP useless
  Can give PEP your key, but do you really want to?
Fate Sharing
  Now the PEP is a critical component
Failure diagnostics are difficult to interpret

## Slide 63: Architecture Implications of PEPs [2]
Routing asymmetry
  Stateful PEPs generally require symmetry
  Spacers and ACK killers don’t
Mobility
  Correctness depends on type of state
  (similar to routing asymmetry issue)

## Slide 64: Delay-Tolerant Networking Architecture
Goals
  Support interoperability across ‘radically heterogeneous’ networks
  Tolerate delay and disruption
    Acceptable performance in high loss/delay/error/disconnected environments
    Decent performance for low loss/delay/errors
Components
  Flexible naming scheme
  Message abstraction and API
  Extensible Store-and-Forward Overlay Routing
  Per-(overlay)-hop reliability and authentication

## Slide 65: Disruption Tolerant Networks

## Slide 66: Disruption Tolerant Networks

## Slide 67: Naming Data (DTN)
Endpoint IDs are processed as names
  refer to one or more DTN nodes
  expressed as Internet URI, matched as strings
URIs
  Internet standard naming scheme [RFC3986]
  Format: <scheme> : <SSP>
SSP can be arbitrary, based on (various) schemes
More flexible than DOT/DONA design but less secure/scalable

## Slide 68: Naming
Support ‘radical heterogeneity’ using URI’s:
  {scheme ID (allocated), scheme-specific-part}
  associative or location-based names/addresses optional
  Variable-length, can accommodate “any” net’s names/addresses
Endpoint IDs:
  multicast, anycast, unicast
Late binding of EID permits naming flexibility:
  EID “looked up” only when necessary during delivery
  contrast with Internet lookup-before-use DNS/IP

## Slide 69: Message Abstraction
Network protocol data unit: bundles
  “postal-like” message delivery
  coarse-grained CoS [4 classes]
  origination and useful life time [assumes sync’d clocks]
  source, destination, and respond-to EIDs
  Options: return receipt, “traceroute”-like function, alternative reply-to field, custody transfer
  fragmentation capability
  overlay atop TCP/IP or other (link) layers [layer ‘agnostic’]
Applications send/receive messages
  “Application data units” (ADUs) of possibly-large size
  Adaptation to underlying protocols via ‘convergence layer’
  API includes persistent registrations

## Slide 70: DTN Routing
DTN Routers form an overlay network
  only selected/configured nodes participate
  nodes have persistent storage
DTN routing topology is a time-varying multigraph
  Links come and go, sometimes predictably
  Use any/all links that can possibly help (multi)
  Scheduled, Predicted, or Unscheduled Links
    May be direction specific [e.g. ISP dialup]
    May learn from history to predict schedule
Messages fragmented based on dynamics
  Proactive fragmentation: optimize contact volume
  Reactive fragmentation: resume where you failed

## Slide 71: Example Routing Problem
Village
Internet
City
bike
2
3
1

## Slide 72: Example Graph Abstraction
time (days)
bike (data mule)
intermittent high capacity
Geo satellite
medium/low capacity
dial-up link
low capacity
City
Village 1
Village 2
Connectivity: Village 1 – City
bandwidth
bike
satellite
phone

## Slide 73: So, is this just e-mail?
Many similarities to (abstract) e-mail service
Primary difference involves routing, reliability and security
E-mail depends on an underlying layer’s routing:
  Cannot generally move messages ‘closer’ to their destinations in a partitioned network
  In the Internet (SMTP) case, not disconnection-tolerant or efficient for long RTTs due to “chattiness”
E-mail security authenticates only user-to-user

## Slide 74: Interoperability: Datagrams vs. Data Blocks
 | Datagrams | Data Blocks
What must be standardized? | IP Addresses NameAddress translation (DNS) | Data Labels Name  Label translation (Google?)
Application Support | Exposes much of underlying network’s capability | Practice has shown that this is what applications need
Lower Layer Support | Supports arbitrary links Requires end-to-end connectivity | Supports arbitrary links Supports arbitrary transport Support storage (both in-network and for transport)

## Slide 76: Performance: Opportunistically Aggregate Upstream Bandwidth
Challenges:
  Multi-hop: decide whether to send upstream or forward one extra hop
  Requires both data-oriented design and opportunistic forwarding
Sender broadcasts to available neighbors
Neighbors decide whether to ship the pieces upstream

## Slide 77: The DTN Routing Problem
Inputs: topology (multi)graph, vertex buffer limits, contact set, message demand matrix (w/priorities)
An edge is a possible opportunity to communicate:
  One-way: (S, D, c(t), d(t))
  (S, D): source/destination ordered pair of contact
  c(t): capacity (rate); d(t): delay
  A Contact is when c(t) > 0 for some period [ik,ik+1]
Vertices have buffer limits; edges in graph if ever in any contact, multigraph for multiple physical connections
Problem: optimize some metric of delivery on this structure
  Sub-questions: what metric to optimize?, efficiency?

## Slide 78: Knowledge-Performance Tradeoff
Use of Knowledge Oracles
Performance
Contacts
+
Queuing
+
Traffic
Contacts
Summary
Contacts
Contacts
+
Queuing
(local)
Contacts
+
Queuing
(global)
None
Algorithm
LP
MED
ED
EDLQ
EDAQ
Higher performance, higher complexity
Oracle
FC
Notes: MED == Minimized expected delay E[everything over time]
ED, EDLQ, EDAQ: Dijkstra w/ different weight fn
If ED -> EDLQ immediate
Weakness: all require pretty good contact knowledge
NOTE: FC missing from slides

## Slide 79: Knowledge-Performance Tradeoff

## Slide 80: Routing Solutions - Replication
“Intelligently” distribute identical data copies to contacts to increase chances of delivery
  Flooding (unlimited contacts)
  Heuristics: random forwarding, history-based forwarding, predication-based forwarding, etc. (limited contacts)
Given “replication budget”, this is difficult
  Using simple replication, only finite number of copies in the network [Juang02, Grossglauser02, Jain04, Chaintreau05]
  Routing performance (delivery rate, latency, etc.) heavily dependent on “deliverability” of these contacts (or predictability of heuristics)
  No single heuristic works for all scenarios!
Notes: Long delays could be incurred if the contacts selected don’t see the destination in the near future.

## Slide 81: Using Erasure Codes
Rather than seeking particular “good” contacts, “split” messages and distribute to more contacts to increase chance of delivery
  Same number of bytes flowing in the network, now in the form of coded blocks
  Partial data arrival can be used to reconstruct the original message
    Given a replication factor of r, (in theory) any 1/r code blocks received can be used to reconstruct original data
  Potentially leverage more contacts opportunity that result in lowest worse-case latency
Intuition:
  Reduces “risk” due to outlier bad contacts
Notes: High-level overview. However, in reality, we need to take those factors into consideration. We plan to look at these issues in future work.

## Slide 82: Erasure Codes
Message n blocks
Encoding
Opportunistic Forwarding
Decoding
Message n blocks

## Slide 83: DTN Security
Payload Security Header (PSH) end-to-end security header
Bundle Authentication Header (BAH) hop-by-hop security header
Bundle Agent



Bundle Application


Security Policy Router
(may check PSH value)

Source
BAH
PSH
Sender
Receiver/
Sender
Receiver/
Sender
Receiver/
Sender
Destination
BAH
BAH
BAH
credit: MITRE

## Slide 85: Naming Data (DONA)
Names organized around principals.
Names are of the form P : L.
  P is cryptographic hash of principal’s public key, and
  L is a unique label chosen by the principal.
Granularity of naming left up to principals.
Names are “flat”.

## Slide 86: Name Resolution (DONA)
Resolution infrastructure consists of Resolution Handlers.
  Each domain will have one logical RH.
Two primitives FIND(P:L) and REGISTER(P:L).
  FIND(P:L) locates the object named P:L.
  REGISTER messages set up the state necessary for the RHs to route FINDs effectively.

## Slide 87: Locating Data (DONA)
REGISTER state
FIND being routed

## Slide 88: Establishing REGISTER state
Any machine authorized to serve a datum or service with name P:L sends a REGISTER(P:L) to its first-hop RH
RHs maintain a registration table that maps a name to both next-hop RH and distance (in some metric)
REGISTERs are forwarded according to interdomain policies.
  REGISTERs from customers to both peers and providers.
  REGISTERs from peers optionally to providers/peers.

## Slide 89: Forwarding FIND(P:L)
When FIND(P:L) arrives to a RH:
  If there’s an entry in the registration table, the FIND is sent to the next-hop RH.
  If there’s no entry, the RH forwards the FIND towards to its provider.
In case of multiple equal choices, the RH uses its local policy to choose among them.

## Slide 90: Redundancy Elimination
Object-level caching
  Application layer approaches like Web proxy caches
  Store static objects in local cache
  [Summary Cache: SIGCOMM 98, Co-operative Caching: SOSP 99]
Packet-level caching
  [Spring et. al: SIGCOMM 00]
  WAN Optimization Products: Riverbed, Peribit, Packeteer, ..
Packet-Cache
Packet-Cache
Access link
Internet
Enterprise
Packet-level caching is better than object-level caching

## Slide 91: Towards Universal RE
However, existing RE approaches apply only to point deployments
  E.g. at stub network access links, or between branch offices
They only benefit the system to which they are directly connected.
Why not make RE a native network service that everyone can use?

## Slide 92: From WAN acceleration to router packet caches
Internet2
Packet cache at every router
Network RE service: apply protocol-indep RE at the packet-level on network links
 IP-layer RE service
Wisconsin
Berkeley
CMU
Router upstream removes redundant bytes
Router downstream reconstructs full packet
(Hop-by-hop works for slow links
Alternate approaches to scale to faster links…)

## Slide 93: Outline
RE
DOT
CCN
DTNs

## Slide 94: Data-Oriented Network Design
Multi-path
USB
USB
Xfer
NET
( DSL )
Xfer
NET
NET
wireless
SENDER
RECEIVER
Internet
Store-carry-forward
Multipath and Mirror support
NET
CACHE
Xfer
Features

## Slide 95: New Approach: Adding to the Protocol Stack
Transport
Network
Data Link
Physical
Router
Bridge
Internet Protocol Layers
ALG
Middleware
Application
Software-defined radio
Object Exchange
Data Transfer
Notes: Application layer gateways (ALGs) are one way. The tend to be specific to the protocols being interconnected.

## Slide 96: Data Transfer Service
Transfer Service responsible for finding/transferring data
  Transfer Service is shared by applications
How are users, hosts, services, and data named?
How is data secured and delivered reliably?
How are legacy systems incorporated?
Application Protocol
Sender
Receiver
Xfer Service
Xfer Service
and Data
Data
Notes: We believe that a possible solution to this problem is the creation of a transfer service.

## Slide 97: Naming Data (DOT)
Application defined names are not portable
Use content-naming for globally unique names
Objects represented by an OID
Objects are further sub-divided into “chunks”
Secure and scalable!
File
Desc3
Foo.txt
OID
Cryptographic Hash
Desc1
Desc2

## Slide 98: Naming Data (DOT)
All objects are named based only on their data
Objects are divided into chunks based only on their data
Object “A” is named the same
  Regardless of who sends it
  Regardless of what application deals with it
Similar parts of different objects likely to be named the same
  e.g., PPT slides v1, PPT slides v1 + extra slides
  First chunks of these objects are same
98

## Slide 99: Locating Data (DOT)
Xfer Service
Xfer Service
Sender
Receiver
Request File X
OID, Hints
put(X)
OID, Hints
get(OID, Hints)
read() data
Transfer
Plugins