## Slide 1: Achieving Single Channel, Full Duplex Wireless Communication
Jung Il Choi, Mayank Jain, Kannan Srinivasan, Philip Levis, Sachin Katti
Stanford University
Mobicom 10’

## Slide 2: Wireless Channel – Half Duplex?
“It is generally not possible for radios to receive and transmit on the same frequency band because of the interference that results.”
- Andrea Goldsmith, “Wireless Communications,” Cambridge Press, 2005.
Reason: The signal from a local transmitting antenna is hundreds of thousands of times stronger than transmissions from other nodes.

## Slide 3: Challenge for Full Duplex
Decoding method
  Subtract transmit signal from receive antenna signal
Problem: Very strong self-interference ~70dB

## Slide 4: Existing Techniques
Digital cancellation
  Subtracting known interference digital samples from received digital samples
  Reduction in interference: ~15dB
Hardware cancellation
  RF noise cancellation circuits with transmit signal as noise reference
  Reduction in interference: ~25dB
Not Enough!

## Slide 5: Antenna Cancellation
Two Transmit antennas, one Receive antenna ~30dB
Where to place the receive antenna?
  Distance from the two transmit antennas differs by an odd multiple of half the wavelength of the center frequency of transmission -- Signal add destructively

## Slide 6: Antenna Cancellation - Performance

## Slide 7: Antenna Cancellation - Performance

## Slide 8: Antenna Cancellation - Performance

## Slide 9: Antenna Cancellation - Performance

## Slide 10: Antenna Cancellation - Bandwidth
Bandwidth constraint
  λ/2 offset is precise for one frequency
  BUT not for the whole bandwidth
  WiFi (2.4G, 20MHz) => ~0.26mm precision error

## Slide 11: Antenna Cancellation - Bandwidth
Higher Bandwidth => Less Cancellation
Higher Carrier Frequency => More Cancellation⇧

## Slide 12: System Diagram
Three steps
  Antenna Cancellation ~30dB
  Hardware Cancellation ~25dB
  Digital Cancellation ~15dB
Achieves ~70dB cancellation

## Slide 13: Evaluation – Aggregate Throughput
Median throughput 92% of ideal full-duplex

## Slide 14: Evaluation – Link Reliability
Little loss in link reliability: 88% of half-duplex on average

## Slide 15: Full Duplex - Applications
True benefit lies beyond the physical layer
Breaks a basic assumption in wireless
Can solve some fundamental problems with wireless networks
  Hidden terminals
  Reducing Congestion with MAC Scheduling
  Wormhole Routing in Multihop Networks
  Cognitive Radios

## Slide 16: Mitigating Hidden Terminals
Full Duplex solves hidden terminals
N2 hears the transmission from the access point and delays its transmission, thereby avoiding a collision.

## Slide 17: Reducing Congestion with MAC Scheduling
Aggregate Network throughput: 1/n -> 1*link_cap (2n+1 nodes, star topology)

## Slide 18: Wormhole Routing in Multihop Networks
Problem: Long delivery and round-trip times in multihop networks
Solution: Forward a packet while receiving it

## Slide 19: Limitations
High Transmit Power
Bandwidth Constraint
Time-varying wireless channel
  Auto-tuning of the hardware cancellation circuit
Mayank Jain, Jung Il Choi, Taemin Kim, Dinesh Bharadia, Kannan Srinivasan, Siddharth Seth, Philip Levis, Sachin Katti and Prasun Sinha. “Practical, Real-time, Full Duplex Wireless.” In Proceedings of the 17th Annual International Conference on Mobile Computing and Networking (Mobicom 2011).

## Slide 20: Questions