## Slide 1: 15-744: Computer Networking
L-23 Next Generation Wireless

## Slide 2: Overview
802.11 Deployment patterns
White space networks
Ambient backscatter

## Slide 3: Characterizing Current Deployments
Datasets
Place Lab: 28,000 APs
  MAC, ESSID, GPS
  Selected US cities
  www.placelab.org
Wifimaps: 300,000 APs
  MAC, ESSID, Channel, GPS (derived)
  wifimaps.com
Pittsburgh Wardrive: 667 APs
  MAC, ESSID, Channel, Supported Rates, GPS
Notes: Caveats
Subset, old,
Relative strengths of each
Placelab: data collected as part of Intel’s placelab project, this is software that allows commodity hardware clients such as notebooks, PDAs to locate themselves by listening to radio beacons such as 802.11…
Wifimaps: provides a graphic visualization tool to map out access points in specific areas of the world. This under database is contributed by various war-drive efforts.
War-drive: small scale war drive of some dense areas of pittsburgh

## Slide 4: AP Stats, Degrees: Placelab
Portland | 8683 | 54
San Diego | 7934 | 76
San Francisco | 3037 | 85
Boston | 2551 | 39
#APs
Max. degree
  (Placelab: 28000 APs, MAC, ESSID, GPS)
1
2
1
50 m
Notes: Data in placelab to understand how many APs in each city are in interference range of each other.
Figure on the right shows a distribution of the number on interfering neighboring APs in the various cities. More than 4…

## Slide 5: Degree Distribution: Place Lab
Notes: Color
Don’t say graph coloring, channel selection
Search for “placelab”
Data in placelab to understand how many APs in each city are in interference range of each other.
Figure on the right shows a distribution of the number on interfering neighboring APs in the various cities. More than 4…

## Slide 6: Unmanaged Devices
Most users don’t change default channel
Channel selection must be automated
6 | 51
11 | 21
1 | 14
10 | 4
Channel
%age
WifiMaps.com (300,000 APs, MAC, ESSID, Channel)
Notes: Change titles: as was done here…
Caveat
Mention autocell is used by new vendors, but solution is ?
Newer access points include
This is top 4 channels, number are unclassified
We computed several interesting statistics about deployment and usage. 6 – default on most APs, showing that users more often than not leave their def configs on. In the table on the right, I show the relatives levels of deployment a and g. We can determine this by looking at the supporting rates info for the APs… relatively recent standardization….

## Slide 7: Overview
802.11 Deployment patterns
White space networks
Ambient backscatter

## Slide 8
Higher Frequency
Wi-Fi (ISM)
Broadcast TV

## Slide 9: What are White Spaces?
dbm
Frequency
-60
-100
“White spaces”
470 MHz
700 MHz
0
MHz
7000
MHz
TV
ISM (Wi-Fi)
700
470
2400
5180
2500
5300
are Unoccupied TV Channels
White Spaces
54-90
170-216
Wireless Mic
TV Stations in America
  50 TV Channels
  Each channel is 6 MHz wide
FCC Regulations*
    Sense TV stations and Mics
    Portable devices on channels 21 - 51

## Slide 10: The Promise of White Spaces
0
MHz
7000
MHz
TV
ISM (Wi-Fi)
700
470
2400
5180
2500
5300
54-90
174-216
Wireless Mic
More Spectrum
Longer Range
Up to 3x of 802.11g
at least 3 - 4x of Wi-Fi

## Slide 11: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
1
2
3
4
5
Each TV Channel is 6 MHz wide
 Use multiple channels for more bandwidth
Spectrum is Fragmented
Chart: # Contiguous Channels
| 1 | 2 | 3 | 4 | 5 | 6 | >6
Urban | 0.739 | 0.231 | 0 | 0.028 | 0 | 0 | 0
Suburban | 0.716 | 0.15 | 0.056 | 0.056 | 0 | 0.018 | 0
Rural | 0.367 | 0.122 | 0.122 | 0.102 | 0.081 | 0.04 | 0.14

## Slide 12: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
Location impacts spectrum availability
 Spectrum exhibits spatial variation
Cannot assume same
channel free everywhere
1
2
3
4
5
Spatial Variation
TV
Tower

## Slide 13: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
Incumbents appear/disappear over time
 Must reconfigure after disconnection
Spatial Variation
Cannot assume same
channel free everywhere
1
2
3
4
5
1
2
3
4
5
Temporal Variation
Same Channel will
not always be free
Any connection can be
disrupted any time

## Slide 14: Channel Assignment in Wi-Fi
Fixed Width Channels
 Optimize which channel to use
1
6
11
1
6
11

## Slide 15: Spectrum Assignment in WhiteFi
1
2
3
4
5
Spatial Variation
 BS must use channel iff free at client
Fragmentation
 Optimize for both, center channel and width
1
2
3
4
5
Spectrum Assignment Problem
Goal
Maximize Throughput
Include
Spectrum at clients
Assign
Center Channel
Width
&

## Slide 16: Accounting for Spatial Variation
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

=
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

1
2
3
4
5

## Slide 17: Intuition
BS
Use widest possible channel
Intuition
1
3
4
5
2
Limited by most busy channel
But
Carrier Sense Across All Channels
All channels must be free
  ρBS(2 and 3 are free) = ρBS(2 is free) x ρBS(3 is free)
Tradeoff between wider channel widths
and opportunity to transmit on each channel

## Slide 18: Discovering a Base Station
Can we optimize this discovery time?
1
2
3
4
5
Discovery Time = (B x W)
1
2
3
4
5
How does the new client discover channels used by the BS?
BS and Clients must use same channels
Fragmentation
 Try different center channel and widths

## Slide 19: SIFT, by example
ADC
SIFT
Time
Amplitude
10 MHz
5 MHz
SIFT
Pattern match in time domain
Does not decode packets
Data
ACK
SIFS

## Slide 20: Overview
802.11 Deployment patterns
White space networks
Ambient backscatter

## Slide 21: Goal
Interactive devices that compute and communicate without batteries

## Slide 22: What We Are After
How to power computation, sensing,
and communication?

## Slide 23: Leverage Existing Wireless Signals
TV
Cellular
Wi-Fi
Available at almost any time and place, rain or shine

## Slide 24: Recent Work Harvests 10s of μW [‘09]
Enough for computation and sensing
Orders of magnitude less power than needed for radio communication [‘13]

## Slide 25: Challenge: Communication Between Battery-Free Devices
Generating radio signals is expensive
Could duty cycle
  Limits interactive applications
  Can we communicate without
  either device generating radio signals?

## Slide 26: Ambient Backscatter
Alice
Bob
‘0’ bit – Absorb TV Signals
‘1’ bit – Reflect TV signals
TV Tower
Reception
Unaffected
Use existing signals instead of generating our own
Additional
Multipath
Works with only ~5% of the harvested power!

## Slide 27
Ambient Backscatter
Reader sends constant wave
Receive chain: 100s of mW
Reader centrally coordinates
RFID
Reader
Tag
Chart: 

## Slide 28
Tag
Tag
Ambient Backscatter
Uses uncontrollable signals
Receive chain: 0.5 μW
Need distributed MAC
Chart: 
Reader
Tag
Reader sends constant wave
Receive chain: 100s of mW
Reader centrally coordinates
Chart: 
RFID

## Slide 29: Challenges
Extracting backscattered signals from ambient signals we don’t control
Decoding on a battery-free device
Designing distributed MAC for battery-free devices

## Slide 30: How Do We Extract The Backscattered Signals?
Case 1: Alice absorbs
At Bob: TV signal
Case 2: Alice reflects
At Bob: TV signal
+ Weak Reflection
Alice’s reflections change the average amplitude
Alice
Bob
TV Tower

## Slide 31: Solution: Detect Changes in Average Amplitude
Chart: 
Chart: 
Chart: 
Chart: 
Alice Sends 1010…
Alice Inactive
Moving Window Average

## Slide 32
If we had digital samples, averaging would be easy
Need power-hungry analog-to-digital converters

## Slide 33: Use RC Circuits to Average
Capacitor slowly charges/discharges when voltage is applied/removed
Provides a cheap, analog,
exponential moving average
R
C
Chart: 
Chart: 

## Slide 34: Use RC Circuits to Average
R
C
Capacitor slowly charges/discharges when voltage is applied/removed
Provides a cheap, analog,
exponential moving average
Chart: 
By picking the right RC values,
we can selectively filter out the high TV frequencies
Chart: 

## Slide 35: Now that we can decode bits…
Physical Layer
Link Layer
Distributed MAC?

## Slide 36: We Use CSMA
CSMA uses carrier sense, i.e. energy detection
Battery-free devices do not have energy levels
  Requires power-hungry ADCs
  Challenge: Energy detection
  without access to the energy levels

## Slide 37: Solution: Leverage Hardware Properties for Energy Detection
RC circuit filters out the TV signals  Removes high-amplitude variations
Hardware elements have a threshold  Low-amplitudes don’t change output
Chart: 
Chart: 
Constant Output
In the absence of backscattering,
we see a constant output

## Slide 38: Solution: Leverage Hardware Properties for Energy Detection
No backscatter  See all 0s or all 1s
Backscatter  See many transitions
Use bit transitions as proxy for
energy detection

## Slide 39: Prototype Using Off-the-Shelf Components
Battery-free
Harvests and backscatters TV signals at 539 MHz
Microcontroller performs computation
LEDs
Touch Sensors

## Slide 40: Tested Locations
Seattle area with a 1MW TV tower at 539 MHz
Indoor and outdoor environments
Distances up to 10.5 km from the TV tower
  TV power ranged between -24dBm and -8dBm

## Slide 41: What Bit Rates Can We Achieve?
Three bit rates: 10kbps, 1kbps, 100bps
BER versus distance between two devices
Distance

## Slide 42: What Bit Rates Can We Achieve?
Chart: Distance Between Tags (ft)
| 0.49 | 0.82 | 1.15 | 1.48 | 1.8 | 2.13 | 2.46 | 2.79 | 3.12 | 3.44
100 bps | 0.0001 | 0.004 | 0.01 | 0.07
1 kbps | 0.0001 | 0.0225 | 0.0903 | 0.229 | 0.3446
10 kbps | 0.0001 | 0.00175 | 0.09156 | 0.0771 | 0.14929 | 0.13839 | 0.08661 | 0.12947 | 0.23305
100 bps
10 kbps
1 kbps
These results show the feasibility
of Ambient Backscatter

## Slide 43: Identifying Misplaced Items
With ambient backscatter, devices can figure out they are misplaced on their own
In Grocery stores or Warehouses (e.g., Amazon)

## Slide 44: Identifying Misplaced Items
Works even if not all tags are in range of a reader

## Slide 45: Overview
Carrier Sense vs. Rate Adaptation
Wireless TCP
802.11 Deployment patterns
Mesh networks
White space networks

## Slide 46: Roofnet
Share a few wired Internet connections
Goals
  Operate without extensive planning or central management
  Provide wide coverage and acceptable performance
Design decisions
  Unconstrained node placement
  Omni-directional antennas
  Multi-hop routing
  Optimization of routing for throughput in a slowly changing network

## Slide 47: Roofnet Design
Deployment
  Over an area of about four square kilometers in Cambridge, Messachusetts
  Most nodes are located in buildings
    3~4 story apartment buildings
    8 nodes are in taller buildings
  Each Rooftnet node is hosted by a volunteer user
Hardware
  PC, omni-directional antenna, hard drive …
  802.11b card
    RTS/CTS disabled
    Share the same 802.11b channel
    Non-standard “pseudo-IBSS” mode
      Similar to standard 802.11b IBSS (ad hoc)
      Omit beacon and BSSID (network ID)

## Slide 48: Roofnet Node Map
1 kilometer

## Slide 49: Typical Rooftop View

## Slide 50: Roofnet

## Slide 51: Lossy Links are Common

## Slide 52: Delivery Probabilities are Uniformly Distributed

## Slide 53: Delivery vs. SNR
SNR not a good predictor

## Slide 54: Key Implications
Lack of a link abstraction!
  Links aren’t on or off… sometimes in-between
Protocols must take advantage of these intermediate quality links to perform well
How unique is this to Roofnet?
  Cards designed for indoor environments used outdoors

## Slide 55: Evaluation
Method
  Multi-hop TCP
    15 second one-way bulk TCP transfer between each pair of Roofnet nodes
  Single-hop TCP
    The direct radio link between each pair of routes
  Loss matrix
    The loss rate between each pair of nodes using 1500-byte broadcasts
  Multi-hop density
    TCP throughput between a fixed set of four nodes
    Varying the number of Roofnet nodes that are participating in routing

## Slide 56: Evaluation
Basic Performance (Multi-hop TCP)
  The routes with low hop-count have much higher throughput
  Multi-hop routes suffer from inter-hop collisions

## Slide 57: Evaluation
Basic Performance (Multi-hop TCP)
  TCP throughput to each node from its chosen gateway
  Round-trip latencies for 84-byte ping packets to estimate interactive delay

## Slide 58: Evaluation
Link Quality and Distance (Single-hop TCP, Multi-hop TCP)
  Most available links are between 500m and 1300m and give 500 kbits/s
  Srcr
    Use almost all of the links faster than 2 Mbits/s and ignore majority of the links which are slower than that
    Fast short hops are the best policy

## Slide 59: Evaluation
Link Quality and Distance (Multi-hop TCP, Loss matrix)
  Median delivery probability is 0.8
  1/4 links have loss rates of 50% or more
  802.11 detects the losses with its ACK mechanism and resends the packets

## Slide 60: Evaluation
Architectural Alternatives
  Maximize the number of additional nodes with non-zero throughput to some gateway
  Ties are broken by average throughput

## Slide 61: Evaluation
Inter-hop Interference (Multi-hop TCP, Single-hop TCP)
  Concurrent transmissions on different hops of a route collide and cause packet loss

## Slide 62: Roofnet Summary
The network’s architectures favors
  Ease of deployment
  Omni-directional antennas
  Self-configuring software
  Link-quality-aware multi-hop routing
Evaluation of network performance
  Average throughput between nodes is 627kbits/s
  Well served by just a few gateways whose position is determined by convenience
  Multi-hop mesh increases both connectivity and throughput

## Slide 63: Roofnet Link Level Measurements
Analyze cause of packet loss
Neighbor Abstraction
  Ability to hear control packets or No Interference
  Strong correlation between BER and S/N
RoofNet pairs communicate
  At intermediate loss rates
  Temporal Variation
  Spatial Variation

## Slide 64: A Roofnet Self-Installation Kit
Computer ($340)
533 MHz PC, hard disk, CDROM
802.11b card ($155)
Engenius Prism 2.5, 200mW
Software (“free”)
Our networking software based on Click
Antenna ($65)
8dBi, 20 degree vertical
Miscellaneous ($75)
Chimney Mount,
Lightning Arrestor, etc.
50 ft. Cable ($40)
Low loss (3dB/100ft)
Takes a user about 45 minutes to install on a flat roof
Total: $685

## Slide 65: Software and Auto-Configuration
Linux, routing software, DHCP server, web server …
Automatically solve a number of problems
  Allocating addresses
  Finding a gateway between Roofnet and the Internet
  Choosing a good multi-hop route to that gateway
Addressing
  Roofnet carries IP packets inside its own header format and routing protocol
  Assign addresses automatically
  Only meaningful inside Roofnet, not globally routable
  The address of Roofnet nodes
    Low 24 bits are the low 24 bits of the node’s Ethernet address
    High 8 bits are an unused class-A IP address block
  The address of hosts
    Allocate 192.168.1.x via DHCP and use NAT between the Ethernet and Roofnet

## Slide 66: Software and Auto-Configuration
Gateway and Internet Access
  A small fraction of Roofnet users will share their wired Internet access links
  Nodes which can reach the Internet
    Advertise itself to Roofnet as an Internet gateway
    Acts as a NAT for connection from Roofnet to the Internet
  Other nodes
    Select the gateway which has the best route metric
  Roofnet currently has four Internet gateways

## Slide 67: Roofnet Design - Routing Protocol
Srcr
  Find the highest throughput route between any pair of Roofnet nodes
  Source-routes data packets like DSR
  Maintains a partial database of link metrics
Learning fresh link metrics
  Forward a packet
  Flood to find a route
  Overhear queries and responses
Finding a route to a gateway
  Each Roofnet gateway periodically floods a dummy query
  When a node receives a new query, it adds the link metric information
  The node computes the best route
  The node re-broadcasts the query
  Send a notification to a failed packet’s source if the link condition is changed

## Slide 68: Roofnet Design
Routing Metric
  ETT (Estimated Transmission Time) metric
    Srcr chooses routes with ETT
    Predict the total amount of time it would take to send a data packet
    Take into account link’s highest-throughput transmit bit-rate and delivery probability
    Each Roofnet node sends periodic 1500-byte broadcasts
Bit-rate Selection
  802.11b transmit bit-rates
    1, 2, 5.5, 11 Mbits/s
  SampleRate
    Judge which bit-rate will provide the highest throughput
    Base decisions on actual data transmission
    Periodically sends a packet at some other bit-rate

## Slide 69: ETX measurement results
Delivery is probabilistic
  A 1/r^2 model wouldn’t really predict this!
  Sharp cutoff (by spec) of “good” vs “no” reception. Intermediate loss range band is just a few dB wide!
Why?
  Biggest factor: Multi-path interference
    802.11 receivers can suppress reflections < 250ns
    Outdoor reflections delay often > 1 \mu sec
    Delay offsets == symbol time look like valid symbols (large interferece)
    Offsets != symbol time look like random noise
    Small changes in delay == big changes in loss rate

## Slide 70: Deciding Between Links
Most early protocols: Hop Count
  Link-layer retransmission can mask some loss
  But: a 50% loss rate means your link is only 50% as fast!
Threshold?
  Can sacrifice connectivity. 
  Isn’t a 90% path better than an 80% path?
Real life goal: Find highest throughput paths

## Slide 71: Is there a better metric?
Cut-off threshold
  Disconnected network
Product of link delivery ratio along path
  Does not account for inter-hop interference
Bottleneck link (highest-loss-ratio link)
  Same as above
End-to-end delay
  Depends on interface queue lengths

## Slide 72: ETX Metric Design Goals
Find high throughput paths
Account for lossy links
Account for asymmetric links
Account for inter-link interference
Independent of network load (don’t incorporate congestion)

## Slide 73: Forwarding Packets is Expensive
Throughput of 802.11b =~ 11Mbits/s
  In reality, you can get about 5.
What is throughput of a chain?
  A  B  C ?
  A  B  C  D ?
  Assume minimum power for radios.
Routing metric should take this into account! Affects throughput

## Slide 74: ETX
Measure each link’s delivery probability with broadcast probes (& measure reverse)
P(delivery) = ( df * dr ) (ACK must be delivered too…)
Link ETX = 1 / P(delivery)
Route ETX =  link ETX
  Assumes all hops interfere - not true, but seems to work okay so far

## Slide 75: ETX: Sanity Checks
ETX of perfect 1-hop path: 1
ETX of 50% delivery 1-hop path: 2
ETX of perfect 3-hop path: 3
(So, e.g., a 50% loss path is better than a perfect 3-hop path! A threshold would probably fail here…)

## Slide 76: Rate Adaptation
What if links @ different rates?
ETT – expected transmission time
  ETX / Link rate = 1 / ( P(delivery) * Rate)
What is best rate for link?
  The one that maximizes ETT for the link!
  SampleRate is a technique to adaptively figure this out.

## Slide 77: Discussion
Value of implementation & measurement
  Simulators did not “do” multipath
    Routing protocols dealt with the simulation environment just fine
    Real world behaved differently and really broke a lot of the proposed protocols that worked so well in simulation!
Rehash: Wireless differs from wired…
Metrics: Optimize what matters; hop count often a very bad proxy in wireless
What we didn’t look at: routing protocol overhead
  One cool area: Geographic routing

## Slide 78: Growing Interference in Unlicensed Bands
Anecdotal evidence of problems, but how severe?
Characterize how 802.11 operates under interference in practice
Other 802.11
Notes: The main problem we’re concerned with today is the impact of growing RF interference in unlicensed spectrum such as the 2.4GHz band used by 802.11. There has recently been a spate of anecdotal reports about the increasing severity of RF interference problems on the operation of wireless networks such as 802.11, but we don’t yet clearly know what the magnitude or the trend of the problem is. So, we would like to characterize how 802.11 performs under interference in reality.
Today, an 802.11 network has to contend with other 802.11 networks, as well as with other wireless devices that share the same spectrum, such as cordless phones, microwave ovens, car alarm systems, bluetooth, and a growing variety of other unlicensed band devices.

## Slide 79: What do we expect?
Throughput to decrease linearly with interference
There to be lots of options for 802.11 devices to tolerate interference
  Bit-rate adaptation
  Power control
  FEC
  Packet size variation
  Spread-spectrum processing
  Transmission and reception diversity
Interferer power
(log-scale)
Throughput (linear)
Theory
Notes: The standard SINR or (Signal to Interference and Noise Ratio) model predicts that throughput should decrease linearly with interferer power. The interferer power is on a log-scale. If this standard model holds in practice, then 802.11 devices have a variety of options at their disposal to tolerate interference gracefully. For example, they can change the bit rate at which they transmit, they can change the transmission power, they can use forward error correction, they can use smaller packets, and exploit various diversity techniques for transmission and reception, such as using multi-antenna systems.

## Slide 80: Key Questions
How damaging can a low-power and/or narrow-band interferer be?
How can today’s hardware tolerate interference well?
  What 802.11 options work well, and why?
Notes: The key questions before us are whether 802.11 copes well with different types of low-power and/or narrow-band interferers, and which of the 802.11 options work well in practice, and why.

## Slide 81: What we see
Effects of interference more severe in practice
Caused by hardware limitations of commodity cards, which theory doesn’t model
Practice
Interferer power
(log-scale)
Throughput (linear)
Theory
Notes: The most interesting result we see is that the effects of interference are more severe in practice than theory would predict. There is a large gap between theory and practice at both low-end and high-end of the interference range. In fact, we find that the link throughput can drop to zero at medium to high end of the interference range. Such a rapid and severe degradation in performance is caused by several hardware limitations of commodity cards, which are not adequately modeled by theory.

## Slide 82: Experimental Setup
802.11 Client
Access Point
UDP flow
802.11 Interferer
Notes: Our setup is a controlled testbed within an office building consisting of 802.11 transmitter and receiver that use different commodity cards. They exchange UDP flows. Interferers are various types of wireless devices such as an 802.11 interferer that can output arbitrary modulated 802.11 bit patterns, ZigBee sensor nodes, cordless phones, and camera jammers. They represent both worst-case natural and adversarial interferers arising in practice. The interferer varies in power as its physical distance to the 802.11 link changes. In order to simulate the effects of such an interferer in a controlled manner, we use hardware attenuators to vary the output power. The picture here shows such an attenuated 802.11 interferer.

## Slide 83: 802.11 Receiver Path
Extend SINR model to capture these vulnerabilities
Interested in worst-case natural or adversarial interference
  Have developed range of “attacks” that trigger these vulnerabilities
MAC
PHY
Timing Recovery
Preamble Detector/ Header CRC-16 Checker
AGC
Barker
Correlator
Descrambler
ADC
6-bit
samples
To RF Amplifiers
Receiver
Data
(includes beacons)
Demodulator
Analog
signal
SYNC
SFD
CRC
Payload
PHY header
Notes: For example, when three consecutive beacons from the AP are lost by the MAC layer, the link is commonly assumed to be dead.

## Slide 84: Timing Recovery Interference
Interferer sends continuous SYNC pattern
Interferes with packet acquisition (PHY reception errors)
Weak interferer
Moderate
interferer
Log-scale
Notes: We found an interferer that sends a continuous sync pattern

## Slide 85: Interference Management
Interference will get worse
  Density/device diversity is increasing
  Unlicensed spectrum is not keeping up
Spectrum management
  “Channel hopping” 802.11 effective at mitigating some performance problems [Sigcomm07]
  Coordinated spectrum use – based on RF sensor network
Transmission power control
  Enable spatial reuse of spectrum by controlling transmit power
  Must also adapt carrier sense behavior to take advantage

## Slide 86: Is it Bursty Interference?
May interfere but not impact SNR measurement

## Slide 87: Two Different Roofnet Links
Top is typical of bursty interference, bottom is not
Most links are like the bottom

## Slide 88: Is it Multipath Interference?
Simulate with channel emulator

## Slide 89: A Plausible Explanation
Multi-path can produce intermediate loss rates
Appropriate multi-path delay is possible due to long-links